## Slide 1: Memory; Sequential & Clocked Circuits; Finite State Machines
COS 116, Spring 2012
Adam Finkelstein
Notes: Did an extensive demo that clarified what determines clock speed.

## Slide 2: Recap: Boolean Logic
Boolean Expression E = S AND D
Truth table: Value of E for every possible D, S. TRUE=1; FALSE= 0.
0
0
1
0
1
1
1
1
0
0
0
0
E
S
D
Boolean Circuit
E
S
D
Truth table has
rows if
the number of
variables is k

## Slide 3: Boole’s reworking of Clarke’s “proof” of existence of God (see handout – after midterm)
General idea: Try to prove that Boolean expressions E1, E2, …, Ek cannot simultaneously be true
Method: Show E1· E2 · … · Ek = 0
Discussion for after Break: What exactly does Clarke’s “proof” prove? How convincing is such a proof to you?
Also: Do Google search for “Proof of God’s Existence.”

## Slide 4: Circuit for binary addition?
Want to design a circuit to add any two N-bit integers.
Q: Is the truth table method useful for N=64?
    25
    + 29
    54
    11001
    11101
    110110

## Slide 5: Modular design for N-bit adder
Suffices to use N 1-bit adders!
cN-1 cN-2 … c1 c0
aN-1 aN-2 … a1 a0
+ bN-1 bN-2 … b1 b0
sN sN-1 sN-2 … s1 s0
Carry bits

## Slide 6: Modular design
Have small number
of basic components.
Put them together to achieve desired functionality
Basic principle of modern industrial design; recurring theme in next few lectures.

## Slide 7: 1-bit adder
(Carry from previous adder)
Do yourself: Write truth table, circuit.
ak
bk
ck
1-ADD
ck+1
sk
Carry bit for next adder.

## Slide 8: A Full Adder (see logic reading)

## Slide 9: Timing Diagram
5V
0V
Time
X
5V
0V
Time
output
NOT gate
delay

## Slide 10: Memory
Rest of this lecture:
How boolean circuits have “memory”.

## Slide 11: What do you understand by ‘memory’…?
How can you tell that a 1-year old child has it?
Behaviorist’s answer: Child’s actions depend upon past events.

## Slide 12: Combinational circuit
Boolean gates connected by wires
Important: no cycles allowed
Wires: transmit voltage
(and hence value)
Today: Circuits with loops; aka “Sequential Circuits”

## Slide 13: Matt likes Sue but he doesn’t like changing his mind
Represent with a circuit: Matt will go to the party if Sue goes or if he already wanted to go
S
M
Is this well-behaved?!?

## Slide 14: Sequential Circuits
Circuits with AND, OR and NOT gates.
Cycles are allowed (ie outputs can feed back into inputs)
Can exhibit “memory”.
Sometimes may have “undefined” values

## Slide 15: Enter Rita
Matt will go to the party if Sue goes OR if the following holds: if Rita does not go and he already wanted to go.
?
M
S
R
M
R, S: “control” inputs
What combination of R, S changes M?

## Slide 16: R-S Flip-Flop
S
R
M

## Slide 17: A more convenient form of memory
Fact: “Data Flip-Flop” (or “D flip flop”) can be created using R-S flip flops!
No “undefined” outputs ever!

## Slide 18: Register with 4 bits of memory

## Slide 19: What controls the “Write” signal?

## Slide 20
The “symphony” inside a computer
Clock
Combinational circuit
Memory
Clocked Sequential Circuit (aka Synchronous Circuits)

## Slide 21: Clocked Sequential Circuits

## Slide 22: Synchronous Sequential Circuit (aka Clocked Sequential Circuit)
CLOCK
INPUTS
Combinational Circuit
Memory
(flip-flops)

## Slide 23: Shorthand
Combinational Circuit
Memory
(flip-flops)
CLK
This stands for “lots of wires”

## Slide 24: Clock Speeds
Heinrich Hertz 1857-94
1974 | Intel 8080 | 2 MHz (Mega = Million)
1981 | Original IBM PC | 4.77 MHz
1993 | Intel Pentium | 66 MHz
2005 | Pentium 4 | 3.4 GHz (Giga = Billion)

## Slide 25: What limits clock speed?
Combinational Circuit
Memory
(flip-flops)
CLK
Delays in combinational logic (remember the adder)
During 1 clock cycle of Pentium 4, light travels: 4 inches

## Slide 26: Finite State Machines
Next lecture….

## Slide 27: Example: State diagram for automatic door at grocery store
Closed
Open
Detected Person
No Person Detected
Detected Person
No Person Detected