## Slide 1: Switches Reading: Section 3.2
COS 461: Computer Networks
Spring 2006 (MW 1:30-2:50 in Friend 109)
Jennifer Rexford
Teaching Assistant: Mike Wawrzoniak
http://www.cs.princeton.edu/courses/archive/spring06/cos461/

## Slide 2: Midterm Exam
Location
  Room 104 in the Computer Science building
  NOT in the usual Friend classroom
Time
  1:30pm-2:50pm on Wednesday March 15
  Usual class time
Open book, notes, slides, etc.
  Just no computer, PDA, calculator, etc.
Preparation
  Required reading from textbook, plus lecture notes
  Practice exams, plus questions in the text book

## Slide 3: Goals of Today’s Lecture
Devices that shuttling packets at different layers
  Repeaters and hubs
  Bridges and switches
  Routers
Switch protocols and mechanisms
  Dedicated access and full-duplex transfers
  Cut-through switching
  Self learning of the switch table
  Spanning trees
  Virtual LANs (VLANs)

## Slide 4: Shuttling Data at Different Layers
Different devices switch different things
  Physical layer: electrical signals (repeaters and hubs)
  Link layer: frames (bridges and switches)
  Network layer: packets (routers)
Application gateway
Transport gateway
Router
Bridge, switch
Repeater, hub
Frame header
Packet header
TCP header
User
data

## Slide 5: Physical Layer: Repeaters
Distance limitation in local-area networks
  Electrical signal becomes weaker as it travels
  Imposes a limit on the length of a LAN
Repeaters join LANs together
  Analog electronic device
  Continuously monitors electrical signals on each LAN
  Transmits an amplified copy

## Slide 6: Physical Layer: Hubs
Joins multiple input lines electrically
  Designed to hold multiple line cards
  Do not necessarily amplify the signal
Very similar to repeaters
  Also operates at the physical layer
hub
hub
hub
hub

## Slide 7: Limitations of Repeaters and Hubs
One large collision domain
  Every bit is sent everywhere
  So, aggregate throughput is limited
  E.g., three departments each get 10 Mbps independently
  … and then connect via a hub and must share 10 Mbps
Cannot support multiple LAN technologies
  Does not buffer or interpret frames
  So, can’t interconnect between different rates or formats
  E.g., 10 Mbps Ethernet and 100 Mbps Ethernet
Limitations on maximum nodes and distances
  Does not circumvent the limitations of shared media
  E.g., still cannot go beyond 2500 meters on Ethernet

## Slide 8: Link Layer: Bridges
Connects two or more LANs at the link layer
  Extracts destination address from the frame
  Looks up the destination in a table
  Forwards the frame to the appropriate LAN segment
Each segment is its own collision domain
host
host
host
host
host
host
host
host
host
host
host
host
Bridge

## Slide 9: Link Layer: Switches
Typically connects individual computers
  A switch is essentially the same as a bridge
  … though typically used to connect hosts, not LANs
Like bridges, support concurrent communication
  Host A can talk to C, while B talks to D
switch
A
B
C
D

## Slide 10: Dedicated Access and Full Duplex
Dedicated access
  Host has direct connection to the switch
  … rather than a shared LAN connection
Full duplex
  Each connection can send in both directions
  Host sending to switch, and host receiving from switch
  E.g., in 10BaseT and 100Base T
Completely avoids collisions
  Each connection is a bidirectional point-to-point link
  No need for carrier sense, collision detection, and so on

## Slide 11: Bridges/Switches: Traffic Isolation
Switch breaks subnet into LAN segments
Switch filters packets
  Frame only forwarded to the necessary segments
  Segments become separate collision domains
hub
hub
hub
switch/bridge
collision domain
collision domain
collision domain

## Slide 12: Advantages Over Hubs/Repeaters
Only forwards frames as needed
  Filters frames to avoid unnecessary load on segments
  Sends frames only to segments that need to see them
Extends the geographic span of the network
  Separate collision domains allow longer distances
Improves privacy by limiting scope of frames
  Hosts can “snoop” the traffic traversing their segment
  … but not all the rest of the traffic
Applies carrier sense and collision detection
  Does not transmit when the link is busy
  Applies exponential back-off after a collision
Joins segments using different technologies

## Slide 13: Disadvantages Over Hubs/Repeaters
Delay in forwarding frames
  Bridge/switch must receive and parse the frame
  … and perform a look-up to decide where to forward
  Storing and forwarding the packet introduces delay
  Solution: cut-through switching
Need to learn where to forward frames
  Bridge/switch needs to construct a forwarding table
  Ideally, without intervention from network administrators
  Solution: self-learning
Higher cost
  More complicated devices that cost more money

## Slide 14: Motivation For Cut-Through Switching
Buffering a frame takes time
  Suppose L is the length of the frame
  And R is the transmission rate of the links
  Then, receiving the frame takes L/R time units
Buffering delay can be a high fraction of total delay
  Propagation delay is small over short distances
  Making buffering delay a large fraction of total
  Analogy: large group walking through NYC
A
B
switches

## Slide 15: Cut-Through Switching
Start transmitting as soon as possible
  Inspect the frame header and do the look-up
  If outgoing link is idle, start forwarding the frame
Overlapping transmissions
  Transmit the head of the packet via the outgoing link
  … while still receiving the tail via the incoming link
  Analogy: different folks crossing different intersections
A
B
switches

## Slide 16: Motivation For Self Learning
Switches forward frames selectively
  Forward frames only on segments that need them
Switch table
  Maps destination MAC address to outgoing interface
  Goal: construct the switch table automatically
switch
A
B
C
D

## Slide 17: Self Learning: Building the Table
When a frame arrives
  Inspect the source MAC address
  Associate the address with the incoming interface
  Store the mapping in the switch table
  Use a time-to-live field to eventually forget the mapping
A
B
C
D
Switch learns how to reach A.

## Slide 18: Self Learning: Handling Misses
When frame arrives with unfamiliar destination
  Forward the frame out all of the interfaces
  … except for the one where the frame arrived
  Hopefully, this case won’t happen very often
A
B
C
D
When in doubt, shout!

## Slide 19: Switch Filtering/Forwarding
When switch receives a frame:
index switch table using MAC dest address
if entry found for destination then{
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 20: Flooding Can Lead to Loops
Switches sometimes need to broadcast frames
  Upon receiving a frame with an unfamiliar destination
  Upon receiving a frame sent to the broadcast address
Broadcasting is implemented by flooding
  Transmitting frame out every interface
  … except the one where the frame arrived
Flooding can lead to forwarding loops
  E.g., if the network contains a cycle of switches
  Either accidentally, or by design for higher reliability

## Slide 21: Solution: Spanning Trees
Ensure the topology has no loops
  Avoid using some of the links when flooding
  … to avoid forming a loop
Spanning tree
  Sub-graph that covers all vertices but contains no cycles
  Links not in the spanning tree do not forward frames

## Slide 22: Constructing a Spanning Tree
Need a distributed algorithm
  Switches cooperate to build the spanning tree
  … and adapt automatically when failures occur
Key ingredients of the algorithm
  Switches need to elect a “root”
    The switch with the smallest identifier
  Each switch identifies if its interface is on the shortest path from the root
    And it exclude from the tree if not
  Messages (Y, d, X)
    From node X
    Claiming Y is the root
    And the distance is d
root
One hop
Three hops

## Slide 23: Steps in Spanning Tree Algorithm
Initially, each switch thinks it is the root
  Switch sends a message out every interface
  … identifying itself as the root with distance 0
  Example: switch X announces (X, 0, X)
Switches update their view of the root
  Upon receiving a message, check the root id
  If the new id is smaller, start viewing that switch as root
Switches compute their distance from the root
  Add 1 to the distance received from a neighbor
  Identify interfaces not on a shortest path to the root
  … and exclude them from the spanning tree

## Slide 24: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Then, switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Then, switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 25: Example From Switch #4’s Viewpoint
Switch #2 hears about switch #1
  Switch 2 hears (1, 1, 3) from 3
  Switch 2 starts treating 1 as root
  And sends (1, 2, 2) to neighbors
Switch #4 hears from switch #2
  Switch 4 starts treating 1 as root
  And sends (1, 3, 4) to neighbors
Switch #4 hears from switch #7
  Switch 4 receives (1, 3, 7) from 7
  And realizes this is a longer path
  So, prefers its own three-hop path
  And removes 4-7 Iink from the tree
1
2
3
4
5
6
7

## Slide 26: Robust Spanning Tree Algorithm
Algorithm must react to failures
  Failure of the root node
    Need to elect a new root, with the next lowest identifier
  Failure of other switches and links
    Need to recompute the spanning tree
Root switch continues sending messages
  Periodically reannouncing itself as the root (1, 0, 1)
  Other switches continue forwarding messages
Detecting failures through timeout (soft state!)
  Switch waits to hear from others
  Eventually times out and claims to be the root
See Section 3.2.2 in the textbook for details and another example

## Slide 27: Evolution Toward Virtual LANs
In the olden days…
  Thick cables snaked through cable ducts in buildings
  Every computer they passed was plugged in
  All people in adjacent offices were put on the same LAN
  Independent of whether they belonged together or not
More recently…
  Hubs and switches changed all that
  Every office connected to central wiring closets
  Often multiple LANs (k hubs) connected by switches
  Flexibility in mapping offices to different LANs
Group users based on organizational structure, rather than the physical layout of the building.

## Slide 28: Why Group by Organizational Structure?
Security
  Ethernet is a shared media
  Any interface card can be put into “promiscuous” mode
  … and get a copy of all of the traffic (e.g., midterm exam)
  So, isolating traffic on separate LANs improves security
Load
  Some LAN segments are more heavily used than others
  E.g., researchers running experiments get out of hand
  … can saturate their own segment and not the others
  Plus, there may be natural locality of communication
  E.g., traffic between people in the same research group

## Slide 29: People Move, and Roles Change
Organizational changes are frequent
  E.g., faculty office becomes a grad-student office
  E.g., graduate student becomes a faculty member
Physical rewiring is a major pain
  Requires unplugging the cable from one port
  … and plugging it into another
  … and hoping the cable is long enough to reach
  … and hoping you don’t make a mistake
Would like to “rewire” the building in software
  The resulting concept is a Virtual LAN (VLAN)

## Slide 30: Example: Two Virtual LANs
Red VLAN and Orange VLAN
Bridges forward traffic as needed
R
RO
RO
O
RO

## Slide 31: Example: Two Virtual LANs
Red VLAN and Orange VLAN
Switches forward traffic as needed
R
O
RO
R
R
R
O
O
O
R
O
R
R
R
O
O
O

## Slide 32: Making VLANs Work
Bridges/switches need configuration tables
  Saying which VLANs are accessible via which interfaces
Approaches to mapping to VLANs
  Each interface has a VLAN color
    Only works if all hosts on same segment belong to same VLAN
  Each MAC address has a VLAN color
    Useful when hosts on same segment belong to different VLANs
    Useful when hosts move from one physical location to another
Changing the Ethernet header
  Adding a field for a VLAN tag
  Implemented on the bridges/switches
  … but can still interoperate with old Ethernet cards

## Slide 33: Moving From Switches to Routers
Advantages of switches over routers
  Plug-and-play
  Fast filtering and forwarding of frames
  No pronunciation ambiguity (e.g., “rooter” vs. “rowter”)
Disadvantages of switches over routers
  Topology is restricted to a spanning tree
  Large networks require large ARP tables
  Broadcast storms can cause the network to collapse

## Slide 34: Comparing Hubs, Switches, & Routers

## Slide 35: Conclusion
Shuttling data from one link to another
  Bits, frames, packets, …
  Repeaters/hubs, bridges/switches, routers, …
Key ideas in switches
  Cut-through switching
  Self learning of the switch table
  Spanning trees
  Virtual LANs (VLANs)
Next time: midterm exam
After the break
  Routing
  Application-level protocols