## Slide 1: Rateless Codes
COS 463: Wireless Networks
Lecture 10
Kyle Jamieson

## Slide 2: Today
Rateless fountain codes
  Luby Transform (LT) Encoding
  LT Decoding
Rateless Spinal codes

## Slide 3: Fixed-rate codes require channel adaptation

## Slide 4: Existing rate adaptation algorithms
SNR/BER-based
Frame-based
Estimate frame loss rate
at each bit rate
Data
ACK
Data
Lookup table:
SNR/BER  best rate
SNR using preamble

## Slide 5: Rateless codes: Motivation (1)
Sender transmits information at a rate higher than the channel can sustain
  At first glance, this sounds disastrous!
Receiver extracts information at the rate the channel can sustain at that instant
  No adaptation loop is needed!

## Slide 6: Rateless codes: Motivation (2)
Sender sends a potentially limitless stream of encoded bits
Receiver(s) collect bits until they are reasonably sure that they can recover the content from the received bits, then send STOP feedback to sender
Automatic adaptation: Receivers with larger loss rate need longer to receive the required information

## Slide 7: LT encoding
Consider a message m with K bits
LT encoding produces N coded bits, for any N
  Variable code rate: K / N
To produce the nth coded bit:
  Choose at random the coded bit’s degree dn from a degree distribution
  Choose dn distinct message bits, uniformly at random
    Xor them together to form one coded bit cn

## Slide 8: LT encoding
m1
m2
m3
m4
m5
m6
m7
m8
Message bits:
Coded bits:
c1 = m1 ⊕ m3
c2 = m5 ⊕ m7
c3 = m4
c4 = m2 ⊕ m4
c5 = m6
c6 = m1 ⊕ m8
c7 = m6
c8 = m3 ⊕ m4 ⊕ m7
c9 = m5 ⊕ m7
c10 = m8

## Slide 9: LT decoding algorithm
Find a coded bit cn with degree one
  If not possible, fail
Decide its incident message bit i: mi = cn
Add mi (with xor) to all coded bits cn incident on mi
Remove all edges incident on mi
Repeat Steps 1 to 4 until all mi are found

## Slide 10: LT decoding example

## Slide 11: LT decoding example

## Slide 12: LT decoding example

## Slide 13: LT decoding example

## Slide 14: Today
Rateless fountain codes
  Luby Transform (LT) Encoding
  LT Decoding
Rateless Spinal codes
  Encoding Spinal Codes
  Decoding Spinal codes
  Performance evaluation

## Slide 15: Spinal encoder: Computing the spines
Start with a hash function h and an initial random v-bit state s0
  Sender and receiver agree on h and s0 a priori
Sender divides its n-bit message M into k-bit chunks mi
h maps the state and a message chunk into a new state
  The v-bit states s1, …, s⌈n/k⌉ are the spines

## Slide 16: Spinal encoder: Information flow
Observe: State si contains information about chunks m1, …, mi
  A stage’s state depends on the message bits up to that stage
So only state s⌈n/k⌉ has information about entire message

## Slide 17: Spinal encoder: Computing the spines
Each spine seeds a random number generator RNG
RNG generates a sequence of c-bit numbers
Encoder output is a series of passes of ⌈n/k⌉ symbols xi,l each

## Slide 18: Spinal encoder: RNG to symbols
A constellation mapping function translates c-bit numbers xi,l from the RNG to in-phase (I) and quadrature (Q)
  Generates in-phase (I) and quadrature (Q) components independently from two separate xi,l
Uniform
Truncated Gaussian

## Slide 19: Today
Rateless fountain codes
  Luby Transform (LT) Encoding
  LT Decoding
Rateless Spinal codes
  Encoding Spinal Codes
  Decoding Spinal codes
      “Maximum-likelihood” decoding
      The Bubble Decoder
      Puncturing for higher rate
  Performance evaluation

## Slide 20: Decode by replaying the encoder
Sender transmits “1”, “0”:
h
s0
1
h
0


h
s0
0
×
×


Instead of inverting the hash function, the decoder replays all four possibilities:
Transmitted symbols
h
0
h
s0
1
h
0
×
×


h
s0
0
h
1
×
×


h
s0
1
h
1
×
×


   Replayed symbol
  × Received symbol

## Slide 21: Decode by measuring distance
How to decide between the four possible messages?
Measure total distance between:
  Received symbols, corrupted by noise (×), and
  Replayed symbols ()
Sum across stages: the distance increases at first incorrect symbol
h
s0
0
h
0
×
×


h
s0
1
h
0
×
×


h
s0
0
h
1
×
×


h
s0
1
h
1
×
×


   Replayed symbol
  × Received symbol

## Slide 22: Adding additional passes
Recall: The encoder sends multiple passes over the same message blocks

## Slide 23: Adding additional passes
What’s a reasonable strategy for decoding now?
Take the average distance from the replayed symbol (), across all received symbols (×, ×)
  Intuition: As number of passes increases, noise and bursts of interference average out and impact the metric less
h
s0
0
h
0
×
×


h
s0
1
h
0
×
×


h
s0
0
h
1
×
×


h
s0
1
h
1
×
×


×
×
×
×
×
×
×
×
   Replayed symbol
  × Received symbol

## Slide 24: The Maximum Likelihood (ML) decoder
Consider all 2n possible messages that could have been sent
  The ML decoder minimizes probability of error
Pick the message M′ that minimizes the vector distance between:
  The vector of all received constellation points y
  The vector of constellation points sent if M′ were the message, x(M′)
In further detail:
  xt,l(M′): tth constellation point sent in the lth pass for M′
  yt,l: tth constellation point received in the lth pass

## Slide 25: ML decoding over a tree
Observe: Hypotheses whose initial stages share the same symbol guesses are identical in those stages
h
s0
0
h
0
×
×


h
s0
1
h
0
×
×


h
s0
0
h
1
×
×


h
s0
1
h
1
×
×



## Slide 26: ML decoding over a tree
Observe: Hypotheses whose initial stages share the same symbol guesses are identical in those stages
Therefore we can merge these initial identical stages:
h
s0
0
h
0
×
×


h
s0
1
h
0
×
×


h
1
×

h
1
×


## Slide 27: ML decoding over a tree
General tree properties:
  n/k levels, one per spine
  Branching factor 2k (per choice of k-bit message chunk)
Let s′t be the tth spine value associated with all messages that share s′t
We find cost of a particular message by summing costs on path from root to leaf
h
0
h
0
×
×


h
s0
1
h
0
×
×


h
1
×

h
1
×

✔
✔
✔
s1
s2

## Slide 28: ML decoding over a tree: Multiple passes
Suppose the sender transmits L passes, in a poor channel
Average (sum) metric across passes, and label branches
However, the tree has 2n leaves to compare so this approach is still impracticable (too computationally demanding)
h
0
h
0✔
×
×


h
s0
1
h
0
×
×


h
1
×

h
1
×

✔
✔
s1
s2

## Slide 29: Efficiently exploring the tree
Observation: Suppose the ML message M* and some other message M′ differ only in the ith bit
  Only symbols including and after index ⌈i/k⌉ will disagree
  So the earlier the error in M′, the larger the cost
  Can show that the “runners-up” to M* differ only in the last O(log n) bits
Consider the best 100 leaves in the ML tree:
  Tracing back through the tree, they will have a common ancestor with M* in O(log n) steps
  This suggests a strategy in which we only keep a limited number of ancestors

## Slide 30: Bubble decoder
Maintain a beam of B tree node ancestors to explore, each to a certain depth d
Expand each ancestor, score every child, propagate best child score for each ancestor, pick B best survivors
Example: B = d = 2, k = 1 (lighter color = better score)
beam

## Slide 31: Decoding complexity
The bubble decoder operates in n/k − d steps
  Each step explores B∙2kd nodes, evaluating the RNG L times
  Selecting the best B candidates takes B∙2k comparisons
Overall cost: O((n/k)BL∙2kd) hashes, O((n/k)B∙2k) comparisons
Comparison with LDPC belief propagation algorithms
  These operate in iterations, too, involve all message bits
  But, these are also quite parallelizable
  Hard to give exact head-to-head comparison

## Slide 32: Adjusting the rate
Spinal codes as described so far uses different numbers of passes to adjust the rate
Two problems in Spinal codes as described so far:
  Must transmit one full pass, so max out at k bits/symbol
    Increase k? No: Decoding cost is exponential in k
  Sending L passes reduces rate to k/L—abrupt drop
    Introduces plateaus in the rate versus SNR curve

## Slide 33: Puncturing for higher and finer-controlled rates
Idea: Systematically skip some spines
  Sender and receiver agree on the pattern beforehand
  Receiver can now attempt a decode before a pass concludes
Decoder algorithm unchanged, missing symbols get zero score
Max rate of this puncturing: 8∙k bits/symbol

## Slide 34: Framing at the link layer
Sender and receiver need to maintain synchronization
  Sender uses a short sequence number protected by a highly redundant code
Unusual property of Spinal codes: Shorter message length n is more efficient
  This is in opposition to the trend most codes follow
  Divide the link-layer frame into shorter checksum-protected code blocks
If half-duplex radio, when should sender wait for feedback?
  For more information, see RateMore (MobiCom ‘12)

## Slide 35: Today
Rateless fountain codes
  Luby Transform (LT) Encoding
  LT Decoding
Rateless Spinal codes
  Encoding Spinal Codes
  Decoding Spinal codes
  Performance evaluation

## Slide 36: Methodology
Software simulation: Simulated wireless channel (additive white Gaussian noise and Rayleigh fading)
Hardware platform: Airblue (FPGA based platform)
  Real 10, 20 MHz bandwidth channels in 2.4 GHz ISM band
Gap to capacity: How much more noise could a capacity-achieving code tolerate at same rate?
  Smaller gap is better
  e.g.: This code achieves six bits/symbol at 20 dB SNR, for a 2 dB gap to capacity
Rate (bits per symbol)
0
2
4
6
8
2 dB

## Slide 37: Spinal codes: Higher rate on AWGN channel
Simulated AWGN channel: no link-layer performance effects here
LDPC envelope: Choose best-performing rated LDPC code at each SNR to mimic the best a rate adaptation strategy could do
Strider+: Strider + puncturing: finer rate control, but significant gap to capacity

## Slide 38: Rateless codes can “hedge their bets”
Constant SNR means constant average noise power
  But, noise impacting any particular symbol(s) may be higher or lower
Rated codes must be risk averse (send at lower rate)
Rateless codes can decode with fewer symbols when noise is momentarily lower
But this result requires perfect and instantaneous feedback so the rateless code knows when to stop

## Slide 39: Spinal codes: Better at sending short messages
Longer code block means more opportunities to prune correct path
  So Spinal codes achieves better performance (smaller gap to capacity) with smaller code block length n
We can see artifacts due to puncturing at higher SNRs

## Slide 40: Spinal Codes: Conclusion
Spinal Codes give performance close to Shannon capacity
Eliminate the need to run a bit rate adaptation algorithm
Simpler design and better performance
Link layer design more open, incurs overhead between transmissions

## Slide 41: Midterm format
Timing: 60 minutes in a 90 minute timeslot
True/False/Don’t Know questions
  One point for a correct T/F response
  No effect for a don’t know response or no response
  Minus one point for an incorrect T/F response
  Rescaled as a section with a zero floor
Short answer questions
  One to two, each on a theme

## Slide 42
Friday Precept:
Midterm Review
Tuesday Topic:
Signals and Systems Preliminaries
Next Thursday:
In-Class Midterm