## Slide 1: Visible Light Communication
COS 463: Wireless Networks
Lecture 23
Kyle Jamieson

## Slide 2: What is VLC
Visible light communication (VLC)
  visible light source as a signal transmitter
  air as a transmission medium
  appropriate photodiode as a signal receiving component

## Slide 3: What is VLC
Key idea behind VLC
  Eye cannot detect fast light switching but semiconductor‐ based photodetector can do

## Slide 4: What is VLC – Light source
5%
25%
60%
Light emitting diode (LED) – since 1990s
Compact and 50% light
Uses 2-17 watts of electricity
More than 100,000 hours lifespan
Fluorescent lamp
White light
25% light
Lifetime ~10,000s hours
Incandescent bulb
First industrial light source
5% light, 95% heat
Few thousand hours of life
Efficiency
Power
usage
10%
20%
> 40%
80%
Lumens/W: 10-18
Lumens/W: 35-100
Lumens/W: 35-150

## Slide 5: What is VLC － Light detector
PIN photodiode
  low cost, large area
  limited sensitivity
Image sensors
  Charge-Coupled Device (CCD): low cost, slow due to serial read-out

## Slide 6: Motivation of VLC
Privacy-preserving
Resilient to Interference
Radio spectrum crunch
  Ever-growing user demands meet limited radio spectrum

## Slide 7: Looking into VLC spectrum
VLC has a large frequency band
  390 nm – 700 nm in wavelengths
  430 – 770 THz in frequency

## Slide 8: Key difference from RF
RF communication works in a Non-line-of-sight environment
VLC requires Line-of-sight between the transmitter and the receiver
VLC
RF signals

## Slide 9: VLC Modulation Schemes
Many conventional schemes can be applied:
  On-off keying (OOK)
  Frequency-shift keying (FSK)
  Pulse amplitude modulation (PAM)
  Pulse width modulation (PWM)

## Slide 10: Current VLC Systems
 | Range (m) | Data rate | Modulation | Year
Langer et.al. | 1.5 | 230Mb/s | OOK | 2010
Khalid et.al. | 0.5 | 1Gb/s | OFDM | 2012
Kottke et.al. | 0.3 | 1.25Gb/s | OFDM | 2012
Sewaiwar et.al. | 0.85 | 3Gb/s | OFDM+RGB | 2015