## Slide 1: End-to-End Transport Over Wireless II: Snoop and Explicit Loss Notification
COS 463: Wireless Networks
Lecture 3
Kyle Jamieson
[Various parts adapted from S. Das, B. Karp, N. Vaidya]

## Slide 2: Today
Transmission Control Protocol (TCP), Part II
  Window-based flow control
  Retransmissions and congestion control
TCP over Wireless
  TCP Snoop
  Explicit Loss Notification

## Slide 3: Window-Based Flow Control: Motivation
Suppose sender sends one packet, awaits ACK, repeats…
Result: At most one packet sent, per RTT
e.g., 70 ms RTT, 1500-byte packets  Max t’put: 171 Kbps

## Slide 4
Dispatch window of segments sequentially, w/o awaiting ACKs
  Retain packets until ACKed, track which are ACKed
  Set retransmit timer for each window
    When expires, resend unACKed segments in window
Idea: Pipeline Transmissions
(Fixed Window-Based Flow Control)
But: RTT idle time from grant of new
window to data arrival at receiver
Better approach (TCP): sliding window, extends as each ACK returns, so no idle time!

## Slide 5: Choosing Window Size
Network bottleneck: link of slowest rate along path between sender and receiver
What size sender window keeps the pipe full?
  Window too small: can’t fill pipe
  Window too large: unnecessary network load/queuing/loss
Bottleneck link
Sender
Receiver
Network

## Slide 6: Increasing utilization with pipelining
First bit sent, t = 0
RTT
ACK arrives, send next packet
last bit of 2nd packet, send ACK
Time ↓
Bottleneck link

## Slide 7: The Bandwidth-Delay Product
First bit sent, t = 0
RTT
ACK arrives, send next packet
Time ↓
Bottleneck link
 Rate = R bits/s
So window size bits / RTT seconds = R bits / second

## Slide 8: The bandwidth-delay product
Goal: window size = RTT × bottleneck rate
e.g.: to achieve a bottleneck rate of 1 Mbps across a 70 ms RTT, need a window size:
(106 bps × .07 s) = 70 Kbits = 8.75 Kbytes
sender
receiver
RTT

## Slide 9: TCP Packet Header
TCP header: 20 bytes long
Checksum covers TCP packet + “pseudo header”
  IP header source and destination addresses, protocol
  Length of TCP segment (TCP header + data)

## Slide 10: TCP Header Details
Connections inherently bidirectional; all TCP headers carry both data & ACK sequence numbers
32-bit sequence numbers are in units of bytes
Source and destination port numbers
  Multiplexing of TCP by applications
  UNIX: local ports below 1024 reserved (only root may use)
Window field: advertisement of number of bytes advertiser willing to accept

## Slide 11: TCP: Data Transmission
Each byte numbered sequentially (modulo 232)
Sender buffers data in case retransmission required
Receiver buffers data for in-order reassembly
Sequence number (seqno) field in TCP header indicates first user payload byte in packet

## Slide 12: TCP: Receiver functionality
Receiver indicates offered window size W explicitly to sender in window field in TCP header
  Corresponds to available buffer space at receiver
Receiver sends cumulative ACKs:
  ACK number in TCP header names highest contiguous byte number received thus far, +1
  one ACK per received packet, or:
    Delayed ACK: receiver batches ACKs, sends one for every pair of data packets (200 ms max delay)

## Slide 13: TCP: Sender’s Window
Usable window at sender:
  Left edge advances as packets sent
  Right edge advances as receive window updates arrive
Offered window (advertised by receiver)

## Slide 14: Today
Transmission Control Protocol (TCP)
  Window-based flow control
  Retransmissions and congestion control
TCP over Wireless
  TCP Snoop
  Explicit Loss Notification

## Slide 15: TCP: Retransmit Timeouts
Recall: Sender sets timer for each sent packet
  Expected time for ACK to return: RTT
  when ACK returns, timer canceled
  if timer expires before ACK returns, packet resent
TCP estimates RTT using measurements mi from timed packet/ACK pairs
  RTTi = ((1 − α) x RTTi − 1 + α x mi)
Original TCP retransmit timeout: RTOi = β × RTTi
  original TCP: β = 2

## Slide 16: Mean and Variance: Jacobson’s RTT Estimator
Above 30% link load at router, β × RTTi retransmits too early!
  Response to increasing load: waste bandwidth on duplicate packets; result: congestion collapse!
Idea [Jacobson 88]: Estimate mean deviation vi, (EWMA of |mi – RTTi|), a stand-in for variance:
  vi = vi-1×(1-γ) + γ×|mi − RTTi|
  Then use retransmission timeout RTOi = RTTi + 4vi
Mean and Variance RTT estimator used by all modern TCPs

## Slide 17: Self-Clocking Transmission
Self-clocking transmission: Conservation of Packets
  each ACK returns, one data packet sent
  spacing of returning ACKs: matches spacing of packets in time at slowest link on path

## Slide 18: Goals in Congestion Control
Achieve high utilization on links; don’t waste capacity!
Divide bottleneck link capacity fairly among users
Be stable: converge to steady allocation among users
Avoid congestion collapse

## Slide 19: Congestion Collapse
Cliff behavior observed in [Jacobson 88]
Offered load (bps)
Throughput (bps)
Congestion collapse!
Knee

## Slide 20: Congestion Requires Slowing Senders
Bigger buffers cannot prevent congestion: senders must slow down
Absence of ACKs implicitly indicates congestion
TCP sender’s window size determines sending rate
Recall: Correct window size is bottleneck link bandwidth-delay product
How can the sender learn this value?
  Search for it, by adapting window size
  Feedback from network: ACKs return (window OK) or do not return (window too big)

## Slide 21: Reaching Equilibrium: Slow Start
At connection start, sender sets congestion window size, cwnd, to pktSize (one packet’s worth of bytes), not whole window
Sender sends up to min(cwnd, W)
  Upon return of each ACK, increase cwnd by pktSize bytes until W reached
  “Slow” means exponential window increase!
Takes log2(W / pktSize) RTTs to reach receiver’s advertised window size W

## Slide 22: Avoiding Congestion: Multiplicative Decrease
Recall sender uses window of size min(cwnd, W), where W is receiver’s advertised window
Upon timeout for sent packet, sender presumes packet lost to congestion, and:
  sets ssthresh = cwnd / 2
  sets cwnd = pktSize
  uses slow start to grow cwnd up to ssthresh
End result: cwnd = cwnd / 2, via slow start

## Slide 23: Taking Your Fair Share: Additive Increase
Drops indicate sending more than fair share of bottleneck
No feedback to indicate using less than fair share
Solution: Speculatively increase window size as ACKs return
  Additive increase: For each returning ACK,
  cwnd = cwnd + (pktSize × pktSize) / cwnd
  Increases cwnd by ≈ pktSize bytes per RTT
Combined algorithm: Additive Increase,
Multiplicative Decrease (AIMD)

## Slide 24: Refinement: Fast Retransmit (I)
Sender must wait well over RTT for timer to expire before loss detected
TCP’s minimum retransmit timeout: 1 second
Another indicator of loss:
  Suppose sender sends: 1, 2, 3, 4, 5 (...but 2 is lost)
  Receiver receives: 1, 3, 4, 5
  Receiver sends cumulative ACKs: 2, 2, 2, 2
    Loss causes duplicate ACKs

## Slide 25: Fast Retransmit (II)
Upon arrival of three duplicate ACKs, sender:
sets cwnd = cwnd / 2
retransmits “missing” packet
no slow start
Not only loss causes dup ACKs
  Packet reordering, too
data, seqno = 1
ACK = 513
data, seqno = 513
time
A
B
data, seqno = 513
data, seqno = 1025
data, seqno = 1537
ACK = 513
ACK = 513
data, seqno = 2049
ACK = 513

## Slide 26: AIMD in Action

## Slide 27: Modeling Throughput, Loss, and RTT
How do packet loss rate and RTT affect throughput TCP achieves?
Assume:
Only fast retransmits
No timeouts (so no slow starts in steady-state)

## Slide 28: Evolution of Window Over Time
Average window size: ¾W
One window of packets is sent per RTT
Bandwidth:
  ¾W packets per RTT
  (¾W x packet size) / RTT bytes per second
  W depends on loss rate…
time
W
W/2

## Slide 29: Window Size Versus Loss
Assume no delayed ACKs, fixed RTT
cwnd grows by one packet per RTT
  So it takes W/2 RTTs to go from window size W/2 to window size W; this period is one cycle
How many packets sent in total, in a cycle?
  ( ¾W packets / RTT) x (W/2 RTTs) = 3W2/8 packets
One loss per cycle (as window reaches W)
  So, the packet loss rate p = 8/3W2
  W = √(8/3p)

## Slide 30: Throughput, Loss, and RTT Model
W = √(8/3p) = (4/3) x √(3/2p)
Recall, bandwidth B = (3W/4 x packet size) / RTT
Consequences:
Increased loss quickly reduces throughput
At same bottleneck, flow with longer RTT achieves less throughput than flow with shorter RTT!
B = packet size / (RTT x √(2p/3))

## Slide 31: Stretch Break, Q&A
Suppose a Princeton Plasma Physics Lab experiment is generating scientific data at 5 Gbit/sec
Want to send this data across the Internet to CERN, Switzerland for analysis with a 5 Gbit/s backbone link
  Arrange for 10 Gbit/s links from PPPL to Internet Service Provider (ISP), and ISP to CERN
  PPPL-CERN round trip time is 200 milliseconds
How large would the TCP sender’s send window need to be at a minimum in order to achieve a throughput of 5 Gbit/s?

## Slide 32: Today
Transmission Control Protocol (TCP) primer, cont’d
TCP over Wireless
  TCP Snoop
  Explicit Loss Notification

## Slide 33: Review: TCP on Wireless Links
TCP interprets any packet loss as a sign of congestion
  TCP sender reduces congestion window
On wireless links, packet loss can also occur due to random channel errors, or interference
  Temporary loss not due to congestion
  Reducing window may be too conservative
  Leads to poor throughput

## Slide 34: Review: Two Broad Approaches
Mask wireless losses from TCP sender
  Then TCP sender will not reduce congestion window
  Split Connection Approach
  TCP Snoop
Explicitly notify TCP sender about cause of packet loss

## Slide 35: TCP Snoop: Introduction
Removes most significant problem of split connection: breaking end-to-end semantics
  No more split connection
  Single end-to-end connection like regular TCP
TCP Snoop only modifies the AP
Basic Idea (Downlink traffic):
  AP “snoops” on TCP traffic to and from the mobile
    Quickly retransmits packets it thinks may be lost over the wireless link

## Slide 36: Snoop Protocol: High-level View
wireless
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
transport
application
Per TCP-connection state
TCP connection
Retransmit

## Slide 37: TCP Snoop: Downlink traffic case
AP buffers downlink TCP segments
  Until it receives corresponding ACK from mobile
AP snoops on uplink TCP ACKs
  Detects downlink wireless TCP segment loss via duplicate ACKs or time-out
40
39
37
38
36
34
Wired Internet
Wireless Link
TCP Segments
TCP ACKs
Content
Server
Mobile
AP

## Slide 38: TCP Snoop Goal: Recover wireless downlink loss
When AP detects a lost TCP segment:
  Locally, quickly retransmit that segment over the wireless link
  Minimize duplicate ACKs flowing back to server
Goal: Content server unaware of wireless loss and retransmission
  No reduction in cwnd

## Slide 39: TCP Snoop: Downlink Example
40
39
37
38
36
34
36
37
38
35
Snoop Cache (at AP):
TCP segments seen (whose ACKs have not yet been seen)
Wired Internet
Wireless Link
TCP Segments
TCP ACKs

## Slide 40: Downlink traffic operation, at Snoop AP
Downlink TCP segments:

## Slide 41: TCP Snoop: Downlink example
41
40
38
39
36
34
36
37
38
35
39

## Slide 42: Downlink traffic operation, at Snoop AP
Downlink TCP segments:
Uplink TCP ACKs:

## Slide 43: TCP Snoop: Downlink example
41
40
38
39
34
37
38
39
36
36
35

## Slide 44: TCP Snoop: Downlink example
42
41
39
40
36
TCP receiver does not delay duplicate ACKs (dupacks)
36
First
dupack
37
38
39
40

## Slide 45: TCP Snoop: Downlink example
40
36
36
36
41
43
42
37
38
39
40
41
Second
dupack
First
dupack

## Slide 46: Downlink traffic operation, at Snoop AP
Downlink TCP segments:
Uplink TCP ACKs:

## Slide 47: TCP Snoop: Downlink example
41
36
36
37
44
43
36
37
38
39
40
41
42
Dupack triggers retransmission of packet 37 from AP
Second
dupack
First
dupack
Third
dupack

## Slide 48: Downlink traffic operation, at Snoop AP
Downlink TCP segments:
Uplink TCP ACKs:

## Slide 49: TCP Snoop: Downlink example
37
36
42
45
44
36
37
38
39
40
41
42
43
36
Discard
2nd dupack

## Slide 50: TCP Snoop: Downlink example
42
36
43
46
45
36
37
38
39
40
41
42
43
41
36
44
Discard
3rd dupack

## Slide 51: TCP Snoop: Downlink example
43
36
44
47
46
36
37
38
39
40
41
42
43
41
36
44
TCP sender does not fast retransmit
45
Discard
4th dupack

## Slide 52: TCP Snoop: Downlink example
44
36
45
48
47
36
42
43
41
36
44
45
43
46

## Slide 53: Uplink traffic case
Less-common case but becoming more prevalent
Buffer & retransmit TCP segments at AP? Not likely useful
Run Snoop agent on the Mobile? Not likely useful
40
39
37
38
36
34
Wireless Link
Wired Internet
TCP Segments
TCP ACKs
Server
Mobile
AP

## Slide 54: Snoop TCP: Advantages
Works without modification to mobile or server
Preserves end-to-end semantics. Crash does not affect correctness, only performance.
After an AP handoff: New AP needn’t Snoop TCP
  Can automatically fall back to regular TCP operation
  No state need be migrated (but if done, can improve performance)
  Note such “state” is called soft state
    Good if available, but correct functionality otherwise

## Slide 55: Two Broad Approaches
Mask wireless losses from TCP sender
  Then TCP sender will not reduce congestion window
  Split Connection Approach
  TCP Snoop
Explicitly notify TCP sender about cause of packet loss

## Slide 56: Explicit Loss Notification (ELN)
Notify the TCP sender that a wireless link (not congestion) caused a certain packet loss
Upon notification, TCP sender retransmits packet, but doesn’t reduce congestion window
Many design options:
  Who sends notification? How is notification sent? How is notification interpreted at sender?
    We’ll discuss one example approach

## Slide 57: ELN for uplink TCP traffic
AP keeps track of gaps in the TCP packet sequence received from the mobile sender
4
3
2
1
1
3
4
Wireless Link
TCP Segments
TCP ACKs
Gap, size 1 at seqno 2
Server
Mobile

## Slide 58: ELN for uplink TCP traffic
When AP sees a dupack:
  AP compares dupack seqno with its recorded gaps
    If match: AP sets ELN bit in dupack and forwards it
When mobile receives dupack with ELN bit set:
  Resends packet, but doesn’t reduce congestion window
4
3
2
1
1
3
4
1
1
1
1
Dupack with ELN set
TCP Segments
Gap, size 1 at seqno 2
Server
Mobile

## Slide 59
Thursday Topic:
Link Layer I: Time, Frequency,
and Code Division
Precepts Next Week:
Introduction to Lab 1