## Slide 1: Convolutional Codes
COS 463: Wireless Networks
Lecture 9
Kyle Jamieson
[Parts adapted from H. Balakrishnan]

## Slide 2: Convolutional Coding: Motivation
So far, we’ve seen block codes
Convolutional Codes:
  Simple design, especially at the transmitter
  Very powerful error correction capability (used in NASA Pioneer mission deep space communications)
[Credit: Nasa Ames Research Center]

## Slide 3: Convolutional Coding: Applications
Wi-Fi (802.11 standard) and cellular networks (3G, 4G, LTE standards)
Deep space satellite communications
Digital Video Broadcasting (Digital TV)
Building block in more advanced codes (Turbo Codes), which are in turn used in the above settings

## Slide 4: Today
Encoding data using convolutional codes
  How the encoder works
  Changing code rate: Puncturing
Decoding convolutional codes: Viterbi Algorithm

## Slide 5: Convolutional Encoding
Don’t send message bits, send only parity bits
Use a sliding window to select which message bits may participate in the parity calculations
1
0
1
1
0
1
0
0
1
0
1
Constraint length K
Message bits:

## Slide 6: Sliding Parity Bit Calculation
0
0
1
1
0
1
0
0
1
0
1
K = 4
0
0
-3 -2 -1 0 1 2 3 4 5 6 7 8 …..
+
P[0]= 0
Output: 0
Message
bits:

## Slide 7: Sliding Parity Bit Calculation
0
0
1
1
0
1
0
0
1
0
1
K = 4
0
0
-3 -2 -1 0 1 2 3 4 5 6 7 8 …..
+
P[1] = 1
Output: 01
Message
bits:

## Slide 8: Sliding Parity Bit Calculation
0
0
1
1
0
1
0
0
1
0
1
K = 4
0
0
-3 -2 -1 0 1 2 3 4 5 6 7 8 …..
+
P[2] = 0
Output: 010
Message
bits:

## Slide 9: Sliding Parity Bit Calculation
0
0
1
1
0
1
0
0
1
0
1
K = 4
0
0
-3 -2 -1 0 1 2 3 4 5 6 7 8 …..
+
P[3] = 1
Output: 0100
Message
bits:

## Slide 10: Multiple Parity Bits
0
0
1
1
0
1
0
0
1
0
1
0
0
-3 -2 -1 0 1 2 3 4 5 6 7 8 …..
+
P1[3] = 1
+
P2[3] = 1
Output: ….11
Message
bits:

## Slide 11: Multiple Parity Bits
0
0
1
1
0
1
0
0
1
0
1
0
0
-3 -2 -1 0 1 2 3 4 5 6 7 8 …..
+
P1[4] = 0
+
P2[4] = 0
Output: ….1100
Message
bits:

## Slide 12: Multiple Parity Bits
0
0
1
1
0
1
0
0
1
0
1
0
0
-3 -2 -1 0 1 2 3 4 5 6 7 8 …..
+
P1[5] = 0
+
P2[5] = 1
Output: ….110001
Message
bits:

## Slide 13: Encoder State
Input bit and K-1 bits of current state determine state on next clock cycle
  Number of states: 2K-1
0
0
1
1
0
1
0
0
1
0
1
0
0
State
Constraint length K
Input bit
Message
bits:

## Slide 14: Constraint Length
K is the constraint length of the code
Larger K:
  Greater redundancy
  Better error correction possibilities (usually, not always)

## Slide 15: Transmitting Parity Bits
Transmit the parity sequences, not the message itself
  Each message bit is “spread across” K bits of the output parity bit sequence
  If using multiple generators, interleave the bits of each generator
    e.g. (two generators):

## Slide 16: Transmitting Parity Bits
Code rate is 1 / #_of_generators
  e.g., 2 generators  rate = ½
Engineering tradeoff:
  More generators improves bit-error correction
    But decreases rate of the code (the number of message bits/s that can be transmitted)

## Slide 17: Shift Register View
One message bit x[n] in, two parity bits out
  Each timestep: message bits shifted right by one, the incoming bit moves into the left-most register

## Slide 18: Equation View
0th stream: p0[n] = x[n] + x[n − 1] + x[n − 2] (mod 2)
1st stream: p1[n] = x[n] + x[n − 2] (mod 2)

## Slide 19: Today
Encoding data using convolutional codes
  Encoder state machine
  Changing code rate: Puncturing
Decoding convolutional codes: Viterbi Algorithm

## Slide 20: State Machine View
Example: K = 3, code rate = ½, convolutional code
  There are 2K-1 states
  States labeled with (x[n-1], x[n-2])
  Arcs labeled with x[n]/p0[n]p1[n]
  Generator: g0 = 111, g1 = 101
  msg = 101100
00
10
01
11
0/00
1/11
1/01
0/01
0/11
1/00
0/10
Starting state
1/10

## Slide 21: State Machine View
msg = 101100
Transmit:
00
10
01
11
0/00
1/11
1/01
0/01
0/11
1/00
0/10
Starting state
P0[n] = (1*x[n] + 1*x[n-1] + 1*x[n-2]) mod 2
P1[n] = (1*x[n] + 0*x[n-1] + 1*x[n-2]) mod 2
Generators: g0 = 111, g1 = 101
1/10

## Slide 22: State Machine View
msg = 101100
Transmit: 11
00
10
01
11
0/00
1/11
1/01
0/01
0/11
1/00
0/10
Starting state
P0[n] = 1*1 + 1*0 + 1*0 mod 2
P1[n] = 1*1 + 0*0 + 1*0 mod 2
Generators: g0 = 111, g1 = 101
1/10

## Slide 23: State Machine View
00
10
01
11
0/00
1/11
1/01
0/01
0/11
1/00
0/10
Starting state
P0[n] = 1*0 + 1*1 + 1*0 mod 2
P1[n] = 1*0 + 0*1 + 1*0 mod 2
Generators: g0 = 111, g1 = 101
1/10
msg = 101100
Transmit: 11 10

## Slide 24: State Machine View
00
10
01
11
0/00
1/11
1/01
0/01
0/11
1/00
0/10
Starting state
P0[n] = 1*1 + 1*0 + 1*1 mod 2
P1[n] = 1*1 + 0*0 + 1*1 mod 2
Generators: g0 = 111, g1 = 101
1/10
msg = 101100
Transmit: 11 10 00

## Slide 25: State Machine View
00
10
01
11
0/00
1/11
1/01
0/01
0/11
1/00
0/10
Starting state
P0[n] = 1*1 + 1*1 + 1*0
P1[n] = 1*1 + 0*1 + 1*0
Generators: g0 = 111, g1 = 101
1/10
msg = 101100
Transmit: 11 10 00 01

## Slide 26: State Machine View
00
10
01
11
0/00
1/11
1/01
0/01
0/11
1/00
0/10
Starting state
P0[n] = 1*0 + 1*1 + 1*1
P1[n] = 1*0 + 0*1 + 1*1
Generators: g0 = 111, g1 = 101
1/10
msg = 101100
Transmit: 11 10 00 01 01

## Slide 27: State Machine View
00
10
01
11
0/00
1/11
1/01
0/01
0/11
1/00
0/10
Starting state
P0[n] = 1*0 + 1*0 + 1*1
P1[n] = 1*0 + 0*0 + 1*1
Generators: g0 = 111, g1 = 101
1/10
msg = 101100
Transmit: 11 10 00 01 01 11

## Slide 28: Today
Encoding data using convolutional codes
  How the encoder works
  Changing code rate: Puncturing
Decoding convolutional codes: Viterbi Algorithm

## Slide 29: Varying the Code Rate
N
p
How to increase the rate of a convolutional code?
Transmitter and receiver agree on coded bits to omit
  Puncturing table indicates which bits to include (1)
    Contains p rows (one per parity equation), N columns
Example:
(Omitted)
(Omitted)

## Slide 30: Punctured convolutional codes: example
Coded bits =
With Puncturing:
0
0
1
0
1
0
0
1
1
1
P1=
Puncturing table

## Slide 31: Punctured convolutional codes: example
Coded bits =
With Puncturing matrix:
P1=
5 out of 8 bits are retained
0
0
1
0
1
0
0
1
1
1

## Slide 32: Punctured convolutional codes: example
Coded bits =
With Puncturing matrix:
Punctured, coded bits:
0
0
0
0
1
0
1
0
0
1
1
1
P1=

## Slide 33: Punctured convolutional codes: example
Coded bits =
With Puncturing matrix:
Punctured, coded bits:
0
0
0
0
1
0
1
0
0
1
1
1
P1=
0

## Slide 34: Punctured convolutional codes: example
Coded bits =
With Puncturing matrix:
Punctured, coded bits:
0
0
0
0
1
0
1
0
0
1
1
1
P1=
0
1

## Slide 35: Punctured convolutional codes: example
Coded bits =
With Puncturing matrix:
Punctured, coded bits:
0
0
0
0
1
0
1
0
0
1
1
1
P1=
0
1
1

## Slide 36: Punctured convolutional codes: example
Coded bits =
With Puncturing matrix:
Punctured, coded bits:
0
0
0
0
1
0
1
0
0
1
1
1
P1=
0
1
1
1
1

## Slide 37: Punctured convolutional codes: example
Coded bits =
Punctured, coded bits:
Punctured rate is increased to: R = (1/2) / (5/8) = 4/5
0
0
0
0
1
0
1
0
0
1
1
1
0
1
1
1
1

## Slide 38: Stretch Break and Question
Consider a convolutional code whose parity equations are:
What’s the rate of this code? How many states are in the state machine representation of this code?
To increase the rate of the given code, 463 student Lem E. Tweakit punctures it with the following puncture matrix:
. What’s the rate of the resulting code?
[MIT 6.02 Chp. 8, #1]

## Slide 39: Today
Encoding data using convolutional codes
Decoding convolutional codes: Viterbi Algorithm
  Hard decision decoding
  Soft decision decoding

## Slide 40: Motivation: The Decoding Problem
Message | Coded bits | Hamming distance
0000 | 000000000000 | 5
0001 | 000000111011 | 6
0010 | 000011101100 | 4
0011 | 000011010111 | ...
0100 | 001110110000 | 
0101 | 001110001011 | 
0110 | 001101011100 | 
0111 | 001101100111 | 2
1000 | 111011000000 | 
1001 | 111011111011 | 
1010 | 111000101100 | 
1011 | 111000010111 | 
1100 | 110101110000 | 
1101 | 110101001011 | 
1110 | 110110011100 | 
1111 | 110110100111 | 
Received bits:
000101100110
Some errors have occurred
What’s the 4-bit message?
Most likely: 0111
  Message whose coded bits is closest to received bits in Hamming distance

## Slide 41: The Trellis
x[n-1] x[n-2]
0 0
0 1
1 0
1 1
0/00
1/11
00
10
01
11
0/00
1/11
0/01
0/11
1/00
0/10
Starting state
1/10
1/01
Vertically, lists encoder states
Horizontally, tracks time steps
Branches connect states in successive time steps
States
1/01
0/00
1/11
0/11
1/00
0/01
1/10
1/01
0/00
1/11
0/10
0/10
1/01
0/00
1/11
0/11
1/00
0/01
1/10
0/10
Time 
Branch
Trellis:

## Slide 42: The Trellis: Sender’s View
x[n-1] x[n-2]
0 0
0 1
1 0
1 1
1/11
At the sender, transmitted bits trace a unique, single path of branches through the trellis
  e.g. transmitted data bits 1 0 1 1
Recover transmitted bits ⟺ Recover path
States
1/00
0/10
1/01
Time 

## Slide 43: Viterbi algorithm
Hard input Viterbi algorithm: Have possibly-corrupted encoded bits, after reception
Soft input Viterbi algorithm: Have possibly-corrupted likelihoods of each bit, after reception
  e.g.: “this bit is 90% likely to be a 1.”
Want: Most likely sent bit sequence
Calculates most likely path through trellis
Andrew Viterbi (USC)

## Slide 44: Viterbi algorithm: Summary
Branch metrics score likelihood of each trellis branch
At any given time there are 2K-1 most likely messages we’re tracking (one for each state)
  One message ⟷ one trellis path
  Path metrics score likelihood of each trellis path
Most likely message is the one that produces the smallest path metric

## Slide 45: Today
Encoding data using convolutional codes
Decoding convolutional codes: Viterbi Algorithm
  Hard input decoding
  Soft input decoding

## Slide 46: Hard-input branch metric
Hard input  input is bits
Label every branch of trellis with branch metrics
  Hard input Branch metric: Hamming Distance between received and transmitted bits
Received: 00
0 0
0 1
1 0
1 1
States
1/01  1
0/00  0
1/11  2
0/11  2
1/00  0
0/01  1
1/10  1
0/10  1

## Slide 47: Hard-input branch metric
Suppose we know encoder is in state 00, receive bits: 00
Received: 00
0 0
0 1
1 0
1 1
0/00
1/11
States
Time 
0
2

## Slide 48: Hard-input path metric
Hard-input path metric: Sum Hamming distance between sent and received bits along path
Encoder is initially in state 00, receive bits: 00
Received: 00
0
0 0
0 1
1 0
1 1
0
2
0/00  0
1/11  2

## Slide 49: Hard-input path metric
Right now, each state has a unique predecessor state
Path metric: Total bit errors along path ending at state
  Path metric of predecessor + branch metric
Received: 00 11
0
0 0
0 1
1 0
1 1
0
2
0/00  0
1/11  2
1/01  1
0/00  2
1/11  0
0/10  1
2
3
0
3

## Slide 50: Hard-input path metric
0/00  2
0/00  0
Each state has two predecessor states, two predecessor paths (which to use?)
Winning branch has lower path metric (fewer bit errors): Prune losing branch
Received: 00 11 01
0
0 0
0 1
1 0
1 1
0
2
1/11  2
0/11  1
0/00  1
1/01  1
2
3
0
3
1/11  0
0/10  1
3

## Slide 51: Hard-input path metric
0/10  2
Prune losing branch for each state in trellis
Received: 00 11 01
0
0 0
0 1
1 0
1 1
0
2
0/00  0
1/11  2
3
2
0/01  0
1/01  1
2
3
0
3
0/00  2
1/11  0
0/10  1
0/00  1

## Slide 52: Pruning non-surviving branches
1/01  0
0/10  2
1/11  1
0/00  1
1/11  2
Survivor path begins at each state, traces unique path back to beginning of trellis
  Correct path is one of four survivor paths
Some branches are not part of any survivor: prune them
Received: 00 11 01
0
0 0
0 1
1 0
1 1
0
2
0/00  0
3
2
3
0
1/01  1
2
3
0
3
0/00  2
1/11  0
0/10  1

## Slide 53: Making bit decisions
When only one branch remains at a stage, the Viterbi algorithm decides that branch’s input bits:
0 0
0 1
1 0
1 1
0
0
0/00  0
2
0
0/00  2
1/11  0
Decide: 0
1/01  0
3
2
3
0
1/11  1
0/10  2
0/00  1
Received: 00 11 01

## Slide 54: End of received data
1/11  0
Trace back the survivor with minimal path metric
Later stages don’t get benefit of future error correction, had data not ended
0 0
0 1
1 0
1 1
0
2
0
0/00  2
Decide: 0 1 1 1
1/01  0
3
2
3
0
1/11  1
0/10  2
0/00  1
3
2
3
0
0/11 1
1/00  1
0/01  2
1/10  0
Received: 00 11 01 10

## Slide 55: Terminating the code
Sender transmits two 0 data bits at end of data
Receiver uses the following trellis at end:
After termination only one trellis survivor path remains
  Can make better bit decisions at end of data based on this sole survivor
0 0
0 1
1 0
1 1
0/00
0/11
0/01
0/10
0/00
0/11

## Slide 56: Viterbi with a Punctured Code
Punctured bits are never transmitted
Branch metric measures dissimilarity only between received and transmitted unpunctured bits
  Same path metric, same Viterbi algorithm
  Lose some error correction capability
Received: 0-
0 0
0 1
1 0
1 1
States
1/01  0
0/00  0
1/11  1
0/11  1
1/00  0
0/01  0
1/10  1
0/10  1

## Slide 57: Today
Encoding data using convolutional codes
Decoding convolutional codes: Viterbi Algorithm
  Hard input decoding
    Error correcting capability
  Soft input decoding

## Slide 58: How many bit errors can we correct?
Think back to the encoder; linearity property:
  Message m1  Coded bits c1
  Message m2  Coded bits c2
  Message m1 ⨁ m2  Coded bits c1 ⨁ c2
So, dmin = minimum distance between 000...000 codeword and codeword with fewest 1s
0
0
1
1
0
1
0
0
1
0
1
0
0
+
+

## Slide 59: Calculating dmin for the convolutional code
Find path with smallest non-zero path metric going from first 00 state to a future 00 state
Here, dmin = 4, so can correct 1 error in 8 bits:

## Slide 60: Today
Encoding data using convolutional codes
  Changing code rate: Puncturing
Decoding convolutional codes: Viterbi Algorithm
  Hard input decoding
  Soft input decoding

## Slide 61: Model for Today
Coded bits are actually continuously-valued “voltages” between 0.0 V and 1.0 V:
0.0 V
1.0 V
Strong “0”
Weak “0”
Weak “1”
Strong “1”

## Slide 62: On Hard Decisions
Hard decisions digitize each voltage to “0” or “1” by comparison against threshold voltage 0.5 V
  Lose information about how “good” the bit is
    Strong “1” (0.99 V) treated equally to weak “1” (0.51 V)
Hamming distance for branch metric computation
But throwing away information is almost never a good idea when making decisions
  Find a better branch metric that retains information about the received voltages?

## Slide 63: Soft-input decoding
Idea: Pass received voltages to decoder before digitizing
  Problem: Hard branch metric was Hamming distance
“Soft” branch metric
  Euclidian distance between received voltages and voltages of expected bits:
0.0, 1.0
1.0, 1.0
0.0, 0.0
1.0, 0.0
(Vp0, Vp1)
“Soft” metric
Expected parity bits: (0, 1)

## Slide 64: Soft-input decoding
Different branch metric, hence different path metric
  Same path metric computation
Same Viterbi algorithm
Result: Choose path that minimizes sum of squares of Euclidean distances between received, expected voltages

## Slide 65: Putting it together: Convolutional coding in Wi-Fi
Data bits
Convolutional encoder
Modulation (BPSK, QPSK, …)
Coded bits
Demodulation
Data bits
Viterbi Decoder
Coded bits (hard-input decoding) or
Voltage Levels (soft-input decoding)

## Slide 66
Thursday Topic:
Rateless Codes
Next week’s Precepts:
Lab 2