## Slide 1: MIMO III: Channel Capacity, Interference Alignment
COS 463: Wireless Networks
Lecture 18
Kyle Jamieson
[Parts adapted from D. Tse]

## Slide 2: Today
Interference Channel Capacity
  Single-Antenna Context
MIMO Channel Capacity
Interference Alignment

## Slide 3: Two-User Interference Channel
On the same frequency channel at the same time:
  Sender 1 sends signal x1 with power P1
  Sender 2 sends signal x2 with power P2
AP receives: y[m] = x1[m] + x2[m] + w[m]
  w[m] is background Gaussian Noise with variance σ2
What are the fundamental limits of communication here?
Sender 1
Sender 2
AP

## Slide 4: Extension of Capacity to Multiple Users
Single-channel Shannon capacity is a single rate (bits/s/Hz)
Generalizing for two users capacity becomes a region:
  Set of all pairs such that simultaneously,
    User 1 can reliably communicate at rate R1 and
    User 2 can reliably communicate at rate R2
  Tradeoff between reliable communication rates:
    If User 1 wants to increase its rate, User 2 may need to decrease its rate

## Slide 5: Two-User Interference Channel: Single-User Bounds
User 2’s rate
User 1’s rate
User 1 sending alone
User 2 sending alone

## Slide 6: Interference Doesn’t Help
Assumption: User 1’s data are completely independent from User 2’s data, and vice-versa
Thought exercise: Point-to-point link sending with power
  Must outperform interfering link (otherwise interference helps)
So therefore,

## Slide 7: Two-User Interference Channel: Capacity Region
User 2’s rate
User 1’s rate

## Slide 8: Successive Interference Cancellation (SIC)
Receiver decodes information from both senders in three stages:
Decode data of user 1, treating signal from user 2 as noise
Reconstruct user 1’s signal (x’1[m]) from decoded data and subtract from aggregate received signal y[m], cancelling it:
  y’ [m] = y [m] − x’1[m]
  = x2[m] + (x1[m] – x’1[m]) + w[m]
Decode user 2’s signal from y’[m]

## Slide 9: Decoding Strong BPSK with weak QPSK
“1”
“0”
I
Q
−1
+1
Input bit=“0”
Input bit=“1”
BPSK model
“10”
“00”
“01”
“11”
=
=
Interference-cancelled QPSK
BPSK decoding
BPSK bit
decisions
−
−
Received r(t)

## Slide 10: Power Difference Helps Superposition Coding
I
Q
−1
+1
Input bit=“0”
Input bit=“1”
−

## Slide 11: SIC: Choice of User Order
User 2’s rate
User 1’s rate

## Slide 12: Comparison with CDMA
CDMA: Every user decoded treating the other users as noise
  Achieves Point C
    But, User 1 starves
CDMA power control: Reduce power of the strong user
  Achieves Point D

## Slide 13: Comparison with TDMA/FDMA + Power Control
Allocate α time- or frequency-fraction to User 1; 1 − α to User 2
Scale each user’s power according to allocated proportion
User 1 maximum rate:
User 2 maximum rate:

## Slide 14: Comparison with TDMA/FDMA + Power Control
Allocate as follows:
  α time- or frequency-fraction to User 1; 1 − α to User 2
Tuning α, the users can achieve a point on the (optimal) A-B line

## Slide 15: Today
Interference Channel Capacity
MIMO Channel Capacity
Interference Alignment

## Slide 16: Review: The MIMO Channel
Transmit three symbols per symbol time:
Represent the MIMO channel as
  is the MIMO channel matrix, noise
antenna separation
Send x1, x2, x3
Receive y1, y2, y3
1
2
3
1
2
3

## Slide 17: Recap: MIMO Radio Channel
MIMO link with nt transmit, nr receive antennas
MIMO radio channel itself:

## Slide 18: Recap: Zero-Forcing MIMO
Transmitter does not know H (channel)
Each symbol time:
  Sends nt symbols (original Data), one per transmit antenna
Data arrives mixed together at receiver antennas y
Sender
Receiver

## Slide 19: Recap: Zero-Forcing MIMO
Receiver knows H (channel)
Each symbol time:
  Receive nr mixed-up signals y
  For each of the nt transmitted symbols:
    Zero-Forcing Receiver nulls all but that symbol

## Slide 20: Today
Interference Channel Capacity
MIMO Channel Capacity
  Vector Space Intuition
  Eigenmode Forcing via Singular Value Decomposition
Interference Alignment

## Slide 21: MIMO Channel Capacity: Motivation
The story so far: Copy data into each symbol time
  Looked at when this performed well, poorly
    Answer: MIMO channel conditioning  “Rich multipath environment” around sender, receiver
* * *
Today’s first topic: Is this the best bits/seconds/Hz possible?
  What’s the capacity of a MIMO channel?
    Similar question: Shannon capacity of a single-input, single-output (SISO) channel

## Slide 22: Where’s the Room for Improvement?
Suppose the transmitter knows H (channel)
Zero-forcing receiver heard h1, h2, h3
  Power loss at receiver (due to Proj⟘) for h3
Idea: Use transmit antennas 2 and 3 to send the ideal direction
  No longer simply one symbol, one transmit antenna
h2
Send this instead of h3
h1
h3

## Slide 23: How Might We Control Directions?
Sender precodes data into actual transmission in desired directions x
Receiver processing changes accordingly
Sender
Receiver

## Slide 24: What Kind of Precoding?
Recall, we wanted to make independent channels on each wireless channel path
Suppose H were diagonal:
Then the yk channel output would only depend on xk
  Parallel, independent channels

## Slide 25: Today
Interference Channel Capacity
MIMO Channel Capacity
  Vector Space Intuition
  Eigenmode Transmission
Interference Alignment

## Slide 26: Singular Value Decomposition (SVD)
The insight lies in a special way of “factoring” matrix H
Any matrix H has an SVD: H  UΛV*
  Λ is a diagonal matrix (contains zeroes off-diagonal)
  U and V are unitary (UU* = U*U = VV* = V*V = I)
H
=
nt
nr
Λ
nt
nr
V*
×
nt
nt
U
×
nr
nr

## Slide 27: Interpreting the SVD Steps
Λ matrix with the singular values
  One per significant radio channel path
V* translates to the radio channel path coordinate system where channels are decoupled
U translates back, to antenna coordinate system (undoes the V* translation)
H
=
nt
nr
Λ
nt
nr
V*
×
nt
nt
U
×
nr
nr

## Slide 28: Leveraging the SVD in a Practical System
  Alone, SVD does nothing (just analyzes what H does)
  Want to put data into the radio channel coordinate system
Want here 
Insight: VV* = I (Unitary property)

## Slide 29: Leveraging the SVD in a Practical System
  Sender precodes with V, receiver “post-codes” with U*
    V is unitary, so V*V = I (same for U)
      So data sees independent channels
  This is called MIMO eigenmode transmission
Sender
Receiver
No effect

## Slide 30: A Model for Eigenmode Transmission
Performance model for the eigenmode transmitter/receiver
All channels decoupled, transmit power Pk  SNR on i th channel:
Sender
Receiver

## Slide 31: Performance: Uniform Power Division
  At high SNR (the common case in wireless LANs), with total transmit power P evenly divided over spatial paths
  Data rate =
  * * *
  How can we do better?
    Idea: Allocate different transmit powers to different radio channel paths i
    Problem we’ve seen before in 463 in OFDM context

## Slide 32: Waterfilling for MIMO Power Allocation
Physical Channel Path / Eigenmode i
μ
Allocated transmit power Pi

## Slide 33: MIMO Capacity: Takeaways
OFDM – MIMO analogy:
  A transformation (OFDM: FFT, MIMO: SVD)
  renders interfering channels in
  (OFDM: frequency, MIMO: space) independent
MIMO Eigenmode transmission:
  Transmitter sends directionally, along spatial paths of the radio channel
  Receiver listens directionally, along same spatial paths
  Achieves the MIMO channel capacity

## Slide 34: Today
Interference Channel Capacity
MIMO Channel Capacity
Interference Alignment

## Slide 35: Interference Alignment (IA)
Number of concurrent MIMO streams a client can send is limited by the number of antennas
  Sending more streams results in interference between streams
  Also limited by the amount of multipath in the environment
New Idea: Use MIMO precoding techniques to align interference at receivers to advantage
Requires APs cooperating via a wired backhaul
  e.g. APs owned by one organization

## Slide 36: MIMO channel representation
As before, model channel from one antenna i to another j as one complex number
Channel matrix H from a client to an AP is formed by []

## Slide 37: Uplink: Interference Between Networks
Client 1 has 2 packets for AP 1; Client 2 has a packet for AP 2
  Two-antenna APs, so each decoding in a 2-D space
Three packets form three vectors in the 2-D space at each AP
  Therefore, the APs can’t decode these 3 packets
1
2
1
2

## Slide 38: Interference alignment: Basic idea (1)
Clients transmit p2 and p3 aligned at access point (AP) 1
  They add up in their one direction
AP 1 zero-forces to decode p1, sends it over backhaul to AP 2
AP 2 subtracts p1 from the signal it receives, cancelling it
1
2
1
2

## Slide 39: Interference alignment: Basic idea (2)
AP 2 uses zero-forcing receiver to decode p2, p3
AP 2 sends p2 to AP 1 (or onward on behalf of client 1)
1
2
1
2

## Slide 40: Uplink: Sketching a Practical Protocol
Client 2 chooses v3 so that H11v2 = H21v3
  How does client 2 know H11 and H21?
    Client 1 can include in its packet header
1
2
1
2
Transmit precoding: client multiplies packet by vector v
  Changes alignment at receiver
Client 1 picks random precoding vectors v1 and v2
Client 1 begins transmission

## Slide 41: Uplink: Four Concurrent Packets?
All packets but one (p1) must align at AP 1, so AP 1 can decode
Subtract p1 from the four packets at AP 2, leaving three packets
AP 2 can only decode two packets at a time (2-d space)
  Can’t decode p3 and p4 at AP 2: Can only decode p1 and p2
1
2

## Slide 42: Downlink Interference Alignment
Clients can’t exchange frames over backhaul
Instead, align neighboring APs’ interference at each client
p2, p3 aligned:
p1, p3 aligned:
p1, p2 aligned:

## Slide 43
Thursday Topic:
Ripple II: Faster Communication
through Physical Vibration
(Download & Pre-read paper!)