## Slide 1: Programming Abstractions for Software-Defined Networks
Jennifer Rexford
Princeton University

## Slide 2: Software-Defined Networking
Can program the network
  Network-wide visibility
  Direct control over the switches
  Simple data-plane abstraction
But, does not make it easy
  Low-level programming interface
  Explicit resource control
  Non-modular
Controller

## Slide 3: SDN Research at Princeton
Programming languages
  Raise the level of abstraction
  Queries, composition, and updates
Grappling with reality
  One controller platform  Coexisting platforms
  Central controller  Replicated controllers
  Simple data plane  Flexible packet processing
Real applications
  Server load balancing
  Cellular core networks
  Internet eXchange Points

## Slide 4: Programming Languages
Frenetic Project
frenetic-lang.org
Joint work with the research groups of David Walker (Princeton), Nate Foster (Cornell), and Arjun Guha (Umass-Amherst), and Josh Reich (now at AT&T Research)

## Slide 5: Network Control Loop
Read
state
OpenFlow
Switches
Write
policy
Compute Policy

## Slide 6: Network Control Loop
Query
language
OpenFlow
Switches
Consistent updates
Module Composition

## Slide 7: Query Abstractions
Declarative queries
  What to collect, not how
Efficient compilation
  Keep traffic in the “fast path”
  … using OpenFlow rules
Recent work: path queries
  Regular expression on paths
  Tagging of packets in the data plane
Select(bytes)
Where(inport:2)
GroupBy([dstmac])
Every(60)
Select(packets)
GroupBy([srcmac])
SplitWhen([inport])
Limit(1)
Learning Host Location
Traffic Histogram
ingress() ^ (switch != FW)* ^ egress()
Packets avoiding firewall

## Slide 8: Policy Composition: Operators
Modular controller application
Policy as a function
  From “located packet” to set of located packets
Composition operators
  Parallel: Monitor + Route
  Sequential: LB >> Route
Controller Platform
LB
Route
Monitor
FW

## Slide 9: Policy Composition: Compilation
Synthesizing low-level rules
Recent work: incremental compilation
Controller Platform
Route
Load Balancer
>>
dstip = 10.0.0.1  fwd(1)
dstip = 10.0.0.2  fwd(2)
srcip = 0*, dstip=1.2.3.4  dstip=10.0.0.1
srcip = 1*, dstip=1.2.3.4  dstip=10.0.0.2
srcip = 0*, dstip = 1.2.3.4  dstip = 10.0.0.1, fwd(1)
srcip = 1*, dstip = 1.2.3.4  dstip = 10.0.0.2, fwd(2)

## Slide 10: Consistent Updates
Transition from policy P1 to P2
  New access control, new paths, …
Preserve invariants
  No loops, blackholes, congestion, …
Using OpenFlow mechanisms
  Tag packets with policy version number
  Two-phase update (internal, then ingress)
Recent work
  Dynamic schedules for faster updates (with MSR)

## Slide 11: Grappling With Reality
Joint with David Walker (Princeton), Mike Freedman (Princeton), and P4 team (p4.org)

## Slide 12: CoVisor: Compositional Hypervisor
Mix-and-match “best of breed” apps
  Different languages, different controllers
Using Frenetic composition operators
Prototype as an extension of OpenVirteX
Monitor
Floodlight
OpenFlow
POX
Load Balancer
OpenFlow
Route
ONOS
OpenFlow
OpenFlow
Compositional Hypervisor

## Slide 13: Ravana: Replicated Controllers
Logically centralized control
  Abstraction of one controller
  Replication for reliability
Beyond replicated state machine
  Switches maintain state
  Commands are not idempotent
  One event  commands to many switches
  Observations by hosts and controller app
New replication protocol
  For SDN, NFV, software-defined storage, …
Controller

## Slide 14: P4: Flexible Packet Processing
OpenFlow 1.0 is too simple
  12 header fields, one match-action table
OpenFlow 1.x is too complicated
  42 header fields, various match-action tables
Protocol-independent packet processing
  Protocol independence
  Target independence
  Reconfigurability in the field
Ongoing work: efficient compilation

## Slide 15: SDN Applications

## Slide 16: Controller Applications
Niagara: server load balancing
  Split traffic over multiple backend servers
  … using commodity OpenFlow switches
  Demo at the REANNZ exchange point
SoftCell: cellular core networks
  Support user mobility and middlebox steering
  … using commodity OpenFlow switches
  Evaluation on traces from a large LTE network
SDX: Internet eXchange Points
  Laurent Vanbever’s talk!

## Slide 17: Conclusion
For SDN to succeed, we need
  Programming abstractions
  Practical underlying systems
  Compelling applications
SPAN collaboration
  Frenetic: Josh Reich (AT&T)
  P4: Nick McKeown (Stanford), Dan Daly (Intel)
  SDX: Scott Shenker (UCB)
Exploring tech transfer with On.Lab
  OpenVirteX: compositional hypervisor
  ONOS: Frenetic support on top of ONOS