## Slide 1: Network Layers
Jennifer Rexford
COS 316 Guest Lecture

## Slide 2: Modularity in System Design
Barbara Liskov, MIT
“Modularity based on abstraction is the way things get done.”

## Slide 3: Modularity Through Layering
Or, “Can I Explain How the Internet Works in One Lecture?”

## Slide 4: Modularity Through Protocol Layering
name
address
path
Notes: Each layer provides a service to the layer above, and relies on the service of the layer below

## Slide 5: Internet Protocol Layers
Link
Network
Transport
Application
Physical
Between a device and the physical medium
Between physically-connected devices
Between nodes in different networks
Between hosts while maintaining quality-of-service
Between software applications running on hosts

## Slide 6: Internet Protocol Layers
Best-effort local frame delivery
Best-effort global packet delivery
Reliable streams
Application Messages
Datagrams
Link
Network
Transport
Application
Bit delivery
Physical
Ethernet, WiFi, etc.
IP
TCP, UDP
HTTP, SMTP, FTP, Skype, etc.

## Slide 7: Layers in Action
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Ethernet frame
Ethernet frame

## Slide 8: Encapsulation: Layers of Headers
Get index.html
Connection ID
Source/Destination
Link Address
Host
Host
Link hardware
Host-to-host
connectivity
App-to-app
channels
Application
Ethernet header
IP header
TCP header
HTTP
message

## Slide 9: The Internet Hourglass with “Narrow Waist”
TCP
UDP
Link
Physical
Applications
The Hourglass Model
Waist
The “narrow waist” facilitates interoperability
FTP
HTTP
TFTP
NV
TCP
UDP
IP
LINK1
LINK2
LINK3
…

## Slide 10: Network Protocols

## Slide 11: What is a Network Protocol?
Rules that govern communication
  How to identify the devices and establish connectivity
  Message format (syntax) and meaning (semantics)
A distributed solution to a problem
  Deliver an ordered, reliable stream of bytes to another end-point
  Share network bandwidth fairly
  Compute shortest paths on a graph
  Automatically learn how to reach remote hosts
  Share an individual link’s bandwidth fairly

## Slide 12: Application: HyperText Transfer Protocol (HTTP)
GET /courses/archive/spr12/cos461/ HTTP/1.1
Host: www.cs.princeton.edu
User-Agent: Mozilla/4.03
CRLF
HTTP/1.1 200 OK
Date: Mon, 6 Feb 2012 13:09:03 GMT
Server: Netscape-Enterprise/3.5.1
Last-Modified: Mon, 7 Feb 2011 11:12:23 GMT
Content-Length: 21
CRLF
Site under construction
Request
Response
Notes: Relies on delivery of an ordered, reliable byte stream

## Slide 13: Transport Protocols: TCP and UDP
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 5.6.7.8
Echo server
(port 7)
Service request for
5.6.7.8:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 14: Transport: Transmission Control Protocol (TCP)
Ordered, reliable stream of bytes
  Built on top of best-effort packet delivery at the network layer (IP)
Challenges with IP
  Lost or delayed packets
  Corrupted packets
  Out-of-order packet arrivals
  Receiver that runs out of space
  Network that cannot handle the load

## Slide 15: TCP: Lost or Delayed Packets
Internet
GET index.html
Problem: Lost or Delayed Data
Internet
GET index.html
Solution: Timeout and Retransmit
GET index.html
GET index.html
Waiting for an acknowledgment…

## Slide 16: TCP: Corrupted Data
Sender computes a checksum
  Sender sums up all of the bytes
  And sends the sum to the receive
Receiver checks the checksum
  Received sums up all of the bytes
  And compares against the checksum
Internet
GET index.html
GET indey.html
134
+ 212
= 346
134
+ 216
= 350
Then what?

## Slide 17: TCP: Out-of-Order Packet Arrivals
Solution: Add Sequence Numbers
Problem: Out of Order
GET
x.ht
inde
ml
GET x.htindeml
GET index.html
ml
4
inde
2
x.ht
3
GET
1

## Slide 18: TCP: Receiver that Runs Out of Space
Receiver maintains a window size
  Amount of data it can buffer
Advertises window to the sender
  Amount sender can send without acknowledgment
Ensures that sender does not send too much
  While still sending as much as possible
?
Flow control!

## Slide 19: Network that Cannot Handle the Load
Some TCP senders need to slow down…
TCP congestion control (future lecture)!

## Slide 20: Network Layer: Internet Protocol (IP)
Best-effort global packet delivery
  Packet delivery: each packet handled independently
  Best-effort: allow loss, delay, corruption, and out-of-order delivery
source
destination
IP network

## Slide 21: IP: Best-Effort Packet Delivery is Simpler
Never having to say you’re sorry…
  Don’t reserve bandwidth and memory
  Don’t do error detection and correction
  Don’t remember anything from one packet to next
Easier to survive failures
  Transient disruptions are okay during failover
Can run on nearly any link technology
  Greater interoperability and evolution
  RFC 1149: IP Datagrams over Avian Carriers

## Slide 22: IP: Statistical Multiplexing
Data traffic is bursty
  Logging in to remote machines
  Exchanging e-mail messages
Don’t waste bandwidth
  No traffic exchanged during idle periods
Better to allow multiplexing
  Different transfers share access to same links

## Slide 23: IP: Scalable Global Packet Delivery
Hierarchical IP addresses (“zip code”)
  Variable-length prefix, identified by mask length
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.2.4
1.2.2.156
1.2.3.232
5.6.7.8
5.6.7.9
5.6.7.212
1.2.2.0/23
5.6.7.0/24
forwarding table
Today’s IP routers have ~800,000 prefixes

## Slide 24: IP: Scalable Global Packet Delivery
Distributed global IP routing
  Internet: a “network of networks” (Autonomous Systems)
7
6
5
3
2
1
4
5.6.7.0/24
Today’s Internet has ~60,000 ASes

## Slide 25: IP: Scalable Global Packet Delivery
Distributed, policy-based IP routing
  Interdomain routing: diffusion of IP prefixes (Border Gateway Protocol)
3
2
1
5.6.7.8
“5.6.7.0/24:
path (2,1)”
“5.6.7.0/24:
path (1)”
data traffic
data traffic

## Slide 26: Link Layer: Ethernet Local Area Networks
Automatic bootstrapping of best-effort local frame delivery
  MAC address in end-host network interface card
  MAC learning to reach other hosts in the LAN
When an Ethernet frame arrives
  Switch inspects the source MAC address
  … and associates the address with the incoming interface
A
B
C
D
Switch learns how to reach A.

## Slide 27: Link Layer: Ethernet Local Area Networks
Automatic bootstrapping of best-effort local frame delivery
  MAC address in end-host network interface card
  MAC learning and flooding to reach other hosts in the LAN
When the frame has an unfamiliar destination
  Switch forwards the frame out all interfaces
  … except the incoming interface
A
B
C
D
When in doubt, shout!

## Slide 28: Putting it All Together: Crossing the Layers
Crossing the layers
  Application: HTTP request and response messages
  Transport: TCP ordered reliable byte stream
  Network: best-effort global IP packet delivery
  Link: best-effort local Ethernet frame delivery
Web client
Web server
Internet

## Slide 29: Putting it All Together: Crossing the Layers
Naming at different layers
  Application: http://www.cs.princeton.edu/courses/archive/spr12/cos461/
  Transport: TCP connection to IP address 5.6.7.8 on port 80
  Network: server host interface with IP address 5.6.7.8
  Link: server host interface with MAC address 00:15:C5:49:04:A9
Web client
Web server
Internet
Notes: With DNS mapping the www.cs.princeton.edu to IP address 5.6.7.8, and ARP translating IP address 5.6.7.8 to MAC address…

## Slide 30: Putting it All Together: Crossing the Layers
Routing at different layers
  Application: maps request to local object /courses/archive/spr12/cos461/
  Transport: directs TCP segments to specific transport port (e.g., port 80)
  Network: directs IP packets toward IP destination prefix 5.6.7.0/24
  Link: directs Ethernet frames to MAC address 00:15:C5:49:04:A9
Web client
Web server
Internet

## Slide 31: Conclusion
Modularity
  The way to build and manage large systems
  Protocol layering in computer networks
Network protocol layers
  Application, transport, network, link, and physical
  Internet “hourglass” model with IP as the “narrow waist”
Customized protocol designs
  Separation of concerns that are unique to each layer
  Content naming and delivery, ordered reliable byte stream, scalable best-effort delivery, autoconfiguration of best-effort frame delivery