## Slide 1: Networks Capable of Change
Jennifer Rexford Princeton University

## Slide 2: The Great Success of the Internet
IP network
Best-effort packet delivery
Arbitrary applications
Programmability: determines who can effect change, and where

## Slide 3: Innovation Above, Below, and Alongside
Applications
Media
Internet
Hosts
Notes: But, ironically, the Internet did not plant the seeds of its own reinvention

## Slide 4: But, Limited Innovation “Inside” the ’Net
Over specified
  Slow protocol standardization
  Standards in fixed-function hardware
Closed equipment
  Software bundled with hardware
  Vendor-specific interfaces
Few people can innovate
  Equipment vendors write the code
  Long delays for new features
But, the inside of the network does need to change
Notes: Needs to change because of performance, reliability, security, and more. And unique needs in different settings.

## Slide 5: Traditional (Non-Programmable) Network
Management System
Control Plane
Control Plane
Control Plane
Data Plane
(proprietary)
Data Plane
Data Plane
(proprietary)
Long standards process,
Closed software & APIs

## Slide 6: Modern Programmable Network
Central Controller
Local Controller
Local Controller
Local
Controller
Data Plane
(programmable)
Data Plane
Data Plane
(programmable)
Open source
Open APIs
Various “apps”
Open or closed network OS

## Slide 7: Programmable Networks: A Brief History
“The Road to SDN: An Intellectual History of Programmable networks”: https://queue.acm.org/detail.cfm?id=2560327
active networks
control-data separation
OpenFlow and network OS
programmable data planes and P4
1995
2000
2005
2010
2015
2020

## Slide 8: Programmable Data Planes
Data plane designed for programmability
  RMT paper at SIGCOMM’13 (from Stanford and TI)
  A performance-first variant of active networking
Stages
Deparser
Parser
Memory
Persistent State
ALU
Match-
Action
Table
Notes: Pragmatic in limited programmability, and pragmatic now because of changes in hardware trends

## Slide 9: P4 Language
Protocol independence
  Configure a packet parser
  Define typed match+action tables
Target independence
  Program without knowledge of switch details
  Rely on compiler to configure the target switch
Reconfigurability
  Change parsing and processing in the field
Networking
Languages
Hardware
“P4: Programming Protocol-Independent Packet Processors”: https://www.sigcomm.org/sites/default/files/ccr/papers/2014/July/0000000-0000004.pdf
Notes: A group of us came together to think about the language for programming such devices. Not just an API for installing rules, but a language.
Setting up the P4 Consortium with Nick McKeown, and later Amin Vahdat (Google) joined us

## Slide 10: Killer App: Network Telemetry
Traffic
  Heavy-hitter traffic flows (by IP, by domain name, …)
  Flow responsible for backlogs in packet queues
Performance
  Packet loss, queuing delay, round-trip time, ...
  Root cause of low throughput
  Video quality-of-experience
Security
  Traffic scanning
  Distributed denial-of-service attacks
  Intrusion detection systems
Goal: Hardware-friendly data structures!

## Slide 11: Heavy-Hitter Flows

## Slide 12: Heavy-Hitter Detection
Heavy hitters
  The k largest trafic flows
  Flows exceeding threshold T
Space-saving algorithm
  Table of (key, value) pairs
  Evict the key with the minimum value
Id | Count
K1 | 4
K2 | 2
K3 | 7
K4 | 10
K5 | 1
K6 | 5
New Key K7
Table scan

## Slide 13: Approximating the Approximation
Evict minimum of d entries
  Rather than minimum of all entries
  E.g., with d = 2 hash functions
Id | Count
K1 | 4
K2 | 2
K3 | 7
K4 | 10
K5 | 1
K6 | 5
New Key K7
Multiple memory accesses

## Slide 14: Approximating the Approximation
Divide the table over d stages
  One memory access per stage
  Two different hash functions
Id | Count
K1 | 4
K2 | 2
K3 | 7
New Key K7
Id | Count
K4 | 10
K5 | 1
K6 | 5
Going back to the first table

## Slide 15: Approximating the Approximation
Rolling minimum across stages
  Avoid recirculating the packet
  … by carrying the minimum along the pipeline
Id | Count
K1 | 4
K2 | 10
K3 | 7
New Key K7
Id | Count
K4 | 2
K5 | 1
K6 | 5
Id | Count
K1 | 4
K7 | 1
K3 | 7
Id | Count
K2 | 10
K5 | 1
K6 | 5
(K2, 10)

## Slide 16: P4 Prototype and Evaluation
Id | Count
K1 | 4
K2 | 10
K3 | 7
Id | Count
K4 | 2
K5 | 1
K6 | 5
New Key K7
(K2, 10)
Hash on packet header
Packet metadata
Conditional updates to compute minimum
Register arrays
High accuracy with overhead proportional to # of heavy hitters

## Slide 17: Alleviating Microbursts

## Slide 18: Alleviating Microbursts
Small timescale traffic bursts
  Clog the packet queues
  Cause packet delay and loss
Manage microbursts to handle
  Bursty workloads
  Low-cost switches (shallow buffers)
  High link utilization
Goal: penalize the most responsible flows
5x
3x
1x
16:00:00
0:00:00
8:00:00
16:00:00
Time in day (24h)
Queue Length
Microbursts

## Slide 19: Microburst Management Policy
Active queue management
  Mark each packet probabilistically
  In proportion to its flow’s contribution to the heavy queue
55%
10%

## Slide 20: Detecting Heavy Flows in the Queue
For each flow, how many packets are in the queue?
P4 data structure challenges
  Updating on packet arrival and departure
  Per-flow state (key and count)
Key | Count
 | 1
 | 5
 | 1
 | 1
 | 2
 | 1

## Slide 21: Processing Each Packet Only Once
S1 | S2 | S3 | S4 | …
Memory access
Flow | ~Count
 | 1
 | 5
 | 1
 | 1
Slice traffic into time windows
Each snapshot records T=4 packets
Queue
Egress
B
B
Historical Departures
D
B
A
C
C
D
B
B
B
A
B
B
I enqueued at t=5
I dequeued at t=14
Why am I waiting?
?
A
B
C
D

## Slide 22: Round-Robin Snapshots
Clean and Reuse the snapshots in the data plane!
Read
Read
Write
Clean
Read
Read
Read

## Slide 23: Avoiding Per-Flow State
Compact data structures
  With limited memory and processing
  … at the expense of lower accuracy
Estimate per-flow counts per snapshot
  With accurate estimates for large flows
Count-Min Sketch per snapshot
  C columns indexed by hash functions
  Increment hashi(flowid) in column I
  Estimate is the min of the C counts
Count-Min Sketch [CM ‘05]
C columns
B Buckets
f
+1
+1
+1

## Slide 24: On the Princeton Campus
Performance symptoms
  Big neuroscience data transfers
  High loss with low average load
  Router with limited measurements
Microburst analytics on Tofino
  Microbursts on a small timescale
  Caused by PerfSONAR active probes
Recent deployment with AT&T
Internet2
Mirrored traffic
Tofino
Network TAPs
Neuroscience
Institute
See https://p4campus.cs.princeton.edu/ web site for more details!

## Slide 25: Path Performance

## Slide 26: Multipath Load Balancing
Load balancing entirely in the data plane
  Collect real-time, path-level performance statistics
  Group packets into “flowlets” based on time & headers
  Direct each new flowlet over the current best path
S1
S2
S3
S4
ToR 10
ToR 1
Data

## Slide 27: Path Performance Statistics
Using the best-hop table
  Update the best next-hop upon new probes
  Assign a new flowlet to the best next-hop
S1
S3
S4
Best-hop table
Best Next-Hop | Path Utilization
S3 | 50%
S4 | 10%
… | …
0
1
…
Dest ToR
Data
Data
Probe
Probe

## Slide 28: Flowlet Routing
Using the flowlet table
  Update the next hop if enough time has elapsed
  Update the timestamp to the current time
Forward the packet to the chosen next hop
Flowlet table
S1
S3
S4
Dest ToR | Timestamp | Next-Hop
ToR 10 | 1 | S2
ToR 0 | 17 | S4
… | … | …
0
1
…
h(flowid)
Data
Data

## Slide 29: Putting it all Together Using P4
data packet
current best next-hop S3
chosen next-hop
Update next-hop (if enough time elapsed) and time
Dest ToR | Timestamp | Next-Hop
ToR 10 | 1 | S2
ToR 0 | 17 | S4
… | … | …
Best Next-Hop | Path Utilization
S3 | 50%
S4 | 10%
… | …
0
1
…
Dest ToR
0
1
…
h(flowid)

## Slide 30: Sonata Platform

## Slide 31: Flexible Telemetry for Network Management
Many analysis questions
  Performance diagnosis
  Cyber attack detection
  Traffic engineering
Familiar query language
  Packet as a tuple
  Dataflow operators
  E.g., Spark-like queries
E.g., DNS reflection attacks
👺
😵
Src: Victim
Dst: DNS
Src: Victim
Dst: DNS
Src: DNS
Dst: Victim
Src: DNS
Dst: Victim
DNS
DNS
Attacker
Victim
DNS Response Traffic
From Unique DNS Servers
To a Single Victim
Exceeds a Threshold

## Slide 32: Spark-Like Query Language
victimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
DNS Response Traffic
From Unique DNS Servers
To a Single Victim
Exceeds a Threshold
1
2
3
4
5
6
7
Notes: Let’s see how this type of monitoring query might be expressed in a modern data flow-like language.
[🌀] On line two we see a filter operator that specifies DNS Traffic,
[🌀] lines 3-4 to narrow that down to traffic from unique DNS servers,
[🌀] line 5 further narrows the query down to a single Victim, and
[🌀] lines 6-7 determine when the number of unique DNS servers contacting that single victim exceeds a threshold.
This query is easy to express in a high-level language, and easy to compute at a modern stream processor. But how does executing this query scale?

## Slide 33: Query-Driven Collection and Analysis
Scalability challenges
  Many packets and flows
  Many queries
  Many switches
Query-driven collection
  Integrate collection and analysis
  Customize collection to the query
  Fine-grained with low overhead
Query partitioning
tuples

## Slide 34: Compiling Individual Operators
filter(p)
Stream of Elements
Elements Statisfying
Predicate (p)
Match | Action
p | 
udp.sport == 53 | 
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
Notes: Let's start by looking at what it takes to compile individual operators to match-action tables, one at a time.
[🌀] The filter operator takes [🌀] a stream of elements as input, and returns[🌀] the set of elements that satisfy some predicate p.
We can implement this in a [🌀] match-action table by simplying supply p as the match component.
If we return to the [🌀] DNS reflection query I described in the beginning, we see that the predicate performs an exact match on the UDP source port. We would implement this [🌀] directly in the match-action table as shown.

## Slide 35: Compiling Individual Operators
filter(p)
Stream of Elements
Elements Statisfying
Predicate (p)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
control ingress {
apply(filter_map_table);
...
apply(reduce_table);
if (m.reduce_table_sum > Th) {
apply(report_table)
}
Notes: The filter operator can also be used to apply a conditional predicate, as we see in the last line of this query.
In this case, we would instead choose to implement the filter in the control flow between match-action tables in the pipeline. [🌀] If we look at this code block, we see that the match-action tables that each operator compiles to is applied in the control flow of the processing pipeline. After the reduce_table is applied, the final filter’s predicate is supplied in conditional control flow that then conditionally applies the table that performs the reporting to the stream processor, when the predicate is satisfied.

## Slide 36: Compiling Individual Operators
map(f)
Match | Action
 | f
* | m.dstIP = p.dstIP m.srcIP = p.srcIP
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Stream of Elements
Result of Applying
Function f to Each Element
1
2
3
4
5
6
7
Notes: Similar to filter, [🌀] The map operator also takes [🌀] a stream of elements as input and [🌀] returns the set of elements with a function(f) applied to each element.
We can implement that, in general, [🌀] as the action body of a match-action table where the function f, if supported by the data plane, is applied.
Returning to our example query [🌀] , the function applied here is simply a projection of the entire original packet to a single dstIP, srcIP pair. In this case, [🌀] we would just store the values from the packet in metadata for subsequent processing. However, other actions such as decrementing a TTL field are possible.

## Slide 37: Compiling Individual Operators
reduce(f)
Match | Action
* | idx = hash(m.dstIP)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Stream of Elements
Result of Applying
Function f Over All Elements
Stateful Memory
Match | Action
* | stateful[idx] += 1
1
2
3
4
5
6
7
Notes: The [🌀] reduce operator also takes [🌀] a stream of elements as input and returns [🌀] a single result that is the application of the function f over all elements. Naturally, we break up the stream into windows of size (w) seconds to compute this function over a finite stream.
Unlike map and filter, the reduce function requires some stateful memory to store the intermediate value of the function between the arrival of successive elements. Just like with the map operator, the function to be applied must still be executable in the data plane.
Like the map operator, we would also apply the function f in the action body of a match-action table, but since stateful memory is implemented as a hash-table in PISA switches, we must first compute an index into the hash table before looking up the value stored in it.
In the case of our example query, [🌀] the first table computes an index by hashing the key of interest, in this case dstIP. Since lookup into the hash-table depends on the value of the index, both the value in the hash table in the index cannot be looked up in the same table. The second table applies the function (sum) to the intermediate value and the next element (1).

## Slide 38: Compiling a Query
Programmable Deparser
Stages
Programmable Parser
State
Filter Map
Filter
D1
D2
Map
R1
R2
Notes: To compile an entire query, we would just sequentially apply [🌀] the set of match-action tables generated by each individual operator. Here the D1/D2 and R1/R2 abbreviate the first and second tables of the distinct and reduce operators, respectively.

## Slide 39: Compiling a Query
Programmable Deparser
Stages
Programmable Parser
State
Filter Map
Filter
D1
D2
Map
R1
R2
Notes: In reality, the compilation can be optimized such that two match action tables can occupy the same stage as long as the values do not depend on one another. For example the actions in the first map table and actions in the first lookup for the distinct operator could be coalesced into a single table in the first stage. But as described before the two tables implementing distinct and reduce cannot be executed in the same stage due to the data dependency.

## Slide 40: Partitioning Decisions
Query Planner
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
Target Resources?
Reduce Load?
Notes: So we’ve seen how a [🌀] single query, is compiled to a sequence of match action tables in the data plane. However, we want to run [🌀] several different queries concurrently. Now we must consider, for all of the operators in all of the queries that can be compiled to the data plane, which ones do we actually choose to offload to the data plane? Determining the answer to that question is the [🌀] job of the query planner which takes into consideration two questions? First, [🌀] does the target have enough remaining resources and to offload a partitioning to the data plane and Second, [🌀] does this partitioning reduce the load on the stream processor optimally?

## Slide 41: Closed-Loop Control

## Slide 42: Traditional Network Management
1. Measure
(load, performance, traffic, failures)
2. Analyze
(traffic matrix, route optimization, anomaly detection, fault localization)
3. Configure
(reconfigure tunnels, link weights, access control lists)

## Slide 43: Grand Challenge
High-level goals
Compiler
Switch OS
switch
Controller
Switch OS
switch
NIC
NIC
vSwitch
NIC
NIC
vSwitch
Distributed Software
control loop

## Slide 44: Conclusions
Programmable networks
  High-speed packet-processing hardware
  P4 programming language
  Networking use cases (e.g., telemetry)
Exciting grand challenges
  Closed-loop control
  Correct by construction
  Network-wide programming