## Slide 1
Compiling Network Path Queries
Srinivas Narayana
Princeton University
Notes: 1

## Slide 2: Network Management is Complex
Computer networks getting bigger
Commodity components: high failure rates
Outages are costly!
  ~ $300K/hour, 200 minutes/outage
Management tools are useful
Programmatic tools can really help!
“The cost of downtime.” Andrew Lerner, 2014
“Downtime, outages and failures: Understanding their true costs.” Evolven, 2012

## Slide 3: Management = Measure + Control
Network Operators
Measure
Control
Software-Defined Networking (SDN)

## Slide 4: Software-Defined Networking
SDN controller
Forwarding
Control logic
Rules

## Slide 5: Measuring is a Hard Problem
A few standard tools:
  Ping, traceroute, SNMP, NetFlow, tcpdump
An operator must “join” multiple data streams:
  Forwarding: controller policy, topology updates
  Traffic: packet samples, counters

## Slide 6: Example: Where’s the Packet Loss?
A
B
Suspect: Faulty network device(s) along the way.
100 pkts
25 pkts 

## Slide 7: Example: Where’s the Packet Loss?
A
B
Idea: “Follow” the path of packets through the network.
Fine-grained (AB) counters
+ Forwarding
Understand Complex Policies
100 pkts
25 pkts 
Program Complex
Rules

## Slide 8: Lots of Measurement Use-Cases
Traffic matrix
Uneven load balancing
DDoS source identification
Port-level traffic matrix
Congested link diagnosis
Slice isolation
Loop detection
Middlebox traversal order
Incorrect NAT rewrite
Firewall evasion
...
Resource management
Policy enforcement
Problem diagnosis
Complex join procedure
Inaccurate results
High overheads
Notes: Yet, challenging:
  Accuracy: Hard to infer trajectories in data plane
  Efficiency: bandwidth, packet bits, rules
  Composition: measurements with forwarding

## Slide 9: Solution Approach
Declarative Query Specification
  Forwarding independence
  Co-Measurement independence
  Hardware independence
Query-Driven Measurement
  Accurate answers
  Pay exactly for what you query
  Commodity hardware
Path Query Language
Query
Run-Time
System

## Slide 10: Solution Approach
1. Path Query Language
2. Query Run-Time System
SDN controller
Payloads
Statistics
3. Optimizations
Query Expressions
Statistics
Forwarding

## Slide 11: Solution Approach
2. Query Run-Time System
3. Optimizations
Expressive measurement
Accurate measurements
on commodity hardware
Efficient measurement
1. Path Query Language

## Slide 12: Example: Where’s the Packet Loss?
A
B
Instead: get A  B packet counts each step along paths where A  B traffic flows
100 pkts
25 pkts 
50
100
50
25
25
25
25
50
0
(srcip=a & dstip=b) ^
repeat(groupby(true, [switch]), MAX_HOPS)

## Slide 13
I. Path Query Language

## Slide 14: Goal: Declarative Measurement Spec
Packet loss localization
Uneven load balancing
Traffic matrix
Slice isolation
DDoS source identification
Port-level traffic matrix
Congested link diagnosis
Loop detection
Middlebox traversal order
Incorrect NAT rewrite
Firewall evasion
...
Q: Common Primitives?

## Slide 15: Common Goals?
  Relate a packet across interfaces it flows through
Specify multiple related trajectories
Extract different outputs: packets, counters, ...
Specify where to collect measurement
How to design general primitives
that are efficiently implemented
in the network?

## Slide 16: Common Goals?
  Relate a packet across interfaces it flows through
  ... in the data plane
Static analysis of policy
isn’t enough

## Slide 17: Key Primitive: Packet Path
Packet paths:
  Tests on packets at a single location in network
  Same packet must satisfy multiple tests
   Regular expressions!
General
Inefficient
Narrow
Efficient
Single location packet test
Packet paths over regular expressions
Tests on sets of packets

## Slide 18: Key Primitive: Packet Path
Packet paths:
  Tests on packets at a single location in network
  Same packet must satisfy multiple tests
   Regular expressions!
Multiple related trajectories:
  SQL-like constructs for aggregation
Specify measurements precisely:
  Upstream and downstream capture
  Capture packets, counters, packet samples

## Slide 19: Expressing Packet Paths
Regular expressions:
  natural to state paths on graphs
S1
S2
S3
S4
S5
S6
S1 ^ .* ^ S4

## Slide 20: Expressing Packet Paths
Regular expressions:
  natural to state paths on graphs
S1
S2
S3
S4
S5
S6
S1 ^ .* ^ S4
Boolean packet predicate
pred ::= true | false
| header=value
| location=value
| pred & pred
| pred | pred
| ~pred
| ingress()
| egress()

## Slide 21: Expressing Packet Paths
Regular expressions:
  natural to state paths on graphs
S1
Input packet
Output packet
Forwarding
atom ::= in_atom(pred)
| out_atom(pred)
| in_out_atom(pred,
pred)

## Slide 22: Expressing Packet Paths
Regular expressions:
  natural to state paths on graphs
S1
S2
S3
S4
S5
S6
in_atom(sw=S1) ^ in_atom(true)* ^ in_atom(sw=S4)
S1 ^ .* ^ S4

## Slide 23: Query Language
path ::= atom
      | path ^ path
      | path | path
      | path*
      | path & path
      | ~path
p1
p2
“hop”

## Slide 24: An Example
0 or more
repetitions
Capture packets evading a firewall in the network
    ingress()
    ^
    (~switch=FW)*
    ^
    egress()
ingress
egress
ingress
ingress
egress
egress

## Slide 25: An Example
ingress
egress
ingress
ingress
egress
egress
Capture packets evading a firewall in the network
    ingress()
    ^
    (~switch=FW)*
    ^
    egress()

## Slide 26: Query Language: Aggregation
Switch-level traffic matrix:
 | E1 | E2 | ...
I1 | 250 | 100 | ...
I2 | 120 | 95 | ...
... | ... | ... | ...

## Slide 27: Query Language: Aggregation
Switch-level traffic matrix:
  in_atom(ingress())
  ^
  in_atom(true)*
  ^
  out_atom(egress())
Count all packets, going from any ingress to any egress.
Flow | #pkts
* | 1000

## Slide 28: Query Language: Aggregation
Switch-level traffic matrix:
  in_group(ingress(),
  [switch])
  ^
  in_atom(true)*
  ^
  out_group(egress(),
  [switch])
Group counts by
packet’s ingress and egress switch!
 Traffic matrix!
Flow | #pkts
sw=I1, sw=E1 | 250
sw=I1, sw=E2 | 100
... | ...

## Slide 29: Query Language
path ::= atom
      | path ^ path
      | path | path
      | path*
      | path & path
      | ~path
atom ::=
| in_atom(pred)
| out_atom(pred)
| in_out_atom(pred,
pred)
| in_group( pred,
[fields])
| out_group(pred,
[fields])
| in_out_group(pred,
[fields], pred,
[fields])

## Slide 30: Where to capture matching packets?
Upstream
Downstream
Queried Path
Packet flow
{path}.up()
{path}.down()
For a given query: packets may be different!

## Slide 31: How to process matching packets?
{path}.set_bucket(bucket)
count_bucket()
(Get switch counters)
packet_bucket()
(Send to controller)
sampling_bucket()
(Get sFlow packet samples)

## Slide 32: More Query Examples
Compiling path queries, to appear in NSDI 2016

## Slide 33: More Query Examples
Compiling path queries, to appear in NSDI 2016

## Slide 34: Path Query Language: Summary
Predicates: single point tests
Paths: regular expressions on predicates
Aggregation: groupby construct
Location: downstream and upstream measurement
Result format: packets, counts, samples

## Slide 35
II. The Run-Time System

## Slide 36: Solution Approach
Query expressions
Statistics
2. Query Run-Time System
SDN controller
Payloads
Statistics
3. Optimizations
1. Path Query Language

## Slide 37: Goal: Query  Network Measurement
Accurate answer
Pay exactly for what you query
Commodity hardware

## Slide 38: Commodity HW: Match-Action Tables
38
match1  action1
match2  action2
...
Wildcard bit pattern
(ternary matching)
Forward/Drop/Modify

## Slide 39: Commodity HW: Multi-Stage Match-Act
match1  action1
match2  action2
...
match1  action1
match2  action2
...
...

## Slide 40: Goal: Query  Network Measurement
Accurate answer
Pay exactly for what you query
Commodity hardware
Consider downstream measurement...

## Slide 41: Goal: Query  Network Measurement
Accurate answer
Pay for what you query
Commodity hardware
How to observe a packet’s
path accurately in the data plane
with low overhead?

## Slide 42: Approach 1: Join Traffic & Forwarding
Traffic dataset
e.g., NetFlow, SNMP
Forwarding updates
e.g., OF/routing protocol updates
X
Dynamic
Timestamps not aligned!
Packets may be dropped downstream
Deriving traffic demands for operational IP networks. Feldmann et al., 2001
Sampled NetFlow

## Slide 43: Approach 1: Join Traffic & Forwarding
Traffic dataset
e.g., NetFlow, SNMP
Forwarding updates
e.g., OF/routing protocol updates
X
Dynamic
Timestamps not aligned!
??
Ambiguity between identical packets downstream
Packet traceback for software-defined networks. Zhang et al., 2015

## Slide 44: Approach 1: Join Traffic & Forwarding
Traffic dataset
e.g., NetFlow, SNMP
Forwarding updates
e.g., OF/routing protocol updates
X
Dynamic
Timestamps not aligned!
??
Ambiguity between identical packets downstream
Trajectory sampling for direct traffic observation. Duffield et al., 2001
Packet rewriting compounds the ambiguity!

## Slide 45: Approach 2: Collect at Every Hop
Using packet histories to troubleshoot networks. Handigol et al., 2014
Hash-based IP traceback. Snoeren et al., 2001
Packet-level telemetry in large data-center networks. Zhu et al., 2015

## Slide 46: Approach 2: Collect at Every Hop
Too expensive to collect up front!
Using packet histories to troubleshoot networks. Handigol et al., 2014
Hash-based IP traceback. Snoeren et al., 2001
Packet-level telemetry in large data-center networks. Zhu et al., 2015

## Slide 47: Approach 2: Collect at Every Hop
Too expensive to collect up front!
Sampling to reduce overhead may miss the packets you care about…
Trajectory sampling for direct traffic observation. Duffield et al., 2001

## Slide 48: Approach 3: Write Path into Packet
sw: S1,
srcip: ___,
dstip: ___,
...
sw: S2,
srcip: ___,
dstip: ___;
sw: S1, ...;
sw: S3, ...;
sw: S2, ...;
sw: S1, ...;
Too much info on packet! :-(
Switches have very accurate info on prior packet path 
IP record route, RFC 791. Postel, 1981
Tracing packet trajectory in data-center networks. Tammana et al., 2015
Match-action HW can’t match regexes :-(

## Slide 49: Approach 3: Write Path into Packet
sw: S1,
srcip: ___,
dstip: ___,
...
sw: S2,
srcip: ___,
dstip: ___;
sw: S1, ...;
sw: S3, ...;
sw: S2, ...;
sw: S1, ...;
As such, too much info on packet! 
Switches have very accurate info on prior packet path 
[8] IP record route
[9] Tracing packet trajectory in data-center networks. Tammana et al., 2015
How to reduce the amount of path information on packets?

## Slide 50: Reducing Path Info on Packets
Observation 1: Queries already tell us what’s needed!
  Only record path info needed by queries
Observation 2: Queries are regular expressions
  Processing: Finite automaton (DFA)
  Distinguish only DFA states on the network!

## Slide 51: Reducing Path Info on Packets
Observation 1: Queries already tell us what’s needed!
  Only record path state needed by queries
Observation 2: Queries are regular expressions
  Regular expressions  Finite automaton (DFA)
  Distinguish only paths corresponding to DFA states
Record only DFA state on packets (1-2 bytes)
Use existing “tag” fields (e.g., VLAN)

## Slide 52: Downstream Query Compilation
Queries
Forwarding
Data Plane Rules
Downstream Query Compiler
Regex Matching on Packet Trajectories!

## Slide 53: Downstream Query Compilation
Queries
Forwarding
Data Plane Rules
(1) Get Query DFA
(2) Get Transitioning & Accepting Policies
(3) Compose into Unified Policy

## Slide 54: Downstream Query Compilation (1/3)
  p = (switch=S1 & srcip=10.0.0.1)
  ^ (switch=S2 & dstip=10.0.0.3)
  p.set_bucket(count_bucket())
Q0
Q1
Q2
switch=S1 & srcip=10.0.0.1
switch=S2 & dstip=10.0.0.3
S1
S2
Notes: Not only do we know, but also modify packet processing on switches to make measurements easier.  need to make this point somewhere.
Note that there are details to make the execution of the automaton deterministic on the data plane – which we are skipping in the interest of time.
Also, the queries are assumed to be matching a packet only once on each switch: typically there are 2 matching points, but let’s assume only ingress queries exist for the time being.

## Slide 55: Downstream Query Compilation (2/3)
Q0
Q1
Q2
switch=S1 & srcip=10.0.0.1
switch=S2 & dstip=10.0.0.3
DFA
Transition
DFA Accept
state=Q0 & switch=S1 & srcip=10.0.0.1  stateQ1
state=Q1 & switch=S2 & dstip=10.0.0.3  stateQ2
state=Q1 & switch=S2 & dstip=10.0.0.3  count
Generate “match-action-able” rules
Notes: Not only do we know, but also modify packet processing on switches to make measurements easier.  need to make this point somewhere.

## Slide 56: Downstream Query Compilation (3/3)
All acting on the same data plane packets!
Use policy composition operators and compiler
DFA-Transitioning
Forwarding
DFA-Accepting
>>
+
)
(
Composing software-defined networks. Monsanto et al., 2013
Notes: Why does this composed policy make sense? Explain.

## Slide 57: Downstream Query Compilation (3/3)
DFA-Transitioning
Forwarding
DFA-Accepting
>>
+
)
(
state=Q0 & switch=S1 & srcip=10.0.0.1  stateQ1
state=Q1 & switch=S2 & dstip=10.0.0.3  stateQ2
dstip=10.0.0.1  fwd(1)
dstip=10.0.0.2  fwd(2)
dstip=10.0.0.3  fwd(3)
...
>>
state=Q0 & switch=S1 & srcip=10.0.0.1 & dstip=10.0.0.2
 stateQ1, fwd(2)
Composing software-defined networks. Monsanto et al., 2013
Notes: Why does this composed policy make sense? Explain.

## Slide 58: Downstream Query Compilation (3/3)
(DFA-Ingress-Transitioning >> Forwarding >> DFA-Egress-Transitioning) +
(DFA-Ingress-Accepting)
+
(DFA-Ingress-Transitioning >> Forwarding >> DFA-Egress-Accepting)

## Slide 59: Compiling the Full Language
DFA construction with overlapping predicates
Upstream queries
Groupby atoms
Generate an ‘orthogonal basis’ for predicates
Formulate reachability test with Filter output
Traverse AST proactively, rewriting to “basic” atoms

## Slide 60: Query Run-Time System: Summary
Translation of Queries to Network Measurements
Accurate measurement
  Packets carry trajectories
  Efficient encoding through DFA states
Pay exactly for what you query
  Only collect packets matching queries
Use commodity hardware
  Path regex matching on match-action tables!

## Slide 61
III. Optimizations

## Slide 62: Solution Approach
Query expressions
Statistics
2. Query Run-Time System
SDN controller
Payloads
Statistics
3. Optimizations
1. Path Query Language

## Slide 63: Goal: Make Run-Time Efficient
Metrics:
  Rule space
  Query compile time
  Packet state space
Stanford network on a mix of queries (~550 statistics)
  Unoptimized: didn’t compile in 2 hours
Fully optimized:
    Query compile time: ~ 5 seconds
  Rule space: ~ 650 rules (TCAM capacity 2-4K)
  Packet state space: state fits in VLAN header
Fit in switch rule memory?
Debugging “interactive”?
Fit on typical “tag” headers?

## Slide 64: Optimizations: Summary
Optimization | # Rules? | Time? | # States?
Separate query & forwarding actions into separate stages |  |  | 
Optimize conditional policy compilation |  |  | 
Integrate tagging and capture policies |  |  | 
Pre-partition predicates by flow space |  |  | 
Cache predicate overlap decisions |  |  | 
Decompose query predicates into multiple stages |  |  | 
Detect predicate overlaps with Forwarding Decision Diagrams |  |  | 
Notes: // table of optimizations + intended metrics that should be reduced

## Slide 65: Optimizations: Summary
Optimization | # Rules? | Time? | # States?
Separate query & forwarding actions into separate stages |  |  | 
Optimize conditional policy compilation |  |  | 
Integrate tagging and capture policies |  |  | 
Pre-partition predicates by flow space |  |  | 
Cache predicate overlap decisions |  |  | 
Decompose query predicates into multiple stages |  |  | 
Detect predicate overlaps with FDDs |  |  | 
Cross-Product Explosion
Notes: // table of optimizations + intended metrics that should be reduced

## Slide 66: Cross-Product Explosion (1/2)
DFA-Transitioning
Forwarding
DFA-Accepting
>>
+
)
(
state=Q0 & srcip=10.0.0.2  stateQ1
state=Q1 & srcip=10.0.0.3  stateQ2
state=Q2 & port=4  stateQ4
state=Q3 & srcmac=01:*  stateQ5
state=Q4 & srcip=10.0.0.1  stateQ3
state=Q5 & tpdstport=80  stateQ5
state=Q6 & srcip=10.0.0.3  stateQ6
state=Q7 & dstip=10.0.0.4  stateQ2
...
>>
dstip=10.0.0.1  fwd(1)
dstip=10.0.0.2  fwd(2)
dstip=10.0.0.3  fwd(3)
dstip=10.0.0.4  fwd(4)
dstip=10.0.0.5  fwd(5)
dstip=10.0.0.6  fwd(6)
dstip=10.0.0.7  fwd(7)
dstip=10.0.0.8  fwd(8)
...
state=Q0 & srcip=10.0.0.2 & dstip=10.0.0.1
 stateQ1, fwd(1)

## Slide 67: Cross-Product Explosion (2/2)
Packets can satisfy both p1 and p101
  Also p1 and p102; p1 and p103; ...
Query DFA edges (and rules) for each combination!
p1: srcip=10.0.0.1
p2: srcip=10.0.0.2
...
p100: srcip=10.0.0.100
p101: dstip=192.168.0.101
p102: dstip=192.168.0.102
...
p200: dstip=192.168.0.200

## Slide 68: Taming Cross-Product Explosion
Key Problem: Coerce multiple actions on overlapping sets of packets

## Slide 69: Taming Cross-Product Explosion
Key Problem: Coerce multiple actions on overlapping sets of packets
match1  action1
match2  action2
...
Idea: Can we leverage multiple passes on each packet in hardware?
Multi-stage match-action tables can already do this!

## Slide 70: Taming Cross-Product Explosion
Key Idea: Leverage multiple passes for each packet
  Overlapping actions on different tables!
match1  action1
match2  action2
...
match1  action1
match2  action2
...
...
Rule space O(M+N), not O(M*N)

## Slide 71: Taming Huge Policies
(DFA-Ingress-Transitioning >> Forwarding >> DFA-Egress-Transitioning) +
(DFA-Ingress-Accepting)
+
(DFA-Ingress-Transitioning >> Forwarding >> DFA-Egress-Accepting)

(DFA-Ingress-Transitioning + DFA-Ingress-Accepting)
>>
Forwarding
>>
(DFA-Egress-Transitioning + DFA-Egress-Accepting)

## Slide 72: Taming Huge Policies
in_transition
+
in_accept
forwarding
out_transition
+
out_accept
(DFA-Ingress-Transitioning + DFA-Ingress-Accepting) >> Forwarding
>> (DFA-Egress-Transitioning + DFA-Egress-Accepting)
O(M*N)  O(M+N)

## Slide 73: Taming Overlapping Query Predicates
p1: srcip=10.0.0.1
p2: srcip=10.0.0.2
...
p100: srcip=10.0.0.100
p101: dstip=192.168.0.101
p102: dstip=192.168.0.102
...
p200: dstip=192.168.0.200
in_transition
+
in_accept
srcip=10.0.0.1  state1q1
srcip=10.0.0.2  state1q2
...
dstip=192.168.0.101  state2q1
dstip=192.168.0.102  state2q2
...
...
Running many parallel Query DFAs!
O(M*N)  O(M+N)

## Slide 74: Taming Overlapping Query Predicates
Approach: “pack” queries into tables to minimize cost while respecting per-stage rule capacities and #stages
Total # stages
# Rules in stage j

## Slide 75: Taming Overlapping Query Predicates
Cost function: upper bound on actual # rules
Move “dissimilar” predicates into different table stages
Concurrent NetCore: From policies to pipelines. Schlesinger et al., 2014
Compiling packet programs to reconfigurable swithces. Jose et al., 2015

## Slide 76: Implementation
Prototype
  Pyretic SDN controller
  NetKAT (Ocaml) compiler
  Install rules on OpenVSwitch
Currently single-threaded
  Intel Xeon E3, 3.70Ghz 32GB
Implementation publicly available online
  http://frenetic-lang.org/pyretic/
Composing software-defined networks. Monsanto et al., 2013
A fast compiler for NetKAT. Smolka et al., 2015
OpenVSwitch.org

## Slide 77: Benefit of Optimizations
Stanford campus network topology
Several queries:
  Traffic matrix, DDoS detection, per-hop packet loss, firewall evasion, slice isolation, congested link
Metrics and Stanford results (all queries together):
  Compile time: > 2 hours  5 seconds
  # Rules: ~ 650
  # State bytes: 2 bytes
Notes: Rule space estimation for DNF cases.
Stanford forwarding policy has 3840 rules overall – that’s 240 per device on average. Almost all rules match on destination ip address, which almost none of the queries actually match on. This means the best-case reduction applies: ~240 times or two orders of magnitude reduction of rule count going from single-stage to multi-stage tables.
Then there’s at least a factor of 6.6 from the instances that _do_ terminate. Together, that’s 7 * 240 = 1680, or three orders of magnitude reduction in rule space from the unoptimized case.

## Slide 78: Benefit of Optimizations (Stanford)
Cumulative Optimization | Time (s) | # Rules | # State Bits
None | > 7900 | DNF | DNF
Separate query & forwarding actions into separate stages | > 4920 | DNF | DNF
Optimize conditional policy compilation | > 4080 | DNF | DNF
Integrate tagging and capture policies | 2991 | 2596 | 10
Pre-partition predicates by flow space | 56.19 | 1846 | 10
Cache predicate overlap decisions | 35.13 | 1846 | 10
Decompose query predicates into multiple stages | 5.467 | 260 | 16
Notes: Rule space estimation for DNF cases.
Stanford forwarding policy has 3840 rules overall – that’s 240 per device on aveage. Almost all rules match on destination ip address, which almost none of the queries actually match on. This means the best-case reduction applies: ~240 times or two orders of magnitude reduction of rule count going from single-stage to multi-stage tables.
Then there’s at least a factor of 6.6 from the instances that _do_ terminate. Together, that’s 7 * 240 = 1680, or three orders of magnitude reduction in rule space from the unoptimized case.

## Slide 79: Scalability Trends
Five synthetic ISP (Waxman) topologies at various network sizes
At each network size, run mix of queries from before
  Averaged metrics across queries & topologies

## Slide 80: I. Query Compile Time
Response time in man-computer conversational transactions. Miller, 1968
Interactive problem solving (15s)

## Slide 81: II. Rule Count
Switch TCAM capacity: 2K-4K rules

## Slide 82: III. Packet State Bits
VLAN
MPLS

## Slide 83: Summary
Declarative path query language
  Regular expressions, grouping
  Capture locations, capture actions
Compositional run-time system
  Query-DFA packet state
Key optimizations for a practical system
  Addressing cross-product explosion
Paper and more info at http://www.cs.princeton.edu/~narayana/pathqueries

## Slide 84
Queries? 