## Slide 1: Programming the Networks of the Future
Jennifer Rexford
Princeton University

## Slide 2: The Internet: A Remarkable Story
Tremendous success
  From research experiment to global infrastructure
Brilliance of under-specifying
  Network: best-effort packet delivery
  Hosts: arbitrary applications
Enables innovation
  Apps: Web, P2P, VoIP, social networks, …
  Links: Ethernet, fiber optics, WiFi, cellular, …

## Slide 3: Inside the ‘Net: A Different Story…
Closed equipment
  Software bundled with hardware
  Vendor-specific interfaces
Over specified
  Slow protocol standardization
Few people can innovate
  Equipment vendors write the code
  Long delays to introduce new features

## Slide 4: Do We Need Innovation Inside?
Many boxes (routers, switches, firewalls, …), with different interfaces.
Notes: Enterprise network.

## Slide 5: Software Defined Networks
control plane: distributed algorithms
data plane: packet processing

## Slide 6: Software Defined Networks
decouple control and data planes

## Slide 7: Software Defined Networks
decouple control and data planes by providing open standard API

## Slide 8: Simple, Open Data-Plane API
Prioritized list of rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
srcip=1.2.*.*, dstip=3.4.5.*  drop
srcip = *.*.*.*, dstip=3.4.*.*  forward(2)
3. srcip=10.1.2.3, dstip=*.*.*.*  send to controller

## Slide 9: (Logically) Centralized Controller
Controller Platform

## Slide 10: Protocols  Applications
Controller Platform
Controller Application

## Slide 11: Seamless Mobility
See host sending traffic at new location
Modify rules to reroute the traffic

## Slide 12: Server Load Balancing
Pre-install load-balancing policy
Split traffic based on source IP
src=0*,
dst=1.2.3.4
src=1*,
dst=1.2.3.4
10.0.0.1
10.0.0.2

## Slide 13: Example SDN Applications
Seamless mobility and migration
Server load balancing
Dynamic access control
Using multiple wireless access points
Energy-efficient networking
Blocking denial-of-service attacks
Adaptive traffic monitoring
Network virtualization
Steering traffic through middleboxes
<Your app here!>

## Slide 14: A Major Trend in Networking
Entire backbone
runs on SDN
Bought for $1.2 x 109
(mostly cash)

## Slide 15: Programming SDNs
http://frenetic-lang.org
Joint work with the research groups of Nate Foster (Cornell), Arjun Guha (UMass-Amherst), and David Walker (Princeton)

## Slide 16: Programming SDNs
Images by Billy Perkins
The Good
  Network-wide visibility
  Direct control over the switches
  Simple data-plane abstraction
The Bad
  Low-level programming interface
  Functionality tied to hardware
  Explicit resource control
The Ugly
  Non-modular, non-compositional
  Programmer faced with challenging distributed programming problem

## Slide 17: Network Control Loop
Read
state
OpenFlow
Switches
Write
policy
Compute Policy

## Slide 18: Language-Based Abstractions
SQL-like query language
OpenFlow
Switches
Consistent updates
Module Composition

## Slide 19: Computing (and Composing) Policy
Composition Operators
Topology Abstraction

## Slide 20: Combining Many Networking Tasks
Controller Platform
Monitor + Route + FW + LB
Monolithic application
Hard to program, test, debug, reuse, port, …
Notes: But, real networks perform a wide variety of tasks
Routing, network monitoring, firewalls, server load balancing, etc.

## Slide 21: Modular Controller Applications
Controller Platform
LB
Route
Monitor
FW
Easier to program, test, and debug
Greater reusability and portability
A module for each task

## Slide 22: Beyond Multi-Tenancy
Controller Platform
Slice 1
Slice 2
Slice n
...
Each module controls a different portion of the traffic
Relatively easy to partition rule space, link bandwidth, and network events across modules
Notes: Simple case: multi-tenancy
Each module controls a different subset of the traffic
Relatively easy to partition traffic, rule space, and bandwidth resources
We want to write a single application out of modules that affect the handling of same traffic

## Slide 23: Modules Affect the Same Traffic
Controller Platform
LB
Route
Monitor
FW
How to combine modules into a complete application?
Each module partially specifies the handling of the traffic

## Slide 24: Policy as a Function
Input: a located packet
  Packet header fields (e.g., src and dst IP)
  Packet’s location (e.g., switch and port)
Output: a set of located packets
  Empty set: drop (or count)
  Single element at new location: forwarding
  Multiple elements: multicast
See recent work on NetKAT
  Boolean algebra and regular expressions

## Slide 25: Parallel Composition
Controller Platform
Route on destination
Monitor on source
+
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
srcip = 5.6.7.8  count
srcip = 5.6.7.8, dstip = 1.2.3.4  fwd(1), count
srcip = 5.6.7.8, dstip = 3.4.5.6  fwd(2), count
srcip = 5.6.7.8  count
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
Notes: From ICFP’11 and POPL’12

## Slide 26: Sequential Composition
Controller Platform
Routing
Load Balancer
>>
dstip = 10.0.0.1  fwd(1)
dstip = 10.0.0.2  fwd(2)
srcip = 0*, dstip=1.2.3.4  dstip=10.0.0.1
srcip = 1*, dstip=1.2.3.4  dstip=10.0.0.2
srcip = 0*, dstip = 1.2.3.4  dstip = 10.0.0.1, fwd(1)
srcip = 1*, dstip = 1.2.3.4  dstip = 10.0.0.2, fwd(2)
Notes: Load balancer splits traffic sent to public IP address over multiple replicas, based on client IP address, and rewrites the IP address

## Slide 27: Dividing the Traffic Over Modules
Predicates
  Specify which traffic traverses which modules
  Based on input port and packet-header fields
Routing
Load Balancer
Monitor
Routing
Non-web
dstport != 80
Web traffic
dstport = 80
>>
+

## Slide 28: Abstract Topology: Load Balancer
Present an abstract topology
  Information hiding: limit what a module sees
  Protection: limit what a module does
  Abstraction: present a familiar interface
28
Real network
Abstract view

## Slide 29: Abstract Topology: Gateway
Left: learning switch on MAC addresses
Middle: ARP on gateway, plus simple repeater
Right: shortest-path forwarding on IP prefixes
IP Core
Ethernet
IP Core
Gateway
Ethernet

## Slide 30: High-Level Architecture
Controller Platform
M1
M2
M3
Main
Program

## Slide 31: Reading State
SQL-Like Query Language

## Slide 32: From Rules to Predicates
Traffic counters
  Each rule counts bytes and packets
  Controller can poll the counters
Multiple rules
  E.g., Web server traffic except for source 1.2.3.4
Solution: predicates
  E.g., (srcip != 1.2.3.4) && (srcport == 80)
  Run-time system translates into switch patterns
1. srcip = 1.2.3.4, srcport = 80
2. srcport = 80

## Slide 33: Dynamic Unfolding of Rules
Limited number of rules
  Switches have limited space for rules
  Cannot install all possible patterns
Must add new rules as traffic arrives
  E.g., histogram of traffic by IP address
  … packet arrives from source 5.6.7.8
Solution: dynamic unfolding
  Programmer specifies GroupBy(srcip)
  Run-time system dynamically adds rules
1. srcip = 1.2.3.4
1. srcip = 1.2.3.4
2. srcip = 5.6.7.8

## Slide 34: Suppressing Unwanted Events
Common programming idiom
  First packet goes to the controller
  Controller application installs rules
packets

## Slide 35: Suppressing Unwanted Events
More packets arrive before rules installed?
  Multiple packets reach the controller
packets

## Slide 36: Suppressing Unwanted Events
Solution: suppress extra events
  Programmer specifies “Limit(1)”
  Run-time system hides the extra events
packets
not seen by
application

## Slide 37: SQL-Like Query Language
Get what you ask for
  Nothing more, nothing less
SQL-like query language
  Familiar abstraction
  Returns a stream
  Intuitive cost model
Minimize controller overhead
  Filter using high-level patterns
  Limit the # of values returned
  Aggregate by #/size of packets
Select(bytes) *
Where(in:2 & srcport:80) *
GroupBy([dstmac]) *
Every(60)
Select(packets) *
GroupBy([srcmac]) *
SplitWhen([inport]) *
Limit(1)
Learning Host Location
Traffic Monitoring

## Slide 38: Path Queries
Many questions span multiple switches
  Troubleshooting performance problems
  Diagnosing a denial-of-service attack
  Collecting the “traffic matrix”
Path queries as regular expressions
  E.g., all packets that go from switch 1 to 2
    (sw=1) ^ (sw=2)
  E.g., all packets that avoid firewall FW
    (sw=1) ^ (sw != FW)* ^ (sw=2)

## Slide 39: Writing State
Consistent Updates

## Slide 40: Avoiding Transient Disruption
Invariants
No forwarding loops
No black holes
Access control
Traffic waypointing

## Slide 41: Installing a Path for a New Flow
Rules along a path installed out of order?
  Packets reach a switch before the rules do
Must think about all possible packet and event orderings.
packets

## Slide 42: Update Consistency Semantics
Per-packet consistency
  Every packet is processed by
  … policy P1 or policy P2
  E.g., access control, no loops or blackholes
Per-flow consistency
  Sets of related packets are processed by
  … policy P1 or policy P2,
  E.g., server load balancer, in-order delivery
P1
P2

## Slide 43: Policy Update Abstraction
Simple abstraction
  Update entire configuration at once
Cheap verification
  If P1 and P2 satisfy an invariant
  Then the invariant always holds
Run-time system handles the rest
  Constructing schedule of low-level updates
  Using only OpenFlow commands!
P1
P2

## Slide 44: Two-Phase Update Algorithm
Version numbers
  Stamp packet with a version number (e.g., VLAN tag)
Unobservable updates
  Add rules for P2 in the interior
  … matching on version # P2
One-touch updates
  Add rules to stamp packets with version # P2 at the edge
Remove old rules
  Wait for some time, then remove all version # P1 rules

## Slide 45: Update Optimizations
Avoid two-phase update
  Naïve version touches every switch
  Doubles rule space requirements
Limit scope
  Portion of the traffic
  Portion of the topology
Simple policy changes
  Strictly adds paths
  Strictly removes paths

## Slide 46: Consistent Update Abstractions
Many different invariants
  Beyond packet properties
  E.g., avoiding congestion during an update
Many different algorithms
  General solutions
  Specialized to the invariants
  Specialized to a setting (e.g., optical nets)

## Slide 47: Frenetic Abstractions
SQL-like queries
OpenFlow
Switches
Consistent
Updates
Policy Composition

## Slide 48: Related Work
Programming languages
  FRP: Yampa, FrTime, Flask, Nettle
  Streaming: StreamIt, CQL, Esterel, Brooklet, GigaScope
  Network protocols: NDLog
OpenFlow
  Language: FML, SNAC, Resonance
  Controllers: ONIX, POX, Floodlight, Nettle, FlowVisor
  Testing: Mininet, NICE, FlowChecker, OF-Rewind, OFLOPS
Standardizing the switch API
  http://www.openflow.org/
  https://www.opennetworking.org/
  http://p4.org

## Slide 49: Conclusion
SDN is exciting
  Enables innovation
  Simplifies management
  Rethinks networking
SDN is happening
  Practice: APIs and industry traction, cool apps
  Principles: higher-level abstractions
Great opportunity
  Practical impact on future networks
  Placing networking on a strong foundation