## Slide 1: Toward Self-Driving Networks
Jennifer Rexford

## Slide 2: Self-Driving Network
Complete control loop
  Measure
  Analyze
  Control
Examples
  Direct traffic over the best performing path
  Block or slow the heavy-hitter flows
Possible now in the data plane!
measure
analyze
control

## Slide 3: A Constrained Computational Model
Packet
parser
Match | Action
m1 | a1
Registers
Match-action tables
Match | Action
m1 | a1
Registers
Match-action tables
. . .
metadata
Small amount of memory
Pipelined computation
Limited computation

## Slide 4: Hop-by-Hop Utilization-aware Load-balancing Architecture
Naga Katta, Mukesh Hira, Changhoon Kim, Anirudh Sivaraman, and Jennifer Rexford
http://conferences.sigcomm.org/sosr/2016/papers/sosr_paper67.pdf
HULA

## Slide 5: HULA Multipath Load Balancing
Load balancing entirely in the data plane
  Collect real-time, path-level performance statistics
  Group packets into “flowlets” based on time & headers
  Direct each new flowlet over the current best path
S1
S2
S3
S4
ToR 10
ToR 1
Data

## Slide 6: Path Performance Statistics
Using the best-hop table
  Update the best next-hop upon new probes
  Assign a new flowlet to the best next-hop
S1
S3
S4
Best-hop table
Best Next-Hop | Path Utilization
S3 | 50%
S4 | 10%
… | …
0
1
…
Dest ToR
Data
Data
Probe
Probe

## Slide 7: Flowlet Routing
Flowlet table
S1
S3
S4
Using the flowlet table
  Update the next hop if enough time has elapsed
  Update the timestamp to the current time
Forward the packet to the chosen next hop
Dest ToR | Timestamp | Next-Hop
ToR 10 | 1 | S2
ToR 0 | 17 | S4
… | … | …
0
1
…
h(flowid)
Data
Data

## Slide 8: Putting it all Together
data packet
current best next-hop S3
chosen next-hop
Update next-hop (if enough time elapsed) and time
Dest ToR | Timestamp | Next-Hop
ToR 10 | 1 | S2
ToR 0 | 17 | S4
… | … | …
Best Next-Hop | Path Utilization
S3 | 50%
S4 | 10%
… | …
0
1
…
Dest ToR
0
1
…
h(flowid)

## Slide 9: Heavy Hitter Detection Entirely in the Data Plane
Vibhaalakshmi Sivaraman, Srinivas Narayana, Ori Rottenstreich, S. Muthukrishnan, and Jennifer Rexford
https://conferences.sigcomm.org/sosr/2017/papers/sosr17-heavy-hitter.pdf
HashPipe

## Slide 10: Heavy-Hitter Detection
Heavy hitters
  The k largest trafic flows
  Flows exceeding threshold T
Space-saving algorithm
  Table of (key, value) pairs
  Evict the key with the minimum value
Id | Count
K1 | 4
K2 | 2
K3 | 7
K4 | 10
K5 | 1
K6 | 5
New Key K7
Table scan

## Slide 11: Approximating the Approximation
Evict minimum of d entries
  Rather than minimum of all entries
  E.g., with d = 2 hash functions
Id | Count
K1 | 4
K2 | 2
K3 | 7
K4 | 10
K5 | 1
K6 | 5
New Key K7
Multiple memory accesses

## Slide 12: Approximating the Approximation
Divide the table over d stages
  One memory access per stage
  Two different hash functions
Id | Count
K1 | 4
K2 | 2
K3 | 7
New Key K7
Id | Count
K4 | 10
K5 | 1
K6 | 5
Going back to the first table

## Slide 13: Approximating the Approximation
Rolling min across stages
  Avoid recirculating the packet
  … by carrying the minimum along the pipeline
Id | Count
K1 | 4
K2 | 10
K3 | 7
New Key K7
Id | Count
K4 | 2
K5 | 1
K6 | 5
Id | Count
K1 | 4
K7 | 1
K3 | 7
Id | Count
K2 | 10
K5 | 1
K6 | 5
(K2, 10)

## Slide 14: P4 Prototype and Evaluation
Id | Count
K1 | 4
K2 | 10
K3 | 7
Id | Count
K4 | 2
K5 | 1
K6 | 5
New Key K7
(K2, 10)
Hash on packet header
Packet metadata
Conditional updates to compute minimum
Register arrays
High accuracy with overhead
proportional to # of heavy hitters

## Slide 15: Conclusion
Self-driving networks
  Integrate measure, analyze, and control
  Distribute across the network devices
Enabled by programmable switches
  Parsing, processing, and state
Approximate data structures
  Limited memory for storing state
  Limited processing per packet