## Slide 1: Toward Self-Driving Networks
Jennifer Rexford

## Slide 2: Self-Driving Network
Complete control loop
Examples
  Slow flows causing microbursts
  Block or slow heavy-hitter flows
  Direct traffic over the best paths
Now possible in the data plane!
measure
analyze
control

## Slide 3: Protocol-Independent Switch Architecture (PISA)
Packet
parser
Match | Action
m1 | a1
registers
Match-action
tables
Match | Action
m1 | a1
registers
Match-action tables
. . .
metadata
headers

## Slide 4: But, a Constrained Computational Model
Packet
parser
Match | Action
m1 | a1
registers
Match-action
tables
Match | Action
m1 | a1
registers
Match-action tables
. . .
metadata
Small amount of memory
Pipelined computation
Limited computation
headers
Limited # of bits

## Slide 5: Design compact data structures and streaming algorithms

## Slide 6: Catching the Microburst Culprits With Snappy
Xiaoqi Chen, Shir Landau Feibish, Yaron Koral, Jennifer Rexford, and Ori Rottenstreich
http://www.cs.princeton.edu/~jrex/papers/snappy18.pdf

## Slide 7: Microbursts are Expensive
Microbursts cause performance degradation
  Packet loss
  Packet delay
But, simultaneously handle
  Bursty workloads
  Low-cost switches (with shallow buffers)
  High link utilization
Must micromanage the microbursts!

## Slide 8: Detecting Heavy Flows in the Queue
For each flow, how many packets are in the queue?
Data structure challenges
  Per-flow state (key and count)
  Updating on packet arrival and departure
Key | Count
 | 1
 | 5
 | 1
 | 1
 | 2
 | 1

## Slide 9: Multiple, Approximate Snapshots of the Queue
Avoiding updates on both packet arrival and departure
  Implicitly handle departures in small batches
  E.g., windows of packets
Avoiding per-flow state
  Approximate data structure (e.g., Count-Min)
  Packet checks its flow’s status, and acts
Count-Min Sketch [CM ‘05]
C columns
B Buckets
f
+1
+1
+1

## Slide 10: Multiple Snapshots Across the Pipeline
Snap 2:
Read
Snap 1:
Read
Snap h:
Read
length
Snap 3:
write

## Slide 11: Heavy Hitter Detection Entirely in the Data Plane
Vibhaalakshmi Sivaraman, Srinivas Narayana, Ori Rottenstreich, S. Muthukrishnan, and Jennifer Rexford
https://conferences.sigcomm.org/sosr/2017/papers/sosr17-heavy-hitter.pdf

## Slide 12: Heavy-Hitter Detection
Heavy hitters
  The k largest trafic flows
  Flows exceeding threshold T
Space-saving algorithm
  Table of (key, value) pairs
  Evict the key with the minimum value
Id | Count
K1 | 4
K2 | 2
K3 | 7
K4 | 10
K5 | 1
K6 | 5
New Key K7
Table scan

## Slide 13: Approximating the Approximation
Evict minimum of d entries
  Rather than minimum of all entries
  E.g., with d = 2 hash functions
Id | Count
K1 | 4
K2 | 2
K3 | 7
K4 | 10
K5 | 1
K6 | 5
New Key K7
Multiple memory accesses

## Slide 14: Approximating the Approximation
Divide the table over d stages
  One memory access per stage
  Two different hash functions
Id | Count
K1 | 4
K2 | 2
K3 | 7
New Key K7
Id | Count
K4 | 10
K5 | 1
K6 | 5
Going back to the first table

## Slide 15: Approximating the Approximation
Rolling minimum across stages
  Avoid recirculating the packet
  … by carrying the minimum along the pipeline
Id | Count
K1 | 4
K2 | 10
K3 | 7
New Key K7
Id | Count
K4 | 2
K5 | 1
K6 | 5
Id | Count
K1 | 4
K7 | 1
K3 | 7
Id | Count
K2 | 10
K5 | 1
K6 | 5
(K2, 10)

## Slide 16: P4 Prototype and Evaluation
Id | Count
K1 | 4
K2 | 10
K3 | 7
Id | Count
K4 | 2
K5 | 1
K6 | 5
New Key K7
(K2, 10)
Hash on packet header
Packet metadata
Conditional updates to compute minimum
Register arrays
High accuracy with overhead proportional to # of heavy hitters

## Slide 17: Hop-by-Hop Utilization-aware Load-balancing Architecture
Naga Katta, Mukesh Hira, Changhoon Kim, Anirudh Sivaraman, and Jennifer Rexford
http://conferences.sigcomm.org/sosr/2016/papers/sosr_paper67.pdf

## Slide 18: HULA Multipath Load Balancing
Load balancing entirely in the data plane
  Collect real-time, path-level performance statistics
  Group packets into “flowlets” based on time & headers
  Direct each new flowlet over the current best path
S1
S2
S3
S4
ToR 10
ToR 1
Data

## Slide 19: Path Performance Statistics
Using the best-hop table
  Update the best next-hop upon new probes
  Assign a new flowlet to the best next-hop
S1
S3
S4
Best-hop table
Best Next-Hop | Path Utilization
S3 | 50%
S4 | 10%
… | …
0
1
…
Dest ToR
Data
Data
Probe
Probe

## Slide 20: Flowlet Routing
Flowlet table
S1
S3
S4
Using the flowlet table
  Update the next hop if enough time has elapsed
  Update the timestamp to the current time
Forward the packet to the chosen next hop
Dest ToR | Timestamp | Next-Hop
ToR 10 | 1 | S2
ToR 0 | 17 | S4
… | … | …
0
1
…
h(flowid)
Data
Data

## Slide 21: Putting it all Together Using P4
data packet
current best next-hop S3
chosen next-hop
Update next-hop (if enough time elapsed) and time
Dest ToR | Timestamp | Next-Hop
ToR 10 | 1 | S2
ToR 0 | 17 | S4
… | … | …
Best Next-Hop | Path Utilization
S3 | 50%
S4 | 10%
… | …
0
1
…
Dest ToR
0
1
…
h(flowid)

## Slide 22: Conclusion
Self-driving networks
  Integrate measure, analyze, and control
  Implement directly in the network devices
Enabled by programmable switches
  Parsing, processing, and state
  Approximate data structures, plus control actions
New programming abstractions
  Higher-level goals  synthesize the control loop