## Slide 1: Closing the Network Control Loop
Jennifer Rexford

## Slide 2: Programmability From Top-to-Bottom and End-to-End
NIC
NIC
Kernel stack
User space
vSwitch
DPDK
XDP/eBPF
5G Mobile
Network
DoS Mitigation
Traffic Engineering
Load
Balancing
…
Overlay Virtualization
SDN Controller

## Slide 3: What Will Network Owner’s Do?
What will network owners do with this new flexibility?
They will want to run their networks better!

## Slide 4: Adding New “Dials”
Traffic
Performance
Cyberattacks
Failures
Signal strength
<Your measurement here>

## Slide 5: Adding New “Knobs”
Drop
Mark
Rate-limit
Reroute
Hand-off
<your knob here>

## Slide 6: Closed-Loop Control
Measure (dials)
Adapt (knobs)
Analyze

## Slide 7: Example #1: Microbursts [ConQuest, CoNEXT’19]
Small timescale traffic bursts
  Long queues caused by incast, attacks, etc.
  Lead to high packet delay and loss
  … despite low average link utilization
5x
3x
1x
16:00:00
0:00:00
8:00:00
16:00:00
Time in day (24h)
Queue Length
Microbursts

## Slide 8: Example #1: Microburst Measurement
Data-plane measurement and analysis
  Backlog in the queue
  A flow’s own contribution to the queue
55%
10%

## Slide 9: Example #1: Microburst Mitigation
Data-plane adaptation
  Drop or mark an arriving packet probabilistically
  Based on its flow’s contribution to the queue
55%
10%

## Slide 10: Example #2: DDoS Attacks [BeauCoup, SIGCOMM’20]
DDoS attacks
  DNS reflection attack
  SYN flooding
  HTTP flooding
  Slowloris attack
Overwhelm the victim
  Exhausting network and server resources
😵
Victim
DNS
DNS
👺
Attacker
. . .

## Slide 11: Example #2: DDoS Detection
Data-plane measurement and analysis
  Identify suspected victim destinations (key DstIP)
  … receiving traffic from distinct senders (attribute SrcIP)
  … in excess of a threshold (threshold T)
select DstIP where distinct(SrcIP) > T
Key
Attribute
Threshold

## Slide 12: Example #2: DDoS Mitigation
Data-plane adaptation
  Drop or rate-limit packets to suspected victims
  Run stateful firewall for suspected victims
  Pushback upstream toward the senders
DNS
DNS
👺
Attacker
. . .

## Slide 13: Example #3: Path Performance [Contra, NSDI’20]
Network path diversity
Load balancing to achieve good performance
  Track the performance (load, loss, delay) of paths
  Split traffic effectively over the multiple paths

## Slide 14: Example #3: Path Performance Monitoring
Data-plane tracking of path performance
  E.g., lowest maximum link utilization
  E.g., minimum end-to-end latency or loss
30%
25%
20%
50%
20%
10%
10%
30%
30%
10%
50%
Probes along reverse path

## Slide 15: Example #3: Performance-Aware Load Balancing
Adaptation to direct traffic over the best path
  Sending packets in the forward direction
  … along the path with the best performance
30%
25%
20%
50%
20%
10%

## Slide 16: Enabler: Programmable Data Planes
Stages
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table
p4.org

## Slide 17: Challenges: Resource Limitations
Limited
depth
Limited
# bits
Limited
# rules
Limited # registers
and # of accesses
Limited ALU
operations
Stages
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table

## Slide 18: Solution: Compact Data Structures
Approximate analysis is fine
  All flows  small number of large flows
  Exact metrics  approximate metrics
Data structures can fit in data-plane registers
  Sketch (e.g., Bloom filter, count-min sketch, etc.)
  Small hash table (e.g., cache of the popular keys)

## Slide 19: ConQuest: Detecting Heavy Flows in the Queue
For each flow, how many packets are in the queue?
Data-plane implementation challenges
  Updating on packet arrival and departure
  Per-flow state (key and count)

## Slide 20: Updating Data Structure Once Per Packet
Slice traffic into time windows
Each snapshot records T=4 packets
Enqueued at time 5
Dequeued at time 14

## Slide 21: Avoiding Per-Flow State
Compact data structures
  With limited memory and processing
  … at the expense of loss in accuracy
Estimate per-flow counts
  With accurate estimate for large flows
Count-Min Sketch per snapshot
  C columns indexed by hash functions
  Increment hashi(flowid) in column i
  Estimate is the min of the C counts

## Slide 22: Grand Challenge
High-level goals
Compiler
Switch OS
switch
Controller
Switch OS
switch
NIC
NIC
vSwitch
NIC
NIC
vSwitch
Distributed software
control loop

## Slide 23: Conclusions
Network programmability
  Top-to-bottom
  End-to-end
Closed-loop network control
  Measure
  Analyze
  Adapt
Compact data structures
  Closing the control loop in the data plane
  … through approximate data structures

## Slide 24: Lessons Learned
Grand challenges
  Networks worthy of society’s trust
Technology enablers
  Deep programmability
Interdisciplinary research
  Programming languages (expressiveness)
  Compact data structures (scarcity)
Prototype systems
  Learning by doing, evaluating under realistic conditions
Building community

## Slide 25: References
ConQuest: Xiaoqi Chen, Shir Landau Feibish, Yaron Koral, Jennifer Rexford, Ori Rottenstreich, Steven A. Monetti, and Tzuu-Yi Wang, "Fine-grained queue measurement in the data plane," in ACM SIGCOMM CoNEXT Conference, December 2019.
BeauCoup: Xiaoqi Chen, Shir Landau-Feibish, Mark Braverman, and Jennifer Rexford, "BeauCoup: Answering many network traffic queries, one memory update at a time," in ACM SIGCOMM, August 2020.
Contra: Kuo-Feng Hsu, Ryan Beckett, Ang Chen, Jennifer Rexford, Praveen Tammana, and David Walker, "Contra: A programmable system for performance-aware routing," in USENIX Networked Systems Design and Implementation, February 2020.