## Slide 1
Closing the Network Control Loop
Jennifer Rexford
Princeton University

## Slide 2
Programmability From Top-to-Bottom and End-to-End
NIC
NIC
Kernel stack
User space
vSwitch
DPDK
XDP/eBPF
5G Mobile
Network
DoS Mitigation
Traffic Engineering
Load
Balancing
…
Overlay Virtualization
SDN Controller

## Slide 3
What Will Network Owner’s Do?
What will network owners do with this new flexibility?
We believe they will want to run their networks better!

## Slide 4
Adding New Dials
Traffic
Performance
Cyberattacks
Failures
Signal strength
<Your measurement here>

## Slide 5
Adding New Knobs
Drop
Mark
Rate-limit
Reroute
Hand-off
<your knob here>

## Slide 6
Closed-Loop Control
Measure (dials)
Adapt (knobs)
Analyze

## Slide 7
Example #1: Microbursts
5x
3x
1x
16:00:00
0:00:00
8:00:00
16:00:00
Time in day (24h)
Queue Length
Microbursts
Small timescale traffic bursts
  Long queues caused by incast, attacks, etc.
  Lead to high packet delay and loss
  … despite low average link utilization

## Slide 8
Example #1: Microburst Measurement
Data-plane measurement and analysis
  Backlog in the queue
  A flow’s own contribution to the queue
55%
10%
ConQuest: "Fine-grained queue measurement in the data plane" in CoNEXT’19.

## Slide 9
Example #1: Microburst Mitigation
Data-plane adaptation
  Drop or mark an arriving packet probabilistically
  Based on its flow’s contribution to the queue
55%
10%

## Slide 10
Example #2: Distributed Denial-of-Service Attacks
DDoS attacks
  DNS reflection attack
  SYN or HTTP flooding
  Slowloris attack
Overwhelm the victim
  Exhausting network and server resources
Victim
DNS
DNS
Attacker
. . .

## Slide 11
Example #2: DDoS Detection
Data-plane measurement and analysis
  Identify suspected victim destinations (key DstIP)
  … receiving traffic from distinct senders (attribute SrcIP)
  … in excess of a threshold (threshold T)
select DstIP where distinct(SrcIP) > T
Key
Attribute
Threshold
BeauCoup: “Answering many network traffic queries, one memory update at a time” in SIGCOMM’20

## Slide 12
Example #2: DDoS Mitigation
Data-plane adaptation
  Drop or rate-limit packets to suspected victims
  Run stateful firewall for suspected victims
  Pushback upstream toward the senders
Victim
DNS
DNS
Attacker
. . .

## Slide 13
Example #3: Path Performance
Network path diversity
Load balancing to achieve good performance
  Track the performance (load, loss, delay) of paths
  Split traffic effectively over the multiple paths

## Slide 14
Example #3: Path Performance Monitoring
Data-plane tracking of path performance
  E.g., lowest maximum link utilization
  E.g., minimum end-to-end latency or loss
30%
25%
20%
50%
20%
10%
10%
30%
30%
10%
50%
Probes along reverse path

## Slide 15
Example #3: Performance-Aware Load Balancing
Data-plane adaptation to direct traffic over the best path
  Sending packets in the forward direction
  … along the path with the best performance
30%
25%
20%
50%
20%
10%
Contra: "A programmable system for performance-aware routing” (NSDI’20)

## Slide 16
p4.org
Enabler: Programmable Data Planes
Stages
Memory
Registers
ALU
Match-
Action
Table
Parser
Deparser

## Slide 17
p4.org
Challenges: Resource Limitations
Stages
Memory
Registers
ALU
Match-
Action
Table
Parser
Deparser
Limited
depth
Limited
# bits
Limited
# rules
Limited # registers
and # of accesses
Limited ALU
operations

## Slide 18
Solution: Compact Data Structures
Approximate analysis is fine
  Microbursts: size estimate for just the large flows
  DDoS: rough count for large #s of distinct sources
  Path performance: rough estimates for best paths
Data structures can fit in data-plane registers
  Sketch (e.g., Bloom filter, count-min sketch, etc.)
  Small hash table (e.g., cache of the popular keys)

## Slide 19
Grand Challenge
High-level goals
Compiler
Switch OS
switch
Controller
Switch OS
switch
NIC
NIC
vSwitch
NIC
NIC
vSwitch
Distributed software
control loop

## Slide 20
THANKS