## Slide 1: Towards Software Defined Cellular Networks
Li Erran Li (Bell Labs, Alcatel-Lucent)
Morley Mao (University of Michigan) Jennifer Rexford (Princeton University)

## Slide 2: Outline
Critiques of LTE Architecture
CellSDN Use Cases
CellSDN Architecture
Related Work
Conclusion and Future Work

## Slide 3: LTE Data plane is too centralized
Cellular Core Network
eNodeB 3
S-GW 2
P-GW
S-GW 1
eNodeB 1
eNodeB 2
Internet and
Other IP Networks
GTP Tunnels
UE 2
UE 1
UE: user equipment
eNodeB: base station
S-GW: serving gateway
P-GW: packet data network gateway
Data plane is too centralized
Scalability challenges at P-GW on charging and policy enforcement!
Notes: Verizon claims that, at its current rate of traffic growth, which is roughly doubling each year, it will reach the capacity thresholds on both its 3G EV-DO and LTE networks beginning in some markets by the end of 2013, and across its entire network by the end of 2015. Unless it can get new spectrum — i.e., the cable operators’ 20 MHz of AWS spectrum — its customers’ connection speeds and service quality will start suffering.

## Slide 4: LTE Control plane is too distributed
Problem with Inter-technology (e.g. 3G to LTE) handoff
Problem of inefficient radio resource allocation
User Equipment (UE)
Gateway (S-GW)
Mobility Management Entity (MME)
Network Gateway
(P-GW)
Home Subscriber Server (HSS)
Policy Control and Charging Rules Function (PCRF)
Station (eNodeB)
Base
Serving
Packet Data
Control Plane
Data Plane
No clear separation of control plane and data plane

## Slide 5: Advantages of SDN for Cellular Networks
Advantage of logically centralized control plane
  Flexible support of middleboxes
  Better inter-cell interference management
  Scalable distributed enforcement of QoS and firewall policies in data plane
  Flexible support of virtual operators by partitioning flow space
Advantage of common control protocol
  Seamless subscriber mobility across technologies
Advantage of SDN switch
  Traffic counters enable easy monitoring for network control and billing

## Slide 6: Flexible Middlebox Support
eNodeB 3
eNodeB 1
eNodeB 2
Internet and
Other IP Networks
Path setup for UE
by SDN controller
UE 2
UE 1
Easy to control flow to middleboxes for content adaptation, echo cancellation, etc
Reduce traffic to middleboxes
SDN Switch
Middlebox
SDN provides fine grained packet classification and flexible routing

## Slide 7: Flexible Middlebox Support (Cont’d)
eNodeB 3
eNodeB 1
eNodeB 2
Internet and
Other IP Networks
UE 2
UE 1
Easy to satisfy policy for traffic not leaving cellular network
Reduce the need for extra devices
SDN Switch
Path setup for UE
by SDN controller
SDN switch can support some middlebox functionality

## Slide 8: Monitoring for Network Control & Billing
Packet handling rules in SDN switches can efficiently monitor traffic at different level of granularity
  Enable real time control and billing
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
+ mask
Packet + byte counters

## Slide 9: Seamless Subscriber Mobility
eNodeB 3
eNodeB 1
eNodeB 2
Internet and
Other IP Networks
UE 2
UE 1
SDN provides a common control protocol works across different cellular technologies
Forwarding rules can be pushed to switches in parallel
SDN Switch
SDN Control Plane
Path setup for UE
by SDN controller
X-Gen Cellular Network
X+1-Gen Cellular Network

## Slide 10: Distributed QoS and ACL Enforcement
eNodeB 3
eNodeB 1
eNodeB 2
Internet and
Other IP Networks
UE 2
UE 1
LTE’s PCEF is centralized at P-GW which is inflexible
SDN Switch
Access policy checked
In SDN switches distributedly
Path setup for UE
by SDN controller

## Slide 11: Virtual Operators
eNodeB 3
eNodeB 1
eNodeB 2
Internet and
Other IP Networks
UE 2
UE 1
Virtual operators may want to innovate in mobility, billing, charging, radio access
SDN Switch
Slicing Layer: CellVisor
Virtual Operator(VO)
(Slice 1)
Virtual Operator
(Slice N)
Flexible network virtualization by slicing flow space
VO1
VO2

## Slide 12: Inter-Cell Interference Management
eNodeB 3
eNodeB 1
eNodeB 2
Internet and
Other IP Networks
UE 2
UE 1
LTE distributed interference management is suboptimal
SDN Switch
Network Operating System: CellOS
Radio Resource Manager
Central base station control: better interference management
  Global view and more computing power

## Slide 13: CellSDN Architecture
CellSDN provides scalable, fine-grain real time control with extensions:
  Controller: fine-grain policies on subscriber attributes
  Switch software: local control agents to improve control plane scalability
  Switch hardware: fine-grain packet processing to support DPI
  Base stations: remote control and virtualization to enable flexible real time radio resource management

## Slide 14: CellSDN Architecture (Cont’d)
Mobility Manager
Subscriber Information Base
Policy and Charging Rule Function
Network Operating System: CellOS
Infra-structure Routing
Cell Agent
Radio Hardware
Packet Forwarding Hardware
Cell Agent
Radio Resource Manager
Packet Forwarding Hardware
Cell Agent
DPI to packet classification based on application
SCTP instead of TCP to
avoid head of line blocking
Offloading controller actions, e.g. change priority if counter exceed threshold
Translates policies on subscriber attributes to rules on packet header
Central control of radio resource allocation

## Slide 15: CellSDN Virtualization
Cell Agent
Radio Hardware
Packet Forwarding Hardware
Cell Agent
Packet Forwarding Hardware
Cell Agent
Slicing Layer: CellVisor
Network OS
(Slice 1)
Network OS
(Slice 2)
Network OS
(Slice N)
Slice semantic space, e.g. all roaming subscribers, all iPhone users

## Slide 16: Related Work
Stanford OpenRoad
  Introduced openflow, FlowVisor, SNMPVisor to wireless networks
Stanford OpenRadio
  Programmable cellular data plane
NEC base station virtualization
  Slicing radio resources at the MAC layer
Ericsson CloudEPC
  Modify LTE control plane to control openflow switches

## Slide 17: Conclusion and Future Work
CellSDN advantages:
  Simple and easy to manage
  Simple and easy to introduce new services
  Easy to inter-operate with other wireless technologies
Future work: detailed CellSDN design