## Slide 1: Measurement Query Languages for Software-Defined Networks
Jennifer Rexford
Princeton University
http://www.cs.princeton.edu/~jrex
Joint work with Srinivas Narayana, Mina Tahmasbi, and David Walker
To appear in NSDI’16: http://www.cs.princeton.edu/~narayana/pathqueries/

## Slide 2: Management = Measure + Control
Network Management
Measure
Control
Software-Defined Networking (SDN)

## Slide 3: Measuring is a Hard (Big-Data) Problem
A few standard tools:
  Ping, traceroute, SNMP, NetFlow, tcpdump
Global state of the network is complex & dynamic:
  Switches: rules, counters, buffers
  Packets: in flight, rewritten, dropped
An operator must “join” multiple data streams:
  Forwarding: protocol, controller, topology updates
  Traffic: packet samples, counters, etc.
Result: inaccurate or high overhead 

## Slide 4: Declarative Query Language
2. Query Run-Time System
3. Optimizations
Expressive measurement
Accurate measurements
on commodity hardware
Efficient measurement
1. Path Query Language

## Slide 5
I. Path Query Language

## Slide 6: Goal: Declarative Measurement Spec
Packet loss localization
Uneven load balancing
Traffic matrix
Slice isolation
DDoS source identification
Port-level traffic matrix
Congested link diagnosis
Loop detection
Middlebox traversal order
Incorrect NAT rewrite
Firewall evasion
...
Q: Common Primitives?
Without referring to:
Forwarding policy
Other measurements
Hardware specifics

## Slide 7: Key Primitive: Packet Path
Common goal in the examples:
  Relate packets across switches and interfaces, as they flow through the network
Packet paths:
  Tests on packets at a single location in network
  Same packet must satisfy multiple tests
Specify measurements precisely:
  Where to capture the packets?
  How to capture the packets?

## Slide 8: Expressing Packet Paths
Regular expressions:
  natural to state paths on graphs
S1
S2
S3
S4
S5
S6

## Slide 9: Expressing Packet Paths
Regular expressions:
  natural to state paths on graphs
S1
S2
S3
S4
S5
S6
S1 ^ S6 ^ S3 ^ S4

## Slide 10: Expressing Packet Paths
Regular expressions:
  natural to state paths on graphs
S1
S2
S3
S4
S5
S6
S1 ^ .* ^ S4

## Slide 11: Expressing Packet Paths
Regular expressions:
  natural to state paths on graphs
S1
S2
S3
S4
S5
S6
S1 ^ .* ^ S4
Boolean packet predicate
pred ::= true | false
| header=value
| location=value
| pred & pred
| pred | pred
| ~pred
| ingress()
| egress()

## Slide 12: Expressing Packet Paths
Regular expressions:
  natural to state paths on graphs
S1
Input packet
Output packet
Forwarding
atom ::= in_atom(pred)
| out_atom(pred)
| in_out_atom(pred,
pred)

## Slide 13: Expressing Packet Paths
Regular expressions:
  natural to state paths on graphs
S1
S2
S3
S4
S5
S6
S1 ^ .* ^ S4
in_atom(sw=S1)
in_atom(true)*
in_atom(sw=S4)
in_atom(sw=S1) ^ in_atom(true)* ^ in_atom(sw=S4)

## Slide 14: Query Language
path ::= atom
      | path ^ path
      | path | path
      | path*
      | path & path
      | ~path
p1
p2
“hop”

## Slide 15: Packets Evading a Firewall
    ingress()
    ^
    (~switch=FW)*
    ^
    egress()
ingress
egress
ingress
ingress
egress
egress

## Slide 16: Evaluation: Let’s write queries!
Switch-level traffic matrix:
 | E1 | E2 | ...
I1 | 250 | 100 | ...
I2 | 120 | 95 | ...
... | ... | ... | ...

## Slide 17: Evaluation: Let’s write queries! (3/3)
Switch-level traffic matrix:
  in_atom(ingress())
  ^
  in_atom(true)*
  ^
  out_atom(egress())
Count all packets, going from any ingress to any egress.
Flow | #pkts
* | 1000

## Slide 18: Evaluation: Let’s write queries!
Switch-level traffic matrix:
  in_group(ingress(),
  [switch])
  ^
  in_atom(true)*
  ^
  out_group(egress(),
  [switch])
Group counts by
packet’s ingress and egress switch!
 Traffic matrix!
Flow | #pkts
sw=I1, sw=E1 | 250
sw=I1, sw=E2 | 100
... | ...

## Slide 19: Query Language
path ::= atom
      | path ^ path
      | path | path
      | path*
      | path & path
      | ~path
atom ::=
| in_atom(pred)
| out_atom(pred)
| in_out_atom(pred,
pred)
| in_group( pred,
[fields])
| out_group(pred,
[fields])
| in_out_group(pred,
[fields], pred,
[fields])

## Slide 20: Where to capture matching packets?
Upstream
Downstream
Queried Path
Packet flow
{path}.up()
{path}.down()
For a given query: packets may be different!

## Slide 21: How to process matching packets?
{path}.set_bucket(bucket)
count_bucket()
(Get switch counters)
packet_bucket()
(Send to controller)
sampling_bucket()
(Get sFlow packet samples)

## Slide 22: More Query Examples

## Slide 23
II. The Run-Time System

## Slide 24: Solution Approach
Query expressions
Statistics
2. Query Run-Time System
SDN controller
Payloads
Statistics
3. Optimizations
1. Path Query Language

## Slide 25: Goal: Query  Network Measurement
Accurate answer
Pay exactly for what you query
Commodity hardware

## Slide 26: Commodity HW: Match-Action Tables
26
match1  action1
match2  action2
...
Wildcard bit pattern
(ternary matching)
Forward/Drop/Modify

## Slide 27: Commodity HW: Multi-Stage Mat-Act
match1  action1
match2  action2
...
match1  action1
match2  action2
...
...

## Slide 28: Goal: Query  Network Measurement
Accurate answer
Pay exactly for what you query
Commodity hardware

## Slide 29: Goal: Query  Network Measurement
Accurate answer
Pay for what you query
Commodity hardware
How to observe a packet’s
path accurately in the data plane
with low overhead?
Avoid inaccuracy of joining traffic and forwarding data, and the overhead of recording every hop of every packet.

## Slide 30: Recording Limited Path Info on Packets
Observation 1: Queries already tell us what’s needed!
  Only record path info needed by queries
Observation 2: Queries are regular expressions
  Regular expressions  Finite automaton (DFA)
  Distinguish only paths corresponding to query DFA states

## Slide 31: Reducing Path Information on Packets
Observation 1: Queries already tell us what’s needed!
  Only record path state needed by queries
Observation 2: Queries are regular expressions
  Regular expressions  Finite automaton (DFA)
  Distinguish only paths corresponding to DFA states
Record only DFA state on packets (1-2 bytes)
Use existing “tag” fields (e.g., VLAN)

## Slide 32: Downstream Query Compilation (1/3)
  p =
  (switch=S1 & srcip=10.0.0.1)
  ^ (switch=S2 & dstip=10.0.0.3)
  p.set_bucket(count_bucket())
Q0
Q1
Q2
switch=S1 & srcip=10.0.0.1
switch=S2 & dstip=10.0.0.3
S1
S2
Notes: Not only do we know, but also modify packet processing on switches to make measurements easier.  need to make this point somewhere.
Note that there are details to make the execution of the automaton deterministic on the data plane – which we are skipping in the interest of time.
Also, the queries are assumed to be matching a packet only once on each switch: typically there are 2 matching points, but let’s assume only ingress queries exist for the time being.

## Slide 33: Downstream Query Compilation (2/3)
Q0
Q1
Q2
switch=S1 & srcip=10.0.0.1
switch=S2 & dstip=10.0.0.3
DFA
Transition
DFA Accept
state=Q0 & switch=S1 & srcip=10.0.0.1  stateQ1
state=Q1 & switch=S2 & dstip=10.0.0.3  stateQ2
state=Q1 & switch=S2 & dstip=10.0.0.3  count
Generate “match-action-able” rules
Notes: Not only do we know, but also modify packet processing on switches to make measurements easier.  need to make this point somewhere.

## Slide 34: Downstream Query Compilation (3/3)
All acting on the same data plane packets!
Use policy composition operators and compiler
DFA-Transitioning
Forwarding
DFA-Accepting
>>
+
)
(
Composing software-defined networks. Monsanto et al., 2013
Notes: Why does this composed policy make sense? Explain.

## Slide 35: Downstream Query Compilation (3/3)
DFA-Transitioning
Forwarding
DFA-Accepting
>>
+
)
(
state=Q0 & switch=S1 & srcip=10.0.0.1  stateQ1
state=Q1 & switch=S2 & dstip=10.0.0.3  stateQ2
dstip=10.0.0.1  fwd(1)
dstip=10.0.0.2  fwd(2)
dstip=10.0.0.3  fwd(3)
...
>>
state=Q0 & switch=S1 & srcip=10.0.0.1 & dstip=10.0.0.2
 stateQ1, fwd(2)
Composing software-defined networks. Monsanto et al., 2013
Notes: Why does this composed policy make sense? Explain.

## Slide 36
III. Optimizations

## Slide 37: Solution Approach
Query expressions
Statistics
2. Query Run-Time System
SDN controller
Payloads
Statistics
3. Optimizations
1. Path Query Language

## Slide 38: Goal: Make Run-Time Efficient
Metrics:
  Rule space
  Query compile time
  Packet state space
Stanford network on a mix of queries:
  Unoptimized: didn’t compile in 2 hours
Fully optimized:
    Query compile time: ~ 5 seconds
  Rule space: ~ 650 rules (TCAM capacity 2-4K)
  Packet state space: state fits in VLAN header
Fit in switch rule memory?
Debugging “interactive”?
Fit on typical “tag” headers?

## Slide 39: Optimizations: Summary
Optimization | # Rules? | Time? | # States?
Separate query & forwarding actions into separate stages |  |  | 
Optimize conditional policy compilation |  |  | 
Integrate tagging and capture policies |  |  | 
Pre-partition predicates by flow space |  |  | 
Cache predicate overlap decisions |  |  | 
Decompose query predicates into multiple stages |  |  | 
Detect predicate overlaps with Forwarding Decision Diagrams |  |  | 
Notes: // table of optimizations + intended metrics that should be reduced

## Slide 40: Optimizations: Summary
Optimization | # Rules? | Time? | # States?
Separate query & forwarding actions into separate stages |  |  | 
Optimize conditional policy compilation |  |  | 
Integrate tagging and capture policies |  |  | 
Pre-partition predicates by flow space |  |  | 
Cache predicate overlap decisions |  |  | 
Decompose query predicates into multiple stages |  |  | 
Detect predicate overlaps with FDDs |  |  | 
Cross-Product Explosion
Notes: // table of optimizations + intended metrics that should be reduced

## Slide 41: Cross-Product Explosion
DFA-Transitioning
Forwarding
DFA-Accepting
>>
+
)
(
state=Q0 & srcip=10.0.0.2  stateQ1
state=Q1 & srcip=10.0.0.3  stateQ2
state=Q2 & port=4  stateQ4
state=Q3 & srcmac=01:*  stateQ5
state=Q4 & srcip=10.0.0.1  stateQ3
state=Q5 & tpdstport=80  stateQ5
state=Q6 & srcip=10.0.0.3  stateQ6
state=Q7 & dstip=10.0.0.4  stateQ2
...
>>
dstip=10.0.0.1  fwd(1)
dstip=10.0.0.2  fwd(2)
dstip=10.0.0.3  fwd(3)
dstip=10.0.0.4  fwd(4)
dstip=10.0.0.5  fwd(5)
dstip=10.0.0.6  fwd(6)
dstip=10.0.0.7  fwd(7)
dstip=10.0.0.8  fwd(8)
...
state=Q0 & srcip=10.0.0.2 & dstip=10.0.0.1
 stateQ1, fwd(1)

## Slide 42: Taming Cross-Product Explosion
Key Problem: Coerce multiple actions on overlapping sets of packets
match1  action1
match2  action2
...

## Slide 43: Taming Cross-Product Explosion
Key Idea: Leverage multiple passes for each packet
  Multi-stage match-action tables on switch hardware
match1  action1
match2  action2
...
match1  action1
match2  action2
...
...
Rule space O(M+N), not O(M*N)

## Slide 44: Taming Huge Policies
(DFA-Ingress-Transitioning >> Forwarding >> DFA-Egress-Transitioning) +
(DFA-Ingress-Accepting)
+
(DFA-Ingress-Transitioning >> Forwarding >> DFA-Egress-Accepting)

(DFA-Ingress-Transitioning + DFA-Ingress-Accepting)
>>
Forwarding
>>
(DFA-Egress-Transitioning + DFA-Egress-Accepting)

## Slide 45: Taming Huge Policies
in_transition
+
in_accept
forwarding
out_transition
+
out_accept
(DFA-Ingress-Transitioning + DFA-Ingress-Accepting) >> Forwarding
>> (DFA-Egress-Transitioning + DFA-Egress-Accepting)
O(M*N)  O(M+N)

## Slide 46: Taming Overlapping Query Predicates
p1: srcip=10.0.0.1
p2: srcip=10.0.0.2
...
p100: srcip=10.0.0.100
p101: dstip=192.168.0.101
p102: dstip=192.168.0.102
...
p200: dstip=192.168.0.200
in_transition
+
in_accept
srcip=10.0.0.1  state1q1
srcip=10.0.0.2  state1q2
...
dstip=192.168.0.101  state2q1
dstip=192.168.0.102  state2q2
...
...
Running many parallel Query DFAs!
O(M*N)  O(M+N)

## Slide 47: Implementation
Prototype
  Pyretic SDN controller
  NetKAT (Ocaml) compiler
  Install rules on OpenVSwitch
Currently single-threaded
  Intel Xeon E3, 3.70Ghz 32GB
Implementation publicly available online
  http://frenetic-lang.org/pyretic/
Composing software-defined networks. Monsanto et al., 2013
A fast compiler for NetKAT. Smolka et al., 2015
OpenVSwitch.org

## Slide 48: Benefit of Optimizations
Stanford campus network topology
Several queries:
  Traffic matrix, DDoS detection, per-hop packet loss, firewall evasion, slice isolation, congested link
Metrics and Stanford results (all queries together):
  Compile time: > 2 hours  5 seconds
  # Rules: ~ 650
  # State bytes: 2 bytes
Notes: Rule space estimation for DNF cases.
Stanford forwarding policy has 3840 rules overall – that’s 240 per device on aveage. Almost all rules match on destination ip address, which almost none of the queries actually match on. This means the best-case reduction applies: ~240 times or two orders of magnitude reduction of rule count going from single-stage to multi-stage tables.
Then there’s at least a factor of 6.6 from the instances that _do_ terminate. Together, that’s 7 * 240 = 1680, or three orders of magnitude reduction in rule space from the unoptimized case.

## Slide 49: Benefit of Optimizations (Stanford)
Cumulative Optimization | Time (s) | # Rules | # State Bits
None | > 7900 | DNF | DNF
Separate query & forwarding actions into separate stages | > 4920 | DNF | DNF
Optimize conditional policy compilation | > 4080 | DNF | DNF
Integrate tagging and capture policies | 2991 | 2596 | 10
Pre-partition predicates by flow space | 56.19 | 1846 | 10
Cache predicate overlap decisions | 35.13 | 1846 | 10
Decompose query predicates into multiple stages | 5.467 | 260 | 16
Notes: Rule space estimation for DNF cases.
Stanford forwarding policy has 3840 rules overall – that’s 240 per device on aveage. Almost all rules match on destination ip address, which almost none of the queries actually match on. This means the best-case reduction applies: ~240 times or two orders of magnitude reduction of rule count going from single-stage to multi-stage tables.
Then there’s at least a factor of 6.6 from the instances that _do_ terminate. Together, that’s 7 * 240 = 1680, or three orders of magnitude reduction in rule space from the unoptimized case.

## Slide 50: Scalability Trends
Five synthetic ISP (Waxman) topologies at various network sizes
At each network size, run mix of queries from before
  Averaged metrics across queries & topologies

## Slide 51: I. Query Compile Time
Response time in man-computer conversational transactions. Miller, 1968
Interactive problem solving (15s)

## Slide 52: II. Rule Count
Switch TCAM capacity: 2K-4K rules

## Slide 53: III. Packet State Bits
VLAN
MPLS

## Slide 54: Summary
Declarative path query language
  Regular expressions, grouping
  Capture locations, capture actions
Compositional run-time system
  Query-DFA packet state
Key optimizations for a practical system
  Addressing cross-product explosion
Paper and more info at http://www.cs.princeton.edu/~narayana/pathqueries