## Slide 1: FlowN: Software-Defined Network Virtualization
Dmitry Drutskoy, Eric Keller, Jennifer Rexford.

## Slide 2: What is Network Virtualization
Ability to run multiple virtual networks that:
  Each has a separate control and data plane

## Slide 3: What is Network Virtualization
Ability to run multiple virtual networks that:
  Each has a separate control and data plane
  Coexist together on top of one physical network

## Slide 4: What is Network Virtualization
Ability to run multiple virtual networks that:
  Each has a separate control and data plane
  Coexist together on top of one physical network

## Slide 5: What is Network Virtualization
Ability to run multiple virtual networks that:
  Each has a separate control and data plane
  Coexist together on top of one physical network
  Can be managed by individual parties that potentially don’t trust each other

## Slide 6: Applications of Virtualization
Traffic isolation in enterprise and campus networks

## Slide 7: Applications of Virtualization
Traffic isolation in enterprise and campus networks
VLANs

## Slide 8: Applications of Virtualization
Traffic isolation in enterprise and campus networks
VLANs
Secure private networks operating across wide areas

## Slide 9: Applications of Virtualization
Traffic isolation in enterprise and campus networks
VLANs
Secure private networks operating across wide areas
VPNs

## Slide 10: Applications of Virtualization
Traffic isolation in enterprise and campus networks
VLANs
Secure private networks operating across wide areas
VPNs
Multi-tenant datacenters

## Slide 11: Applications of Virtualization
Traffic isolation in enterprise and campus networks
VLANs
Secure private networks operating across wide areas
VPNs
Multi-tenant datacenters
A collection of VM’s connected to a “virtual switch”

## Slide 12: Applications of Virtualization
Traffic isolation in enterprise and campus networks
VLANs
Secure private networks operating across wide areas
VPNs
Multi-tenant datacenters
A collection of VM’s connected to a “virtual switch”
Can we do better?

## Slide 13: Virtualization in Datacenters
Hosted Cloud infrastructures aim to
Provide service to many different clients at once
Be efficient: resources are shared
Provide required isolation between clients

## Slide 14: Virtualization in Datacenters
Hosted Cloud infrastructures aim to
Provide service to many different clients at once
Be efficient: resources are shared
Provide required isolation between clients
We propose to virtualize the network using Software-Defined Networking to achieve this

## Slide 15: Software-Defined Networking
New approach to networking that has:
Centralized control plane (smart controller)
Separate from data plane (dumb switches)
Control plane software programmable
Standardized interface for network management

## Slide 16: SDN Simplified Virtualization
Each virtual network can have it’s own virtual controller
A central controller can perform virtualization to separate the virtual networks without need to support it on every switch
Since controllers are in software, do not need vendor support or proprietary protocols to do this

## Slide 17: What is the right abstraction?

## Slide 18: What is the right abstraction?
Clients can have different requirements
Just a set of VM’s with given IP’s

## Slide 19: What is the right abstraction?
Clients can have different requirements
Just a set of VM’s with given IP’s
“Big switch” abstraction with VMs connected to it

## Slide 20: What is the right abstraction?
Clients can have different requirements
Just a set of VM’s with given IP’s
“Big switch” abstraction with VMs connected to it
Proximity of certain VM’s to others

## Slide 21: What is the right abstraction?
Clients can have different requirements
Just a set of VM’s with given IP’s
“Big switch” abstraction with VMs connected to it
Proximity of certain VM’s to others
Using their own addresses in the network

## Slide 22: Need a General Approach
Provide the clients with a virtual network consisting of:
  VM’s
  A network of switches
  A controller
We can match any requirements by making virtual network look like a real one
  For simple networks can run a simple controller
  Can be as elaborate as needed

## Slide 23: Need a General Approach
Provide the clients with a virtual network consisting of:
  VM’s
  A network of switches
  A controller
We can match any requirements by making virtual network look like a real one
  For simple networks can run a simple controller
  Can be as elaborate as needed
FlowN!

## Slide 24: FlowN
What properties do we want to guarantee?
How does our system accommodate them?

## Slide 25: 1: Complete Independence
Address space isolation – each virtual network can use their full address space
Virtual networks are decoupled from the physical topology – changes in the physical network are not necessarily seen by the virtual network
Each virtual network sees its own topology, and nothing else
Each virtual network controller is independant

## Slide 26: 2: Control over network
Arbitrary topologies allow any (reasonable) configuration
Use of own virtual network controller allows fine-grained control of the network
“Big switch” or “collection of VM’s” abstraction can be realized as a simple topology
Embedding algorithm left up to datacenter owner

## Slide 27: 3: Scalability and Efficiency
This approach should be scalable
  Support large amounts of virtual networks
  Ability to scale out in the physical network
And efficient
  Small latency increases for network traversal
  Small resource consumption of virtualization layer

## Slide 28: FlowN System Design
We have designed, prototyped and tested a system with some constraints
Based on OpenFlow
While parts of this have been looked at before, full virtualization using SDN is novel

## Slide 29: FlowN System Design
Scalable
  Mappings done using a database, leveraging existing scalability research
  Database can be replicated in the future
  Caching already improves performance
  Design supports multiple physical controllers in the future
And efficient
  We run virtual controllers in a container to lower resource consumption
  Remap function calls, don’t send packets

## Slide 30: FlowN System Design
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Arbitrary Embedder

## Slide 31: System Design Overview
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Arbitrary Embedder
Tenant Applications

## Slide 32: System Design Overview
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Arbitrary Embedder
Arbitrary Embedder

## Slide 33: System Design Overview
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Arbitrary Embedder
Virtualization layer

## Slide 34: System Design Overview
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Arbitrary Embedder
Database for address mappings

## Slide 35: Tenant Applications
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Arbitrary Embedder
Tenant Applications

## Slide 36: Tenant Applications
Modified controller software
  Derived from existing controller with minimal changes
  Function calls are remapped in our virtualization layer

## Slide 37: Tenant Applications
Modified controller software
  Derived from existing controller with minimal changes
  Function calls are remapped in our virtualization layer
Virtual network specification

## Slide 38: Virtual Network Specification
Nodes
  Servers – each occupy 1 VM slot
  Switches – have some capacity
Interfaces
  Port number, name
  Each switch has some number of interfaces
Links
  Bandwidth
  A link connects one interface on one node to another interface on another node

## Slide 39: Embedding
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Arbitrary Embedder
Embedding

## Slide 40: Embedding
Particular choice of algorithm is left up to the datacenter manager
We provide the abstraction that
  Virtual networks are specified as before
  Each virtual node of a virtual network maps to a unique physical node
  Physical network has remaining capacities specified

## Slide 41: Physical and Virtual Topology
…
…
Switch
Server with VM slots

## Slide 42: Embed Virtual obeying constraints
…
…
Switch
Server with VM slots

## Slide 43: Address Mapping Database
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Arbitrary Embedder
Database for address mappings

## Slide 44: Address Mapping Database
Leverages existing database research
  Simplifies storing state of network mappings

## Slide 45: Address Mapping Database
Leverages existing database research
  Simplifies storing state of network mappings
  Centralizes state, allowing multiple controllers to have the same view in the future

## Slide 46: Address Mapping Database
Leverages existing database research
  Simplifies storing state of network mappings
  Centralizes state, allowing multiple controllers to have the same view in the future
  Support for high throughput

## Slide 47: Address Mapping Database
Leverages existing database research
  Simplifies storing state of network mappings
  Centralizes state, allowing multiple controllers to have the same view in the future
  Support for high throughput
  Low latency achieved through caching

## Slide 48: Address Mapping Database
Leverages existing database research
  Simplifies storing state of network mappings
  Centralizes state, allowing multiple controllers to have the same view in the future
  Support for high throughput
  Low latency achieved through caching
  Guarantees on consistency even in the events of database server failure – no partial network mappings

## Slide 49: Address Mapping Database
Leverages existing database research
  Simplifies storing state of network mappings
  Centralizes state, allowing multiple controllers to have the same view in the future
  Support for high throughput
  Low latency achieved through caching
  Guarantees on consistency even in the events of database server failure – no partial network mappings
  Updates are atomic, allowing changes to network mappings to be atomic

## Slide 50: Example Query
SELECT L.Customer_ID, L.node_ID1, L.node_ID2, L.node_port1, L.node_port2
FROM Customer_Link L, Node_C2P_Mapping M
WHERE
M.customer_ID = L.customer_ID AND
(L.node_ID1 = M.customer_node_ID OR L.node_ID2 = M.customer_node_ID)
VLAN_tag = 10 AND M.physical_node_ID = 3
  Looks up which virtual link a packet belongs to based on the switch it arrived at and the VLAN tag (used for encapsulation)

## Slide 51: Example Query
SELECT L.Customer_ID, L.node_ID1, L.node_ID2, L.node_port1, L.node_port2
FROM Customer_Link L, Node_C2P_Mapping M
WHERE
M.customer_ID = L.customer_ID AND
(L.node_ID1 = M.customer_node_ID OR L.node_ID2 = M.customer_node_ID)
VLAN_tag = 10 AND M.physical_node_ID = 3
  Get the virtual link

## Slide 52: Example Query
SELECT L.Customer_ID, L.node_ID1, L.node_ID2, L.node_port1, L.node_port2
FROM Customer_Link L, Node_C2P_Mapping M
WHERE
M.customer_ID = L.customer_ID AND
(L.node_ID1 = M.customer_node_ID OR L.node_ID2 = M.customer_node_ID)
VLAN_tag = 10 AND M.physical_node_ID = 3
  Looks at virtual links table and node mapping table

## Slide 53: Example Query
SELECT L.Customer_ID, L.node_ID1, L.node_ID2, L.node_port1, L.node_port2
FROM Customer_Link L, Node_C2P_Mapping M
WHERE
M.customer_ID = L.customer_ID AND
(L.node_ID1 = M.customer_node_ID OR L.node_ID2 = M.customer_node_ID)
VLAN_tag = 10 AND M.physical_node_ID = 3
  Table “glue”

## Slide 54: Example Query
SELECT L.Customer_ID, L.node_ID1, L.node_ID2, L.node_port1, L.node_port2
FROM Customer_Link L, Node_C2P_Mapping M
WHERE
M.customer_ID = L.customer_ID AND
(L.node_ID1 = M.customer_node_ID OR L.node_ID2 = M.customer_node_ID)
VLAN_tag = 10 AND M.physical_node_ID = 3
  Given packet arrived on physical switch 3 with vlan tag 10

## Slide 55: Virtualization Layer
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Arbitrary Embedder
Container-based Controller

## Slide 56: Container-Based Virtualization
Virtual controllers are run as objects in the physical controller, not stand-alone applications
  Can use function calls to notify them of network events
  Saves computing resources
  Requires minimal changes to already written controller applications

## Slide 57: Virtualization
SDN enabled
Network
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Incoming packet

## Slide 58: Virtualization
SDN enabled
Network
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
packet_in event

## Slide 59: Virtualization
SDN enabled
Network
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
  Address
  Mapping
DB
Map to virtual address

## Slide 60: Virtualization
SDN enabled
Network
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
packet_in call

## Slide 61: Virtualization
SDN enabled
Network
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
packet_in call
No need to run separate controller – can be done with a function call!

## Slide 62: Virtualization
SDN enabled
Network
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
install_datapath_flow call

## Slide 63: Virtualization
SDN enabled
Network
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
install_datapath_flow call
Same thing

## Slide 64: Virtualization
SDN enabled
Network
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
  Address
  Mapping
DB
Map to physical rules

## Slide 65: FlowN System Design
SDN enabled
Network
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
install_datapath_flow calls

## Slide 66: FlowN System Design
SDN enabled
Network
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Flow installation

## Slide 67: Prototype and Evaluation

## Slide 68: Prototype
Modified python NOX 1.0 controller
MySQL database using InnoDB engine
memcached (pylibmc wrapper for C implementation) for caching results
VLAN tags used for encapsulation
4000ish lines of code in total

## Slide 69: Evaluation
VM running on Core i5-2500 @ 3.30Ghz, 4GB RAM, Ubuntu 10.04
Test VM co-located, but each has their own cores
Modified cbench for throughput/latency tests, generating packets within the network
Mininet simulation used for failure experiments

## Slide 70: Latency Overhead
Learning Switch
Learning Switch
Learning Switch
Run many virtual networks
Virtual controller is a simple learning switch
…
Virtualization Layer (NOX)

## Slide 71: Latency Overhead
Use cbench to simulate packet-in events one at a time
Learning Switch
Learning Switch
Learning Switch
…
cbench
Virtualization Layer (NOX)
cbench: http://www.openflow.org/wk/index.php/Oflops

## Slide 72: Latency Overhead
Use cbench to simulate packet-in events one at a time
Record time for packets to be sent on the network
Learning Switch
Learning Switch
Learning Switch
…
cbench
Virtualization Layer (NOX)
cbench: http://www.openflow.org/wk/index.php/Oflops

## Slide 73: Latency Overhead

## Slide 74: Failure Recovery Time
Simulate physical network using mininet
Virtualization Layer (NOX)

## Slide 75: Failure Recovery Time
Simulate physical network using mininet
Run many virtual networks on top of it
…
Virtualization Layer (NOX)

## Slide 76: Failure Recovery Time
Virtual controller is a host-aware controller which installs shortest path layer-2 routing rules, based on link status
…
Virtualization Layer (NOX)
Superswitch
Superswitch
Superswitch

## Slide 77: Failure Recovery Time
Run high-speed ping between virtual hosts
…
Virtualization Layer (NOX)
Superswitch
Superswitch
Superswitch
ping!
pinging!

## Slide 78: Failure Recovery Time
Bring link down
…
Virtualization Layer (NOX)
Superswitch
Superswitch
Superswitch
link broke!
I broke!

## Slide 79: Failure Recovery Time
Record remapping time
…
Virtualization Layer (NOX)
Superswitch
Superswitch
Superswitch
Use this instead!
Ping resumes!

## Slide 80: Failure Recovery Time

## Slide 81: Future Work
Replicate physical controllers

## Slide 82: Replication
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
SDN enabled
Network
Tenant 3
Application
Container Based
Application Virtualization
Replicate Virtualization Servers

## Slide 83: Future Work
Replicate physical controllers
Evaluate different embedding algorithms and their properties

## Slide 84: Future Work
Replicate physical controllers
Evaluate different embedding algorithms and their properties
Perform many-to-one mappings within the same virtual network

## Slide 85: Questions?

## Slide 86: BELOW THIS: OLD/UNUSED SLIDES

## Slide 87: Database design
Node
Network specification lends itself to database design
Type
Capacity
Link
Capacity
VLAN#
Interface
Port#
Name
1:n
2:1
Topology
Controller
Owner
…
n:1
1:n

## Slide 88: Summary
Network virtualization for:
  Arbitrary networks
  Container-based controller virtualization
Database approach
  Lends itself to network representation
  Uses existing database research

## Slide 89: Database design
Node
Type
Capacity
Link
Capacity
VLAN#
Interface
Port#
Name
1:n
2:1
Topology
Controller
Owner
…
n:1
1:n
Physical Node
Type
Rem. capacity
Physical Link
Rem. Capacity
Physical Interface
Port#
Name
Virtual Networks
1:n
2:1

## Slide 90: Database design
Node
Type
Capacity
Link
Capacity
VLAN#
Interface
Port#
Name
Topology
Controller
Owner
…
n:1
1:n
Physical Node
Type
Rem. capacity
Physical Link
Rem. Capacity
Node Mapping
1:n
2:1
Physical Interface
Port#
Name
Each VM slot houses 1 VM
Each physical switch houses
many virtual
1:n
2:1

## Slide 91: Database design
Node
Type
Capacity
Link
Capacity
VLAN#
Interface
Port#
Name
Topology
Controller
Owner
…
n:1
1:n
Physical Node
Type
Rem. capacity
Physical Link
Rem. Capacity
Path Mapping
1:n
2:1
Physical Interface
Port#
Name
Each Virtual link becomes
A path of physical links
1:n
2:1

## Slide 92: Database design
Node
Type
Capacity
Link
Capacity
VLAN#
Interface
Port#
Name
1:n
2:1
Topology
Controller
Owner
…
n:1
1:n
Physical Node
Type
Rem. capacity
Physical Link
Rem. Capacity
Physical Interface
Port#
Name
Path Mapping
Node Mapping
1:n
2:1

## Slide 93: Caching
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Cache
Cache Results

## Slide 94: Current Work
Multi-controller environments
  Run multiple physical controller server, each housing a number of virtual controllers.
  Forward messages to the right controller server if needed.
Caching for faster access
  Put a cache in front of each physical controller to speed up access times.

## Slide 95: FlowN System Design
SDN enabled
Network
  Address
  Mapping
DB
Tenant 1
Application
Tenant 2
Application
Container Based
Application Virtualization
Arbitrary Embedder
Database for address mappings

## Slide 96: Current SDN Virtualization (OLD)
Address space
  “Slice” the address space [FlowVisor][Pflow]
  “Virtualize” by providing each virtual network with own address space [VL2][Nicira].
Topology
  Edge switches with full connectivity [VL2][Nicira]
  Subset existing topology [FlowVisor][PFlow]
Notes: Mention what each is good for (you want topology to be able to control your own bandwidth allocation among your VMs, and manage failure yourself).

## Slide 97: Topology
Edge switches with full connectivity [VL2][Nicira]
Notes: Mention what each is good for (you want topology to be able to control your own bandwidth allocation among your VMs, and manage failure yourself).

## Slide 98: FlowN System Design (1)
Database for address mappings

## Slide 99: FlowN System Design (2)
Container based controller

## Slide 100: Physical and Virtual Topology
3
3
3
3
3
3
25
25
50
…
…
20
6
6
6
20
6
6
6
2
2
5
5
2
2
5
5
10
10
10
Switch with N capacity
Server with N VM’s
N
N

## Slide 101: Embed Virtual obeying constraints
2
…
…
2
2
5
5
2
2
5
5
10
10
10
2
2
2
5
5
5
5
10
10
10
10
Switch with N capacity
Server with N VM’s
N
N

## Slide 102: Update Constraints
1
1
3
1
1
3
15
15
50
…
…
10
1
1
6
10
6
1
1
2
2
5
5
2
2
5
5
10
10
10
Switch with N capacity
Server with N VM’s
N
N

## Slide 103: Why virtualize the Network? (don’t use this slide)
Virtualization in a Datacenter environment common practice.
  Virtual networks as a service.
  Datacenter incurs smaller costs per resource due to size (dedicated facility, personnel, design, etc.).
  Customers avoid start-up costs, pay per resources used.
Can be useful in other places.
  Managing a virtual network can be easier than a (especially new) physical.
  Allows running multiple virtual networks over one physical for things like research testbeds.

## Slide 104: Arbitrary Virtual Networks (don’t use this slide)
Current approaches do not give an arbitrary virtual network.
  One approach abstracts away inner network operation, presenting users with either:
    A point-to-point mesh of edge switches (Nicira).
    A set of VM’s with given addresses (Microsoft Azure).
  Another “slices” the network.
    Each tenant subscribes to certain addresses of a global address scheme (FlowVisor).
Full Virtualization has its benefits.
  Allows fine-grained network management.
  Masking of real network operation to virtual networks.
  Allows you to use your favorite network anywhere!

## Slide 105: Current SDN Virtualization
Abstract away inner network operation [Nicira][VL2]
“Slice” the network [FlowVisor][Pflow]
Picture here

## Slide 106: Current SDN Virtualization
Abstract away inner network operation [Nicira][VL2]
Picture here

## Slide 107: Full Virtualization

## Slide 108: Current SDN Virtualization
Address space
  “Slice” the address space [FlowVisor][Pflow]
  “Virtualize” by providing each virtual network with own address space [VL2][Nicira].
VN 1:
VM1: ip=10.0.0.1
VM2: ip=10.0.0.2
VM3: ip=10.0.0.3
…
VN 1:
VM1: ip=10.0.0.1
mac=…:00:01
VM2: ip=10.0.1.1
mac=…:00:02
…
VN 1:
VM1: mac=…00:01
VM2: mac=…00:02
VM3: mac=…00:03
…

## Slide 109: Why Virtualize the Network
...
Controller
Application
Controller
Application
Controller
Application
Virtual to Physical Mapping

## Slide 110: FlowN System Design