## Slide 1: Serval: An End-Host Stack for Service-Centric Networking
Erik Nordström
David Shue, Prem Gopalan, Rob Kiefer,
Mat Arye, Steven Ko, Jen Rexford, Mike Freedman
Princeton University
serval-arch.org

## Slide 2: The Internet of the 1970s
Network designed for accessing hosts
Killer Apps:
telnet, ftp
IMP 1
UCLA
IMP 4
Utah
IMP 2
SRI
IMP 3
UCSB

## Slide 3: The Internet of the 2000s
Users agnostic of actual service location and host
Datacenter
Datacenter

## Slide 4: What does Service Access Involve?
Locate a nearby service datacenter
  Map service name to location
Connect to service
  Establish data flow to instance
  Load balance between pool of replicas
Maintain connectivity to service
  Migrate between interfaces and networks

## Slide 5: Today’s (Overloaded) Abstractions
Service is IP + port
  Exposes location
  Specifies app. protocol
  One service per IP
Flow is “five tuple”
  Binds flow to interface and location
  Cannot migrate between interfaces or networks
TCP/IP
demux (IP + port)
Network
connect (IP + port)
Transport
Application

## Slide 6: Service Access Today
Cellular
Provider
Enterprise
Network
4G
Transit
Provider
Datacenter
Datacenter

## Slide 7: Finding a Service Location
Cellular
Provider
Enterprise
Network
4G
Transit
Provider
Load-Balanced
Web Service
DNS binds service to location at client (early binding)
  Caching and ignoring TTL exacerbates the problem
  Slow failover when instance or load balancer fail
DNS

## Slide 8: Connecting to Service
Cellular
Provider
Enterprise
Network
4G
Transit
Provider
Load-Balanced
Web Service
Datacenter LB maps single IP to multiple servers
  Must do this for every packet on path -> fate sharing
  Increases complexity and cost

## Slide 9: Maintaining Connectivity to Service
Cellular
Provider
Enterprise
Network
4G
Transit
Provider
VM
Migration
Datacenter
Migrate VMs to balance load in the cloud
  Requires flat addressing or tunneling within datacenter

## Slide 10: Maintaining Connectivity to Service
Cellular
Provider
Enterprise
Network
4G
Datacenter
Datacenter
Physical
Mobility
Multi-
Homing
Transit
Provider
Flows break when switching networks or interfaces

## Slide 11: Contributions
Naming abstractions
  Services, flows
  Clean role separation in the network stack
Software architecture for services (Serval)
  Service-level control/data plane split
  Service-level events

## Slide 12: Naming Abstractions

## Slide 13: Today’s (Overloaded) Abstractions
TCP/IP
demux (IP + port)
Network
forward (IP)
connect (IP + port)
Transport
Application

## Slide 14: Serval Abstractions
Service
Access
Serval cleans the slate
  (But not completely)
Network layer unmodified!
Service Access Layer (SAL)
  Connects to services
  Maintains connectivity
Transport
Application
Network
forward (IP)
Serval

## Slide 15: Serval Abstractions
Service = ServiceID
  Group of processes with identical functionality
Flow = FlowID
  Invariant demux key
  Host-local, ephemeral
Location = IP address
  Location, interface
  Can change dynamically
connect (serviceID)
Transport
Application
demux ( )
serviceID
Network
forward (IP)
Service
Access
flowID
Serval

## Slide 16: A Clean Role Separation in the Stack
What you access (serviceID), over which flows (flowIDs), and at which service instance (IP address)
TCP/IP
Serval
demux (IP + port)
forward (IP)
forward (IP)
connect (IP + port)
connect (serviceID)
demux ( )
serviceID
flowID
Transport
Network
Application
Service
Access

## Slide 17: Service Names (ServiceIDs)
ServiceIDs allocated in blocks
  Prefix ensures global uniqueness
  Prefix-based aggregation and LPM
A ServiceID late binds to service instance
  ServiceID in first packet of connection
  Service-level routing and forwarding
Provider prefix
Provider-specific
Self-certifying

## Slide 18: A Service-Aware Network Stack
connect(sock, serviceID)
bind(sock, serviceID)
listen(sock)
Network stack must resolve service to instance for client
Network stack must advertise service for server

## Slide 19: Software Architecture

## Slide 20: Serval End-host Architecture
Service Controller
ServiceID | Action | Sock/Addr
FlowID | Socket
Application
Dest Address | Next Hop
IP Forwarding Table
Flow Table
Service Table
Service
Control API

## Slide 21: Data Plane: The Service Table
ServiceID | Action | Rule State
Prefix A | FORWARD | Send to addr A1
Prefix B | FORWARD | Send to [A2, A3, A4]
Prefix C | DEMUX | Send to listening sock s
Prefix D | DELAY | Queue and notify service controller
Prefix E | DROP | 
default | FORWARD | Send to A5

## Slide 22: Data Plane: The Service Table
ServiceID | Action | Rule State
Prefix A | FORWARD | Send to addr A1
Prefix B | FORWARD | Send to [A2, A3, A4]
Prefix C | DEMUX | Send to listening sock s
Prefix D | DELAY | Queue and notify service controller
Prefix E | DROP | 
default | FORWARD | Send to A5

## Slide 23: Data Plane: The Service Table
ServiceID | Action | Rule State
Prefix A | FORWARD | Send to addr A1
Prefix B | FORWARD | Send to [A2, A3, A4]
Prefix C | DEMUX | Send to listening sock s
Prefix D | DELAY | Queue and notify service controller
Prefix E | DROP | 
default | FORWARD | Send to A5

## Slide 24: Data Plane: The Service Table
ServiceID | Action | Rule State
Prefix A | FORWARD | Send to addr A1
Prefix B | FORWARD | Send to [A2, A3, A4]
Prefix C | DEMUX | Send to listening sock s
Prefix D | DELAY | Queue and notify service controller
Prefix E | DROP | 
default | FORWARD | Send to A5

## Slide 25: Data Plane: The Service Table
ServiceID | Action | Rule State
Prefix A | FORWARD | Send to addr A1
Prefix B | FORWARD | Send to [A2, A3, A4]
Prefix C | DEMUX | Send to listening sock s
Prefix D | DELAY | Queue and notify service controller
Prefix E | DROP | 
default | FORWARD | Send to A5

## Slide 26: Service Access with Serval
Internet
X
X
a
c
d
e
Datacenter
Service
Router

## Slide 27: Adding a Service Instance
ServiceID | Action | Sock/Addr
FlowID | Socket
Application
Service Controller
S
bind(X)
listen()
Add DEMUX rule
X
DMX
s
Register
Service X

## Slide 28: Removing a Service Instance
ServiceID | Action | Sock/Addr
FlowID | Socket
Application
Service Controller
S
close()
Remove DEMUX rule
X
DMX
s
Unregister
Service X

## Slide 29: Control Plane: The Service Controller
Service Controller
Service X
@ address a
Service Controller
DNS

## Slide 30: Control Plane: The Service Controller
ServiceID | Action | Sock/Addr
FlowID | Socket
Service Controller
Add FORWARD rule
X
FWD
d
Service X
@ address d

## Slide 31: Service Access with Serval
Internet
X
X
a
c
d
e
Datacenter
X | d,e
X@d
X@e
X/24@c
X/24 | c
Service
Router
bind(X)
bind(X)

## Slide 32: Connecting to Service X
Service Controller
ServiceID | Action | Sock/Addr
FlowID | Socket
Application
S
socket()
X
FWD
c
2
s
Allocates local flowID
a

## Slide 33: Connecting to Service X
ServiceID | Action | Sock/Addr
FlowID | Socket
Application
S
connect(X)
X
FWD
c
2
s
a
a
2
SYN
c
-
X
To c

## Slide 34: Load Balancing in Service Router
ServiceID | Action | Sock/Addr
FlowID | Socket
X
FWD
d,e
f
c
To e
From a
a
2
SYN
e
-
X
a
2
SYN
c
-
X

## Slide 35: Service Instance Providing Service X
ServiceID | Action | Sock/Addr
FlowID | Socket
Application
X
DMX
s
a
2
SYN
e
-
X
S
e
From a

## Slide 36: Service Instance Providing Service X
ServiceID | Action | Sock/Addr
FlowID | Socket
Application
accept()
X
DMX
s
3
sc
S
Sc
e
To a
e
3
SYN-ACK
a
2

## Slide 37: Service Access with Serval
Internet
X
X
a
c
d
e
Datacenter
a
SYN
c
X
e
SYN-ACK
a
a
SYN
e
X
X | d,e
e
data
a
Service
Router

## Slide 38: Ad hoc Service Discovery
ServiceID | Action | Rule State
default | FORWARD | “broadcast”
X
X
connect(X)
a
c
b
Accessing service X
a
SYN
*
X
b
SYN-ACK
a
c
SYN-ACK
a

## Slide 39: What does Service Access Involve?
Locating a nearby service datacenter
  Map service name to location
Connecting to service
  Establish data flow to instance
  Load balance between pool of replicas
Maintaining connectivity to service
  Migrate between interfaces and networks

## Slide 40: Migration of Flows
sC
sS
fS1
fC1
a1
a2
a3
Host C
Host S
a4
RSYN
RSYN-ACK
ACK
Migrate flow
a1 -> a2

## Slide 41: Multipath with Multiple Subflows
sC
sS
fS1
fC1
fS2
fC2
a1
a2
a3
Host C
Host S
a4
SYN
SYN-ACK
ACK
Add flow
a2 <-> a4

## Slide 42: Prototype
End-host network stack (28,000 LOC)
  Linux kernel module
  BSD sockets with AF_SERVAL protocol family
  AF_INET sockets can be accessed simultaneously
Legacy middleboxes / NATs handled via encap.
Translator for incremental deployment
  Unmodified apps and end-hosts
  Serval apps with unmodified services

## Slide 43: Incremental Deployment
Translator
App
TCP/IP
Serval

## Slide 44: Incremental Deployment
TCP/IP
Translator
App
Serval
TCP/IP
Translator

## Slide 45: Use of Migration on Clients
WiFi
Cellular
Single Serval TCP connection that never breaks
Saves > 900 MB cellular data per month

## Slide 46: Uses of Migration on Servers
Load balancing across NICs
Both flows use eth0
Flow 1
moved to eth1

## Slide 47: Uses of Migration on Servers
Migrating VMs across subnets
VM changes subnet, acquiring new address
VM migrates flow to new address

## Slide 48: Competitive Performance
 | Mean (Mbit/s)
TCP/IP | 934.5
Serval | 933.8
Translator | 932.1
TCP Throughput
 | Mbit/s | Kpkt/s
IP forwarding | 987 | 388.4
Serval | 872 | 142.8
Service Table Throughput

## Slide 49: Applications are Easy to Port
Application | Codebase | Changes
Iperf | 5,934 | 240
TFTP | 3,452 | 90
wget | 87,164 | 207
Elinks browser | 115,224 | 234
Firefox browser | 4,615,324 | 70
Mongoose webserver | 8,831 | 425
Memcached server | 8,329 | 159
Memcached client | 12,503 | 184

## Slide 50: SDN to the Edges!
SDN about network-wide visibility and control
  Today’s “SDN” (OpenFlow) primarily focuses on layer-2 / layer-3 abstractions
Serval extends SDN model to the network edge
  New programming abstractions for services, flows, hosts, and interfaces
  Service-level control/data plane split
Joint service and network control

## Slide 51: Summary of Contributions
New naming abstractions
  Clean role separation in the stack
  Makes it easier to build and manage services
Software architecture for services
  Flexible service resolution and discovery
  Maintains robust connectivity
  Joint service and network management

## Slide 52
Papers, demos, source code (GPL) online
serval-arch.org
@servalnetwork

## Slide 53: Related Work
Locator/identifier separation
  HIP, i3, HAIR, DOA, LISP, LNA
Data-oriented networking
  DONA, CCNx
Support for mobility and migration
  TCP Migrate, Mobile IP, ROAM
Multipath and multi-homing
  MPTCP, SCTP, Shim6