## Slide 1
Be Fast, Cheap and in Control
with SwitchKV
Xiaozhou Li
Raghav Sethi
Michael Kaminsky
David G. Andersen
Michael J. Freedman

## Slide 2: Goal: fast and cost-effective key-value store
Target: cluster-level storage for modern cloud services
  Massive number of small key-value objects
  Highly skewed and dynamic workloads
  Aggressive latency and throughput performance goals
This talk: scale-out flash-based storage for this setting

## Slide 3: Key challenge: dynamic load balancing
How to handle the highly skewed and dynamic workloads?
Today’s solution: data migration / replication
  system overhead
  consistency challenge
time t
time t+x

## Slide 4: Fast, small cache can ensure load balancing
flash-based backend nodes
frontend cache node
E.g., 100 backends with hundreds of billions of items + cache with 10,000 entries
Need only cache O(nlogn) items to provide good load balance, where n is the number of backend nodes. [Fan, SOCC’11]
How to efficiently serve queries with cache and backend nodes?
How to efficiently update the cache under dynamic workloads?
hottest queries
less-hot queries, better-balanced loads

## Slide 5: High overheads with traditional caching architectures
Cache must process all queries and handle misses
In our case, cache is small and hit ratio could be low
  Throughput is bounded by the cache I/O
  High latency for queries for uncached keys
Look-aside
Look-through
clients
backends
cache
miss
clients
backends
cache (load balancer)
miss
failure point

## Slide 6: SwitchKV: content-aware routing
Switches route requests directly to the appropriate nodes
Latency can be minimized for all queries
Throughput can scale out with # of backends
Availability would not be affected by cache node failures
backends
cache
OpenFlow Switches
clients
controller

## Slide 7: Exploit SDN and switch hardware
Clients encode key information in packet headers
  Encode key hash in MAC for read queries
  Encode destination backend ID in IP for all queries
Switches maintain forwarding rules and route query packets
L2 table
TCAM table
Packet In
Packet Out
miss
hit
exact match rule per cached key
match rule per physical machine
Packet Out
to the cache

## Slide 8: Keep cache and switch rules updated
New challenges for cache updates
  Only cache the hottest O(nlogn) items
  Limited switch rule update rate
  Goal: react quickly to workload changes with minimal updates
cache
backend
switch rule update
top-k <key, load> list
(periodic)
fetch <key, value>
(instant)
bursty hot <key, value>
controller

## Slide 9: Evaluation
How well does a fast small cache improve the system load balance and throughput?
Does SwitchKV improve system performance compared to traditional architectures?
Can SwitchKV react quickly to workload changes?

## Slide 10: Evaluation Platform
Reference backend
1 Gb link
Intel Atom C2750 processor
Intel DC P3600 PCIe-based SSD
RocksDB with 120 million 1KB objects
99.4K queries per second

## Slide 11: Evaluation Platform
Client
40 GbE
Xeon Server 1
Cache
40 GbE
Xeon Server 2
40 GbE
40 GbE
40 GbE
40 GbE
Pica8 P-3922
(OVS 2.3)
Backends
40 GbE
40 GbE
Xeon Server 3
Xeon Server 4
Ryu
Backends
# of backends | 128
backend tput | 100 KQPS
keyspace size | 10 billion
key size | 16 bytes
value size | 128 bytes
query skewness | Zipf 0.99
cache size | 10,000 entries
Default settings in this talk
  Use Intel DPDK to efficiently transfer packets and modify headers
Client adjusts its sending rate, keep loss rate between 0.5% and 1%

## Slide 12: Throughput with and without caching
Cache (10,000 entries)
Backends aggregate (with cache)
Backends aggregate (without cache)

## Slide 13: Throughput vs. Number of backends
backend rate limit: 50KQPS, cache rate limit: 5MQPS

## Slide 14: End-to-end latency vs. Throughput

## Slide 15: Throughput with workload changes
Make 200 cold keys become the hottest keys every 10 seconds
Traditional cache update method
Periodic top-k updates only
Periodic top-k updates + instant bursty hot key updates

## Slide 16: Conclusion
SwitchKV: high-performance and cost-efficient KV store
Fast, small cache guarantees backend load balancing
Efficient content-aware OpenFlow switching
  Low (tail) latency
  Scalable throughput
  High availability
Keep high performance under highly dynamic workloads