## Slide 1: Sonata: Query-Driven Streaming Network Telemetry
Jennifer Rexford
With Arpit Gupta, Rob Harrison, Nick Feamster, Marco Canini (KAUST), Walter Willinger (Niksun)

## Slide 2: Flexible Telemetry for Network Management
Many analysis questions
  Performance diagnosis
  Cyber attack detection
  Traffic engineering
Familiar query language
  Packet as a tuple
  Dataflow operators
  E.g., Spark-like queries
E.g., DNS reflection attacks
👺
😵
Src: Victim
Dst: DNS
Src: Victim
Dst: DNS
Src: DNS
Dst: Victim
Src: DNS
Dst: Victim
DNS
DNS
Attacker
Victim
DNS Response Traffic
From Unique DNS Servers
To a Single Victim
Exceeds a Threshold

## Slide 3: Spark-Like Query Language
victimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
DNS Response Traffic
From Unique DNS Servers
To a Single Victim
Exceeds a Threshold
1
2
3
4
5
6
7
Notes: Let’s see how this type of monitoring query might be expressed in a modern data flow-like language.
[🌀] On line two we see a filter operator that specifies DNS Traffic,
[🌀] lines 3-4 to narrow that down to traffic from unique DNS servers,
[🌀] line 5 further narrows the query down to a single Victim, and
[🌀] lines 6-7 determine when the number of unique DNS servers contacting that single victim exceeds a threshold.
This query is easy to express in a high-level language, and easy to compute at a modern stream processor. But how does executing this query scale?

## Slide 4: Query-Driven Collection and Analysis
Scalability challenges
  Many packets and flows
  Many queries
  Many switches
Query-driven collection
  Integrate collection and analysis
  Customize collection to the query
  Fine-grained with low overhead
Query partitioning
tuples

## Slide 5: Compiling Individual Operators
filter(p)
Stream of Elements
Elements Statisfying
Predicate (p)
Match | Action
p | 
udp.sport == 53 | 
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
Notes: Let's start by looking at what it takes to compile individual operators to match-action tables, one at a time.
[🌀] The filter operator takes [🌀] a stream of elements as input, and returns[🌀] the set of elements that satisfy some predicate p.
We can implement this in a [🌀] match-action table by simplying supply p as the match component.
If we return to the [🌀] DNS reflection query I described in the beginning, we see that the predicate performs an exact match on the UDP source port. We would implement this [🌀] directly in the match-action table as shown.

## Slide 6: Compiling Individual Operators
filter(p)
Stream of Elements
Elements Statisfying
Predicate (p)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
control ingress {
apply(filter_map_table);
...
apply(reduce_table);
if (m.reduce_table_sum > Th) {
apply(report_table)
}
Notes: The filter operator can also be used to apply a conditional predicate, as we see in the last line of this query.
In this case, we would instead choose to implement the filter in the control flow between match-action tables in the pipeline. [🌀] If we look at this code block, we see that the match-action tables that each operator compiles to is applied in the control flow of the processing pipeline. After the reduce_table is applied, the final filter’s predicate is supplied in conditional control flow that then conditionally applies the table that performs the reporting to the stream processor, when the predicate is satisfied.

## Slide 7: Compiling Individual Operators
map(f)
Match | Action
 | f
* | m.dstIP = p.dstIP m.srcIP = p.srcIP
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Stream of Elements
Result of Applying
Function f to Each Element
1
2
3
4
5
6
7
Notes: Similar to filter, [🌀] The map operator also takes [🌀] a stream of elements as input and [🌀] returns the set of elements with a function(f) applied to each element.
We can implement that, in general, [🌀] as the action body of a match-action table where the function f, if supported by the data plane, is applied.
Returning to our example query [🌀] , the function applied here is simply a projection of the entire original packet to a single dstIP, srcIP pair. In this case, [🌀] we would just store the values from the packet in metadata for subsequent processing. However, other actions such as decrementing a TTL field are possible.

## Slide 8: Compiling Individual Operators
reduce(f)
Match | Action
* | idx = hash(m.dstIP)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Stream of Elements
Result of Applying
Function f Over All Elements
Stateful Memory
Match | Action
* | stateful[idx] += 1
1
2
3
4
5
6
7
Notes: The [🌀] reduce operator also takes [🌀] a stream of elements as input and returns [🌀] a single result that is the application of the function f over all elements. Naturally, we break up the stream into windows of size (w) seconds to compute this function over a finite stream.
Unlike map and filter, the reduce function requires some stateful memory to store the intermediate value of the function between the arrival of successive elements. Just like with the map operator, the function to be applied must still be executable in the data plane.
Like the map operator, we would also apply the function f in the action body of a match-action table, but since stateful memory is implemented as a hash-table in PISA switches, we must first compute an index into the hash table before looking up the value stored in it.
In the case of our example query, [🌀] the first table computes an index by hashing the key of interest, in this case dstIP. Since lookup into the hash-table depends on the value of the index, both the value in the hash table in the index cannot be looked up in the same table. The second table applies the function (sum) to the intermediate value and the next element (1).

## Slide 9: Compiling a Query
Programmable Deparser
Stages
Programmable Parser
State
Filter Map
Filter
D1
D2
Map
R1
R2
Notes: To compile an entire query, we would just sequentially apply [🌀] the set of match-action tables generated by each individual operator. Here the D1/D2 and R1/R2 abbreviate the first and second tables of the distinct and reduce operators, respectively.

## Slide 10: Compiling a Query
Programmable Deparser
Stages
Programmable Parser
State
Filter Map
Filter
D1
D2
Map
R1
R2
Notes: In reality, the compilation can be optimized such that two match action tables can occupy the same stage as long as the values do not depend on one another. For example the actions in the first map table and actions in the first lookup for the distinct operator could be coalesced into a single table in the first stage. But as described before the two tables implementing distinct and reduce cannot be executed in the same stage due to the data dependency.

## Slide 11: Partitioning Decisions
Query Planner
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
Target Resources?
Reduce Load?
Notes: So we’ve seen how a [🌀] single query, is compiled to a sequence of match action tables in the data plane. However, we want to run [🌀] several different queries concurrently. Now we must consider, for all of the operators in all of the queries that can be compiled to the data plane, which ones do we actually choose to offload to the data plane? Determining the answer to that question is the [🌀] job of the query planner which takes into consideration two questions? First, [🌀] does the target have enough remaining resources and to offload a partitioning to the data plane and Second, [🌀] does this partitioning reduce the load on the stream processor optimally?

## Slide 12: Query Planning Integer Linear Program
Constraints
Goal: Minimize Tuples Sent to Stream Processor
Programmable Deparser
Stages
Programmable Parser
Memory
Persistent State
ALU
PHV Size
Number of
Actions
Total Stages
Stateful Memory
Packet Header Vector
How do we calculate the number of tuples sent to the stream processor?
Notes: We model this optimization problem as an Integer-Linear-Program. Where the goal [🌀] is to minimize the number of tuples sent to the stream processor subject to the [🌀] constraints of the underlying data plane target.
If we return to the [🌀] PISA architecture, the constraints to the ILP become clear. The size of the packet header vector, the number of actions per stage, the amount of stateful memory per stage, and the total number of stages all determine whether or not a particular set of queries can be concurrently compiled to the data plane.
It is clear how the queries compile to consume these resources in match action tables, but
[🌀] How do we evaluate the number of tuples sent to the stream processor to achieve our goal?

## Slide 13: Training Data
Workload dependence
  Operators consume common switch resources
  Determine which operators reduce the tuples the most
Detect and adapt to traffic dynamics
  Sonata uses training data to size hash tables
  Report collisions to detect deviation!
Iterative refinement
  Queries that “drill down” through the data over time
Notes: We use training data to deal with the [🌀] workload dependence of achieving our goal.
Consider for example, a two different filter operators, one that reduces the number of tuples by 90% and one that reduces by 10%. Given that both consume the same resources in the data plane, Its obvious which operator we would choose to partition, but we might not know the reduction factor until the predicate applied by the filter is evaluated against actual traffic. We rely on the training data to determine which operators best reduce the number of tuples sent to the stream processor.
Relying on training data means that our solution might not be optimal at all times. So to maintain optimality, we must [🌀] detect and adapt to traffic dynamics. Sonata uses the training data to help with this as well. Since the stateful memory I described earlier is implemented as hash tables, we can use the training data to size these hash tables for an expected collision rate.

## Slide 14: Experimental Results
Wide range of queries
  Performance, security, traffic engineering
Realistic traffic
  CAIDA packet traces
Practical data-plane model
  16 stages, 8 stateful operations, 8 Mb stateful memory
Significant scalability benefits
  Orders of magnitude fewer tuples sent to stream processor

## Slide 15: Conclusions
Flexible and scalable telemetry
  Query-driven collection and analysis
  Query partitioning between Spark and P4
  Query planning as an integer linear program
Ongoing work
  Network-wide queries (SOSR’18 heavy-hitters paper)
  Wider range of data-plane targets
  More sophisticated data structures
Open-source software at sonata.cs.princeton.edu, paper to appear at SIGCOMM’18