## Slide 1: Congestion-Aware Load Balancing at the Virtual Edge
Aran Bergman
(Technion, VMware)
Naga Katta, Aditi Ghag, Mukesh Hira, Changhoon Kim, Isaac Keslassy, Jennifer Rexford
CLOVE

## Slide 2: Data center load balancing today
Equal-Cost Multi-Path (ECMP) routing:
  Path(packet) = hash(packet’s 5-tuple)
Coarse-grained
Elephant Hash collisions
Congestion-oblivious
. . . . . .
…
…
…
Servers
Leaf
Switches
Spine
Switches
src,dst IP + src,dst port + protocol

## Slide 3: Previously proposed load balancing schemes
Hypervisors
vSwitch
vSwitch

## Slide 4: Previously proposed load balancing schemes
Hypervisors
Centralized load balancing
Hedera, Fastpass, MicroTE, SWAN
Control-driven feedback
Slow reaction time
Routes computation overhead
Scalability Issues
vSwitch
vSwitch
Central Controller

## Slide 5: Previously proposed load balancing schemes
Hypervisors
CONGA, HULA, LetFlow, DRILL
Needs custom ASIC data center fabric
High capital cost
Controller Involvement may still be required
vSwitch
vSwitch
In-network load balancing

## Slide 6: Previously proposed load balancing schemes
Hypervisors
vSwitch
vSwitch
Presto
Congestion Oblivious
Controller intervention in case of topology asymmetry
MPTCP
Incast collapse
Guest VM network stack changes
Hermes (SIGCOMM’17)
Concurrent effort
End-host load balancing

## Slide 7: vSwitch as the sweet spot
vSwitch
vSwitch
Spine
switches
Leaf
switches
Easy to implement
No Switch HW changes
No guest VM changes

## Slide 8: CLOVE assumptions
vSwitch
vSwitch
Payload
IP
Eth
Eth
IP
TCP
Overlay
Network switches with ECMP using 5-tuple
Outer transport header is used for ECMP traffic distribution
Spine
switches
Leaf
switches
Clove operates over a DC Overlay – e.g., Stateless Transport Tunneling (STT)

## Slide 9: CLOVE in 1 slide
Path discovery using traceroute probes
Load-balancing flowlets [FLARE ‘05]
vSwitch switching between paths based on RTT-scale feedback
  Explicit Congestion Notification - ECN
  In-band Network Telemetry - INT

## Slide 10
Path Discovery
Standard ECMP in the physical network
vSwitch
vSwitch
Hypervisor H1
Hypervisor H2
Hypervisor learns source port to path mapping
Dst | SPort
H2 | P1
H2 | P2
H2 | P3
H2 | P4
H1 to H2
DPort: Fixed
SPort: P1
Overlay
Data
H1 to H2
DPort: Fixed
SPort: P2
Overlay
Data
H1 to H2
DPort: Fixed
SPort: P3
Overlay
Data
H1 to H2
DPort: Fixed
SPort: P4
Overlay
Data
H1
H2
Load balancing flowlets
vSwitch Load balancing
Outer transport source port (with ECMP) maps to network path
ECMP-based source routing

## Slide 11
Load balancing flowlets
Scheme 1: Edge-Flowlet
vSwitch
vSwitch
Eth
IP
TCP src P1
Overlay
Data
Eth
IP
TCP src P2
Overlay
Data
Dst | SPort
H2 | P1
H2 | P2
H2 | P3
H2 | P4
H2
H1
Flowlet gap
Eth
IP
TCP src
P3
Overlay
Data
Eth
IP
TCP src
P4
Overlay
Data
Path Discovery
vSwitch Load balancing

## Slide 12
Dst | SPort | Wt
H2 | P1 | 0.25
H2 | P2 | 0.25
H2 | P3 | 0.25
H2 | P4 | 0.25
Path weight table
Data
Dst | SPort | Wt
H2 | P1 | 0.1
H2 | P2 | 0.3
H2 | P3 | 0.3
H2 | P4 | 0.3
2. Switches mark ECN on data packets
vSwitch
vSwitch
Hypervisor H1
Hypervisor H2
1. Src vSwitch detects and forwards flowlets
3. Dst vSwitch relays ECN and src port to src vSwitch
5. Src vSwitch adjusts path weights for the src port
4. Return packet carries ECN and src port for forward path
vSwitch Load balancing
Scheme2: CLOVE-ECN
Path Discovery
Load balancing flowlets
Congestion-aware balancing based on ECN feedback

## Slide 13
vSwitch Load balancing
Scheme 3: CLOVE-INT
Load balancing flowlets
Path Discovery
Data
Dst | SPort | Util
H2 | P1 | 40
H2 | P2 | 30
H2 | P3 | 50
H2 | P4 | 10
2. Switches add requested link utilization
vSwitch
vSwitch
Hypervisor H1
Hypervisor H2
1. Src vSwitch adds INT instructions to flowlets
3. Dst vSwitch relays path utilization and src port to src vSwitch
5. Src vSwitch updates path utilizations
4. Return packet carries path utilization for forward path
6. Src vSwitch forwards flowlets on least utilized paths
Utilization-aware balancing based on INT feedback

## Slide 14: Performance evaluation setup
2-tier leaf-spine symmetric topology
Web Search Workload
Client on Leaf1 <-> server on Leaf2
Measure Average Flow Completion Time (FCT)
Compare Edge-Flowlet and Clove-ECN to ECMP, MPTCP and Presto
…
…
16 Clients
Spine1
Spine2
Leaf1
4 x 40 Gbps
16 x 10 Gbps
16 Servers
Leaf2
Asymmetric Setup

## Slide 15: Symmetric topology
Better
2.5x
1.8x
…
…

## Slide 16: Asymmetric topology
Better
5x
12x
…
…

## Slide 17: Incast Workload
CLOVE-ECN outperforms MPTCP on Incast Workloads
Better

## Slide 18: NS2 Simulation with CONGA – Asymmetric
1.2x higher FCT than CONGA
CLOVE-ECN captures 80% of the performance gain between ECMP and CONGA
3x lower FCT than ECMP
Better
…
…

## Slide 19: CLOVE highlights
Captures 80% of the performance gain of CONGA
No changes to network hardware, VMs, applications
Adapts to asymmetry within the data plane
Scalable due to distributed state

## Slide 20
THANK YOU
Questions?

## Slide 22: Parameter Sweeping
Empirical values for (flowlet-threshold, ECN-threshold) are 1RTT, 20pkts