## Slide 1: Contra: A Programmable System for Performance-aware Routing
Kuo-Feng Hsu*, Ryan Beckett#, Ang Chen*, Jennifer Rexford+, Praveen Tammana+, David Walker+
Rice University*, Microsoft Research#, Princeton University+
Notes: Thank you for the inducing, XXX. In this talk, I'll describe Contra. Contra is a system that can generate performance-aware routing protocols from high-level policies

## Slide 2: Motivation: Performance-aware routing
G2: Routing Constraints
G1: Traffic Engineering
G3: Fast Adaptation
e.g., prefer least utilized paths
e.g., middlebox traversal
e.g., update path choices upon performance changes
"routing constraints" to "flexibility/generality", then it's not very clear
writing “topology + routing”? Then when explaining (e.g., Hula) we can mention that both topology and routing are fixed. And then in the next part the routing constraints would still make sense.
Notes: Modern applications send a lot of data over the network. So efficient routing is very important.
Typically, we can think of three common goals
Performance and therefore we need traffic engineering. For example, …
Prefer certain route and therefore we have routing constraints. For example, …
Network condition changes very fast and therefore we need fast adaptation. For example, …

## Slide 3: State of the art
G2: Routing Constraints
G1: Traffic Engineering
G3: Fast Adaptation
Some systems focus on G1 and G3
  E.g., Hula (Katta-SOSR’16), Conga (Alizadeh-SIGCOMM'14)
  Load balancing at RTT timescales (e.g., using P4)
  Cannot support routing constraints; not applicable to arbitrary topologies

## Slide 4: State of the art
Other systems focus on G1 and G2
  E.g., Merlin (Soulé-CoNEXT'14)
  Support path constraints (in the form of regular expressions)
  Control plane solutions; adapt slowly
G2: Routing Constraints
G1: Traffic Engineering
G3: Fast Adaptation

## Slide 5: Key question: One system for all three goals?
Notes: Considering a network between sender and receiver.
We may want to avoid path with congestion by finding another path

## Slide 6: Key question: One system for all three goals?
Avoiding paths with low performance
Notes: in the meantime, we also want to make sure the traffic to go through a firewall.

## Slide 7: Key question: One system for all three goals?
Avoiding paths with low performance
Satisfying routing constraints
Notes: Also, when paths with higher performance become available, we may also want to change the paths

## Slide 8: Key question: One system for all three goals?
Avoiding paths with low performance
Satisfying routing constraints
Adapting to changes quickly
Challenging … but Contra achieves all these!
Notes: (Don’t say complicated) As you can see, achieving all the above is quite challenging

## Slide 9: Contra at 10,000 feet
Language + Compiler: Compiles rich, high-level policies
Runtime: Performance-aware routing protocols that run in the data plane
Policy
Topology
Switch programs
Contra
Notes: Now, let me give you an overview of Contra.

## Slide 10: Outline
Motivation: Performance-aware routing
  Existing work
  Contra overview
Our system
  Policy language
  Compilation
  Distance vector protocol
Evaluation
Conclusion
Notes: So far, I have told you about the motivation for performance-aware routing, Next, I will describe how Contra works in the rest of this talk.

## Slide 11: Example policy: Waypointing + load balancing
The Contra language has two components
  Path constraints using regular expressions (e.g., .*(F1 + F2).*)
  Performance metrics (e.g., path utilization)
if .*(F1 + F2).*
then path.util
else
Path Constraints
Metrics
S
D
F1
X
F2
Notes: To see a concrete policy example Contra can support, consider this network topology where we want to have waypointing and load balancing.
By way pointing, we want to forward traffic through either F1 or F2 but not X.
In the meantime, we also want to balance the traffic between the feasible paths.

## Slide 12: Contra language syntax
A policy maps paths to ranks based on their performance
Notes: This is the syntax of Contra; the details are not important. But a policy is just a function that maps paths to rankings based on their metrics.

## Slide 13: Contra can support many policies
More examples and detailed discussions in our paper
Shortest Path: path.len
S
D
Least Utilized: path.util
Source-local preference:
if X.* then path.util else path.len
S
D
X
D
Y
Widest Shortest Path: (path.len, path.util)
S
D
Notes: With this language, contra can support many useful policies.
For examples, user can simply write down a single metric like path DOT len to implement shortest path, and path DOT util to implement least utilized path.
Users can also write path.len comma path.util to implement a widest shortest path policy which prefers shortest paths first, and among all shortest paths, it picks the least utilized one.
Even more with regular expressions, users can even specify different metrics for different types of paths.

## Slide 14: How can we compile the policies to switch programs?
Policy analysis
  1. Convert regular expressions in the polices to automata
  2. Merge automata with topology into an intermediate representation (IR)
Routing protocol
  3. Define routing protocols based on the IR
  4. Synthesize P4 programs which track policy states
Topology
Routing Protocols
Automata
Probe
Data
Intermediate Representation

## Slide 15: Policy analysis
Product graph = automata + topology (Merlin)
Every PG path is a policy-compliant path in the topology
0
3
D
1
2
B
A
0
2
D
1
The automata
if ABD then 0
else if B.*D then path.util
else
The routing policy
D
A
B
C
The network topology
Product graph (PG)
D0
C0
A0
B0
A1
B1
Notes: Abstract policy with graph data structure

## Slide 16: Defining routing protocols on the PG
Goal: Discovering the best paths at runtime
  Destinations send probes, which carry performance metrics
  Nodes update forwarding decisions to choose the best paths
Basically, Contra generates distance vector protocols on the PG
D0
C0
Product graph (PG)
A0
B0
A1
B1
Probe
Data
Dst | bestNxt | Metric
D0 | C0 | 0.8
At node B0
Notes: Because of this property (previous slide), we can now define a routing protocol without violating the path constraint.
To discover the best paths, first, nodes send probes to each other.
during the probe propagation, switches keep tables to always remember the best next hop to a destination and the performance metrics.
Across switches, these tables will form best paths to each for a given destination
(Don’t say Normal)

## Slide 17: Tracking policy states in data plane
Goal: Ensuring the discovered paths are policy-compliant
  Switches encode the PG into tables
  PG states are tagged to packet headers
  Switches update PG tags as they forward packets
D
A
B
C
Routing
D0
C0
The product graph
A0
B0
A1
B1
D0
B1
At node B0
Dst | bestNxt | Metric
D0 | C0 | 0.8
Current
B0
D0 | D0 | 0.7
B1
At switch B
Notes: To ensure the switch implementation follows the product graph and therefore ensure the discovered paths are policy-compliant
We encode the PG into tables on switches.
Since one switch can correspond to multiple PG nodes, we combine their forwarding tables into one.
We need to tag the packets with correct PG states in order to track the state transition.
For example, a path on PG corresponds to a path on network topology.
When packets from node A with tag B1 arrive switch B, switch B can update the tag correctly based on the table.

## Slide 18: Let's see an example!
A simple policy (i.e., least-utilized) over a tree-like topology
All paths are policy-compliant, i.e., no path constraints
Contra would generate a "Hula-like" policy
S
D
A
B
0.1
0.2
0.1
0.1
Probe
Data
Notes: Let’s take a look at a simple example, where we use least utilized policy over a structured topology.
Actually, in this particular scenario, Contra would generate the protocols that are very similar to an existing work called Hula, which I briefly mentioned before. There are some important differences, of course: Hula is specialized only for this policy and topology, but Contra can be programmed to target a wide range of scenarios.

## Slide 19: Handling changing metrics: Loops
Problem 1: Transient loops
   Use sequence numbers in probes (DSDV, Perkins-SIGCOMM ‘94)
D
A
B
C
D
A
B
C
Time = 1
Time = 2
D
A
B
C
Time = 1.5
1
1
1
2
2
2
Probe
Data
Notes: ONE REASON FOR THIS (as there are many reasons that may cause loops) is because probes take time to propagate. So the views of different switches may not be synced in transient states.
this is a common problem with DV protocols *ON GENERAL TOPOLOGIES!* Notice that Hula is specialized for structured topology so it doesn’t have this problem.
So we borrow idea from …
Seq to distinguish probes from diff round
So that we can mitigate transient loops
note that since the network is still async, this does not provide hard guarantees that it eliminates loops; but empirically, this mitigates transient loops very effectively

## Slide 20: Handling changing metrics: Out-of-order delivery
Problem 2: Out-of-order delivery
   Group packets in the same flow into flowlets (FLARE, Sinha-HotNets'04; HULA)
1
2
3
4
4
3
2
1
…
1
3
2
4
…
4
3
2
1
…
FlowID | next
Flowlet switching table
Notes: Changing metrics can raise problems, and we borrow ideas from existing works to solve them
Idea from wireless network routing
Flowlet solves the oscillation problem

## Slide 21: Handling change metrics: Policy violation by flowlets
Problem 3: Flowlet switching might cause policy violations!
  Root cause: Asynchronous expiration of flowlet entries
  E.g., Source picks a different route for new flowlet
  But the middle switch may still pin the flowlet to the upper path
   Policy-aware flowlet switching (extending flowlet switching tables with PG states)
A
C
S
E
B
F
D
Time = 1
Time = 2
FlowID | next
PG state
Flowlet switching table
Notes: traditional flowlet switching can cause policy violation.

## Slide 22: Contra handles many other challenges
Detailed discussions on challenges in our paper
Challenge | Key idea
Reducing transient loops | Sequence numbers
Out-of-order delivery | Policy-aware flowlets
Mitigating view inconsistency | Limited probe frequency
Detecting failures | Routing entry expiration
Multiple metrics | Policy decomposition
Breaking transient loops | Data plane loop detection

## Slide 23: Outline
Motivation: Performance-aware routing
  Existing work
  Contra overview
Our system
  Policy language
  Compilation
  Distance vector protocol
Evaluation
Conclusion

## Slide 24: Evaluation setup
Compiler prototype
  7485 LoC, in F#
  Compiles to bmv2
Experimental environments
  NS3 simulation (w/ bmv2 support)
  Mininet emulation (CloudLab)
Several types of topologies:
  Fattrees, and arbitrary topologies (e.g., Abilene)
Workloads:
  Web search (Alizadeh-SIGCOMM’15), Cache (Roy-SIGCOMM’15)
Fattree
Abilene

## Slide 25: How scalable is the Contra compiler?
The compilation finishes in a few seconds!
  Policy P1: contains a single metric
  Policy P2: contains multiple metrics
  Policy P3: contains regular expressions
Runs before the deployment, not in “critical path”
Lower is better
4
2
0
20
125
405
500
245
Fattree size (# of switches)
Compilation time (s)
P3
P2
P1
Notes: on fattree topologies OF DIFFERENT SIZES
Compilation is done before runtime.

## Slide 26: How competitive is Contra against hand-crafted solutions?
Performance metric: Flow completion time
  Baseline 1 (ECMP): Performance-oblivious static load balancing
  Baseline 2 (Hula): Hardcodes a "least-utilized" policy
  Contra: Implements a Hula-like policy
Lower is better
Symmetric Fattree
100
50
0
100
80
60
40
20
Network load (%)
Average FCT (ms)
ECMP
Hula
Contra
Asymmetric Fattree (with failure)
300
200
100
0
100
80
60
40
20
Network load (%)
Average FCT (ms)
ECMP
Hula
Contra
Notes: Summarize key findings in terms of Contra/Hula vs. ECMP in FCT.
Both Contra and Hula are performance-aware routing so they can outperform ECMP by avoiding congestion and therefore shortening the flow competition time. And the benefits are particularly significant when the network load is high

## Slide 27: How about arbitrary topologies?
Note: ECMP and Hula only work for structured network topologies
Baseline 1 (Shortest paths): Without load balancing
Baseline 2 (SPAIN): Static load balancing over multiple paths (Mudigonda-NSDI’10)
Contra: Implements a “least-utilized” policy for this topology
Lower is better
250
150
50
20
40
60
80
100
Network load (%)
Average FCT (ms)
Shortest paths
SPAIN
Contra

## Slide 28: How often do we see transient loops?
Policy: Least utilized paths. Topology: Fattree
% of packets that traverse shortest vs. non-shortest paths vs. loops
Contra picks non-shortest paths when they have lower congestion
Transient loops do exist, but they are rare!
Shortest: 83.4%
Loop: 0.02%
Non-shortest:
16.6%
Notes: Another important question is how effective can Contra mitigate the loops.
We use least utilized paths policy on a fattree.
And count the number of packets experiencing loops and longer paths and shortest paths.
We found that most packets are using shortest path.
But, some packets use non-shortest path, because the policy itself prefer these paths when they have lower congestion.
Finally, the transient loops do exist, bt they are rare. This shows that Contra can mitigate loops effectively.
Notice that the loops are transient so no packets are caught permanently in a loop.

## Slide 29: See more evaluation results in our paper
How scalable is the Contra compiler?
How competitive is Contra in its performance?
How often and severe are transient loops and longer paths?
How much memory overhead does Contra incur?
How much communication overhead does contra incur?
How well does Contra balance load?
How fast can Contra react to failures?

## Slide 30: Conclusion
Motivation: Performance-aware routing
Our system: Contra
  Programmable: Sophisticated policies
  General: Arbitrary topologies
  Responsive: RTT-timescale adaptations
Evaluation:
  Competitive with hand-crafted solutions
  Supports many useful policies
  Runs entirely in the data plane
Notes: I introduced the three goals of performance-aware routing
The existing works cannot be easily extended to support all of them.
So we proposed Contra,
It can support many policies on arbitrary topologies
Evaluation shows that Contra is scalable and is competitive with hand-crafted solution.
Thank you for your ATTENTION. I am happy to take any question.