## Slide 1
Central Control over Distributed Routing
fibbing.net
SIGCOMM
Stefano Vissicchio
18th August 2015
UCLouvain
Joint work with
O. Tilmans (UCLouvain), L. Vanbever (ETH Zurich) and J. Rexford (Princeton)

## Slide 2
SDN
(e.g., OpenFlow, Segment Routing)
Traditional
(e.g., IGP, distributed MPLS)
SDN is based on antithetical architecture
with respect to traditional networking
Notes: The recent and growing interest to Software Defined Networking makes it clear that operators want networks to be centrally controlled.
This constitutes a huge difference with the traditional networking model, which is based on tweaking the behavior of distributed protocols.
SDN is indeed taking the completely opposite approach, promoting a fully-centralized architecture.
[talk about the controller]

## Slide 3
Centralization improves network management,
but sacrifices robustness of distributed protocols
Manageability
Flexibility
Scalability
Robustness
SDN
ad hoc
low
highest
high
Traditional
IGP, tunnelling (RSVP-TE)
by design
high
low
low
Notes: Centralization as proposed by SDN comes with multiple advantages.
Prominently, it leads to improved manageability, through a high-level interface for operators to configure their networks, and higher flexibility, in terms of packet processing.
On the flip side, SDN also comes with downsides and challenges.
Mainly, centralization sacrifices the robustness and scalability of the current distributed protocols.

## Slide 4
We propose Fibbing, a hybrid SDN architecture
Fibbing
central control over link-state IGPs
Notes: We propose an architecture which is partially centralized and partially distributed.
The architecture is based on Fibbing, that consists in applying central control over a distributed protocol.
We applied this techniques to control intra-domain routing.

## Slide 5
Manageability
Flexibility
Scalability
Robustness
SDN
ad hoc
low
highest
high
Traditional
IGP, tunnelling (RSVP-TE)
by design
high
low
low
Fibbing
by design
high
high
high
Fibbing combines advantages
of SDN and traditional networking
Notes: By centralizing the decisions and coordinating a distributed protocol, we show that Fibbing combines the advantages of traditional and SDN approaches.
In particular…

## Slide 6
Manageability
Flexibility
Scalability
Robustness
Fibbing
by design
high
high
high
same as SDN
per-destination
full control
thanks to partial distribution
some function
are distributed
Fibbing combines advantages
of SDN and traditional networking
Notes: More precisely, …

## Slide 7
Central Control over Distributed Routing
fibbing.net
Manageability
1
Scalability
2
Flexibility
3
Robustness
4
Notes: In the rest of the talk, I will explain how Fibbing achieves high manageability, flexibility, scalability and robustness, addressing each of those features one by one.

## Slide 8
Central Control over Distributed Routing
fibbing.net
Manageability
1
Scalability
2
Flexibility
3
Robustness
4
Notes: Let me start with manageability, for which I will actually overview the Fibbing architecture.

## Slide 9
SDN achieves high manageability
by centralizing both computation and installation
derives FIB entries
install FIB entries
computes paths
requirements
e.g., OpenFlow
controller or RCP
Notes: From an architectural viewpoint, Fibbing is very close to SDN.
You have probably seen this slides multiple times already.
This is a classic SDN architecture, with data-plane devices programmed by a network controller.
Manageability here comes from the fact that the controller exposes a high-level interface to operators.
The controller is then responsible for both computing packet processing based on operators’ requirements and installing the corresponding rules on devices (typically one by one).

## Slide 10
Fibbing is as manageable as SDN,
but centralizes only high-level decisions
Fibbing
controller
computes paths
requirements
Notes: Fibbing relies on a similar approach, still keeping network-wide control centralized. So, the operator can still talk to a centralized controller, hence achieving the same manageability as SDN. What actually changes is the implementation of operators’ requirements. Indeed, the Fibbing controller centralizing only computation of packet processing (e.g., forwarding paths).

## Slide 11
Fibbing keeps installation distributed,
relying on distributed protocols
distributed
control-plane
install FIB entries
computes FIB entries
data-plane
Notes: However, the actual computation of FIB entries and their installation on data-plane devices is done by a distributed control-plane run on the network.

## Slide 12
Distributed installation is controlled
by injecting carefully-computed information
control-plane
messages
Notes: For the distributed control-plane to install FIB entries realizing the paths computed by the controller, the controller injects properly-computed messages in the distributed control-plane.
In our work, we then focus on determining which messages to inject to control the distributed control-plane.

## Slide 13
We study which messages to inject
for controlling intra-domain routing protocols
forwarding
paths
weighted
topology
shortest-path
computation
link-state IGP
input
function
output
Notes: In particular, we focused on link-state IGPs, that is the shortest-path based routing protocols used for intra-domain routing.
Our work is based on the observation that IGPs can be actually seen (e.g., by the controller) as a function, which computes forwarding paths from information about the network topology, represented as a weighted graph.
The applied function is basically Dijkstra.

## Slide 14
The output of the controlled protocol
is specified by operators’ requirements
forwarding
paths
weighted
topology
shortest-path
computation
input
function
provided by operators
or controller optimizers
(e.g., DEFO)
link-state IGP
output
Notes: In particular, we focused on link-state IGPs, that is the shortest-path based routing protocols used for intra-domain routing.
Our work is based on the observation that IGPs can be actually seen (e.g., by the controller) as a function, which computes forwarding paths from information about the network topology, represented as a weighted graph.
The applied function is basically Dijkstra.

## Slide 15
Inverse
To control IGP output, the Fibbing controller
inverts the shortest-path function
forwarding
paths
weighted
topology
shortest-path
computation
Notes: In particular, we focused on link-state IGPs, that is the shortest-path based routing protocols used for intra-domain routing.
Our work is based on the observation that IGPs can be actually seen (e.g., by the controller) as a function, which computes forwarding paths from information about the network topology, represented as a weighted graph.
The applied function is basically Dijkstra.

## Slide 16
Central Control over Distributed Routing
fibbing.net
Manageability
1
Scalability
2
Flexibility
3
Robustness
4

## Slide 17
A
B
C
destination
source
Consider this simple network
(implemented with Cisco routers)
D1
D2
X
Notes: to understand Fibbing flexibility, let me first introduce how Fibbing works.
Consider the example in the figure. [describe example]

## Slide 18
A
B
C
X
An IGP control-plane computes
shortest paths on a shared weighted topology
D1
D2
control-plane
3
1
1
10
shortest paths

## Slide 19
IGP shortest paths are translated into
forwarding paths on the data-plane
D1
D2
data-plane
traffic flow
A
B
C
X
A
B
C
X
D1
D2
control-plane
3
1
1
10
Notes: Let’s consider the example network in the figure.
[Describe the figure]

## Slide 20
In Fibbing, operators can ask
the controller to modify forwarding paths
requirement
(C,A,B,X,D2)
A
B
C
X
D1
D2
3
1
1
10

## Slide 21
The Fibbing controller injects information on
fake nodes and links to the IGP control-plane
node V1,
link (V1,C),
map (V1,C) to (C,A)
A
B
C
X
D1
D2
3
1
1
10
requirement
(C,A,B,X,D2)

## Slide 22
Informations are flooded
to all IGP routers in the network
node V1,
link (V1,C),
map (V1,C) to (C,A)
A
B
C
X
D1
D2
3
1
1
10
requirement
(C,A,B,X,D2)

## Slide 23
Fibbing messages augment
the topology seen by all IGP routers
1
D2
node V1,
link (V1,C),
map (V1,C) to (C,A)
A
B
C
X
D1
D2
3
1
1
10
V1
requirement
(C,A,B,X,D2)

## Slide 24
Augmented topologies translate
into new control-plane paths
A
B
C
X
D1
D2
3
1
1
10
requirement
(C,A,B,X,D2)
1
D2
V1
node V1,
link (V1,C),
map (V1,C) to (C,A)

## Slide 25
Augmented topologies translate
into new data-plane paths
A
B
C
D1
D2
X
A
B
C
X
D1
D2
3
1
1
10
1
D2
V1
node V1,
link (V1,C),
map (V1,C) to (C,A)
requirement
(C,A,B,X,D2)
Notes: - add requirement
- move at the beginning of flexibility section

## Slide 26
Theorem
Fibbing can program
arbitrary per-destination paths
Any set of forwarding DAGs can be enforced by Fibbing

## Slide 27
Fibbing can program
arbitrary per-destination paths
paths to the same destination do not create loops
Theorem
Any set of forwarding DAGs can be enforced by Fibbing

## Slide 28
By achieving full per-destination control,
Fibbing is highly flexible
fine-grained traffic steering (middleboxing)
per-destination load balancing (traffic engineering)
backup paths provisioning (failure recovery)
Theorem
Any set of forwarding DAGs can be enforced by Fibbing

## Slide 29
Central Control over Distributed Routing
fibbing.net
Manageability
1
Scalability
2
Flexibility
3
Robustness
4

## Slide 30
We implemented a Fibbing controller
network
topology
+
path
reqs.
per-destination
forwarding DAGs
augmented
topology
reduced topology
running
network
Compilation
Augmentation
Optimization
Injection/
Monitoring

## Slide 31
We also propose algorithms
to compute augmented topologies of limited size
network
topology
+
path
reqs.
per-destination
forwarding DAGs
augmented
topology
reduced topology
running
network
Compilation
Augmentation
Optimization
Injection/
Monitoring
compilation
heuristics
per-destination
augmentation
cross-destination
optimization

## Slide 32
network
topology
+
path
reqs.
per-destination
forwarding DAGs
augmented
topology
reduced topology
running
network
Compilation
Augmentation
Optimization
Injection/
Monitoring
compilation
heuristics
per-destination
augmentation
simple
merger
cross-destination
optimization
For our Fibbing controller, we propose
algorithms to be run in sequence

## Slide 33
A
B
C
D
E
F
1
1
10
100
1
1
original shortest-path
“down and to the right”
Consider the following example,
with a drastic forwarding path change
A
B
C
D
E
F
100
1
1
10
1
1
desired shortest-path
“up and to the right”

## Slide 34
A
B
C
D
E
F
100
1
1
10
1
1
1
1
1
1
1
Simple adds one fake node for every
router that has to change next-hop
1

## Slide 35
1
1
1
Merger iteratively merges fake nodes
(starting from Simple’s output)
A
B
C
D
E
F
100
1
1
10
1
1
1
1

## Slide 36
1
1
1
A
B
C
D
E
F
100
1
1
10
1
1
1
Merger iteratively merges fake nodes
(starting from Simple’s output)

## Slide 37
This way, Merger programs multiple
next-hop changes with a single fake node
A
B
C
D
E
F
100
1
1
10
1
1
1
Notes: note that this is more powerful than configuring nodes one-by-one

## Slide 38
A
B
C
D
E
F
100
1
1
10
1
1
1
Previous SDN solutions (e.g., RCP) cannot do the same
This way, Merger programs multiple
next-hop changes with a single fake node
Notes: note that this is more powerful than configuring nodes one-by-one

## Slide 39
Simple and Merger achieve different trade-offs
in terms of time and optimization efficiency
and up to 90% with cross-destination optimization
Merger reduces fake nodes by up to 50%
Merger takes 0.1 seconds
Simple runs in milliseconds
We ran experiments on Rocketfuel topologies,
with at least 25% of nodes changing next-hops

## Slide 40
We implemented the machinery to
listen to OSPF and augment the topology
network
topology
+
path
reqs.
per-destination
forwarding DAGs
augmented
topology
reduced topology
running
network
Compilation
Augmentation
Optimization
Injection/
Monitoring
OSPF interaction
module

## Slide 41
Experiments on real routers show that
Fibbing has very limited impact on routers
router
memory (MB)
# fake
nodes
1 000
5 000
10 000
0.7
76.0
153
50 000
100 000
6.8
14.5
DRAM is cheap
>> # real routers

## Slide 42
Experiments on real routers show that
Fibbing has very limited impact on routers
1 000
5 000
10 000
router
memory (MB)
0.7
76.0
153
50 000
100 000
6.8
14.5
# fake
nodes
DRAM is cheap
CPU utilization always under 4%

## Slide 43
Experiments on real routers show that
Fibbing does not impact IGP convergence
Upon link failure, we registered no difference in the (sub-second) IGP convergence with
up to 100,000 fake nodes and destinations
no fake nodes

## Slide 44
Experiments on real routers show that
Fibbing achieves fast forwarding changes
installation
time (seconds)
0.9
44.7
89.50
4.5
8.9
894.50 μs/entry
# fake
nodes
1 000
5 000
10 000
50 000
100 000

## Slide 45
Central Control over Distributed Routing
fibbing.net
Manageability
1
Scalability
2
Flexibility
3
Robustness
4

## Slide 46
Fibbing improves robustness
by relying on the underlying IGP
thanks to its shared topology
see paper
IGP provides fast failure detection and control-plane sync
IGPs re-converge quickly [Filsfils07]
no controller action needed in some cases
Fibbing supports fail-open and fail-close semantics

## Slide 47
D2
V1
A
B
C
X
We ran a failure recovery case study,
with distributed Fibbing controller
D1
D2
( fail-open(D2) );
( fail-close(D1) );
Notes: update performance graph

## Slide 48
Fibbing survives replica failures
with no impact on forwarding
D2
V1
A
B
C
X
D1
D2
( fail-open(D2) );
( fail-close(D1) );
Notes: update performance graph

## Slide 49
Fibbing reacts to network failures
quickly re-optimizing forwarding
A
B
C
X
D1
D2
( fail-open(D2) );
( fail-close(D1) );
Notes: update performance graph

## Slide 50
Fibbing reacts to partitions,
respecting fail-close and fail-open semantics
A
B
C
X
D1
D2
( fail-open(D2) );
( fail-close(D1) );
Notes: update performance graph

## Slide 51
Fibbing recovers correctly
(as soon as failures are fixed)
D2
V1
A
B
C
X
D1
D2
( fail-open(D2) );
( fail-close(D1) );
Notes: update performance graph

## Slide 52
Fibbing shows the benefits of
central control over distributed protocols
heavy work is still done by routers
avoids SDN deployment hurdles
Simplify controllers and improves robustness
network-wide automated control
Realizes SDN management model
Works today, on existing networks

## Slide 53
Stefano Vissicchio
stefano.vissicchio@uclouvain.be
Tell me lies, tell me sweet little lies
— Fleetwood Mac
Central Control over Distributed Routing
fibbing.net