## Slide 1: It Takes Two to Tango: Cooperative Edge-to-Edge Routing
Henry Birge-Lee
Maria Apostolaki, and Jennifer Rexford

## Slide 2: Is today's Internet is good enough for real-time applications?

## Slide 3: Network performance is offered as a paid service
Edge computing: performance-critical services placed close to edge networks
Network-as-a-Service (NaaS): on-demand products offering reliable, reserved bandwidth point-to-point links.

## Slide 4: Network performance is offered as a paid service increasing consolidation

## Slide 5: Network performance is offered as a paid service increasing consolidation
AWS:
Google:
Only hypergiants can afford vast numbers of edge nodes

## Slide 6: Network performance is offered as a paid service increasing consolidation
AWS:
Google:
Packet Fabric:
Only hypergiants can afford vast numbers of edge nodes
Network-as-a-Service can get pricey

## Slide 7: What would it take for the Internet to serve real-time apps?

## Slide 8: What would it take for the Internet to serve real-time apps?
path diversity

## Slide 9: Traditional Internet Routing (BGP) does not expose all paths
  Edge 1 only has a single upstream thus a single path exported by AS 5
AS 2
AS 4
AS 1
Edge 2
AS 5
Edge 1
AS 3

## Slide 10: Traditional Internet Routing (BGP) does not expose all paths
  Edge 2 is multi-homed but only influences a single hop, not the whole route
AS 2
AS 4
AS 1
Edge 2
AS 5
Edge 1
AS 3

## Slide 11: What would it take for the Internet to serve real-time apps?
path diversity
accurate measurement

## Slide 12: Edge networks can’t reliably measure performance of different paths
Edge

## Slide 13: Edge networks can’t reliably measure performance of different paths
Edge

## Slide 14: Edge networks can’t reliably measure performance of different paths
Edge
  An edge network only sees round-trip-time (RTT) not one-way-delay

## Slide 15: Edge networks can’t reliably measure performance of different paths
Edge
  An edge network only sees round-trip-time (RTT) not one-way-delay
  RTT includes edge network delays

## Slide 16: Edge networks can’t reliably measure performance of different paths
Edge
  An edge network only sees round-trip-time (RTT) not one-way-delay
  RTT includes edge network delays
  RTT monitoring requires understanding end host and L4 protocol behavior

## Slide 17: What would it take for the Internet to serve real-time apps?

## Slide 18: What would it take for the Internet to serve real-time apps?
Tango

## Slide 19: What would it take for the Internet to serve real-time apps?
Tango
AS 2
AS 4
AS 1
Tango
AS 5
Tango
AS 3
Cooperative edge-to-edge routing with Tango

## Slide 20: Cooperative edge-to-edge routing with Tango
Path diversity:
Edges collaboratively use BGP tricks to coax additional paths out of the Internet core

## Slide 21: Exposing path diversity through cooperation
Destination Tango nodes can announce multiple IP prefixes along different paths using BGP communities
Source Tango node can select which path to use by selecting a prefix to reach the destination
AS 2
AS 4
AS 1
Edge 2
AS 5
Edge 1
AS 3
abcd:1::/48 abcd:2::/48 abcd:3::/48 abcd:4::/48

## Slide 22: Cooperative edge-to-edge routing with Tango
Path diversity:
Edges collaboratively use BGP tricks to coax additional paths out of the Internet core
Accurate Measurements:
protocol-agnostic monitoring by encapsulating packets with Tango headers
one-way measurements by monitoring at two ends
edge-to-edge measurements by measuring before the access-network uncertainty

## Slide 23: Improved measurements through cooperation
Programmable Switches at the edge of the Internet can add a measurement header
Measurements only include one-way, wide-area component
Measurements do not rely on application behavior
Tango
Tango

## Slide 24: Cooperative edge-to-edge routing with Tango
Path diversity:
Edges collaboratively use BGP tricks to coax additional paths out of the Internet core
Accurate Measurements:
protocol-agnostic monitoring by encapsulating packets with Tango headers
one-way measurements by monitoring at two ends
edge-to-edge measurements by measuring before the access-network uncertainty
Incremental deployment:
Two edge switches work together without cooperation from the core

## Slide 25: Our Tango prototype is real
Made BGP announcements with communities to explore available paths
Found 4 paths in each direction between LA and NY datacenters
Used eBPF to attach measurement headers and measure one-way-delays

## Slide 26: BGP default path had 30% higher latency than optimal path
Default BGP path
Path found wit Tango

## Slide 27: Periods of network instability can be avoided
Alternate Stable Path
Period of Instability

## Slide 28: Conclusion
Two ends cooperatively can get more out of the Internet
  Path diversity through hacking BGP communities
  Accurate measurements through edge-to-edge monitoring
Preliminary results show the advantage of dynamically optimizing routing
Tango

## Slide 29: Questions?
Thank you for your time
Henry Birge-Lee
birgelee@princeton.edu