## Slide 1: Securing Internet Applications from Routing Attacks
Jennifer Rexford
Notes: The Internet’s routing system is notoriously insecure, allowing adversaries to launch attacks that discard traffic, impersonate a service, or perform eavesdropping. Yet, a strategic adversary can do so much more damage by launching application-specific routing attacks on critical Internet applications like certificate authorities, anonymity systems like Tor, and the bitcoin network. In this talk, I examine these application-specific routing attacks, and show how we can readily deploy application-level defenses to protect critical applications as we continue toward the important long-term goal of securing the Internet routing system.

## Slide 2: Interdomain Routing Security
Border Gateway Protocol (BGP)
  Vulnerable to attack and misconfiguration
  Attacks affecting availability and confidentiality
  Yet, deploying BGP security solutions is hard
Notes: The Border Gateway Protocol (BGP) is the glue that holds the Internet together by propagating information about how to reach destinations in remote networks. However, BGP is notoriously vulnerable to misconfiguration and attack. The consequences range from making destinations unreachable to misdirecting traffic through unexpected intermediaries. Efforts to secure the Internet routing system have been underway for many years, but the pace of progress is slow since many parties must agree on solutions and cooperate in their deployment.

## Slide 3: Application Security
Security-sensitive applications
  Use cryptography to protect end users
  Rely on the underlying network to deliver data
  Treat the network as a “dumb pipe”… but should they?
Notes: In the meantime, more and more users rely on the Internet to access a wide range of services, including applications
with security and privacy concerns of their own. Applications such as Tor (The Onion Router) allow users to browse
anonymously, certificate authorities provide certificates for secure access to web services, and blockchain supports secure
cryptocurrencies. However, the privacy and security properties of these applications depend on the network to deliver traffic; Application developers abstract away the details of Internet routing, but BGP does not provide a sufficiently secure scaffolding for these applications.

## Slide 4: Cross-Layer Routing Attacks
Notes: This gap leaves the vulnerabilities due to routing insecurity significantly underestimated. In fact, routing attacks on Internet applications can have devastating consequences for users -- including uncovering users (such as political dissidents) trying to communicate anonymously, impersonating websites even if the traffic uses HTTPS, and stealing cryptocurrency. Instead, the security of Internet applications and the network infrastructure should be considered together, as vulnerabilities in one layer lead to broken assumptions (and new vectors for attacks) in the other.

## Slide 5: Simple BGP Prefix Hijack
1
2
3
4
5
6
7
12.34.0.0/16
12.34.0.0/16: (1)
Notes: To set the stage for discussing strategic BGP attacks, let’s briefly review some common attacks on BGP. The simplest attack (sometimes caused accidentally by configuration mistakes) is a prefix hijack, where an adversary AS erroneously announces an IP prefix belonging to another AS. <Review attack.> The attack causes an availability problem for a portion of the Internet, or it may allow the adversary to impersonate an Internet service. Fortunately, the problem is relatively easy to detect, and to prevent.

## Slide 6: Forged Origin AS
1
2
3
4
5
6
7
12.34.0.0/16
12.34.0.0/16: (1 6)
Forged origin AS!
Notes: Simple BGP security solutions would notice that AS does not actually “own” the IP prefix and, as such, should not originate the prefix into BGP. A smarter adversary can evade these security techniques by adding the AS number of the legitimate AS to the end of the ASPATH. The path gets slightly longer, so some ASes may now prefer the legitimate route over the longer bogus route. Still, the effects are still pretty noticeable with a sizeable fraction of the Internet routing to the wrong place.

## Slide 7: Path Poisoning
1
2
3
4
5
6
7
12.34.0.0/16
Trigger AS loop detection at AS 3!
12.34.0.0/16: (1 3)
Notes: The adversary may prefer to limit the scope of the routing announcement, so only a portion of the ASes select and propagate the route. This is possible with path poisoning by putting additional AS numbers in the path or by using BGP communities. For example…

## Slide 8: Stealthy, Targeted Attacks
Targeted senders
  Specific sender
  Easiest sender to attack of a group
Limited scope
  Limit the other ASes that see the hijack
  Limit the data traffic that follows the hijack path
Limited time
  Short interval of time
  During a sensitive event

## Slide 9: Surgical Hijack
1
2
3
4
5
6
7
8
9
12.34.0.0/16: (4 5 6 7 8)
12.34.0.0/16

## Slide 10: Stealthy, Targeted Attacks
Targeted sender
  Specific sender (e.g., a specific certificate authority)
  Easiest sender to attack of a group (e.g., any certificate authority)
Limited scope
  Limit the other ASes that see the hijack
  Limit the data traffic that follows the hijack path
Limited time
  Short interval of time
  During a sensitive event (e.g., acquiring a certificate)

## Slide 11: CA Domain Control Verification
Certificate
1. Certificate signing request
2. Domain control verification request
3. Server modification
4. GET example.com/verify.html
5. HTTP response
Hijack here!

## Slide 12: Launching Ethical Attacks
Attacking ourselves
  IP prefix we control (PEERING testbed at Columbia University)
  Domain names created for the experiment
  No real clients accessing the server
Bamboozling the certificate authorities
  Let’s Encrypt, GoDaddy, Comodo, Symantec, GlobalSign
  Domain validation using either HTTP request or email
  All five CAs signed our certificate requests in < 2 minutes

## Slide 13: Additional Attacks
More targets (beyond victim web servers)
  Authoritative DNS servers
  E-mail servers
Attacking CA prefixes
  Reverse (victim domain  CA) traffic is also vulnerable
Certificate Authority
DNS
Certificate Authority

## Slide 14: Adversary Can Pick the Easiest CA to Fool
CA 2
Adversary
AS containing
example.com
I own 2.2.2.0/23
I own 2.2.2.0/23
AS 1
AS 3
AS 4
Hijacked portion
Unaffected portion
CA 1
Around 100 CAs
Any CA can sign for a domain

## Slide 15: Application-Level Defense
You can fool some of the people some of the time
  But not all of the people all of the time
Multiple vantage point domain verification by the CA
Deployed by Let’s Encrypt
  Starting February 2020

## Slide 16: Practical Design Challenges
Security
  Vantage points with diverse perspectives
  Strong enough quorum policy to thwart attacks
Manageability
  Compliance with the CA/Browser Forum requirements
  Avoid complexity of vantage points in multiple clouds
Performance
  Minimizing latency and communication overhead
Benign failures
  Avoid rejecting valid requests for certificates

## Slide 17: Compliance with CA/Browser Forum
A primary VA in a data center compliant with CA/Browser Forum
Remote VAs in data centers managed by cloud provider(s)
Primary VA’s validation must succeed.

## Slide 18: Balancing Security and Cloud Complexity
Single cloud provider (AWS) offers sufficient route diversity
Remote VAs in Oregon, Ohio, and Frankfurt.
Primary VA in Denver or Salt Lake City

## Slide 19: Balancing Security and Benign Failures
Primary VA and at least two remote VAs must succeed.
Remote VAs may
respond slowly,
fail to respond, or
answer inconsistently

## Slide 20: Let’s Encrypt Phased Deployment
Staging deployment
  Internal testing of new features
Testing in production environment
  Remote VAs performed domain validation
  But, the primary VA drove all validation decisions
Production deployment with domain exceptions
  Temporarily excluding certain domains renewing their certificates
Full production deployment
  All certificate requests (~1.5M per day) validated by multiple VAs
Notes: Let’s Encrypt populated the exception list with domains that may, based on the logs, have trouble with multi-vantage-point validation to prepare for future certificate renewal. Let’s Encrypt only did this for the domains associated with ACME accounts that have contact information, so it can communicate with the domain owners to inform them that they are on the domain exception list, and troubleshoot the issues

## Slide 21: Deployment Anecdotes
Low validation latency
  Remote VAs usually perform better than the primary VA
Low validation bandwidth
  Only 0.5 Mbps per remote VA for ~20 certificates/second
Low benign failures
  Primary succeeds but any remote VA fails: just 1.2% of validations
  Most due to a remote VA failing DNS resolution of domain’s name
  Some due to multiple validation requests triggering DDoS detection
  Almost all were successful after retrying the request
Notes: Though each day about 1% of certificates were temporarily rejected due to differentials, most domain owners have retried validation and eventually had their certificates signed by Let’s Encrypt after retrying by the end of Sep 22, 2020. Overall, only 0.65% of all certificates that have been validated in 20 days (36.8 M) failed to get signed because of differentials.

## Slide 22: Quantifying the Security Improvement
Ethical attacks on Let’s Encrypt
  Using Columbia University’s PEERING testbed
  Quorum policy caught most of the attacks
  ... though some well-connected adversaries still successful
BGP simulation experiments
  Extensions to model AS connectivity of each AWS data center
  Evaluation of a much wider range of BGP attacks
  Median domain is resilient to attacks from > 90% of ASes
Good to add 1-2 more AWS locations (Paris, Singapore) and/or require a full quorum

## Slide 23: Other BGP Attacks: Sub-Prefix Hijack
1
2
3
4
5
6
7
12.34.0.0/16
12.34.158.0/24: (1)
Not always possible (e.g., domain on /24) and visible in BGP monitoring

## Slide 24: Protecting More Applications
Domain validation (beyond CAs)
  Changing an account password
  Verifying ownership of a restaurant, hotel, etc.
Anonymous communication
  Tor, I2P, and VPNs
  BGP interception attacks to enable traffic-analysis attacks
Bitcoin network
  Disrupting the consensus protocol in the overlay network

## Slide 25: Conclusion
Cross-layer attacks
  Layering simplifies protocol design
  But, adversaries can work across layer boundaries
Cross-layer defenses
  Application-layer defenses are easier to deploy
  But, network-layer defenses are still important
A way forward
  Protect popular applications and important prefixes
  Continue the important work of securing BGP
  Incentivize BGP security by favoring secure prefixes and ASes

## Slide 26: Thank You!
Henry Birge-Lee, Yixin Sun, Annie Edmundson, Jennifer Rexford, and Prateek Mittal, "Bamboozling certificate authorities with BGP," in USENIX Security, August 2018. https://www.cs.princeton.edu/~jrex/papers/bamboozle18.pdf
Yixin Sun, Maria Apostolaki, Henry Birge-Lee, Laurent Vanbever, Jennifer Rexford, Mung Chiang, and Prateek Mittal, “Securing Internet applications from routing attacks,” to appear in Communications of the ACM. https://arxiv.org/pdf/2004.09063.pdf
Henry Birge-Lee, Liang Wang, Daniel McCarney, Roland Shoemaker, Jennifer Rexford, and Prateek Mittal, “Experiences deploying multi-vantage-point domain validation at Let’s Encrypt,” October 2020. https://www.cs.princeton.edu/~jrex/papers/multiva20.pdf