## Slide 1: iSDX: An Industrial-Scale Software-Defined IXP
Arpit Gupta
Princeton University
http://sdx.cs.princeton.edu
Robert MacDavid, Rüdiger Birkner, Marco Canini,
Nick Feamster, Jennifer Rexford, Laurent Vanbever
Notes: Let’s kickoff NSDI 2016 with a talk on software defined IXPs that we now believe are ready for production networks.

## Slide 2: Internet Exchange Points (IXPs)
AS A Router
AS C Router
AS B Router
BGP Session
Switching Fabric
IXP
Route Server
Notes: But, before we talk about software defined IXPs, let’s briefly talk about traditional IXPs. At any IXP, participants connect their border router to the IXP’s switching fabrics to exchange traffic. They establish BGP session with route server to exchange routes with each other.

## Slide 3: Software Defined IXPs (SDXs)
AS A Router
AS C Router
AS B Router
BGP Session
SDN Switch
SDX Controller
SDX
[*Gupta et al., SIGCOMM’14]
Notes: With respect to this traditional model of IXPs, what we proposed few years back was to replace the traditional L2 switching fabric with an SDN switch and route server with SDX controller. This SDX controller now subsumes the behavior of route server, that is it not only receives BGP update messages from the IXP participants, but it also receives SDN policies from them, combines these policies together and pushes them down to the data plane.

## Slide 4: Deployment Ready SDX is Hard!
Deployment Experience:
  Inter-Agency Exchange
  Large IXP in Europe
  Smaller IXPs in Asia
Challenges:
  Data Plane Scalability
  …
Notes: When we first proposed SDX, it resonated well with lot of IXP operators. We worked with various IXP operators to build SDX platforms ready for production networks.
From our experiences we observed that there exist various fundamental challenges that need to solved before we can make SDX production ready.
The most critical challenge is the scalability of the SDX platforms and that is the focus of my talk today

## Slide 5: Data Plane Scalability Challenges
Devices | Operations | Data Plane Performance | 
 |  | State (# entries) | Update Rate (flow-mods/s)
 | Match-Action on Multiple Headers | 100K | 2,500
Notes: Even though SDN switches can support flexible match-action operations, they have limited data plane state and can only support about 2500 flow-mods/second.
Making SDN policies congruent with BGP requires both large forwarding tables and support for very high data plane update rate.

## Slide 6: Data Plane Scalability Challenges
Devices | Operations | Data Plane Performance | 
 |  | State (# entries) | Update Rate (flow-mods/s)
 | Match-Action on Multiple Headers | 100K | 2,500
 | Matches on IP Prefixes only | ~1M | N/A
Problem: Optimize the usage of available devices
Notes: To address the scalability problem we can leverage participants’ border routers at the IXP. Though these routers have a larger TCAM space which we can leverage but they can only support limited operations in the data plane. The problem of scaling SDX boils down to a classic problem, where we need to optimize the usage of multiple components with disparate capabilities and limitations to scale the performance of the system.

## Slide 7: Simple Example
AS A
IXP Fabric
AS B
AS C
announces
10/8, 40/8
AS D
announces
10/8, 40/8, 80/8
AS E
announces
80/8
  dPort = 443 → fwd(C)
  dPort = 22 → fwd(C)
  dPort = 80 → fwd(E)
SDX Controller
Notes: In this talk we will refer to the simple example shown here to better understand the nature of the scalability challenges and how we addressed them. We have 5 IXP participants,
Transition
A-E. A & B express outbound SDN policies forwarding traffic to C, D, and E.
A & B will send their outbound SDN policies to SDX controller, which will compile them and send them to the data plane. Let’s see how many forwarding table entries are required for these SDN policies.

## Slide 8: Forwarding Table Entries at SDX
SDN Policies | # Forwarding Table Entries
dPort = 443 → fwd(C) | 1
dPort = 22 → fwd(C) | 1
dPort = 80 → fwd(E) | 1
Number of forwarding table entries for
A & B’s Outbound SDN Policies
AS A
AS B
Notes: These SDN policies are simple in nature and each require one flow table entry.

## Slide 9: Goal Tracker
Large IXP Dataset:
  BGP RIBs & Updates from large IXP
  511 IXP participants
  96 million peering routes for 300K IP prefixes
  25K BGP updates for 2-hour duration
 | Simple Example
Baseline | 3
Notes: In this talk we will use a goal tracker to keep track of our progress so far.
To get a better sense of how these numbers map to real world scenarios, I will also present results from the analysis we ran using the data from a large IXP with more than 500 participants.

## Slide 10: Goal Tracker
Large IXP Dataset:
  BGP RIBs & Updates from large IXP
  511 IXP participants
  96 million peering routes for 300K IP prefixes
  25K BGP updates for 2-hour duration
 | Simple Example | Large IXP
Baseline | 3 | 62K
Notes: We used a policy generation model to generate SDN policies for the IXP participants.

## Slide 11: Goal Tracker
 | Simple Example | Large IXP
Baseline | 3 | 62K
Satisfies design goals, but …

## Slide 12: Goal Tracker
 | Simple Example | Large IXP
Baseline | 3 | 62K
… not congruent with BGP!

## Slide 13: Challenge: Congruence with BGP
AS A
IXP Fabric
AS C
announces
10/8, 40/8
  dPort = 443 → fwd(C)
p
dIP = 80.0.0.1, dPort = 443
Ensure p is not forwarded to C
SDX Controller
Notes: *Might be dropped

## Slide 14: Solution: SDN Policy Augmentation
AS A
IXP Fabric
AS C
announces
10/8, 40/8
  dIP ∈ {10/8, 40/8} ⋀
  dPort = 443 → fwd(C)
p
dIP = 80.0.0.1, dPort = 443
Match on prefixes advertised by C
SDX Controller
Notes: You cannot match on group of prefixes, not yet, so each match on prefix corresponds to a new forwarding table entry

## Slide 15: Data Plane State Explosion!
SDN Policy Augmentation increases
forwarding table entries
SDN Policies | # Forwarding Table Entries |  | 
 | 10/8 | 40/8 | 80/8
dPort = 443 → fwd(C) | 1 | 1 | 0
dPort = 22 → fwd(C) | 1 | 1 | 0
dPort = 443 → fwd(D) | 1 | 1 | 1
4
3

## Slide 16: Goal Tracker
 | Simple Example | Large IXP
Baseline | 3 | 62K
Policy Augmentation | 7 | 68M
Not possible to support these many
forwarding table entries!

## Slide 17: Forwarding Equivalence Classes
SDN Policies | # Forwarding Table Entries |  | 
 | 10/8 | 40/8 | 80/8
dPort = 443 → fwd(C) | 1 | 1 | 0
dPort = 22 → fwd(C) | 1 | 1 | 0
dPort = 443 → fwd(D) | 1 | 1 | 1
10/8, 40/8 exhibit similar forwarding behavior

## Slide 18: Leveraging Forwarding Equivalence
10/8
40/8
80/8
forward to
BGP Next Hop
AS A
AS C
announces
10/8, 40/8
AS D
announces
10/8, 40/8, 80/8
IXP Fabric
Single BGP Next Hop for 10/8, 40/8
  dPort = 443 → fwd(C)

## Slide 19: Leveraging Forwarding Equivalence
10/8
40/8
80/8
forward to
BGP Next Hop
AS A
IXP Fabric
fwd(C)
match on
BGP Next Hop
AS C
announces
10/8, 40/8
AS D
announces
10/8, 40/8, 80/8
Flow Rules at SDX match on BGP Next Hops
  dPort = 443 → fwd(C)

## Slide 20: Goal Tracker
 | Simple Example | Large IXP
Baseline | 3 | 62K
Policy Augmentation | 7 | 68M
*FEC Computation | 4 | 21M
Still not possible to support these many
forwarding table entries!
[*Gupta et al., SIGCOMM’14]
Notes: This is how far we managed to reach in the previous iteration of SDX. As you can see it is good, but not good enough. There is no way we can afford these many flow table entries
And update rate at larger IXPs.

## Slide 21: More Efficient FEC Computation
SDN Policies | # Forwarding Table Entries | 
 | {10/8, 40/8} | 80/8
dPort = 443 → fwd(C) | 1 | 0
dPort = 22 → fwd(C) | 1 | 0
dPort = 443 → fwd(D) | 1 | 1
Independent FEC Computation
can be more efficient
Notes: We started with exploring schemes that can make FEC computation more efficient.

## Slide 22: Partitioning FEC Computation
Large number of SDX participants
  Many different policies on groups of prefixes
  Leads to a large number of small FECs of prefixes
Compute FECs independently
  Separate computation per participant
  Leads to small number of large FECs, and less frequent recomputation
  Enables “scale out” of the FEC computation

## Slide 23: FEC Computation Partitioning in Action
SDN Policies | # Forwarding Table Entries | 
 | {10/8, 40/8} | 80/8
dPort = 443 → fwd(C) | 1 | 0
dPort = 22 → fwd(C) | 1 | 0
dPort = 443 → fwd(D) | 1
A & B independently compute FECs
2
1

## Slide 24: Goal Tracker
 | Simple Example | Large IXP
Baseline | 3 | 62K
Policy Augmentation | 7 | 68M
FEC Computation | 4 | 21M
Independent FEC Computation | 3 | 763K
Also requires support for
15K flow-mods/seconds
Notes: Still required 15K flow-mods per second

## Slide 25: Undesired BGP & SDN Coupling
SDN Policies | # Forwarding Table Entries |  | 
 | 10/8 | 40/8 | 80/8
dPort = 443 → fwd(C) | 1 | 1 | 0
dPort = 22 → fwd(C) | 1 | 1 | 0
dPort = 443 → fwd(D) | 1  0 | 1 | 1
Incoming BGP Update:
{AS D withdraws route for prefix 10/8}
Notes: Let us try to understand why SDX requires such high data plane update rates.

## Slide 26: Decoupling BGP from SDN Policies
Leverage advances in commodity hw switches
  Support for Bitmask Matching (L2 headers)
Extend BGP “next hop” encoding
  So far: encode FECs (single field)
  New idea: encode reachability bitmask (multi field)
Changing only the BGP announcements
  No need to update the SDX data plane!
Notes: Our goal is to make IXP data plane immune to BGP dynamics

## Slide 27: Reachability Bitmask in Action
10/8
40/8
80/8
forward to
BGP Next Hop
Reachable via AS C
AS A
AS C
announces
10/8, 40/8
AS D
announces
10/8, 40/8, 80/8
IXP Fabric
Reachable via AS D
Dedicate one bit per participant
  dPort = 443 → fwd(C)

## Slide 28: Reachability Bitmask in Action
Reachable via AS C
Reachable via AS D
AS A
AS C
announces
10/8, 40/8
AS D
announces
10/8, 40/8, 80/8
10/8
40/8
80/8
fwd(C)
match on
Reachability Bitmask
IXP Fabric
forward to
BGP Next Hop
Immune to BGP Dynamics
  dPort = 443 → fwd(C)
Notes: I know what you are thinking…;)
Partitioning of the control plane is still critical, as each participant, only consider the participant for which they have SDN policy for the reachability bitmask
The paper talks about how we can encode the reachability information for 100s of participants in limited bitspace. The paper talks about how addressed this problem in greater details.

## Slide 29: Reachability Bitmask in Action
SDN Policies | # Forwarding Table Entries
 | C
dPort = 443 → fwd(C) | 1
dPort = 22 → fwd(C) | 1
dPort = 443 → fwd(D) | 1
Reduces Data Plane State
2
1

## Slide 30: Goal Tracker
 | Simple Example | Large IXP
Baseline | 3 | 62K
Policy Augmentation | 7 | 68M
FEC Computation | 4 | 21M
Independent FEC Computation | 3 | 763K
Reachability Encoding | 3 | 65K
We can now run SDX over
commodity hardware switches

## Slide 31: iSDX Evaluation Summary
Data Plane State:
  Requires 65K < 100K forwarding table entries
Data Plane Update Rate:
  Requires 0 < 2500 flow-mods/second
Other Goals:
  Processes BGP update bursts in real time (50 ms)
  Requires only 360 BGP Next Hops compared to 25K from previous solutions

## Slide 32: You Can Run iSDX Today!
Running code
  Vagrant & Docker based setup
  Instructions to run with Hardware Switches
ONF’s Open Source SDN
  Community: https://community.opensourcesdn.org/wg/iSDX/dashboard
  Mailing List isdx@community.OpenSourceSDN.org
http://sdx.cs.princeton.edu