## Slide 1: Sonata Query-driven Streaming Network Telemetry
Arpit Gupta
Princeton University
Rob Harrison, Marco Canini, Nick Feamster,
Jennifer Rexford, Walter Willinger

## Slide 2: Network Management
Google
Cogent
Level3
Princeton
Outages
Congestion
Cyberattacks
Network Operator
Detect network events in real time

## Slide 3: Network Monitoring Requirements
👺
😵
Src: Victim
Dst: DNS
Src: Victim
Dst: DNS
Src: DNS
Dst: Victim
Src: DNS
Dst: Victim
DNS
DNS
Attacker
Victim
Receive
DNS responses from many distinct sources
jitter
distinct hosts
volume
delay
loss
…
Metrics
address
protocol
payload
device
location
…
Traffic
Flexible network monitoring is desired

## Slide 4: Network Monitoring with Sonata
Malware Detection
Performance Diag..
DDoS Detection
Fault Localization
Flexibility
Scalability
Abstractions
Algorithms
System
Sonata

## Slide 5: Building Sonata is Challenging
Programming abstractions
  How to let network operators express queries for a wide-range of monitoring tasks?
Scalability
  How to execute multiple queries for high-volume traffic in real time?

## Slide 6: Building Sonata is Challenging
Programming abstractions
  How to let network operators express queries for a wide-range of monitoring tasks?
Scalability
  How to execute multiple queries for high-volume traffic in real time?

## Slide 7: Packet as Tuple
Header
Metadata
Payload
Packet
traversed path, queue size, number of bytes, …
source/ destination address, protocol, ports, …
Packet = (path, qsize, nbytes,…
sIP, dIP, proto, sPort, dPort, …
payload)
Treat packet as a tuple

## Slide 8: Monitoring Tasks as Dataflow Queries
Detecting DNS Reflection Attack
Identify if DNS response messages from unique DNS servers to a single host exceeds a threshold (Th)
victimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
DNS Responses
from Unique DNS Servers
to a Single Host
exceeds a Threshold
Express wide range of network monitoring tasks in fewer than 20 lines of code

## Slide 9: Building Sonata is Challenging
Programming abstractions
  How to let network operators express queries for a wide-range of monitoring tasks?
Scalability
  How to execute multiple queries for high-volume traffic in real time?

## Slide 10: Where to Execute Monitoring Queries?
  Univmon [SIGCOMM’16]
  Marple [SIGCOMM’17]
  Gigascope [SIGMOD’03]
  NetQRE [SIGCOMM’17]
Match | Headers + Payload
Actions | Any
State | O(Gb)
Speed | O(μs)
Headers++
add, subtract, bit operations
O(Mb)
O(ns)
Switches
CPUs
Can we use both switches and CPUs?

## Slide 11: PISA* Processing Model
Programmable Deparser
Stages
ip.src=1.1.1.1
ip.dst=2.2.2.2
...
Packet Header Vector
Programmable Parser
Memory
Persistent State
ALU
  *RMT [SIGCOMM’13]

## Slide 12: Mapping Dataflow to Data plane
Which dataflow operators can be compiled to match-action tables?
 | Dataflow | Data plane
Model | Pipeline | Pipeline
Processing Unit | Operators | Match-Action Tables
Structured Data | Tuples | Packets

## Slide 13: Compiling Individual Operators
filter(p)
Stream of elements
Elements satisfying
predicate (p)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
Match | Action
p | 
udp.sport == 53 | 

## Slide 14: Compiling Individual Operators
reduce(f)
Match | Action
* | idx = hash(m.dstIP)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Stream of elements
Result of applying
function f over all elements
Memory
Match | Action
* | stateful[idx] += 1
1
2
3
4
5
6
7

## Slide 15: Compiling a Query
Programmable Deparser
Stages
Programmable Parser
State
Filter Map
Filter
D1
D2
Map
R1
R2

## Slide 16: Query Partitioning Decisions
Query Planner
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Resources?
Reduce Load?
Tuples
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)

## Slide 17: Query Partitioning ILP
Constraints
Goal: Minimize tuples sent to stream processor
Programmable Deparser
Stages
Programmable Parser
Memory
Persistent State
ALU
PHV Size
Number of
Actions
Total Stages
Stateful Memory
Packet Header Vector

## Slide 18: How Effective is Query Partitioning?
Chart: # Tuples at Stream Processor
| CPU-Only
Number of Packet Tuples | 1000000000 | 1
Log Scale
8 Tasks, 100 Gbps Workload
O(1 B)

## Slide 19: How Effective is Query Partitioning?
Chart: # Tuples at Stream Processor
| CPU-Only | Paritioning
Number of Packet Tuples | 1000000000 | 100000000
Log Scale
O(1 B)
O(100 M)
Only one order of magnitude reduction
8 Tasks, 100 Gbps Workload

## Slide 20: Query Partitioning Limitations
Filter Map
Filter
D1
D2
Map
R1
R2
distinct
reduce
How can we reduce the
memory footprint of stateful operators?

## Slide 21: Observations: Nature of Monitoring Tasks
DNS Reflection Attack Victims
All Hosts
Most monitoring tasks are looking for needles in a haystack

## Slide 22: Observations: Possible to Reduce Memory Footprint
Detecting DNS Reflection Attack
victim = pktStream
.map(dIP => dIP/8)
      .filter(p => p.udp.sPort == 53)
      .map(p => (p.dIP, p.sIP))
      .distinct()
      …
Only consider first 8 bits
Queries at coarser levels have smaller memory footprint

## Slide 23: Observations: Possible to Preserve Query Accuracy
Detecting DNS Reflection Attack
victim = pktStream
.map(dIP => dIP/8)
      .filter(p => p.udp.sPort == 53)
      .map(p => (p.dIP, p.sIP))
      .distinct()
      …
Hierarchical packet field
Query accuracy is preserved if refined with hierarchical packet fields

## Slide 24: Iterative Query Refinement
Filter
D1
D2
Map
R1
R2
Packet Stream
t+W
Map
Filter Map
Window
map(dIP=>dIP/8)
PISA Target
First, execute query at coarser level

## Slide 25: Iterative Query Refinement
Filter
D1
D2
Map
R1
R2
Filtered
Packet Stream
Map
Filter Map
Detection
Delay
Filter
Filter Map
Filter
D1
D2
Map
R1
R2
t+2W
Smaller
memory footprint
PISA Target
Then, execute query at finer level(s)
Smaller memory footprint at
the cost of additional detection delay

## Slide 26: Query Planning Problem
Goal
  Minimize tuples sent to the stream processor
Given
  Queries, packet traces
Determine
  Which packet field to use for iterative refinement?
  What levels to use for iterative refinement?
  What’s the partitioning plan for each refined query?
Augment partitioning ILP to compute both refinement and partitioning plans

## Slide 27: Sonata’s Performance
Chart: # Tuples at Stream Processor
| CPU-Only | Paritioning | Partitioning + Refinement
Number of Packet Tuples | 1000000000 | 100000000 | 100000
Log Scale
8 Tasks, 100 Gbps Workload
O(1 B)
O(100 M)
O(100 K)
Up to 4 orders of magnitude reduction

## Slide 28: Summary
Key Takeaways
  Flexible
    Dataflow queries over packet tuples
    Fewer than 20 lines of code
  Scalable
    Query refinement and partitioning algorithms
    4 orders of magnitude workload reduction
Future Directions
  Monitor network-wide events
  Handle traffic dynamics
http://sonata.cs.princeton.edu
https://github.com/sonata-princeton