## Slide 1: Designing Compact Data Structures for Network Measurement and Control
Xiaoqi Chen, FPO Oct 4th, 2023
Advisor: Prof. Jennifer Rexford,
Reader: Prof. Mark Braverman, Prof. Minlan Yu.
Non-Reader: Prof. David Walker, Prof. Maria Apostolaki

## Slide 2: Thesis Outline
Ch2 Background: architectural constraints of high-speed switches
Part 1: Measurement and telemetry
  Ch3 PRECISION: heavy-hitter flow analysis
  Ch4 BeauCoup: run multiple queries simultaneously
Part 2: Real-time, closed-loop control
  Ch5 ConQuest: queue measurement and microburst mitigation
  Ch6 AHAB: scalable fair bandwidth allocation with network slicing
Summary and conclusion

## Slide 3: Fast, faster, fast enough?
1990s: 56kbps
2000s: 50Mbps
2010s: 1Gbps
2023: Beyond bandwidth!
Dial-up
DSL / Cable
Fiber-optics
FTTH, 5G, SD-WAN…
My favorite phone
1997, GSM
Not my favorite phone
2023, 5G mmWave

## Slide 4: Many applications, diverse needs…
1990s: 56kbps
2000s: 50Mbps
2010s: 1Gbps
2023: Beyond bandwidth!
VR/Metaverse: low latency
Internet of Things: security
Data Center: high reliability
Image credit: Google, Minh Pham

## Slide 5: Switches can do more!
Traditionally, the “inside” of network mostly does forwarding
Forwarding rules: DstIP 128.*.*.* -> port 1 DstIP 130.*.*.* -> port 2
…
Forwarding rules
Fixed-function Data Plane
Control Plane

## Slide 6: Switches can do more!
Programmable Data Plane: run custom algorithms inside the network
Prime opportunity for measurement and real-time adaptation
Algorithms
Forwarding rules
Measuring statistics, anomaly detection
Real-time mitigation
Control Plane

## Slide 7: Inside a high-speed switch…
Ingress
Ingress
Egress
Egress
Queue
Crossbar
Queue

## Slide 8: Inside a high-speed switch…
Ingress
Ingress
Egress
Egress
Queue
Crossbar
Queue
Algorithm can read and modify packet “headers”
E.g., read “Destination IP” and make a routing decision
Packet
SrcIP: 13.9.0.5
DstIP: 8.8.8.8
Payload: …
Forwarding:
8.*.*.* -> Port 1
Congested: No

## Slide 9: Inside a high-speed switch…
Ingress
Ingress
Egress
Egress
Queue
Crossbar
Queue
Can also write to local memory, maintain statistics across packets
Memory
Memory
How many packets?
Counter: 2 Popular Destination: 8.8.8.8
Packet
Packet

## Slide 10: Main challenge: memory access constraints
Queue
Crossbar
Limited memory size (compared to huge amount of traffic)
Can only access a small constant number of memory addresses per packet…
Memory
Ingress
Ingress
Queue
Limited bandwidth for updating memory
High bandwidth for reading/writing packets

## Slide 11: Memory access bottleneck: “Moore’s law”?
Chart: 
| 1995 | 1997 | 1998 | 2000 | 2001 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2010 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2022
Network Throughput | 0.1 | 1 | 2 | 10 | 48 | 96 | 40 | 163 | 300 | 600 | 400 | 1200
Memory Bandwidth | 2.128 | 4.2 | 6.4 | 44.8 | 64 | 159 | 140.8 | 576 | 1024 | 2048 | 1344 | 6553
Gbit/s
Year
Sources: 1. Nielsen Norman Group. 2. Amir Gholami, Riselab.
3. Wikipedia: List of interface bit rates.
HBM
GDDR6
HBM3
DDR
EDO
SDRAM
GDDR3
100base-X
Infiniband SDR
Infiniband NDR
400GbE
Memory access is becoming expensive!
Network speed grows 45%-50% annually
Memory bandwidth only grows 33%-40% annually

## Slide 12: The gap between theory and practice…
Streaming Algorithm
Small memory, big data
Arbitrary computation
Arbitrary access to local memory
High-speed switches
Small memory, huge traffic
Constant-time processing
Limited memory access (4-16 addresses per packet)
Bridging the gap!

## Slide 13: In-network algorithms can build better measurement and closed-loop control
Measuring and telemetry:
Ch3: heavy-hitter flows
Ch4: many simultaneous queries
Real-time, closed-loop control:
Ch5: microburst analysis & mitigation
Ch6: fair bandwidth enforcement w/ slicing

## Slide 14: Part 1: network measurement & analytics on high-speed programmable switches
Previously: packet sampling
Network speed⬈, sampling rate⬊
Can’t find needle in haystack
Now: in-network algorithms
Analyze every packet
Only report the findings

## Slide 15: Chapter 3: Heavy-hitter flows
Packets can be grouped into flows (e.g., by source and destination addresses)
A few “Heavy-Hitters”, a.k.a. elephant flows, send most of the packets.
No memory to maintain per-flow counters – only count the elephants!
Flow size
All flows

## Slide 16: Space-saving: just evict the global minimum
Existing algorithm: maintain a table of flow IDs and their counters
  If a counter already exists for this flow ID, simply increment the counter
  Otherwise, take over the global minimum counter, replace its flow ID
Challenge: maintaining global minimum requires many memory accesses!
Flow ID | Count
8.8.8.8:53 | 100
4.2.2.2:53 | 50
1.1.1.1:53 | 20
100.1.2.3:80 | 5
Packet dstIP=4.2.2.2 port=53
Packet dstIP=8.8.4.4 port=53
51
6
8.8.4.4:53

## Slide 17: Adapting to Data Plane: Approximate Global Minimum
Split table into D=4 stages
Find approximate minimum c’min, by randomly querying 4 addresses (based on flow ID)
Inspired by Count-Min Sketch and HashPipe
h1 |  | h2 |  | h3 |  | h4
Graham Cormode and Shan Muthukrishnan. An improved data stream summary: the count-min sketch and its applications. Journal of Algorithms 55.1 (2005): 58-75.
Sivaraman et al. Heavy-hitter detection entirely in the data plane. SOSR 2017
Flow ID: x
h1(x)=0 h2(x)=2 h3(x)=0 h4(x)=3
Flow ID: y
h1(y)=3 h2(y)=2 h3(y)=3 h4(y)=1

## Slide 18: Adapting to Data Plane: Too Late to Update
We only know the approximate minimum count c’min at the end of pipeline. Too late to update!
Packet recirculation: hurts throughput
Solution: probabilistic packet recirculation
With small probability, recirculate (Flow ID, minimum stage #)
h1 |  | h2 |  | h3 |  | h4
5 |  |  |  | 7 |  | 
 |  | 3 |  |  |  | 
 |  |  |  |  |  | 4
Flow ID=x
Stage#=2, c’min=3
4

## Slide 19: The PRECISION algorithm
Visit d=3 random entries, one per stage
  If ID matched, +1
  Otherwise, find out c’min
Flip coin, P=1/(c’min+1)
If coin is head:
  copy and recirculate
  update minimum counter
h1 |  |  | h2 |  |  | h3 | 
ID | # |  | ID | # |  | ID | #
a | 106 |  | N/A | 100 |  | N/A | 100
b | 103 |  | g | 102 |  | N/A | 100
c | 105 |  | f | 130 |  | k | 160
d | 104 |  | N/A | 100 |  | l | 180
Pkt
ID=z
c’min=102
Coin flip: P=1/103
103
z
S#=2
ID=z

## Slide 20: Evaluation: how many stages are enough?

## Slide 21: Chapter 3: PRECISION Summary and Key Insights
Pipeline-friendly data structure: avoid global min! Evict an approximate minimum of random choices
Use D=3~4 choices (stages) is sufficient
Comparable accuracy to SOTA algorithms (that are not hardware-optimized)

## Slide 22: Chapter 4: Count-distinct queries
Internet
DDoS:
Are there many Source IPs sending to one particular Destination IP?
Select DstIP where distinct(SrcIP)>1000
Key
Attribute
Threshold
Strawman solution: 1. Write down a list of SrcIP?
5.x.x.x, 6.x.x.x, 8.x.x.x, …
2. Use HyperLogLog?
0 | 1 | 0 | 0 | 0 | 3 | 0 | 1 | 0 | …
5

## Slide 23: Many network traffic queries
Query | Key | Attribute | Threshold
DDoS | DstIP | SrcIP | 1000
Worm | SrcIP | DstIP | 300
PortScan | SrcIP,DstIP | DstPort | 100
… | … | … | …
Internet
DDoS?
Worm?
Port Scan?
…
Different keys/attrs, need multiple data structures
0 | 1 | 0 | 0 | 0 | 3 | 0 | 1 | …
6 | 6 | 2 | 0 | 1 | 0 | 0 | 9 | …
1 | 4 | 8 | 4 | 5 | 2 | 9 | 3 | …
5
8
4
…

## Slide 24: Many network traffic queries
I have 42 queries
Run 42 data structures?
I can’t…
Memory
Limited bandwidth for updating memory
Memory access is becoming expensive!
Network speed grows 45%-50% annually
Memory bandwidth only grows 33%-40% annually

## Slide 25: One memory update at a time!
Can we process many queries using very few (constant) memory accesses?
Game plan:
  Each query uses only o(1) memory update per packet on average
  Combine many different queries, on average uses O(1)
  Coordinate, at most O(1) per packet
Hardest
NitroSketch [SIGCOMM’19]
~✓
❌
❌
Sampling (inaccurate)
✓
✓
✓

## Slide 26: The coupon collector problem
C
D
A
4 different coupons, collect all of them
Random draws
How many total draws are required?
B
?
[1] Siobhan's Problem: The Coupon Collector Revisited
Brian Dawkins. The American Statistician, Vol 45(1), p76-82. 1991.

## Slide 27: BeauCoup coupon collector
f(10.0.1.15) -> Coupon ?
f(10.0.1.33) -> Coupon ?
f(10.0.1.15) -> Coupon ?
f(10.0.1.42) -> No Coupon
f(SrcIP) -> Coupon
?
Random Mapping
DDoS: Select DstIP where distinct(SrcIP)>1000
Collect different coupons
C
B
C
C
D
A
B
SrcIP: 10.0.1.15
DstIP: 162.249.4.107
SrcIP: 10.0.1.33
DstIP: 162.249.4.107
SrcIP: 10.0.1.42
DstIP: 162.249.4.107
Key: 162.249.4.107
Coupons:

## Slide 28: BeauCoup coupon collector
Generalization: (m, p, n)-coupon collector
m*p<1, most packets collect no coupon
f(SrcIP) -> Coupon
?
m=8 coupons in total
stop at n=4 different coupons
Example:
(m=8, p=1%, n=4)
Given a new SrcIP, each coupon is drawn with probability p=1%

## Slide 29: Query Compiler: finding (m,p,n)
Query set Q = {q1, q2, …}
Query qi
Key, Attribute,
Threshold
Query qi
Key, Attribute,
Threshold
Query qi
Key, Attribute,
Threshold
Query Compiler
qi’s Collector Configuration
Total coupons: m
Each probability: p
Coupons to collect: n
qi’s Collector Configuration
Total coupons: m
Each probability: p
Coupons to collect: n
qi’s Collector Configuration
Total coupons: mi
Each probability: pi
Coupons to collect: ni
m=20, p=1/2048, n=8
-> E[#Attr]=1012.79
Threshold=1000
Per-Query Limit γ=1/|Q|
Key=SrcIP, Attr=DstIP
Threshold=1000
Example: |Q|=100 -> γ=0.01 access per packet
CC Configurations
Goal:
Stop near Threshold
Update limit m*p≤γ
HW limit, e.g., m≤32

## Slide 30: Stacking queries
q1: f(SrcIP) -> Coupon . m1=4, p1=1/8
?
Random
hash function
h1(SrcIP) -> [0,1)
1
1/4
1/2
3/4
0
q1 #1
q1 #2
q1 #3
q1 #4
4 coupons for q1
q2: f(SrcIP) -> Coupon . m2=3, p2=1/16
?
q2 #1
q2 #2
q2 #3
3 coupons for q2
…
…

## Slide 31: One hash function for each attribute
q1: f(SrcIP) -> Coupon . m1=4, p1=1/8
?
q6: g(DstIP) -> Coupon . m6=3, p6=1/8
?
h1(SrcIP) ->
1
1/4
1/2
3/4
0
q1 #1
q1 #2
q1 #3
q1 #4
…
h2(DstIP) ->
1
1/4
1/2
3/4
0
q6 #1
q6 #2
q6 #3
…

## Slide 32: Coupon collector table
Q , Key | Coupons
q4: 8.8.8.8:53 | 
q4: 1.1.1.1:53 | 
q5: 10.0.0.1 | 
q6: 10.0.1.33 | 
q6: 10.0.1.15 | 
1
4
2
3
1
4
2
3
1
2
3
4
3
1
2
3
1
2
3
2
Packet
SrcPort: 25012
DstPort: 443
SrcIP: 10.0.1.15
DstIP: 162.249.4.107
q6 #3
h
q6: SrcIP
q6 Coupon #3
Key: 10.0.1.15
Query q6
Key 10.0.1.33
3
Packet
SrcPort: 27000
DstPort: 443
SrcIP: 10.0.1.33
DstIP: 4.3.2.1
q6 #1
h
q6 Coupon #1
Key: 10.0.1.33
1
q6: DstIP, 1000
SrcIP 10.0.1.33 is sending to >1000 distinct DstIPs.
Space efficiency:
Keys from all queries multiplexed into one table
Only keep rows for “active keys” (at least one coupon)
Clear rows after timeout

## Slide 33: The BeauCoup framework: installing queries
The installed rules represent query set Q
Update queries on the fly, with no downtime caused by recompiling
Table rules
Key, Attribute, Threshold
Code Generator
Query Compiler
(m,p,n)
Rules Generator
Vendor Compiler
Data plane program
Static
program
Dynamic
rules
Query set Q = {q1, q2, …}
code
Programmable Switch
Packets
Alerts
Coupon Bitmaps:
0000000000…
Coupon Bitmaps:
0110111101…
Header field names

## Slide 34: Evaluation highlights
How efficient is BeauCoup?
We uses 4x~10x fewer memory access than the state-of-the-art to achieve the same accuracy.
What about fairness?
Equalized accuracy for same-threshold queries.

## Slide 35: Evaluation metric: Mean Relative Error
Threshold
Wider
Narrow
x = Actual # of distinct
Error=|x - Threshold|
Normalized Metric: MRE= Error / Threshold
A “better” coupon collector, with narrower distribution
Lower accuracy (higher error in when to activate)
Notes: MRE of 20%-30% acceptable for network monitoring. Naturally, more queries means higher error, operator’s tradeoff. performance anomaly detection allows some error 20%, but not
But, first, we compare against other algorithm

## Slide 36: Evaluation: accuracy / mem access tradeoff
NitroSketch-Univmon1
BeauCoup
Sampling2
HyperLogLog
Stricter
Better
Better
1NitroSketch: Robust and General Sketch-based Monitoring in Software Switches. Liu et al., SIGCOMM 2019
2On estimating the number of flows. Spang & McKeown, Buffer Sizing Workshop 2019
4x~10x
Notes: comment: say why 20% is good enough. with these algorithm: could identify DDoS / worm spreader / port spreading attack, with some fuzziness.
also mean more queries

## Slide 37: Evaluation: Across multiple queries
Total memory access per packet
Mean Relative Error
Key=SrcIP
Attribute= DstIP
Threshold=1000
Key=SrcIP
Attribute= DstIP+DstPort
Threshold=1000
Key=DstIP+DstPort
Attribute= SrcIP
Threshold=1000
Key=DstIP+DstPort
Attribute= SrcIP+SrcPort
Threshold=1000
Run |Q|=26 queries simultaneously
Fairness among queries: same accuracy

## Slide 38: Evaluation 2: Across multiple queries
Run |Q|=26 queries simultaneously
Intuition: high-threshold query is ”easier”, low-threshold query benefits from more memory access
Total memory access per packet
Mean Relative Error
Threshold=100
Threshold=500
Threshold=5000
Threshold=10000

## Slide 39: Chapter 4: BeauCoup Summary and Key Insights
Count-distinct using o(1) memory access per packet
4x-10x fewer memory accesses than SOTA
Running many queries, always constant memory access

## Slide 40: In-network algorithms can build better measurement and closed-loop control
Measuring and telemetry:
Ch3: Heavy hitter flows
Ch4: many simultaneous queries
Real-time, closed-loop control:
Ch5: microburst analysis & mitigation
Ch6: fair bandwidth enforcement w/ slicing

## Slide 41
Control Plane
Part 2: real-time, closed-loop reaction for optimizing network performance
“Reaction” based on control plane has high delay…

## Slide 42
Part 2: real-time, closed-loop reaction for optimizing network performance
In-network computing enables closed-loop reaction in real time

## Slide 43: Chapter 5: Queue and microburst analysis
Routing
Routing
Ingress
Ingress
Egress
Egress
Queue
Crossbar
Queue
Queue might become full, when many packets burst in
High delay / packet loss
Pkt
Pkt
Pkt
Pkt

## Slide 44: Microbursts: sub-millisecond queue anomaly
Bad for interactive applications (AR/VR/Streaming)
In data centers, caused by incast.
Also in carrier networks?
Hard to measure: only lasts <1-2ms
Harder to react: By the time it’s detected, harm is already done!
5x
3x
1x
16:00:00
0:00:00
8:00:00
16:00:00
Time in day (24h)
Queue Length
Microbursts
Max queue length stats, at an AT&T metro backbone switch
In-network algorithm to the rescue:
Fine-grained measurement + real-time reaction

## Slide 45: Analyzing queues: Why am I waiting?
Which flow has many packets in the queue?
Queue
Egress
A
B
B
C
E
D
B
B
Flow ID: A
{SrcIP: XXX, DstIP: YYY}
Why am I waiting?
B
It’s because flow B!

## Slide 46: A strawman solution
Flow | Count
Maintain a “flow size in the queue” table
Increment when packet arrives
Subtracts when packet exits
A
1
B
1
C
1
Queue
Egress
A
B
C
0
C
2
Memory access
Memory access

## Slide 47: Challenge: memory partitioned!
Ingress
Ingress
Egress
Egress
Queue
Crossbar
Queue
Memory
Memory
Shared Memory
400 Gbps = 1 packet per 1.67 nanoseconds
Concurrent access is hard to implement, must prevent hazard
Memory partitioned before and after queuing

## Slide 48: Solution: snapshots
S1 | S2 | S3 | S4 | …
Memory access
Flow | ~Count
 | 1
 | 5
 | 1
 | 1
Slice traffic into small time periods, save “snapshots”
Example: each snapshot records T=4 packets
Query last ⌊Δ/T⌋=2 snapshots
Queue
Egress
B
E
Historical Departures
D
B
A
C
C
D
B
B
B
A
B
B
I enqueued at te=5
I dequeued at td=14
High delay: Δ=9
Why I suffered high delay?
?
A
B
C
D

## Slide 49: Round-robin snapshots
Need to clean memory every <1ms, control plane is too slow
Solution: gradually Clean and Recycle the snapshots!
Read
Read
Write
Clean
Read
Read
Read

## Slide 50: The ConQuest data structure
Slice traffic into time windows
For each packet dequeued:
  Write into the latest snapshot
  Read some recent snapshots
  Clean the oldest snapshot

## Slide 51
Check for every packet:
  Is there a microburst? (Queue size)
  Is this flow the culprit? (Snapshots)
Real-time reaction:
  Tagging, Dropping, Rerouting
  Prevent high delay / packet loss
Queue
Egress
B
D
C
D
B
B
B
A
B
B
Mitigating microbursts via closed-loop control

## Slide 52: Evaluation highlights
How accurate is ConQuest?
Achieved >90% Precision and Recall when identifying bursty flows in the queue.
Can ConQuest improve end-to-end performance?
Reduced average Flow Completion Time by 11%

## Slide 53
In Queue Flow Size Estimation
More Snapshots
Lower absolute error
Higher absolute error

## Slide 54: Testbed Evaluation: 10k flows/sec + bursts
Baseline: ECN for all flows when queue is long ConQuest: ECN only for bursty flows
Flow-based ECN reduces Flow Completion Time
Queue remains short, bursty flow effectively suppressed
11%

## Slide 55: Chapter 5: ConQuest Summary and Key Insights
Fine-grained queue buffer analysis in data plane
Mitigate root causes of microbursts in real time
Deployed in real-world campus & carrier networks (Princeton P4Campus, AT&T Labs)

## Slide 56: Chapter 6: Scalable bandwidth fairness
* For simplicity, all slices and users have equal weight. Trivial to add weighted case.
Network slicing: resource allocation and performance isolation.
For bandwidth: First share BW between slices, then between users.

## Slide 57: Fair bandwidth allocation is dynamic
If some user or slice is underutilized, fairly re-allocate the surplus
Allocation is constantly changing
User 1a, 3a go offline User 2a needs only 20

## Slide 58: Scalable hierarchical bandwidth fairness
Goal: Support thousands of slices, millions of users
CPU-based Software switch? High latency
Programmable switch? Hardware constraints
  8-32 hardware queues per port
  Limited arithmetic
  Small memory

## Slide 59: Scalable hierarchical bandwidth fairness
Challenge 1: can’t easily calculate the per-user fair rate limit
Solution: guess a limit, closed-loop iterative update
Challenge 2: can’t use per-user memory to track sending rate
Solution: CMS-LPF sketch, approximate per-user rate

## Slide 60: Challenge 1: Finding fair per-user rate limit
Sort and plot all user’s bandwidth demand
Apply limit Tn
Total bandwidth used is shaded area f(Tn)
Demand: 20Mbps
Demand: 180Mbps Limited to: 110Mbps
Tn 110Mbps

## Slide 61: Challenge 1: Finding fair per-user rate limit
The ”right” limit means total usage equals capacity:
Cn =f(Tn)
But how do we find Tn? Just guess and refine!
Demand: 20Mbps
Demand: 180Mbps Limited to: 110Mbps
Tn 110Mbps

## Slide 62: Fair rate limit via closed-loop refinement
Adjust T : pick 3 candidates, track 3 hypothetical demands

## Slide 63: Fair rate limit via closed-loop refinement
Plot f(T ) on Y-axis. X-axis is different T limits
We can then map Cn into Tnew : approx. linear interpolation
Repeat every epoch, until convergence

## Slide 64: Challenge 2: Tracking per-user sending rate
Per-user rate limit T can be enforced via probabilistic drop*: p= (1-T/R) But this requires knowing the user’s sending rate R
How to get per-user sending rate, without per-user memory?
Idea: we only care about heavy users… Use sketch!
* Disclaimers:
Only when R >T
This is for UDP. For TCP needs something fancier (see paper)

## Slide 65: Solving scalability challenge: CMS-LPF sketch
Count-Min Sketch: approximate data structure for heavy-hitter flows
Low-Pass Filter: self-decaying counter for exponential moving average
CMS-LPF: approximate per-user sending rate
0 | +1 | 0 | 0 | 2
14 | 0 | +1 | 5 | 0
7 | 0 | 23 | 0 | +1
h1(id) h2(id)
h3(id)
Pkt
Flow id
Pkt
Time, Pkt size
Σ
Average total sending rate
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
Σ
h1(id) h2(id)
h3(id)
T, uid, size
Pkt
min
Estimate
flow size
Estimate per-user sending rate
min

## Slide 66: AHAB: Hardware implementation on Tofino
First, look up slice id n and its current per-user rate limit Tn ; Also, use CMS-LPF to get estimated per-user sending rate R .
Approximated probabilistic dropping (using match-action rules).
Linear interpolation for new rate limit Tnew ; update using messenger packets.

## Slide 67: Evaluation overview
1. How fast can AHAB converge to the right limit?
✓ 3.1ms, 13x faster than state-of-the-art
2. How fair (accurate)?
✓ Throughput within 4%-6% of ideal fair rate
3. Can AHAB scale?
✓ Millions of users

## Slide 68: Evaluation: Fast convergence to fairness
Setup: 1 to 4 flows sharing a slice (fixed 100Mbps capacity)
Compare AHAB with prior state-of-the-art, HCSFQ

## Slide 69: Evaluation: Fast convergence to fairness
AHAB’s iterative update converges in 3.1ms
Instead, HCSFQ needs 42ms to converge (13x)

## Slide 70: Evaluation: Accuracy of approximated fairness
Flows with different demands: 10Mbps, 20Mbps, 30Mbps…160Mbps Enforced to within 4%-6% of fair bandwidth limit.

## Slide 71: Evaluation: Scalability
# of Users | CMS-LPF size needed | SRAM utilization
3 millions | 2048x3 (24KB) | 1.56%
6 millions | 4096x3 (48KB) | 2.60%
24 millions (est.) | 16384x3 (768KB) | 8.85%
Simulate CMS-LPF errors for a very large number of users, using local ISP trace (6M users) and CAIDA (7.3M users)
HW Resource | Instr. Words | Hash Unit | TCAM | Stages
Utilization | 28.6% | 37.5% | 5.2% | 12+9
Other hardware resource metrics

## Slide 72: Chapter 6: AHAB Summary and Key Insights
Closed-loop iterative refinement for per-user rate limit
    Approximated linear interpolation for updates
    Quick convergence: 3-5ms (3-5 epochs)
Avoid per-user memory when estimating sending rate
    New sketch: CMS-LPF rate estimator
    Scales to 1k slices, 24 millions of users

## Slide 73: In-network algorithms can build better measurement and closed-loop control
Measuring and telemetry:
Ch3: Heavy hitter flows
Ch4: many simultaneous queries
Real-time, closed-loop control:
Ch5: microburst analysis & mitigation
Ch6: fair bandwidth enforcement w/ slicing

## Slide 74: Conclusion, Q&A
Measurement: tailoring sketches for switches
  Adapt theoretical insights into hardware-friendly design
  Focus on fundamental & long-term constraints, not quirks
Closed-loop control: embrace fuzziness
  Real-timeliness opens new possibility
  All approximated: input, decision-making, and output
Future: more distributed & dynamic network algorithms