## Slide 1: On Cosmic Rays, Bat Droppings and what to do about them
David Walker
Princeton University
with Jay Ligatti, Lester Mackey, George Reis and David August

## Slide 2: A Little-Publicized Fact
1 + 1 =
2
3
Notes: A disastrous hardware manufacturing error that cost Intel millions as it scrambled to replace it’s chips...

## Slide 3: How do Soft Faults Happen?
High-energy particles pass through devices and collides with silicon atom
Collision generates an electric charge that can flip a single bit
“Galactic Particles”
Are high-energy particles that
penetrate to Earth’s surface, through
buildings and walls
“Solar
Particles”
Affect
Satellites;
Cause < 5% of
Terrestrial problems
Alpha particles from
bat droppings
Notes: In 1992, a small company in Louisiana mines bat Guano (bat poop), used most commonly in fertilizer. It opens a new mine in a bat cave near Jordan mountain. The new mine had a high level of radioactive thorium, some of which dissolved into ground water and was absorbed into the food chain and passed into the bat poop. Bat guano is high in phosphates, and one of the mine’s customers was a chemical company that made high-purity phosphoric acid used to etch the aluminum on the semiconductor factory’s chips. The factory was shut down for 8 weeks….

## Slide 4: How Often do Soft Faults Happen?

## Slide 5: How Often do Soft Faults Happen?
NYC
Tucson, AZ
Denver, CO
Leadville, CO
IBM Soft Fail Rate Study; Mainframes; 83-86

## Slide 6: How Often do Soft Faults Happen?
NYC
Tucson, AZ
Denver, CO
Leadville, CO
IBM Soft Fail Rate Study; Mainframes; 83-86 [Zeiger-Puchner 2004]
Some Data Points:
83-86: Leadville (highest incorporated city in the US): 1 fail/2 days
83-86: Subterrean experiment: under 50ft of rock: no fails in 9 months
2004: 1 fail/year for laptop with 1GB ram at sea-level
2004: 1 fail/trans-pacific roundtrip [Zeiger-Puchner 2004]

## Slide 7: How Often do Soft Faults Happen?
Soft Error Rate Trends
[Shenkhar Borkar, Intel, 2004]
we are
approximately
here
6 years
from now

## Slide 8: How Often do Soft Faults Happen?
Soft Error Rate Trends
[Shenkhar Borkar, Intel, 2004]
Soft error rates go up as:
  Voltages decrease
  Feature sizes decrease
  Transistor density increases
  Clock rates increase
we are
approximately
here
6 years
from now
all future
manufacturing
trends

## Slide 9: Mitigation Techniques
Hardware:
  error-correcting codes
  redundant hardware
Pros:
  fast for a fixed policy
Cons:
  FT policy decided at hardware design time
    mistakes cost millions
  one-size-fits-all policy
  expensive
Software and hybrid schemes:
  replicate computations
Pros:
  immediate deployment
  policies customized to environment, application
  reduced hardware cost
Cons:
  for the same universal policy, slower (but not as much as you’d think).
Notes: harware techniques are equipped with multiple acronyms ...

## Slide 10: Mitigation Techniques
Hardware:
  error-correcting codes
  redundant hardware
Pros:
  fast for fixed policy
Cons:
  FT policy decided at hardware design time
    mistakes cost millions
  one-size-fits-all policy
  expensive
Software and hybrid schemes:
  replicate computations
Pros:
  immediate deployment
  policies customized to environment, application
  reduced hardware cost
Cons:
  for the same universal policy, slower (but not as much as you’d think).
  It may not actually work!
    much research in HW/compilers community completely lacking proof
Notes: there are also techniques that combine hardware and software

## Slide 11: Agenda
Answer basic scientific questions about software-controlled fault tolerance:
  Do software-only or hybrid SW/HW techniques actually work?
  For what fault models? How do we specify them?
  How can we prove it?
Build compilers that produce software that runs reliably on faulty hardware
  Moreover: Let’s not replace faulty hardware with faulty software.
Notes:     much recent work in the hardware is without precise fault models or rigorous proof
I am suspicious some of it is wrong or at least misleading

## Slide 12: Lambda Zap: A Baby Step
Lambda Zap [ICFP 06]
  a lambda calculus that exhibits intermittent data faults + operators to detect and correct them
  a type system that guarantees observable outputs of well-typed programs do not change in the presence of a single fault
  expressive enough to implement an ordinary typed lambda calculus
End result:
  the foundation for a fault-tolerant typed intermediate language

## Slide 13: The Fault Model
Lambda zap models simple data faults only
v1
---> v2
Not modelled:
  memory faults (better protected using ECC hardware)
  control-flow faults (ie: faults during control-flow transfer)
  instruction faults (ie: faults in instruction opcodes)
Goal: to construct programs that tolerate 1 fault
  observers cannot distinguish between fault-free and 1-fault runs

## Slide 14: Lambda to Lambda Zap: The main idea
let x = 2 in
let y = x + x in
out y

## Slide 15: Lambda to Lambda Zap: The main idea
let x = 2 in
let y = x + x in
out y
let x1 = 2 in
let x2 = 2 in
let x3 = 2 in
let y1 = x1 + x1 in
let y2 = x2 + x2 in
let y3 = x3 + x3 in
out [y1, y2, y3]
atomic majority vote
+ output
replicate
instructions

## Slide 16: Lambda to Lambda Zap: The main idea
let x = 2 in
let y = x + x in
out y
let x1 = 2 in
let x2 = 2 in
let x3 = 7 in
let y1 = x1 + x1 in
let y2 = x2 + x2 in
let y3 = x3 + x3 in
out [y1, y2, y3]

## Slide 17: Lambda to Lambda Zap: The main idea
let x = 2 in
let y = x + x in
out y
let x1 = 2 in
let x2 = 2 in
let x3 = 7 in
let y1 = x1 + x1 in
let y2 = x2 + x2 in
let y3 = x3 + x3 in
out [y1, y2, y3]
but final output
unchanged
corrupted values
copied and percolate
through computation

## Slide 18: Lambda to Lambda Zap: Control-flow
let x = 2 in
if x then e1 else e2
let x1 = 2 in
let x2 = 2 in
let x3 = 2 in
if [x1, x2, x3] then [[ e1 ]] else [[ e2 ]]
majority vote on
control-flow transfer
recursively translate
subexpressions

## Slide 19: Lambda to Lambda Zap: Control-flow
let x = 2 in
if x then e1 else e2
let x1 = 2 in
let x2 = 2 in
let x3 = 2 in
if [x1, x2, x3] then [[ e1 ]] else [[ e2 ]]
majority vote on
control-flow transfer
(function calls replicate arguments,
results and function itself)
recursively translate
subexpressions

## Slide 20: Almost too easy, can anything go wrong?...
Notes: Initial implementation of SWIFT system [Reis et al.] showed no slow-down due to inserting redundant code! Something must be wrong.

## Slide 21: Faulty Optimizations
let x1 = 2 in
let x2 = 2 in
let x3 = 2 in
let y1 = x1 + x1 in
let y2 = x2 + x2 in
let y3 = x3 + x3 in
out [y1, y2, y3]
In general, optimizations eliminate redundancy,
fault-tolerance requires redundancy.
CSE
let x1 = 2 in
let y1 = x1 + x1 in
out [y1, y1, y1]
Notes: Overhead with optimization:
  43% for 2 copies [Reis et al. 2004]

## Slide 22: The Essential Problem
voters depend on
common value x1
let x1 = 2 in
let y1 = x1 + x1 in
out [y1, y1, y1]
bad code:

## Slide 23: The Essential Problem
let x1 = 2 in
let x2 = 2 in
let x3 = 2 in
let y1 = x1 + x1 in
let y2 = x2 + x2 in
let y3 = x3 + x3 in
out [y1, y2, y3]
voters depend on
common value x1
let x1 = 2 in
let y1 = x1 + x1 in
out [y1, y1, y1]
bad code:
good code:
voters do not depend on
a common value

## Slide 24: The Essential Problem
voters depend on
a common value
let x1 = 2 in
let y1 = x1 + x1 in
out [y1, y1, y1]
bad code:
let x1 = 2 in
let x2 = 2 in
let x3 = 2 in
let y1 = x1 + x1 in
let y2 = x2 + x2 in
let y3 = x3 + x3 in
out [y1, y2, y3]
good code:
voters do not depend on
a common value
(red on red;
green on green;
blue on blue)

## Slide 25: A Type System for Lambda Zap
Key idea: types track the “color” of the underlying value & prevents interference between colors
Colors C ::= R | G | B
Types T ::= C int | C bool | C (T1,T2,T3)  (T1’,T2’,T3’)

## Slide 26: Sample Typing Rules
(x : T) in G
---------------
G |--z x : T
------------------------
G |--z C n : C int
Judgement Form: G |--z e : T where z ::= C | .
simple value typing rules:
------------------------------
G |--z C true : C bool

## Slide 27: Sample Typing Rules
G |--z e1 : R bool
G |--z e2 : G bool
G |--z e3 : B bool
G |--z e4 : T G |--z e5 : T
-----------------------------------------------------
G |--z if [e1, e2, e3] then e4 else e5 : T
Judgement Form: G |--z e : T where z ::= C | .
G |--z e1 : R int
G |--z e2 : G int
G |--z e3 : B int
G |--z e4 : T
------------------------------------
G |--z out [e1, e2, e3]; e4 : T
sample expression typing rules:
G |--z e1 : C int G |--z e2 : C int
-------------------------------------------------
G |--z e1 + e2 : C int

## Slide 28: Theorems
Theorem 1: Well-typed programs are safe, even when there is a single error.
Theorem 2: Well-typed programs executing with a single error simulate the output of well-typed programs with no errors [with a caveat].
Theorem 3: There is a correct, type-preserving translation from the simply-typed lambda calculus into lambda zap [that satisfies the caveat].

## Slide 29: Conclusions
Semi-conductor manufacturers are deeply worried about how to deal with soft faults in future architectures (10+ years out)
It’s a killer app for proofs and types

## Slide 30: end!

## Slide 31: The Caveat

## Slide 32: The Caveat
out [2, 3, 3]
bad, but well-typed code:
outputs 3 after no faults
out [2, 3, 3]
outputs 2 after 1 fault
out [2, 2, 3]
Goal: 0-fault and 1-fault executions should be indistinguishable
Solution: computations must independent, but equivalent

## Slide 33: The Caveat
modified typing:
G |--z e1 : R U
G |--z e2 : G U
G |--z e3 : B U
G |--z e4 : T G |--z e1 ~~ e2 G |--z e2 ~~ e3
----------------------------------------------------------------------------
G |-- out [e1, e2, e3]; e4 : T
see
Lester Mackey’s 60 page TR
(a single-semester undergrad project)

## Slide 34: Function O.S. follows

## Slide 35: Lambda Zap: Triples
let [x1, x2, x3] = e1 in e2
Elimination form:
“triples” (as opposed to tuples) make typing
and translation rules very elegant
so we baked them right into the calculus:
[e1, e2, e3]
Introduction form:
a collection of 3 items
not a pointer to a struct
each of 3 stored in separate register
single fault effects at most one

## Slide 36: Lambda to Lambda Zap: Control-flow
let f = \x.e in
f 2
let [f1, f2, f3] = \x. [[ e ]] in
[f1, f2, f3] [2, 2, 2]
majority vote on
control-flow transfer

## Slide 37: Lambda to Lambda Zap: Control-flow
let f = \x.e in
f 2
let [f1, f2, f3] = \x. [[ e ]] in
[f1, f2, f3] [2, 2, 2]
majority vote on
control-flow transfer
(M; let [f1, f2, f3] = \x.e1 in e2)
--->
(M,l=\x.e1; e2[ l / f1][ l / f2][ l / f3])
operational semantics:

## Slide 38: Related Work Follows

## Slide 39: Software Mitigation Techniques
Examples:
  N-version programming, EDDI, CFCSS [Oh et al. 2002], SWIFT [Reis et al. 2005], ...
  Hybrid hardware-software techniques: Watchdog Processors, CRAFT [Reis et al. 2005] , ...
Pros:
  immediate deployment
    would have benefitted Los Alamos Labs, etc...
  policies may be customized to the environment, application
  reduced hardware cost
Cons:
  For the same universal policy, slower (but not as much as you’d think).

## Slide 40: Software Mitigation Techniques
Examples:
  N-version programming, EDDI, CFCSS [Oh et al. 2002], SWIFT [Reis et al. 2005], etc...
  Hybrid hardware-software techniques: Watchdog Processors, CRAFT [Reis et al. 2005] , etc...
Pros:
  immediate deployment: if your system is suffering soft error-related failures, you may deploy new software immediately
    would have benefitted Los Alamos Labs, etc...
  policies may be customized to the environment, application
  reduced hardware cost
Cons:
  For the same universal policy, slower (but not as much as you’d think).
  IT MIGHT NOT ACTUALLY WORK!