## Slide 1: COS 597E: Software Defined Networking
Jennifer Rexford
Princeton University
MW 11:00am-12:20pm

## Slide 2: The State of Networking

## Slide 3: The Internet: A Remarkable Story
Tremendous success
  From research experiment to global infrastructure
Brilliance of under-specifying
  Network: best-effort packet delivery
  Programmable hosts: arbitrary applications
Enables innovation
  Apps: Web, P2P, VoIP, social networks, …
  Links: Ethernet, fiber optics, WiFi, cellular, …

## Slide 4: Inside the ‘Net: A Different Story…
Closed equipment
  Software bundled with hardware
  Vendor-specific interfaces
Over specified
  Slow protocol standardization
Few people can innovate
  Equipment vendors write the code
  Long delays to introduce new features

## Slide 5: Do We Need Innovation Inside?
Many boxes (routers, switches, firewalls, …), with different interfaces.
Notes: Enterprise network.

## Slide 6: Do We Need Intellectual Progress?
Lots of domain details
  Plethora of protocols
  Heaps of header formats
  Big bunch of boxes
  Tons of tools
Teaching networking
  Practitioners: certification courses, on the job
  Undergraduates: how the Internet works

## Slide 7: Software Defined Networking

## Slide 8: Software Defined Networks
control plane: distributed algorithms
data plane: packet processing

## Slide 9: Software Defined Networks
decouple control and data planes

## Slide 10: Software Defined Networks
decouple control and data planes by providing open standard API

## Slide 11: Simple, Open Data-Plane API
Prioritized list of rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 12: (Logically) Centralized Controller
Controller Platform

## Slide 13: Protocols  Applications
Controller Platform
Controller Application

## Slide 14: Seamless Mobility
See host sending traffic at new location
Modify rules to reroute the traffic

## Slide 15: Server Load Balancing
Pre-install load-balancing policy
Split traffic based on source IP
src=0*,
dst=1.2.3.4
src=1*,
dst=1.2.3.4
10.0.0.1
10.0.0.2

## Slide 16: Example SDN Applications
Seamless mobility and migration
Server load balancing
Dynamic access control
Using multiple wireless access points
Energy-efficient networking
Adaptive traffic monitoring
Denial-of-Service attack detection
Network virtualization
See http://www.openflow.org/videos/

## Slide 17: A Major Trend in Networking
Entire backbone
runs on SDN
Bought for $1.2 x 109
(mostly cash)

## Slide 18: An Opportunity to Rethink
How should future networks be
  Designed
  Managed
  Programmed
What are the right abstractions
  Simple
  Powerful
  Reusable

## Slide 19: Structure of the Course

## Slide 20: Syllabus
Introduction (3)
SDN abstractions (6)
SDN applications (4)
SDN systems challenges (4)
Enhancing the data plane (5)
Course wrap-up (2)

## Slide 21: Paper Reading
Read ~2 papers for each class
  Recent research papers on SDN
  Basis for discussions in class
Write reviews (1 page each)
  Summary (problem, solution)
  What you like
  What could use improvement
  What you would do next
Upload reviews to CS Dropbox before class
See “How to Read” on today’s syllabus

## Slide 22: Lightweight Assignments
Programming assignments
  MiniNet platform (due 5pm Mon Sep 16)
  Ryu controller (due 5pm Tue Oct 1)
  Pyretic language (due 5pm Fri Oct 11)
Assignments are not graded
Collaboration policy
  Can freely collaborate with others
  Each person should understand all material
Will help with your course project

## Slide 23: Course Project
Final research project
  Work alone or in teams of 2-3
  Your own topic, or from a list we suggest
Schedule
  Talk to me (and others) about project ideas
  5pm Mon Oct 21: short proposal due
  5pm Tue Jan 14: written report due
  Later that week: short oral presentation

## Slide 24: Grading
0% programming assignments
30% class participation
30% paper reviews
40% course project (paper, talk)

## Slide 25: To Do
Next steps
  Join the Piazza site:https://piazza.com/princeton/fall2013/cos597e/home
  Complete assignment 1 (due Tuesday)
  Read and review 4D and Ethane papers
Brush up on basic Python programming
  http://docs.python.org/2/tutorial/
  http://www.greenteapress.com/thinkpython/html/index.html

## Slide 26: Review of “How the Internet Works”

## Slide 27: Why Review?
SDN interacts with “legacy” networks
  Unmodified end-host computers
  Hybrid deployments of SDN
  Connecting to non-SDN domains
SDN is a reaction to legacy networks
  Challenges of managing and changing them
General lessons on abstractions
  Practice talking about abstractions
  Some abstractions should be retained

## Slide 28: Main Ideas
Best-effort packet delivery
Protocol layering for modularity
  Internet hourglass design
Relationships between layers
  Naming and addressing
  Directories and routing
Scalability
  Through hierarchy and indirection

## Slide 29: Best-Effort Packet Switching
Packet switching
  Divide data into packets
  Packets travel separately
  Enables statistical multiplexing
Best-effort delivery
  Packets may be lost, delayed, out-of-order
  Simplify network design and failure handling
  Build timely, ordered, reliability delivery on top

## Slide 30: Layering: Internet Protocol Stack
Best-effort local packet delivery
Best-effort global packet delivery
Reliable streams
Applications
Messages
Link
Network
Transport
Application

## Slide 31: Layering: End-to-End
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Ethernet frame
Ethernet frame
SONET frame

## Slide 32: Layering: Packet Encapsulation
Different devices switch different things
  Network layer: packets (routers)
  Link layer: frames (bridges and switches)
  Physical layer: electrical signals (repeaters and hubs)
Application
Transport
Router
Bridge, switch
Repeater, hub
Frame header
Packet header
TCP header
User
data

## Slide 33: Link Layer: Adaptors Communicating
Sending side
  Encapsulates packet in a frame
  Adds error checking bits, flow control, etc.
Receiving side
  Looks for errors, flow control, etc.
  Extracts datagram and passes to receiving node
sending
node
frame
receiving
node
packet
frame
adapter
adapter
link layer protocol
packet

## Slide 34: Link Layer: Medium Access Control Address
MAC address (e.g., 00-15-C5-49-04-A9)
  Numerical address used within a link
  Unique, hard-coded in the adapter when it is built
  Flat name space of 48 bits
Hierarchical allocation
  Blocks: assigned to vendors (e.g., Dell) by the IEEE
  Adapters: assigned by the vendor from its block
Broadcast address (i.e., FF-FF-FF-FF-FF-FF)
  Send the frame to all adapters

## Slide 35: Link Layer: Why Not Just Use IP Addresses?
Links can support any network protocol
  Not just for IP (e.g., IPX, Appletalk, X.25, …)
  Different addresses on different kinds of links
An adapter may move to a new location
  So, cannot simply assign a static IP address
  Instead, must reconfigure the adapter’s IP address
Must identify the adapter during bootstrap
  Need to talk to the adapter to assign it an IP address

## Slide 36: Link Layer: Who am I?
71-65-F7-2B-08-53
1A-2F-BB-76-09-AD
0C-C4-11-6F-E3-98
????
1.2.3.5
1.2.3.6
DHCP server
Dynamic Host Configuration Protocol (DHCP)
  Broadcast “I need an IP address, please!”
  Response “You can have IP address 1.2.3.4.”

## Slide 37: Link Layer: Who are You?
Address Resolution Protocol (ARP)
  Broadcast “who has IP address 1.2.3.6?”
  Response “0C-C4-11-6F-E3-98 has 1.2.3.6!”
71-65-F7-2B-08-53
1A-2F-BB-76-09-AD
0C-C4-11-6F-E3-98
1.2.3.4
1.2.3.5
1.2.3.6

## Slide 38: Network Layer: Connect Local Networks
Main challenges
  Scalability
  Autonomy
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN

## Slide 39: Network Layer: Hierarchical Addressing
Network and host portions (left and right)
12.34.158.0/24 is a 24-bit prefix with 28 addresses
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5

## Slide 40: Network Layer: Address and Mask
00001100
00100010
10011110
00000101
12
34
158
5
11111111
11111111
11111111
00000000
255
255
255
0
Address
Mask

## Slide 41: Network Layer: Scalability
Number related hosts from a common subnet
  1.2.3.0/24 on the left LAN
  5.6.7.0/24 on the right LAN
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 42: Network Layer: Who are You?
Domain Name System
  Hierarchical names
  E.g., gaia.cs.umass.edu
Scalability
  Hierarchical directory
  Caching of results
Autonomy
  Separate name space
  Separate servers
requesting host
cis.poly.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server

## Slide 43: Transport Layer: Two Main Ideas
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 44: Transport Layer: User Datagram Protocol (UDP)
Datagram messaging service
  Demultiplexing: port numbers
  Detecting corruption: checksum
Lightweight communication between processes
  Send and receive messages
  Avoid overhead of ordered, reliable delivery
SRC port
DST port
checksum
length
DATA

## Slide 45: Transport Layer: Transmission Control Protocol (TCP)
Stream-of-bytes service
  Sends and receives a stream of bytes
Reliable, in-order delivery
  Corruption: checksums
  Detect loss/reordering: sequence numbers
  Reliable delivery: acknowledgments and retransmissions
Connection oriented
  Explicit set-up and tear-down of TCP connection
Flow control
  Prevent overflow of the receiver’s buffer space
Congestion control
  Adapt to network congestion for the greater good

## Slide 46: Application Layer: HyperText Transfer Protocol
GET /courses/archive/spr12/cos461/ HTTP/1.1
Host: www.cs.princeton.edu
User-Agent: Mozilla/4.03
CRLF
HTTP/1.1 200 OK
Date: Mon, 6 Feb 2012 13:09:03 GMT
Server: Netscape-Enterprise/3.5.1
Last-Modified: Mon, 7 Feb 2011 11:12:23 GMT
Content-Length: 21
CRLF
Site under construction
Request
Response

## Slide 47: Relationship Between Layers
link
name
session

## Slide 48: Discovery: Mapping Name to Address
link
session
path
name
address

## Slide 49: Routing: Mapping Link to Path
link
session
path
name
address

## Slide 50: Names: Different Kinds
Host name (e.g., www.cs.princeton.edu)
  Mnemonic, variable-length, appreciated by humans
  Hierarchical, based on organizations
IP address (e.g., 128.112.7.156)
  Numerical 32-bit address appreciated by routers
  Hierarchical, based on organizations and topology
MAC address (e.g., 00-15-C5-49-04-A9)
  Numerical 48-bit address appreciated by adapters
  Non-hierarchical, unrelated to network topology

## Slide 51: Names: Hierarchical Assignment
Host name: www.cs.princeton.edu
  Domain: registrar for each top-level domain (e.g., .edu)
  Host name: local administrator assigns to each host
IP addresses: 128.112.7.156
  Prefixes: ICANN, regional Internet registries, and ISPs
  Hosts: static configuration, or dynamic using DHCP
MAC addresses: 00-15-C5-49-04-A9
  Blocks: assigned to vendors by the IEEE
  Adapters: assigned by the vendor from its block

## Slide 52: Directories
A key-value store
  Key: name, value: address(es)
  Answer queries: given name, return address(es)
Caching the response
  Reuse the response, for a period of time
  Better performance and lower overhead
Allow entries to change
  Updating the address(es) associated with a name
  Invalidating or expiring cached responses

## Slide 53: Directory Design: Three Extremes
Flood the query (e.g., ARP)
  The named node responds with its address
  But, high overhead in large networks
Push data to all clients (/etc/hosts)
  All nodes store a full copy of the directory
  But, high overhead for many names and updates
Central directory server
  All data and queries handled by one machine
  But, poor performance, scalability, and reliability

## Slide 54: Directory Design: Distributed Solutions
Hierarchical directory (e.g., DNS)
  Follow the hierarchy in the name space
  Distribute the directory, distribute the queries
  Enable decentralized updates to the directory
Distributed Hash Table (e.g. P2P applications)
  Directory as a hash table with flat names
  Each node handles range of hash outputs
  Use hash to direct query to the directory node

## Slide 55: Routing
More Next Time!

## Slide 56: Conclusions
SDN is exciting
  Great industry traction
  Fresh intellectual space
For next time
  Join the Piazza site
  Read and review 4D and Ethane papers
  Assignment 1: MiniNet set-up