## Slide 1
Jennifer Rexford
Princeton University
MW 11:00am-12:20pm
SDN Programming Languages
COS 597E: Software Defined Networking

## Slide 2: Programming SDNs
Images by Billy Perkins
The Good
  Network-wide visibility
  Direct control over the switches
  Simple data-plane abstraction
The Bad
  Low-level programming interface
  Functionality tied to hardware
  Explicit resource control
The Ugly
  Non-modular, non-compositional
  Challenging distributed programming

## Slide 3: Network Control Loop
Read
state
OpenFlow
Switches
Write
policy
Compute Policy

## Slide 4: Language-Based Abstractions
Query abstractions
OpenFlow
Switches
Update abstractions
Writing/combining modules

## Slide 5: Policy as a Function

## Slide 6: Policy in OpenFlow
Defining “policy” is complicated
  All rules in all switches
  Packet-in handlers
  Polling of counters
Programming “policy” is error-prone
  Duplication between rules and handlers
  Frequent changes in policy (e.g., flowmods)
  Policy changes affect packets in flight

## Slide 7: From Rules to a Policy Function
Located packet
  A packet and its location (switch and port)
Policy function
  From located packet to set of located packets
Examples
  Original packet: identity
  Drop the packet: none
  Modified header: modify(f=v)
  New location: fwd(a)

## Slide 8: From Bit Patterns to Predicates
OpenFlow
  No direct way to specify dstip!=10.0.0.1
  Requires two prioritized bitmatches
    Higher priority: dstip=10.0.0.1
    Lower priority: *
Using boolean predicates
  Providing &, |, and ~
  E.g., ~match(dstip=10.0.0.1)

## Slide 9: Virtual Header Fields
Unified abstraction
  Real headers: dstip, srcport, …
  Packet location: switch and port
  User-defined: e.g., traffic_class
Simple operations
  Match: match(f=v)
  Modify: modify(f=v)
Example
  match(switch=A) & match(dstip=‘1.0.0.3’)

## Slide 10: Queries as Buckets
Forwarding to a “bucket”
  Q = packets(limit=1,group_by=['srcip'])
Callback functions
  Q.register_callback(printer)
Multiple kinds of buckets
  Packets: with limit on number
  Packet counts: with time interval
  Byte counts: with time interval

## Slide 11: Power of Policy as a Function
Dynamic policy
  A stream of policy functions
Composition
  Parallel: Monitor + Route
  Sequential: Firewall >> Route
A >> (B + C) >> D
(A >> P) + (B >> P) (A + B)>>P

## Slide 12: Computing Policy
Parallel and Sequential Composition
Topology Abstraction

## Slide 13: Combining Many Networking Tasks
Controller Platform
Monitor + Route + FW + LB
Monolithic application
Hard to program, test, debug, reuse, port, …
Notes: But, real networks perform a wide variety of tasks
Routing, network monitoring, firewalls, server load balancing, etc.

## Slide 14: Modular Controller Applications
Controller Platform
LB
Route
Monitor
FW
Easier to program, test, and debug
Greater reusability and portability
A module for each task

## Slide 15: Beyond Multi-Tenancy
Controller Platform
Slice 1
Slice 2
Slice n
...
Each module controls a different portion of the traffic
Relatively easy to partition rule space, link bandwidth, and network events across modules
Notes: Simple case: multi-tenancy
Each module controls a different subset of the traffic
Relatively easy to partition traffic, rule space, and bandwidth resources
We want to write a single application out of modules that affect the handling of same traffic

## Slide 16: Modules Affect the Same Traffic
Controller Platform
LB
Route
Monitor
FW
How to combine modules into a complete application?
Each module partially specifies the handling of the traffic

## Slide 17: Parallel Composition
Controller Platform
Route on destination
Monitor on source
+
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
srcip = 5.6.7.8  count
Notes: From ICFP’11 and POPL’12

## Slide 18: Parallel Composition
Controller Platform
Route on destination
Monitor on source
+
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
srcip = 5.6.7.8  count
srcip = 5.6.7.8, dstip = 1.2.3.4  fwd(1), count
srcip = 5.6.7.8, dstip = 3.4.5.6  fwd(2), count
srcip = 5.6.7.8  count
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
Notes: From ICFP’11 and POPL’12

## Slide 19: Sequential Composition
Controller Platform
Routing
Load Balancer
>>
dstip = 10.0.0.1  fwd(1)
dstip = 10.0.0.2  fwd(2)
srcip = 0*, dstip=1.2.3.4  dstip=10.0.0.1
srcip = 1*, dstip=1.2.3.4  dstip=10.0.0.2
Notes: Load balancer splits traffic sent to public IP address over multiple replicas, based on client IP address, and rewrites the IP address

## Slide 20: Sequential Composition
Controller Platform
Routing
Load Balancer
>>
dstip = 10.0.0.1  fwd(1)
dstip = 10.0.0.2  fwd(2)
srcip = 0*, dstip=1.2.3.4  dstip=10.0.0.1
srcip = 1*, dstip=1.2.3.4  dstip=10.0.0.2
srcip = 0*, dstip = 1.2.3.4  dstip = 10.0.0.1, fwd(1)
srcip = 1*, dstip = 1.2.3.4  dstip = 10.0.0.2, fwd(2)
Notes: Load balancer splits traffic sent to public IP address over multiple replicas, based on client IP address, and rewrites the IP address

## Slide 21: Dividing the Traffic Over Modules
Predicates
  Specify which traffic traverses which modules
  Based on input port and packet-header fields
Routing
Load Balancer
Monitor
Routing
Non-web
dstport != 80
Web traffic
dstport = 80
>>
+

## Slide 22: Abstract Topology: Load Balancer
Present an abstract topology
  Information hiding: limit what a module sees
  Protection: limit what a module does
  Abstraction: present a familiar interface
22
Real network
Abstract view

## Slide 23: Abstract Topology: Gateway
IP Core
Ethernet

## Slide 24: Abstract Topology: Gateway
Left: learning switch on MAC addresses
Middle: ARP on gateway, plus simple repeater
Right: shortest-path forwarding on IP prefixes
IP Core
Ethernet
IP Core
Gateway
Ethernet

## Slide 25: High-Level Architecture
Controller Platform
M1
M2
M3
Main
Program

## Slide 26: Paper Discussion
Pyretic and Maple

## Slide 27: Questions
Other ways to combine multiple policies?
How to compile policies efficiently?
Relationships to the other papers we’ve read (e.g., HSA, VeriFlow, NICE, ndb)?
Comparison of Pyretic and Maple?
Support for distributed controllers, fault tolerance, supporting more sophisticated switches, etc.?