## Slide 1
Jennifer Rexford
Princeton University
MW 11:00am-12:20pm
Wide-Area Traffic Management
COS 597E: Software Defined Networking

## Slide 2: Traffic Management
Assigning resources to traffic
  Optimize some objective
    Min congestion, max utility, min delay, …
  Given network resource constraints
Three main “knobs”
  Routing: what path(s) the traffic takes
  Link scheduling: how to share each link
  Rate control: how much a source can send
Host/network split
  Host: rate control
  Network: routing and link scheduling

## Slide 3: Simple Traffic Management
Protocols adapt automatically
  TCP senders send less traffic during congestion
  Routing protocols adapt to topology changes
But, does the network run efficiently?
  Congested link when idle paths exist?
  High-delay path when a low-delay path exists?
How should routing adapt to the traffic?
  Avoiding congested links in the network
  Satisfying application requirements (e.g., delay)

## Slide 4: Automatically Adapting the Link Weights
ARPAnet Routing

## Slide 5: Original ARPAnet Routing (1969)
Routing
  Shortest-path routing based on link metrics
  Distance-vector algorithm (i.e., Bellman-Ford)
Link metrics
  Instantaneous queue length plus a constant
  Each node updates distance computation
3
2
2
1
1
3
1
5
20
congested link

## Slide 6: Problems With the Algorithm
Instantaneous queue length
  Poor indicator of expected delay
  Fluctuates widely, even at low traffic levels
  Leading to routing oscillations
Distance-vector routing
  Transient loops during (slow) convergence
  Triggered by link weight changes, not just failures
Protocol overhead
  Frequent dissemination of link metric changes
  Leading to high overhead in larger topologies

## Slide 7: New ARPAnet Routing (1979)
Averaging of the link metric over time
  Old: Instantaneous delay fluctuates a lot
  New: Averaging reduces the fluctuations
Link-state protocol
  Old: Distance-vector computation leads to loops
  New: Link-state protocol where each router computes paths based on the complete topology
Reduce frequency of updates
  Old: Too many update messages
  New: Send updates if change passes a threshold

## Slide 8: Performance of New Algorithm
Light load
  Delay dominated by the constant part (transmission delay and propagation delay)
Medium load
  Queuing delay is no longer negligible on all links
  Moderate traffic shifts to avoid congestion
Heavy load
  Very high metrics on congested links
  Busy links look bad to all of the routers
  Routers may send packets on longer paths

## Slide 9: Revised ARPAnet Metric (1987)
Limit path length
  Bound the value of the link metric
  “This link is busy enough to go two extra hops”
Prevent over-reacting
  Shed traffic from a congested link gradually
  Starting with alternate paths that are slightly longer
  Through weighted average in computing the metric, and limits on the change from one period to the next
New algorithm
  New way of computing the link weights
  No change to routing protocol or path computation

## Slide 10: Optimizing the “Static” Link Weights

## Slide 11: Routing With “Static” Link Weights
Routers flood information to learn topology
  Determine “next hop” to reach other routers…
  Compute shortest paths based on link weights
Link weights configured by the operator
3
2
2
1
1
3
1
4
5
3

## Slide 12: Setting the Link Weights
How to set the weights
  Inversely proportional to link capacity?
  Proportional to propagation delay?
  Network-wide optimization based on traffic?
3
2
2
1
1
3
1
4
5
3
3

## Slide 13: Measure, Model, Control
Topology/
Configuration
Offered
traffic
Changes to
link weights
Operational network
Network-wide
“what if” model
measure
control

## Slide 14: Pros and Cons
Advantages
  Network-wide optimization
  Avoids oscillation
  No changes to the routing protocols
Disadvantages
  Overhead of collecting the measurements
  Limited splitting of traffic over multiple paths
  Computational complexity of the optimization
  Transient disruptions during weight changes
So, performed at a slow time scale (hours)

## Slide 15: MPLS-TE
MultiProtocol Label Switching

## Slide 16: Explicit End-to-End Paths
Establish end-to-end path in advance
  Learn the topology (as in link-state routing)
  End host or router computes and signals a path
Routers supports virtual circuits
  Signaling: install entry for each circuit at each hop
  Forwarding: look up the circuit id in the table
1
2
1: 7
2: 7
link 7
1: 14
2: 8
link 14
link 8

## Slide 17: MPLS-TE
Learn about congestion
  Dynamically changing link weights
Reserve resources on paths
  Pick a path, and signal to reserve resources
Change paths during congestion
  Pick a new path, and reserve resources
More flexible, but still some limitations
  Uncoordinated decisions at different nodes
  Suboptimal decisions, and non-deterministic
  Complex interaction of several protocols