## Slide 1
Jennifer Rexford
Princeton University
MW 11:00am-12:20pm
Control-Plane Scalability
COS 597E: Software Defined Networking

## Slide 2: Controller Scalability Challenges
Number of switches
  Number of control sessions
  Frequency of events
  Size of topology state
Performance metrics
  Throughput: flow rules installed per second
  Latency: delay to handle a packet-in

## Slide 3: NOX Controller
NOX controller
  Single-threaded, unoptimized C++ controller
  30K flow initiations per second
  Sub-10ms flow install time
NOX-MT
  Multi-threaded, better I/O handling, optimized malloc() implementation, …
  On an 8-core machine, 1.6M request/sec and average response time of 2 msec

## Slide 4: Distributed Controllers
Better scalability
  Smaller topology
  Fewer events
  Fewer flow installations
Better performance
  Closer to the switches
  Lower control-plane latency
Better reliability
  Failover to a backup controller

## Slide 5: Controller Configurations
Hierarchical
  Global controller, with multiple local controllers
Peers
  Each handling different portions of the topology, flow space, slice, or applications
Replicas
  Master, with multiple slaves
  Multiple active replicas

## Slide 6: Working with Multiple Controllers
Local scope
  MAC learning
  Elephant flow detection
  Aggregate/threshold traffic statistics
Network-wide scope
  Computing shortest paths
  Selecting links to shut down to save energy
  User mobility and virtual machine migration

## Slide 7: Discussion Questions
Does the programmer know there is a multi-threaded/distributed controller?
  Automated partitioning? Language constructs?
Does the application have to behave exactly the same as on a single controller?
  Approximate shortest paths?
Do the techniques for scalability interact with the techniques for fault tolerance?
  Shared reliable distributed data store?
Any useful changes to OpenFlow protocol?

## Slide 8: Going Through Some Examples
MAC learning
Histogram by source IP address
Stateful firewall
Shortest-path routing
MAC learning at edge, shortest-path in core
Traffic engineering
Consistent updates
Hedera (elephant flow routing)