## Slide 1
Jennifer Rexford
Princeton University
MW 11:00am-12:20pm
Measurement
COS 597E: Software Defined Networking

## Slide 2: Measurement vs. Metrics
active
measurements
packet and flow
measurements,
link load
topology,
configuration,
routing, link properties
end-to-end
performance
state
traffic
average download
time of a web page
link bit
error rate
link utilization
end-to-end delay
and loss
active topology
traffic matrix
demand matrix
active routes
TCP bulk
throughput

## Slide 3: Reducing Measurement Overhead
Filtering, Aggregation, and Sampling

## Slide 4: Reducing Measurement Overhead
Measurement overhead
  In some areas, you could measure everything
  Information processing not the bottleneck
  Networking: thinning is crucial!
Reducing measurement traffic:
  Filtering
  Aggregation
  Sampling
  ...and combinations thereof

## Slide 5: Filtering
Measure selectively
  Only record statistics for a subset of traffic
Examples
  Matching a destination prefix
  For a certain service class
  Violating an access control list
  TCP SYN or RST packets (attacks, abandoned http download)

## Slide 6: Aggregation
Coarse-grained statistics
  Combine related traffic together
Example: srcip and dstip
src | dest | # pkts | # bytes
a.b.c.d | m.n.o.p | 374 | 85498
e.f.g.h | q.r.s.t | 7 | 280
i.j.k.l | u.v.w.x | 48 | 3465
.... | .... | .... | 

## Slide 7: Sampling
Select a “random” subset of traffic
  Representative of all traffic
Examples
  Random
  Round-robin
  Hash-based
X
X
X
X
X
16 packets: estimate ¾ blue and ¼ red

## Slide 8: Comparison
Sampling
Filtering
Aggregation
Generality
Local
Processing
Local memory
Compression
Precision
exact
exact
approximate
constrained
a-priori
constrained
a-priori
general
filter criterion
for every object
table update
for every object
only sampling
decision
none
one bin per
value of interest
none
depends
on data
depends
on data
controlled

## Slide 9: Traffic Monitoring Techniques
Links, Flows, and Packets

## Slide 10: Traffic Monitoring Techniques
Link monitoring
  Group all packets on the same link
  Average load, loss, corruption, …
Flow monitoring
  Group similar packets into flows
  Same header fields and close in time
Packet monitoring
  Capture first n bytes of a packet

## Slide 11: IP Flows
Set of packets that “belong together”
  Source/destination IP addresses and port numbers
  Same protocol, ToS bits, …
  Same input/output interfaces at a router (if known)
Packets that are “close” together in time
  Max spacing between packets (e.g., 15 sec, 30 sec)
  Example: flows 2 and 4 are different flows due to time
flow 1
flow 2
flow 3
flow 4

## Slide 12: Netflow: Traffic Data
Packet header information
  Src/dst IP, src/dst port numbers, ToS bits, …
Summary statistics
  Start and finish times
  Number of bytes and packets
  TCP flags (logical OR over all packets)
start
finish
4 packets
1436 bytes
SYN, ACK, & FIN
SYN
ACK
ACK
FIN

## Slide 13: Netflow: Routing Information
Routing information
  Input and output ports
  Source and destination prefix
  Source and destination Autonomous System
Switching
Fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
BGP table
forwarding table

## Slide 14: Netflow: Measuring in Passing
input
output
source AS
source
prefix
source
dest AS
dest
prefix
dest
intermediate AS
Source and destination: IP header
Source and dest prefix: forwarding table or BGP table
Source and destination AS: BGP table

## Slide 15: Netflow: Implementation
Maintain a cache of active flows
  Storage of byte/packet counts, timestamps, etc.
Compute a key per incoming packet
  Concatenation of source, destination, port #s, etc.
Index into the flow cache based on the key
  Creation or updating of an entry in the flow cache
#bytes, #packets, start, finish
#bytes, #packets, start, finish
packet
key
header
key
key

## Slide 16: Netflow: Implementation
Flow timeout
  Remove flows that have not received a packet recently
  Periodic sequencing through the cache to time out flows
Cache replacement
  Remove flow(s) when the flow cache is full
  Evict existing flow(s) upon creating a new cache entry
  Apply eviction policy (LRU, random flow, etc.)
Long-lived flows
  Remove flow(s) that persist for a long time (e.g., 30 min)
  … otherwise flow statistics don’t become available
  … and the byte and packet counters might overflow

## Slide 17: Sampled Netflow
Packet sampling
  Perform operations on 1/m packets
Reducing overhead
  Avoid per-packet overhead on (m-1)/m packets
  Avoid creating records for the many small flows
May split some long flows
time
not sampled
two flows
timeout

## Slide 18: Netflow vs. sFlow
Netflow
  Aggregates (sampled) IP packets into flows
  (Data-plane overhead of storing flow state)
  Originally only on Cisco routers
sFlow
  Exports packet samples directly
  Measures layer-two packets (ARP, DHCP)
  Polls on-switch counters
http://blog.sflow.com/2011/10/comparing-sflow-and-netflow-in-vswitch.html

## Slide 19: Sketches

## Slide 20: Streaming Algorithms
Processing data streams
  Input items presented one at a time
  Each item examined (say) only once
Limited resources
  Processing
  Memory
Approximate answer
  Based on a summary or “sketch” of the data
  Provable space-accuracy trade-off

## Slide 21: Bloom Filter
Set-membership problem
  Was element x in the input stream?
Solution (with false positives)
  Per-item: compute s hash functions, set bit to1
  Query: compute s hashes, check if all bits are 1
h1(x)
h2(x)
hs(x)
0
1
0
0
0
1
0
1
0
0
0
0
0
1
0
x
V0
Vm-1
h3(x)

## Slide 22: Count Min Sketch
Counting problem
  Count number of occurrences of item x
Solution
  Per-item: compute s hashes, increment counts
  Query: compute s hashes, select the min value
h1(x)
h2(x)
23
19
15
30
29
x
h3(x)
22
14
18
27
34
22
10
14
31
30

## Slide 23: SDN Measurement
OpenFlow 1.0
  Rules with byte and packet counters
  Sending packets to a collector or controller
Existing measurement techniques
  E.g., sFlow support
What measurement support do we want?