## Slide 1
Jennifer Rexford
Princeton University
MW 11:00am-12:20pm
Programmable Data Planes
COS 597E: Software Defined Networking

## Slide 2: Data Plane
Streaming algorithms that act on packets
  Matching on some bits, taking a simple action
  … at behest of control and management plane
Wide range of functionality
  Forwarding and access control
  Buffering, marking, shaping, and scheduling
  Rewriting header fields (e.g., NAT)
  Traffic monitoring and deep packet inspection
  Encryption, compression, and transcoding

## Slide 3: A Need for Speed
High link speed
  10 Gbps, 40 Gbps, 100 Gbps
Small packets
  40-byte TCP ACK packets
Small time per packet
  40 Gbps =124 Mpps with 320-bit packets
  8 ns to process a packet
Routers need low latency
  Relatively limited opportunity to batch or pipeline

## Slide 4: A Range of Technologies
ASIC (App-Specific Integrated Circuit)
  Fast, dense chip, but expensive to change
FPGAs and network processors
  Fast, reconfigurable, hard to program
Graphics Processing Units
  Massive parallel computation on small cores
Software on commodity computer
  Easy to program, but I/O bandwidth, memory copying, and interrupt overheads

## Slide 5: Click Modular Router

## Slide 6: Click Motivation
Flexibility
  Add new features and enable experimentation
Openness
  Allow users/researchers to build and extend
  (In contrast to most commercial routers)
Modularity
  Simplify the composition of existing features
  Simplify the addition of new features
Speed/efficiency
  Operation (optionally) in the operating system
  Without user needing to grapple with OS internals

## Slide 7: Router as a Graph of Elements
Large number of small elements
  Each performing a simple packet function
  E.g., IP look-up, TTL decrement, buffering
Connected together in a graph
  Elements inputs/outputs snapped together
  Beyond elements in series to a graph
  E.g., packet duplication or classification
Packet flow as main organizational primitive
  Consistent with data-plane operations on a router
  (Larger elements needed for, say, control planes)

## Slide 8: Push vs. Pull
Packet hand-off between elements
  Directly inspired by properties of routers
  Annotations on packets to carry temporary state
Push processing
  Initiated by the source end
  E.g., when an unsolicited packet arrives (e.g., from a device)
Pull processing
  Initiated by the destination end
  E.g., to control timing of packet processing (e.g., based on a timer or packet scheduler)

## Slide 9: Click Language
Declarations
  Create elements
Connections
  Connect elements
Compound elements
  Combine multiple smaller elements, and treat as single, new element to use as a primitive class
Language extensions through element classes
  Configuration strings for individual elements
  Rather than syntactic extensions to the language
src :: FromDevice(eth0);
ctr :: Counter;
sink :: Discard;
src -> ctr;
ctr -> sink;

## Slide 10: Handlers and Control Socket
Access points for user interaction
  Appear like files in a file system
  Can have both read and write handlers
Examples
  Installing/removing forwarding-table entries
  Reporting measurement statistics
  Changing a maximum queue length
Control socket
  Allows other programs to call read/write handlers
  Command sent as single line of text to the server

## Slide 11: An Observation…
Click is widely used
  And the paper on Click is widely cited
Click elements are created by others
  Enabling an ecosystem of innovation
Take-away lesson
  Creating useful systems that others can use and extend has big impact in the research community
  And brings tremendous professional value
  Compensating amply for the time and energy 