## Slide 1: COS 561: Advanced Computer Networks
Jennifer Rexford
Fall 2017 (TTh 1:30-2:50pm in CS 105)
http://www.cs.princeton.edu/courses/archive/fall17/cos561/
Notes: <number>

## Slide 2: The Internet: An Exciting Time
One of the most influential inventions
  A research experiment that escaped from the lab
  … to be a global communications infrastructure
Ever wider reach
  Today: more than 3 billion users
  Tomorrow: more users, computers, things, …
Near-constant innovation
  Apps: Web, P2P, social networks, virtual worlds
  Links: optics, WiFi, cellular, WiMax, ...
<number>

## Slide 3: Transforming Everything
The ways we do business
  E-commerce, advertising, cloud computing, ...
The way we have relationships
  E-mail, IM, Facebook, virtual worlds, online dating
How we think about law
  Interstate commerce? National boundaries?
The way we govern
  E-voting and e-government
  Censorship and wiretapping
The way we fight
  Cyber-attacks, including nation-state attacks
<number>

## Slide 4: The Study of Networking is Cool
Tangible, relates to reality
  Can measure and build things
  Can truly effect far-reaching change in the real world
Inherently interdisciplinary
  Well-motivated problems + rigorous solution techniques
  Interplay with policy, economics, and social science
Widely-read papers
  Many of the most cited papers in CS are in networking
  Congestion control, distributed hash tables, resource reservation, self-similar traffic, multimedia protocols,…
<number>
Notes: <number>

## Slide 5: The Study of Networking is Cool
Young, relatively immature field
  Great if you like to make order out of chaos
  Tremendous intellectual progress is still needed
  You can help decide what networking really is
Defining the problem is a big part of the challenge
  Recognizing a need, formulating a well-defined problem
  … is at least as important as solving the problem…
Lots of platforms for building your ideas
  Programmability: Click, OpenFlow, NetFPGA, P4
  Routing software: Quagga, XORP, Bird, ExaBGP
  Testbeds: Emulab, PlanetLab, Orbit, GENI, …
  Measurements: RouteViews, traceroute, Internet2, …
<number>
Notes: <number>

## Slide 6: But, What is Networking?
<number>

## Slide 7: A Plethora of Protocol Acronyms?
<number>
BGP
ARP
HTTP
DNS
PPP
OSPF
DHCP
TCP
UDP
SMTP
FTP
SSH
MAC
IP
RIP
NAT
CIDR
VLAN
VTP
NNTP
POP
IMAP
RED
ECN
SACK
SNMP
TFTP
TLS
WAP
SIP
IPX
STUN
RTP
RTSP
RTCP
PIM
IGMP
ICMP
MPLS
LDP
HIP
LISP
LLDP
BFD
Notes: Red: network layer
Green: transport layer
Purple: application layer
Blue: routing
Orange: enterprise/edge networks
Black: other stuff
Most have three or four letters, except IP has just two. But IP is special, as it is the center of the known universe.
<number>

## Slide 8: A Heap of Header Formats?
<number>
Notes: Header formats have gotten more colorful in recent years, but they are still awfully boring. Zzzzz…
Have you seen the lego version of the IP and TCP header?
<number>

## Slide 9: TCP/IP Header Formats in Lego
<number>

## Slide 10: A Big Bunch of Boxes?
<number>
Router
Switch
Firewall
NAT
Load
balancer
DHCP
server
DNS
server
Bridge
Hub
Repeater
Base
station
Proxy
WAN
accelerator
Gateway
Intrusion
Detection
System
Packet
shaper
Route
Reflector
Label
Switched
Router
Scrubber
Packet
sniffer
Deep
Packet
Inspection
Notes: Ask yourself what is the real difference between these components? Do we need to think of them as distinct?
Can a common piece of hardware support many of these functions?
Do ever need to do more than one of these functions at the same time and place?
<number>

## Slide 11: A Ton of Tools?
<number>
traceroute
nslookup
ping
ipconfig
rancid
whois
tcpdump
wireshark
NDT
iperf
dummynet
syslog
trat
snort
bro
arpwatch
mrtg
nmap
ntop
dig
wget
net-snmp
Notes: <number>

## Slide 12: A Ton of Tools?
<number>
traceroute
nslookup
ping
ipconfig
rancid
whois
tcpdump
wireshark
NDT
iperf
dummynet
syslog
trat
snort
bro
arpwatch
mrtg
nmap
ntop
dig
wget
net-snmp
Notes: Rancid = really awesome new cisco config differ
<number>

## Slide 13: What Do Peers in Other Fields Say?
“You networking people are very curious. You really love your artifacts.”
“In my college networking class I fell asleep at the start of the semester when the IP header was on the screen, and woke up at the end of the semester with the TCP header on the screen.”
“Networking is all details and no principles.”
“COS 461 final. ARP, DHCP, ICMP, IGMP, IP, SONET, TCP, UDP, FML.” (from princetonfml.com)
<number>
Is networking “just the (arti)facts”?

## Slide 14: What Peers in Other Fields Say?
“Networking papers are strange. They have a lot of text.”
“What are the top ten classic problems in networking? I would like to solve one of them and submit a paper to SIGCOMM.” After hearing that we don't have such a list: "Then how do you consider networking a discipline?”
“So, these networking research people today aren't doing theory, and yet they aren't the people who brought us the Internet. What exactly are they doing?”
“Networking is an opportunistic discipline.”
<number>
Is networking a problem domain or a scholarly discipline?

## Slide 15: But, That Doesn’t Say What Networking Really Is
Or, What Will This Course Be About?
<number>

## Slide 16: One Take on Defining Networking
How to
  Design and manage protocols
  That can be used and combined in many ways
  To do many things
Definition and placement of function
  What to do, and where to do it
The “division of labor”
  Across multiple protocols and mechanisms
  Across components (hosts, routers, administrators)
Goal: search for general principles
  Of protocol design, evaluation, and composition
<number>

## Slide 17: What is a Network Protocol?
Rules that govern communication
  How to identify the devices and establish connectivity
  Message format (syntax) and meaning (semantics)
Distributed solution to a problem
  Deliver an ordered, reliable stream of bytes
  Share link or network bandwidth fairly
  Compute a shortest path on a graph
Tunable platform for network administrators
  Buffer space for incoming data on receiving hosts
  Link weights used to compute shortest paths
  Policies for selecting wide-area Internet paths
<number>

## Slide 18: Syllabus
Course overview
End hosts (TCP congestion control)
Control plane (BGP interdomain routing)
Data plane (programmability with SDN)
Names and locations (DNS, mobility)
Applications (DHTs, P2P, CDNs, video streaming)
Looking forward
<number>

## Slide 19: Structure of the Course
Reading and analyzing research papers
  Design and evaluation of network protocols
  Summaries, critiques, and comparisons of the papers
Classroom time
  Brief overview of background material
  Discussion and debate about the research papers
Programming assignments
  TCP performance, BGP policies, and SDN
  Understanding network protocols empirically
Final research project
  Novel research with a system-building component
<number>

## Slide 20: Course Logistics: Final Project
Final project
  Open-ended research problem
  Can work alone or in small teams
  Must involve writing some software
  Example topics will be presented in class
Can overlap with other projects, with permission
  Undergraduate independent work
  Graduate student research projects
Deliverables
  Short proposal: Nov 17
  Presentation: around Jan 12 (before Dean’s Date)
  Six-page final report: Jan 16 (Dean’s Date)
<number>

## Slide 21: Grading
Class participation (30%)
  Discussion in class is important! Speak up!!
  Paper reviews presented in class
Assignments (30%)
  Three assignments, 10% each
Final project (40%)
  Proposal, presentation, and report
<number>

## Slide 22: Teaching Assistants
Noah Apthorpe
  apthorpe@cs.princeton.edu
<number>
Zhelun (Allen) Wu
  zhelunw@cs.princeton.edu

## Slide 23: Getting Started…
Best-effort packet delivery service
Modularity through layering
Directories and routing
Data, control, and management planes
<number>

## Slide 24: Best-Effort Packet-Delivery Service
<number>

## Slide 25: Host-Network Division of Labor
<number>
Packet switching
  Divide messages into a sequence of packets
  Headers with source and destination address
Best-effort delivery
  Packets may be lost
  Packets may be corrupted
  Packets may be delivered out of order
host
host
network
Notes: <number>

## Slide 26: Host-Network Interface: Why Packets?
<number>
Data traffic is bursty
  Logging in to remote machines
  Exchanging e-mail messages
Don’t want to waste bandwidth
  No traffic exchanged during idle periods
Better to allow multiplexing
  Different transfers share access to same links
Packets can be delivered by most anything
  RFC 1149: IP Datagrams over Avian Carriers
Notes: <number>

## Slide 27: Host-Network Interface: Why Best-Effort?
<number>
Never having to say you’re sorry…
  Don’t reserve bandwidth and memory
  Don’t do error detection & correction
  Don’t remember from one packet to next
Easier to survive failures
  Transient disruptions are okay during failover
Can run on nearly any link technology
  Greater interoperability and evolution
Notes: <number>

## Slide 28: Intermediate Transport Layer
<number>
But, applications want efficient, accurate transfer of data in order, in a timely fashion
  Let the end hosts handle all of that
  (An example of the “end-to-end argument”)
Transport layer can optionally…
  Detect and retransmit lost packets
  Put out-of-order packets back in order
  Detect and handle corrupted packets
  Avoid overloading the receiver
  <insert your requirement here>
Notes: <number>

## Slide 29: Modularity Through Layering
<number>

## Slide 30: IP Protocol Stack
<number>
Best-effort local packet delivery
Best-effort global packet delivery
Reliable streams
Applications
Messages
Link
Network
Transport
Application

## Slide 31: IP Suite: End Hosts vs. Routers
<number>
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Notes: <number>

## Slide 32: The “Narrow Waist” of IP
<number>
UDP
TCP
Data Link
Physical
Applications
The Hourglass Model
Waist
The waist facilitates interoperability
FTP
HTTP
TFTP
NV
TCP
UDP
IP
NET1
NET2
NETn
…
Notes: <number>

## Slide 33: Layer Encapsulation
<number>
Get index.html
Connection ID
Source/Destination
Link Address
User A
User B
Notes: <number>

## Slide 34: Directories and Routing
<number>

## Slide 35: Relationship Between Layers
<number>
link
session
path
name
address

## Slide 36: Directories: Mapping Name to Address
<number>
link
session
path
name
address

## Slide 37: Types of Directories
Simplistic designs
  Ask everyone (e.g., flooding in ARP)
  Tell everyone (e.g., pushing /etc/hosts)
  Central directory
Scalable distributed designs
  Hierarchical namespace (e.g., DNS)
  Flat name space (e.g., Distributed Hash Table)
<number>

## Slide 38: Routing: Mapping Link to Path
<number>
link
session
path
name
address

## Slide 39: Path Computation
Spanning tree (e.g., Ethernet)
  One tree that connects every pair of nodes
Shortest paths (e.g., OSPF, IS-IS, RIP)
  Shortest-path tree rooted at each node
Locally optimal paths (e.g., BGP)
  Each node selects the best among its neighbors
End-to-end paths (e.g., source routing)
  Each node picks the best end-to-end path
<number>

## Slide 40: Data, Control, and Management Planes
<number>

## Slide 41: Inside the Network
<number>
Forward packets from the sender to the receiver

## Slide 42: Split into Data vs. Control Plane
Data plane: packets
  Handle individual packets as they arrive
  Forward, drop, or buffer
  Mark, shape, schedule, …
Control plane: events
  Track changes in network topology
  Compute paths through the network
  Reserve resources along a path
<number>
Motivated by need for high-speed packet forwarding

## Slide 43: Adding the Management Plane
Making the network run well
  Traffic reaches the right destination
  Traffic flows over short, uncongested paths
  Unwanted traffic is discarded
  Failure recovery happens quickly
  Routers don’t run out of resources
A control loop with the network
  Measure (sense): topology, traffic, performance, …
  Control (actuate): configure control and data planes
<number>

## Slide 44: How to Read
You May Think You Already Know How To Read, But…
<number>

## Slide 45: You Spend a Lot of Time Reading
Reading for grad classes
Reviewing conference submissions
Giving colleagues feedback
Keeping up with your field
Staying broadly educated
Transitioning into a new areas
Learning how to write better papers 
<number>
It is worthwhile to learn to read effectively

## Slide 46: Keshav’s Three-Pass Approach: Step 1
A ten-minute scan to get the general idea
  Title, abstract, and introduction
  Section and subsection titles
  Conclusion and bibliography
What to learn: the five C’s
  Category: What type of paper is it?
  Context: What body of work does it relate to?
  Correctness: Do the assumptions seem valid?
  Contributions: What are the main research contributions?
  Clarity: Is the paper well-written?
Decide whether to read further…
<number>
Notes: Keep this in mind when you write your papers, so the readers (and reviewers) decide to read further… 
<number>

## Slide 47: Keshav’s Three-Pass Approach: Step 2
A more careful, one-hour reading
  Read with greater care, but ignore details like proofs
  Figures, diagrams, and illustrations
  Mark relevant references for later reading
Grasp the content of the paper
  Be able to summarize the main idea
  Identify whether you can (or should) fully understand
Decide whether to
  Abandon reading in greater depth
  Read background material before proceeding further
  Persevere and continue for a third pass
<number>

## Slide 48: Keshav’s Three-Pass Approach: Step 3
Several-hour virtual re-implementation of the work
  Making the same assumptions, recreate the work
  Identify the paper’s innovations and its failings
  Identify and challenge every assumption
  Think how you would present the ideas yourself
  Jot down ideas for future work
When should you read this carefully?
  Reviewing for a conference or journal
  Giving colleagues feedback on a paper
  Understanding a paper closely related to your research
  Deeply understanding a classic paper in the field
<number>

## Slide 49: Other Tips for Reading Papers
Read at the right level for what you need
  “Work smarter, not harder”
Read at the right time of day
  When you are fresh, not sleepy
Read in the right place
  Where you are not distracted, and have enough time
Read actively
  With a purpose (what is your goal?)
  With a pen or computer to take notes
Read critically
  Think, question, challenge, critique, …
<number>

## Slide 50: For Next Time
Sign up
  Piazza
Read
  Original 1974 paper proposing TCP/IP
  The 1984 paper on the “end-to-end argument”
<number>