## Slide 1
Jennifer Rexford
Fall 2017 (TTh 1:30-2:50 in CS 105)
COS 561: Advanced Computer Networks
http://www.cs.princeton.edu/courses/archive/fall17/cos561/
BGP Instability
Notes: <number>

## Slide 2: Border Gateway Protocol
ASes exchange info about who they can reach
  IP prefix: block of destination IP addresses
  AS path: sequence of ASes along the path
Policies configured by the AS’s operator
  Path selection: which of the paths to use?
  Path export: which neighbors to tell?
3
2
1
12.34.158.5
“12.34.158.0/24:
path (2,1)”
“12.34.158.0/24:
path (1)”
data traffic
data traffic

## Slide 3: BGP Session Operation
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP session
Notes: <number>

## Slide 4: Incremental Protocol
<number>
A node learns multiple paths to destination
  Stores all of the routes in a routing table
  Applies policy to select a single active route
  … and may advertise the route to its neighbors
Incremental updates
  Announcement
    Upon selecting a new active route, add node id to path
    … and (optionally) advertise to each neighbor
  Withdrawal
    If the active route is no longer available
    … send a withdrawal message to the neighbors
Notes: <number>

## Slide 5: Applying Policy to Routes
Import policy
  Filter unwanted routes from neighbor
    E.g. prefix that your customer doesn’t own
  Manipulate attributes to influence path selection
    E.g., assign local preference to favored routes
Export policy
  Filter routes you don’t want to tell your neighbor
    E.g., don’t tell a peer a route learned from other peer
  Manipulate attributes to control what they see
    E.g., make a path look artificially longer than it is

## Slide 6: BGP Policy: Influencing Decisions
Best Route
Selection
Apply Import
Policies
Best Route
Table
Apply Export
Policies
Install forwarding
entries for best routes.
Receive
BGP
Updates
Best
Routes
Transmit
BGP
Updates
Apply Policy =
filter routes &
tweak attributes
Based on
Attribute
Values
IP Forwarding Table
Apply Policy =
filter routes &
tweak attributes
Open ended programming.
Constrained only by vendor configuration language
Notes: <number>

## Slide 7: BGP Decision Process on a Router
Routing Information Base
  Store all BGP routes for each destination prefix
  Withdrawal message: remove the route entry
  Advertisement message: update the route entry
Selecting the best route
  Consider all BGP routes for the prefix
  Apply rules for comparing the routes
  Select the one best route
    Use this route in the forwarding table
    Send this route to neighbors

## Slide 8: BGP Decision Process
Highest local preference
  Set by import policies upon receiving advertisement
Shortest AS path
  Included in the route advertisement
Lowest origin type
  Included in advertisement or reset by import policy
Smallest multiple exit discriminator
  Included in the advertisement or reset by import policy
Smallest internal path cost to the next hop
  Based on intradomain routing protocol (e.g., OSPF)
Smallest next-hop router id
  Final tie-break

## Slide 9: Hot-Potato Routing
San Francisco
Dallas
New York
Hot-potato routing = route to closest egress point when there is more than one
best BGP route to destination
ISP network
9
10
dest
multiple egress points
Notes: <number>
this and the next slide explain the problem. explain egress point
link weights determine both intradomain path and selection of egress points

## Slide 10: Causes of BGP Routing Changes
Topology changes
  Equipment going up or down
  Deployment of new routers or sessions
BGP session failures
  Due to equipment failures, maintenance, etc.
  Or, due to congestion on the physical path
Changes in routing policy
  Reconfiguration of preferences
  Reconfiguration of route filters
Persistent protocol oscillation
  Policy conflicts

## Slide 11: BGP Session Failure
BGP runs over TCP
  BGP only sends updates when changes occur
  TCP doesn’t detect lost connectivity on its own
Detecting a failure
  Keep-alive: 60 seconds
  Hold timer: 180 seconds
Reacting to a failure
  Discard all routes learned from neighbor
  Send updates for any routes that change
AS1
AS2

## Slide 12: Routing Change: Before and After
0
1
2
3
0
1
2
3
(1,0)
(2,0)
(3,1,0)
(2,0)
(1,2,0)
(3,2,0)

## Slide 13: Routing Change: Path Exploration
AS 1
  Delete the route (1,0)
  Switch to next route (1,2,0)
  Send route (1,2,0) to AS 3
AS 3
  Sees (1,2,0) replace (1,0)
  Compares to route (2,0)
  Switches to using AS 2
0
1
2
3
(2,0)
(1,2,0)
(3,2,0)

## Slide 14: Routing Change: Path Exploration
Initial situation
  Destination 0 is alive
  All ASes use direct path
When destination dies
  All ASes lose direct path
  All switch to longer paths
  Eventually withdrawn
E.g., AS 2
  (2,0)  (2,1,0)
  (2,1,0)  (2,3,0)
  (2,3,0)  (2,1,3,0)
  (2,1,3,0)  null
1
2
3
0
(1,0)
(1,2,0)
(1,3,0)
(2,0)
(2,1,0)
(2,3,0)
(2,1,3,0)
(3,0)
(3,1,0)
(3,2,0)

## Slide 15: Discussion of the “Internet Routing Instability” Paper
<number>

## Slide 16: BGP Stability Without Global Coordination
http://www.cs.princeton.edu/courses/archive/fall17/cos561/papers/BGPstability01.pdf
<number>

## Slide 17: BGP Solutions May Not Be Unique
1
0
2
1 2 0
1 0
2 1 0
2 0
First solution
1
0
2
1 2 0
1 0
2 1 0
2 0
1
0
2
1 2 0
1 0
2 1 0
2 0
Second solution
Notes: <number>

## Slide 18: BGP May Oscillate
2
0
3
1
2 1 0
2 0
1 3 0
1 0
3 2 0
3 0
4
3
Notes: <number>

## Slide 19: Stable System Unstable After Failure
2
0
3
1
2 1 0
2 0
1 3 0
1 0
3 4 2 0
3 0
4
4 0
4 2 0
4 3 0
Becomes a BAD GADGET if link
(4, 0) goes down.
BGP is not robust :
it is not guaranteed
to recover from
network failures.
Notes: <number>

## Slide 20: Ensuring BGP Stability
Create a global Internet routing registry
  Store the AS-level graph and all routing policies
  Store all routing policies
  But, ASes may be unwilling to divulge
Check for conflicting policies
  Analyze the global system and identify conflicts
  Contact the affected ASes to resolve them
  But, checking is an NP-complete problem
  … and, a safe system may be unsafe after failure
Goal: sufficient condition for convergence with local control

## Slide 21: Customer-Provider Relationship
Customer pays provider for Internet access
  Provider exports customer’s routes to everybody
  Customer exports only to downstream customers
d
d
provider
customer
customer
provider
Traffic to the customer
Traffic from the customer
advertisements
traffic

## Slide 22: Peer-Peer Relationship
Peers exchange traffic between customers
  AS exports only customer routes to a peer
  AS exports a peer’s routes only to its customers
peer
peer
Traffic to/from the peer and its customers
d
advertisements
traffic

## Slide 23: Three Restrictions on Policies
Route export
  Do not export a route learned from one peers or provider, to another
Route selection
  Prefer a route learned from a customer over a route learned from a peer or provider
AS graph
  No cycle of provider-customer relationships
Together: guarantee convergence to unique, stable route assignment
<number>

## Slide 24: Valid and Invalid Paths
2
3
1
d
4
5
6
7
8
Provider-Customer
Peer-Peer
Valid paths: “1 2 d” and “7 d”
Invalid path: “5 8 d”
Valid paths: “6 4 3 d” and “8 5 d”
Invalid paths: “6 5 d” and “1 4 3 d”
Notes: <number>

## Slide 25: Solving the Convergence Problem
Result
  Safety: guaranteed convergence to unique stable solution
  Inherent safety: holds under failures and policy changes
Definitions
  System state: current best route at each AS
  Activating AS: re-do decision based on neighbor choices
Sketch of (constructive) proof
  Find an activation sequence that leads to a stable state
  Any “fair” sequence (eventually) includes this sequence
Notes: <number>

## Slide 26: Rough Sketch of the Proof
Two phases
  Walking up the customer-provider hierarchy
  Walking down the provider-customer hierarchy
2
3
1
d
4
5
6
7
8
Provider-Customer
Peer-Peer
Notes: <number>

## Slide 27: Two Interpretations
System is stable because ASes act like this
  High-level argument
    Export and topology assumptions are reasonable
    Path selection rule matches with financial incentives
  Empirical results
    BGP routes for popular prefixes stable for ~10 days
    Most instability from a few flapping destinations
ASes should follow rules for system stability
  Encourage operators to obey these guidelines
  … and provide ways to verify the configuration
  Need to consider more complex relationships