## Slide 1
Jennifer Rexford
Fall 2017 (TTh 1:30-2:50pm in CS 105)
COS 561: Advanced Computer Networks
http://www.cs.princeton.edu/courses/archive/fall17/cos561/
BGP Interactions
Notes: <number>

## Slide 2: Protocol Dynamics
Interaction between BGP mechanisms
  Path exploration vs. route-flap damping
Interaction with end-host applications
  Slow failure detection
  Slow protocol convergence
Interaction with other routing protocols
  Intra-domain routing (e.g., OSPF/IS-IS)
Interaction with traffic-engineering practices
  Frequent changes to routing policies
<number>

## Slide 3: Persistent Routing Changes
Causes
  Link with intermittent connectivity
  Congestion causing repeated session resets
  Persistent oscillation due to policy conflicts
Effects
  Lots of BGP update messages
  Disruptions to data traffic
  High overhead on routers
Solution
  Suppress paths that go up/down repeatedly
  … to avoid updates and prefer stable paths

## Slide 4: Route Flap Damping
BGP-speaking router
  One or more BGP neighbors
  Keep an “RIB-in” per neighbor
  Select single best route per destination prefix
Route-flap damping
  Penalty counter per (peer, prefix) pair
  Increment penalty when peer changes route
  Decrease penalty over time when route is stable
Design and deployed in the mid-to-late 1990s
  Widely viewed as helping improve stability

## Slide 5: Example Why Damping is Good
Consider AS 3
  Path #1: (3,1,0)
  Path #2: (3,2,0)
If link (1,0) fails
  AS 3 switches routes
If link (1,0) restores
  AS 3 switches routes
If this happens a lot
  Better for AS 3 to stick with (3,2,0)
0
1
2
3
(1,0)
(2,0)

## Slide 6: Damping Penalty Function
time
penalty
reuse threshold
suppression threshold

## Slide 7: Configurable Damping Parameters
Penalty for a routing change
  May vary with the type of update message
  Advertisement vs. withdraw? Attributes change?
Decaying in absence of a change
  Exponent in the exponential decay
Suppression threshold
  Trigger for damping the route
  Determines how many updates are tolerated
Reuse threshold
  Trigger for considering the route again
  Determines how long the route is not usable

## Slide 8: Best Common Practices for Damping
Different parameters for different prefixes
  More aggressive with small address blocks
  Disable damping on certain prefixes (e.g., corresponding to the DNS root servers)
Avoid suppressing stable routes
  Tolerate at least four routing changes
Suppress unstable routes for quite a while
  Values ranging from 10 minutes to 1 hour
  Values for 30 minutes are not uncommon

## Slide 9: Interaction with Path Exploration
BGP routing convergence
  Explore one or more alternate paths
  Number of alternate paths may be quite high
  Time between steps is small (e.g., 30 seconds)
Triggering route-flap damping
  Increasing penalty with each step
  Only small amount of decay between steps
Convergence may trigger route flap damping
  Convergence may involve more than 4 changes
  Routing change may trigger lost connectivity!!!
  Ironically penalizes more richly connected sites

## Slide 10: Effects of Damping are Confusing
AS 0 is a stable network
Link (1,3) fails a lot
  AS 3 switches routes back and forth a lot
  Sends new BGP updates to its customers
  Suppose AS 3 does not apply route-flap damping
AS 3’s customers
  Eventually dampen route
  Causes lost reachability to destination in AS 0
0
1
2
3

## Slide 11: Open Questions
Want to suppress unstable routes
  Otherwise, lots of update messages
  … and lots of transient disruptions
Yet, want to tolerate path exploration
  Otherwise, you suppress stable routes
  … and black-hole otherwise reachable destinations
How to reconcile?
  Better flap-damping parameters?
  More information in update messages?
  Something more gentle than suppression?

## Slide 12: Multi-Homing
<number>

## Slide 13: Why Connect to Multiple Providers?
Reliability
  Reduced fate sharing
  Survive ISP failure
Performance
  Multiple paths
  Select the best
Financial
  Leverage through competition
  Game 95th-percentile billing model
Provider 1
Provider 2

## Slide 14: Outbound Traffic: Pick a BGP Route
Easier to control than inbound traffic
  IP routing is destination based
  Sender determines where the packets go
Control only by selecting the next hop
  Border router can pick the next-hop AS
  Cannot control selection of the entire path
Provider 1
Provider 2
“(2, 7, 8, 4)”
“(1, 3, 4)”

## Slide 15: Outbound Traffic: Shortest AS Path
No import policy on border router
  Pick route with shortest AS path
  Arbitrary tie break (e.g., router-id)
Performance?
  Shortest path is not necessarily best
  Propagation delay or congestion
Load balancing?
  Could lead to uneven split in traffic
  E.g., one provider with shorter paths
  E.g., too many ties with a skewed tie-break
s
d

## Slide 16: Outbound Traffic: Primary and Backup
Single policy for all prefixes
  High local-pref for session to primary provider
  Low load-pref for session to backup provider
Outcome of BGP decision process
  Choose the primary provider whenever possible
  Use the backup provider when necessary
But…
  What if you want to balance traffic load?
  What if you want to select better paths?

## Slide 17: Outbound Traffic: Load Balancing
Selectively use each provider
  Assign local-pref across destination prefixes
  Change the local-pref assignments over time
Useful inputs to load balancing
  End-to-end path performance data
    E.g., active measurements along each path
  Outbound traffic statistics per destination prefix
    E.g., packet monitors or router-level support
  Link capacity to each provider
  Billing model of each provider

## Slide 18: Outbound Traffic: What Kind of Probing?
Lots of options
  HTTP transfer
  UDP traffic
  TCP traffic
  Traceroute
  Ping
Pros and cons for each
  Accuracy
  Overhead
  Dropped by routers
  Sets off intrusion detection systems
How to monitor the “paths not taken”?

## Slide 19: Outbound Traffic: How Often to Change?
Stub ASes have no BGP customers
  So, routing changes do not trigger BGP updates
TCP flows that switch paths
  Out-of-order packets during transition
  Change in round-trip-time (RTT)
Impact on the providers
  Uncertainty in the offered load
  Interaction with their own traffic engineering?
Impact on other end users
  Good: move traffic off of congested paths
  Bad: potential oscillation as other stub ASes adapt?