## Slide 1
Jennifer Rexford
Fall 2016 (TTh 3:00-4:20 in CS 105)
COS 561: Advanced Computer Networks
http://www.cs.princeton.edu/courses/archive/fall16/cos561/
P4 Applications
Notes: <number>

## Slide 2: P4 Code Example
Simple Router
https://github.com/p4lang/tutorials/blob/master/ SIGCOMM_2016/heavy_hitter/p4src/heavy_hitter.p4
<number>

## Slide 3: Simple Router
Switching
Fabric
Processor

## Slide 4: Simple Router
Switching
Fabric
Processor
dmac
smac
dmac
smac
ingress port 0
egress port 3
IP Prefix | Next-hop
1.2.3.0/24 | 2
5.6.0.0/16 | 3
7.0.0.0/8 | 4
nhop_ipv4

## Slide 5: Simple Router
Parse the packet
  Ethernet and IPv4 headers
IP forwarding
  Longest-prefix match on destination IP address
  … to determine the “next hop” port for the packet
Update Ethernet frame
  Set the source and destination MAC addresses
  … to correspond to the output link
Updates to the IPv4 header
  Verify and update the IP header checksum
  Decrement the IP “time to live” field
<number>

## Slide 6: Headers: Ethernet and IPv4
<number>
header_type ethernet_t {
fields {
dstAddr : 48;
srcAddr : 48;
etherType : 16;
}
}
header_type ipv4_t {
fields {
version : 4;
ihl : 4;
…
ttl;
protocol;
hdrChecksum : 16;
srcAddr : 32;
dstAddr : 32;
}
}

## Slide 7: Parser Definition: Ethernet and IPv4
<number>
parser start {
return parse_ethernet;
}
parser parse_ethernet {
extract(ethernet);
return select(latest.etherType) {
0x0800 : parse_ipv4;
default: ingress;
}
}
parser parse_ipv4 {
extract(ipv4);
return ingress;
}

## Slide 8: Table Definition: IP Look-up
<number>
table ipv4_lpm {
reads {
ipv4.dstAddr : lpm;
}
actions {
set_nhop;
_drop;
}
size: 1024;
}
Set nhop IP address
Set egress port
Decrement TTL

## Slide 9: Control Flow
<number>
control ingress {
apply(ipv4_lpm);
apply(forward);
}
control egress {
apply(send_frame);
}
Set dmac
Set smac

## Slide 10: Prototyping New Functionality in P4
HULA Load-Sensitive Routing
<number>

## Slide 11: Load Balancing Today
<number>
. . . . . .
…
…
…
Servers
Leaf Switches
Spine Switches
Equal Cost Multi-Path (ECMP) – hashing

## Slide 12: Alternatives Proposed
<number>
Central Controller
HyperV
HyperV
Slow reaction time

## Slide 13: Congestion-Aware Fabric
<number>
Congestion-aware Load Balancing
CONGA – Cisco
HyperV
HyperV
Designed for 2-tier topologies

## Slide 14: Programmable Data Planes
Advanced switch architectures (P4 model)
  Programmable packet headers
  Stateful packet processing
Applications
  In-band Network Telemetry (INT)
  HULA load balancer
Examples
  Barefoot RMT, Intel Flexpipe, etc.
<number>

## Slide 15: Programmable Switches: Capabilities
<number>
Memory
M | A
m1 | a1
Ingress Parser
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Egress Deparser
Queue Buffer
P4 Program
Compile

## Slide 16: Programmable Switches: Capabilities
<number>
Memory
M | A
m1 | a1
Ingress Parser
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Memory
M | A
m1 | a1
Egress Deparser
Queue Buffer
P4 Program
Compile
Programmable Parsing
Stateful
Memory
Switch
Metadata

## Slide 17: Hop-by-hop Utilization-aware Load-balancing Architecture
HULA probes propagate path utilization
  Congestion-aware switches
Each switch remembers best next hop
  Scalable and topology-oblivious
Split elephants to mice flows (flowlets)
  Fine-grained load balancing
<number>

## Slide 18: 1. Probes carry path utilization
<number>
ToR
Aggregate
Spines
Probe originates
Probe replicates
Notes: Let’s dig a little deeper. In HULA, the probes originate at the ToRs (through the servers or the ToRs themselves) and then are replicated on multiple paths as they travel the network. We make sure that each switch replicates only the necessary set of probes to the others so that the probe overhead is minimal.
<number>

## Slide 19: 1. Probes carry path utilization
<number>
ToR
Aggregate
Spines
Probe originates
Probe replicates
P4 primitives
New header format
Programmable Parsing
Switch metadata
Notes: Let’s dig a little deeper. In HULA, the probes originate at the ToRs (through the servers or the ToRs themselves) and then are replicated on multiple paths as they travel the network. We make sure that each switch replicates only the necessary set of probes to the others so that the probe overhead is minimal.
<number>

## Slide 20: 1. Probes carry path utilization
<number>
S1
S2
S3
S4
ToR 10
ToR ID = 10 Max_util = 50%
ToR 1
Probe
ToR ID = 10 Max_util = 80%
ToR ID = 10 Max_util = 60%
Notes: <number>

## Slide 21: 2. Switch identifies best downstream path
<number>
S1
S2
S3
S4
ToR 10
ToR 1
Best hop table
Probe
ToR ID = 10 Max_util = 50%
Notes: Then the switch takes the minimum from among the probe given utilization and stores it in the local routing table. The switch S1 then sends its view of the best path to the upstream switches. And the upstream switches process these probes and update their neighbours. This leads to a distance vector-style propagation of information about network utilization to all the switches. But at the same time, each switch only needs to keep track of the best next hop towards a destination.
<number>

## Slide 22: 2. Switch identifies best downstream path
<number>
S1
S2
S3
S4
ToR 10
ToR 1
Best hop table
Probe
ToR ID = 10 Max_util = 40%
Notes: Then the switch takes the minimum from among the probe given utilization and stores it in the local routing table. The switch S1 then sends its view of the best path to the upstream switches. And the upstream switches process these probes and update their neighbours. This leads to a distance vector-style propagation of information about network utilization to all the switches. But at the same time, each switch only needs to keep track of the best next hop towards a destination.
<number>

## Slide 23: 3. Switches load balance flowlets
<number>
S1
S2
S3
S4
ToR 10
ToR 1
Best hop table
Data
Notes: The switches then route data packets in the opposite direction by spitting flows into smaller groups of packets called flowlets. Flowlets basically are subsequences of packets in a flow separated by a large enough inter-packet gap so that when different flowlets are sent on different paths, the destination does not see packet reordering with high probability.
<number>

## Slide 24: 3. Switches load balance flowlets
<number>
S1
S2
S3
S4
ToR 10
ToR 1
Flowlet table
Best hop table
Data
Hash flow
Notes: The switches then route data packets in the opposite direction by spitting flows into smaller groups of packets called flowlets. Flowlets basically are subsequences of packets in a flow separated by a large enough inter-packet gap so that when different flowlets are sent on different paths, the destination does not see packet reordering with high probability.
<number>

## Slide 25: 3. Switches load balance flowlets
<number>
S1
S2
S3
S4
ToR 10
ToR 1
Flowlet table
Best hop table
Data
P4 primitives
RW access to stateful memory
Comparison/arithmetic operators
Notes: The switches then route data packets in the opposite direction by spitting flows into smaller groups of packets called flowlets. Flowlets basically are subsequences of packets in a flow separated by a large enough inter-packet gap so that when different flowlets are sent on different paths, the destination does not see packet reordering with high probability.
<number>

## Slide 26: Discussion
Load-sensitive routing
Other P4 applications
Abstractions for P4 programming
<number>