## Slide 1: Revisiting Ethernet: Plug-and-play made scalable and efficient
Notes: <number>

## Slide 2: An “All Ethernet” Enterprise Network?
<number>
“All Ethernet” makes network management easier
  Zero-configuration of end-hosts and network due to
    Flat addressing
    Self-learning
  Location independent and permanent addresses also simplify
    Host mobility
    Network troubleshooting
    Access-control policies
Notes: <number>

## Slide 3: But, Ethernet bridging does not scale
<number>
Flooding-based delivery
  Frames to unknown destinations are flooded
Broadcasting for basic service
  Bootstrapping relies on broadcasting
  Vulnerable to resource exhaustion attacks
Inefficient forwarding paths
  Loops are fatal due to broadcast storms; use the STP
  Forwarding along a single tree leads to inefficiency
Notes: <number>

## Slide 4: State of the Practice: A Hybrid Architecture
<number>
Enterprise networks comprised of Ethernet-based IP subnets interconnected by routers
R
R
R
R
Ethernet Bridging
- Flat addressing
- Self-learning
- Flooding - Forwarding along a tree
IP Routing
- Hierarchical addressing
- Subnet configuration
- Host configuration
- Forwarding along shortest paths
R
Notes: <number>

## Slide 5: Motivation
<number>
Neither bridging nor routing is satisfactory.
Can’t we take only the best of each?
Architectures Features | Ethernet Bridging | IP Routing
Ease of configuration |  | 
Optimality in addressing |  | 
Mobility support |  | 
Path efficiency |  | 
Load distribution |  | 
Convergence speed |  | 
Tolerance to loop |  | 
SEATTLE







Notes: <number>

## Slide 6: Avoiding Flooding
<number>
Bridging uses flooding as a routing scheme
  Unicast frames to unknown destinations are flooded
  Does not scale to a large network
Objective #1: Unicast unicast traffic
  Need a control-plane mechanism to discover and disseminate hosts’ location information
“Send it everywhere!
At least, they’ll learn where the source is.”
“Don’t know where destination is.”
Notes: <number>

## Slide 7: Restraining Broadcasting
<number>
Liberal use of broadcasting for bootstrapping (DHCP and ARP)
  Broadcasting is a vestige of shared-medium Ethernet
  Very serious overhead in switched networks
Objective #2: Support unicast-based bootstrapping
  Need a directory service
Sub-objective #2.1: Support general broadcast
  However, handling broadcast should be more scalable
Notes: <number>

## Slide 8: Keeping Forwarding Tables Small
<number>
Flooding and self-learning lead to unnecessarily large forwarding tables
  Large tables are not only inefficient, but also dangerous
Objective #3: Install hosts’ location information only when and where it is needed
  Need a reactive resolution scheme
  Enterprise traffic patterns are better-suited to reactive resolution
Notes: <number>

## Slide 9: Ensuring Optimal Forwarding Paths
<number>
Spanning tree avoids broadcast storms. But, forwarding along a single tree is inefficient.
  Poor load balancing and longer paths
  Multiple spanning trees are insufficient and expensive
Objective #4: Utilize shortest paths
  Need a routing protocol
Sub-objective #4.1: Prevent broadcast storms
  Need an alternative measure to prevent broadcast storms
Notes: <number>

## Slide 10: Backwards Compatibility
<number>
Objective #5: Do not modify end-hosts
  From end-hosts’ view, network must work the same way
  End hosts should
    Use the same protocol stacks and applications
    Not be forced to run an additional protocol
Notes: <number>

## Slide 11: SEATTLE in a Slide
<number>
Flat addressing of end-hosts
  Switches use hosts’ MAC addresses for routing
  Ensures zero-configuration and backwards-compatibility (Obj # 5)
Automated host discovery at the edge
  Switches detect the arrival/departure of hosts
  Obviates flooding and ensures scalability (Obj #1, 5)
Hash-based on-demand resolution
  Hash deterministically maps a host to a switch
  Switches resolve end-hosts’ location and address via hashing
  Ensures scalability (Obj #1, 2, 3)
Shortest-path forwarding between switches
  Switches run link-state routing with only their own connectivity info
  Ensures data-plane efficiency (Obj #4)
Notes: <number>

## Slide 12: How does it work?
<number>
Host discovery
or registration
B
D
x
y
Hash (F(x) = B)
Store <x, A> at B
Traffic to x
Hash
(F(x) = B)
Tunnel to
egress node, A
Deliver to x
Switches
End-hosts
Control flow
Data flow
Notifying <x, A> to D
Entire enterprise
(A large single IP subnet)
LS core
E
Optimized forwarding
directly from D to A
C
A
Tunnel to
relay switch, B
Notes: <number>

## Slide 13: Terminology
<number>
Ingress
Relay (for x)
Egress
x
y
B
A
Dst
Src
< x, A >
< x, A >
< x, A >
D
Ingress applies a cache eviction policy to this entry
cut-through forwarding
Notes: <number>

## Slide 14: Responding to Topology Changes
<number>
Consistent Hash [Karger et al.,STOC’97] minimizes re-registration
A
B
C
D
E
F
h
h
h
h
h
h
h
h
h
h
Notes: <number>

## Slide 15: Single Hop Look-up
<number>
A
B
C
D
F(x)
x
y
y sends traffic to x
E
Every switch on a ring is
logically one hop away
Notes: <number>

## Slide 16: Responding to Host Mobility
<number>
Relay (for x)
x
y
B
A
Src
< x, A >
< x, A >
< x, A >
D
when cut-through
forwarding is used
G
< x, G >
Old Dst
New Dst
< x, G >
< x, G >
< x, G >
Notes: <number>

## Slide 17: Unicast-based Bootstrapping
<number>
ARP
  Ethernet: Broadcast requests
  SEATTLE: Hash-based on-demand address resolution
    Exactly the same mechanism as location resolution
    Proxy resolution by ingress switches via unicasting
DHCP
  Ethernet: Broadcast requests and replies
  SEATTLE: Utilize DHCP relay agent (RFC 2131)
    Proxy resolution by ingress switches via unicasting
Notes: <number>

## Slide 18: Conclusions
<number>
SEATTLE is a plug-and-playable enterprise architecture ensuring both scalability and efficiency
Enabling design choices
  Hash-based location management
  Reactive location resolution and caching
  Shortest-path forwarding
Lessons
  Trading a little data-plane efficiency for huge control-plane scalability makes a qualitatively different system
  Traffic patterns (small static COIs, and short flow interarrival times) are our friends
Notes: <number>