## Slide 1: Programmable Data Plane
COS561, Fall 2018

## Slide 2: Before SDN…
Many boxes (routers, switches, firewalls, …), with different interfaces.

## Slide 3: A Brief History of SDN
Many functions in networking devices
  Routing, Switching, NAT, Firewall, Shaper…
  “Many Boxes, But Similar Functions”
Common functions, Unified control interface!
Match + Action
  Match on subset of header bits
  Action: forward, flood, drop, rewrite, count, etc
Router? Switch? Firewall?

## Slide 5
decouple control and data planes by providing open standard API

## Slide 6
Controller Platform
Controller Application

## Slide 7: From OpenFlow to P4/PISA
OpenFlow 1.0 feature set is “the intersection of all vendors”
From The Original OpenFlow paper:
Programmable action, fixed header matching
Problem: what if… (you never know!)
Version | Date | # Headers
OF 1.0 | Dec 2009 | 12
OF 1.1 | Feb 2011 | 15
OF 1.2 | Dec 2011 | 36
OF 1.3 | Jun 2012 | 40
OF 1.4 | Oct 2013 | 41
Chart: #Headers explode
| OF 1.0 | OF 1.1 | OF 1.2 | OF 1.3 | OF 1.4
Series 1 | 12 | 15 | 36 | 40 | 41

## Slide 8: P4: more programmability
Now you define “program”, not just “rules”.

## Slide 9: Intro to P4
A programming language for packet processing.
Key functionality:
  Customized parsing
  Match-action tables
  Register Memory Access (what we care about)

## Slide 10: Programmable Parsing (State Machine)
Basically a DFA
Read some bytes -> go to new state
Example: Layer 2~4 parsing
This part can be programmable to add customized header types. (E.g., QUIC?)
Ether
VLAN
IPv4
IPv6
TCP
UDP
ICMP
Accept
Start
0x0800
6
47

## Slide 11: Match-Action Table: If…Then…
Match support exact, LPM, ternary
Example: simple IPv4+TCP routing table
Action can be:
  Set egress port / drop
  Set temporary variable (for other actions)
  Read/Write register (persistent)
  Arithmetic operation on header/metadata
  Combination of above
  …
Match: IPv4.dstAddr | Action
10.1.0.0/16 | EgressPort=001 IPv4.ttl -= 1
10.2.0.0/16 | EgressPort=002 IPv4.ttl -= 1
10.255.255.255 | Egress=Broadcast IPv4.ttl -= 1
Else | Drop

## Slide 12: Multiple Match-Action Tables
A “control flow” applies multiple match-action tables to a packet in some order.
In hardware, the “control flow” is actually a pipeline. (Sequential)

## Slide 13: Hardware Support of P4
A software emulator (very slow)
P4-netFPGA, first practical P4 switch
DPDK integration and OpenVSwitch integration – PISCES project
Barefoot Networks, making the first “P4-supported” programmable switches
An unnamed network switch vendor used P4 internally
  but not exposed to their customers!
  “Supported by hardware, not supported by business model” :-(

## Slide 14: Memory Model in PISA Switch (Header vs Register)
Most matches and actions are stateless; no effect for the next packet.
“Interesting” ones are stateful (lifespan >1 packet)
Use SRAMs to implement stateful objects:
  Counters (packet count, byte count)
  Meters (e.g. 2-rate 3-color)
  Registers (programmable! Random access!)

## Slide 15: Register Primitive: Random Access
Read_register: variable=arr[index]
Write_register: arr[index]=variable
  (disclaimer: actual P4 syntax more complicated)
Example: Ternary Match (UDP.sport, UDP.dport)
If UDP.dport==53:
  Tmp=dns_count_array[hashed_src_ip]
  dns_count_array[hashed_src_ip]=Tmp+1
If UDP.sport==53:
  Tmp=dns_count_array[hashed_dst_ip]
  dns_count_array[hashed_dst_ip]=Tmp-1
(reflection attack detection)

## Slide 16: PISA Processing Model
Programmable Deparser
Stages
ip.src=1.1.1.1
ip.dst=2.2.2.2
...
Packet Header Vector
Programmable Parser
Memory
Persistent State
ALU
Match/Action Table
ip.src=3.3.3.3
ip.dst=2.2.2.2
...

## Slide 17: Under the hood
Header
Metadata
Header
Metadata
Pipeline Memory
(stateless)
Pipeline Memory
(stateless)
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | …
0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 
Register SRAM
(stateful)
Packet N
Packet N-1
Packet N+1

## Slide 18: Summary of P4 and PISA
Protocol Independent:
  Any header format, future-proof
Fully programmable:
  Faster feature-to-market time
Pipelined Packet Processing
  Depending on hardware target!
  Other targets exist (e.g., FPGA boards)

## Slide 19: Application: Network Measurement
Collect statistics of network traffic, for...
  Security
  Performance diagnostics
  Capacity planning

## Slide 20: Measurement in the Data Plane?
Opportunity: programmable switches!
  Only report result to controller, upon demand
  Immediate per-packet action in the data plane
Challenges
  Restrictive programming model
  Limited state (memory)
Our solution: Probabilistic Recirculation (PRECISION)

## Slide 21: Challenges of Running Algorithms on PISA
Constrained memory access:
  Partitioned between stages
  Can only R/W one address per stage
Computation: only basic arithmetic
Limited memory size, limited #stages

## Slide 22: Recirculation to the rescue?
Programmable Deparser
Stages
Programmable Parser
Memory
Persistent State
ALU
Packet

## Slide 23: Challenges of Running Algorithms on PISA
Constrained memory access:
  Partitioned between stages
  Can only R/W one address per stage
Computation: only basic arithmetic
Limited memory size, limited #stages
Recirculation helps, but hurts throughput

## Slide 24: The Heavy-Hitter Detection Problem
A few “Heavy-Hitters”, a.k.a. elephant flows, send most of the packets.
To catch these elephants, we:
  Report top-k flows
  Estimate flow size for each flow
Metrics:
  Recall
  On-arrival MSE
Flow size
All flows

## Slide 25: Example P4-based application: Heavy-Hitter Detection
How can we use programmable switches to measure heavy-hitters?
Step 1: Find a good algorithm
  Run on general-purpose computer
Step 2: Adapt it to PISA switches

## Slide 26: Naïve solution: Sample and Hold
Problem: Many small flows get sampled, wasting memory.

## Slide 27: The Space-Saving Algorithm (Metwally et al.)
Metwally, et al. Efficient computation of frequent and top-k elements in data streams. ICDT 2005.

## Slide 28: The Space-Saving Algorithm
Widely used, easy to implement
Performance suffers when there are too many small flows
Flow size
All flows
Too many!
What we care

## Slide 29: Randomized Admission Policy (RAP) (Ben Basat et al.)
What if we don’t always replace the minimum?
When minimum counter is cmin, replace it with a small probability
“Increment 1 in expectation”: P=1/(cmin+1)
Ben Basat, et al. Randomized admission policy for efficient top-k and frequency estimation. INFOCOM 2017

## Slide 30: Randomized Admission Policy (RAP) (Ben Basat et al.)
P=1/2 (cmin=1)
P=1/3 (cmin=2)
P=1/4 (cmin=3)
P=1/4 (cmin=3)

## Slide 31: Adapting RAP to Programmable Switches
Space-Saving and RAP are for computers!
Constraints of programmable switches:
Cannot know the global minimum counter
Partitioned memory – too late to update
How to flip coin?
Recirculation hurts throughput

## Slide 32: Adapting to Data Plane: Cannot Find Minimum
What if you can only R/W a few memory addresses?
Can’t find global minimum cmin
Find approximate minimum c’min, by randomly querying 4 addresses (based on flow ID)
Count-Min Sketch (Cormode and Muthukrishnan), HashPipe (Sivaraman et al.)
h1 |  | h2 |  | h3 |  | h4
Graham Cormode and Shan Muthukrishnan. An improved data stream summary: the count-min sketch and its applications. Journal of Algorithms 55.1 (2005): 58-75.
Sivaraman et al. Heavy-hitter detection entirely in the data plane. SOSR 2017
Flow ID: x
h1(x)=0 h2(x)=2 h3(x)=0 h4(x)=3
Flow ID: y
h1(y)=3 h2(y)=2 h3(y)=3 h4(y)=1

## Slide 33: Adapting to Data Plane: Too Late to Update
We know the approximate minimum count c’min at the end of pipeline. Too late to update!
Solution: use a little recirculation
If coin flip succeeded, recirculate with (Flow ID, minimum stage #)
h1 |  | h2 |  | h3 |  | h4
5 |  |  |  | 7 |  | 
 |  | 3 |  |  |  | 
 |  |  |  |  |  | 4
Flow ID=x
Stage#=2, c’min=3
4
Sivaraman et al. Heavy-hitter detection entirely in the data plane. SOSR 2017
Notes: HashPipe choose to never recirc. The authors considered recirculation, but dismissed it as being impractical; hurts too much throughput.
We choose to recirc only a little bit…

## Slide 34: Adapting to Data Plane: How to flip coin?
We need to flip coin w.p. P=1/(c’min+1)
No arbitrary flip! Only binary flips
Naïve solution:
  Find 2-N ≥ P > 2-(N+1)
  Flip N binary coins, get P’=2-N
(2-approximation of probability P)
Better solution: use Match-Action Table (1.125-approx., see paper)
P | P’ | How many binary coins?
1/2 | 1/2 | 
1/3 | 1/4 | 
1/4 | 1/4 | 
1/5 | 1/8 | 
1/7 | 1/8 | 
1/8 | 1/8 | 
1/9 | 1/16 | 

## Slide 35: Adapting to Data Plane: Recirculation Hurts Throughput
Avoid packet reordering
  Send original (preserve ordering)
  Copy the packet, then recirc+drop
Upper-bound recirc. to a small percentage, e.g., 1%
  By initializing counters to 100
  Switch may have reserved capacity for recirc; no performance penalty.
h1 |  |  | h2 |  |  | h3 | 
ID | # |  | ID | # |  | ID | #
N/A | 100 |  | N/A | 100 |  | N/A | 100
a | 101 |  | N/A | 100 |  | N/A | 100
c | 103 |  | f | 105 |  | N/A | 100
N/A | 100 |  | N/A | 100 |  | N/A | 100
c’min≥ 100, P<1%

## Slide 36: PRECISION Algorithm
Visit d=3 random entries, one per stage
  If ID matched, add 1!
  Otherwise, find out c’min
Flip coin, P=1/(c’min+1)
If coin is head:
  copy and recirculate
  update minimum counter
h1 |  |  | h2 |  |  | h3 | 
ID | # |  | ID | # |  | ID | #
a | 106 |  | N/A | 100 |  | N/A | 100
b | 103 |  | g | 102 |  | N/A | 100
c | 105 |  | f | 130 |  | k | 160
d | 104 |  | N/A | 100 |  | l | 180
Pkt
ID=z
c’min=102
Coin flip: P=1/103
103
z
S#=2
ID=z

## Slide 37: Evaluation Highlight
Problems of recirculation:
Impact throughput?
    Bound probability to 1%!
    No accuracy loss
Delayed update?
    No accuracy loss
Other potential problems:
Approximated coin flip?
    2-approx. is good
    1.125-approx. is great
Limited stages?
    2 stages are good
    4 are great

## Slide 38: Evaluation: Mean-Square Error, CAIDA
Space-Saving:
HashPipe:
2-stage 4-stage 8-stage
PRECISION (2-stage):
2-approx. coin flip
1.125-approx. coin flip
ideal flip (RAP)

## Slide 39: Evaluation: top-32 flows, CAIDA
Space-Saving:
HashPipe:
2-stage 4-stage 8-stage
PRECISION (2-stage):
2-approx. coin flip
1.125-approx. coin flip
ideal flip (RAP)

## Slide 40: Summary
PRECISION: an accurate, hardware-friendly algorithm for heavy-hitter detection on programmable switches.
Takeaway: approximate probabilistic recirculation!
Hardware Friendly.
Little Impact on throughput.
Better Accuracy.

## Slide 41: Any Questions