## Slide 1: Programmable Networks
Jennifer Rexford
Fall 2018 (TTh 1:30-2:50 in Friend 006)
COS 561: Advanced Computer Networks
http://www.cs.princeton.edu/courses/archive/fall18/cos561/

## Slide 2: Software-Defined Networking (SDN)
Controller Platform
Controller Application
Network-wide visibility and control
Direct control via open interface
From distributed protocols to (centralized) controller applications
Notes: Network-wide visibility and control
Direct control via an open interface

## Slide 3: Simple, Open Data-Plane API
Prioritized list of rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
srcip=1.2.*.*, dstip=3.4.5.*  drop
srcip=*.*.*.*, dstip=3.4.*.*  forward(2)
3. srcip=10.1.2.3, dstip=*.*.*.*  send to controller
Notes: Defined in terms of a protocol and mechanism
Clarify that each packet matches exactly one rule (the highest priority one that matches). Primitive execution engine.

## Slide 4: Writing SDN Controller Applications
Controller Platform
Controller Application
OpenFlow protocol
Programming abstractions
OpenFlow is a mechanism, not a linguistic formalism.

## Slide 5: Composition of Policies

## Slide 6: Combining Many Networking Tasks
Controller Platform
Route + Monitor + FW + LB
Monolithic application
Hard to program, test, debug, reuse, port, …

## Slide 7: Modular Controller Applications
Controller Platform
LB
Route
Monitor
FW
Each module partially specifies the handling of the traffic

## Slide 8: Abstract OpenFlow: Policy as a Function
Located packet
  Packet header fields
  Packet location (e.g., switch and port)
Function of a located packet
  To a set of located packets
    Drop, forward, multicast
  Packet modifications
    Change in header fields and/or location
dstip == 1.2.3.4 & srcport == 80  port = 3, dstip = 10.0.0.1
0
1
2
3
Notes: Abstraction of OpenFlow, boolean predicates instead of bit twiddling and rules
In PL historically, look to define the meaning of programs using “denotational semantics” (one that is compositional).
Programmer doesn’t have to look at the syntax to understand.
Goes back to Dana Scott in the 1960s.
Meaning of something as a combination of the meanings of the two parts. Applied those lessons here to networking.
So, functions of located packets is the primitive building block.

## Slide 9: Parallel Composition (+)
Controller Platform
Route on dest prefix
Monitor on source IP
+
dstip == 1.2/16  fwd(1)
dstip == 3.4.5/24  fwd(2)
srcip == 5.6.7.8  count
srcip == 5.6.7.9  count
srcip == 5.6.7.8, dstip == 1.2/16  fwd(1), count
srcip == 5.6.7.8, dstip == 3.4.5/24  fwd(2), count
srcip == 5.6.7.9, dstip == 1.2/16  fwd(1), count
srcip == 5.6.7.9, dstip == 3.4.5/24  fwd(2), count

## Slide 10: Example: Server Load Balancer
Spread client traffic over server replicas
  Public IP address for the service
  Split traffic based on client IP
  Rewrite the server IP address
Then, route to the replica
clients
1.2.3.4
load balancer
server replicas
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 11: Sequential Composition (>>)
Controller Platform
Routing
Load Balancer
>>
dstip==10.0.0.1  fwd(1)
dstip==10.0.0.2  fwd(2)
srcip==0*, dstip==1.2.3.4  dstip=10.0.0.1
srcip==1*, dstip==1.2.3.4  dstip=10.0.0.2
srcip==0*, dstip==1.2.3.4  dstip = 10.0.0.1, fwd(1)
srcip==1*, dstip==1.2.3.4  dstip = 10.0.0.2, fwd(2)
Notes: Load balancer splits traffic sent to public IP address over multiple replicas, based on client IP address, and rewrites the IP address

## Slide 12: Reading State
SQL-Like Query Language

## Slide 13: From Rules to Predicates
Traffic counters
  Each rule counts bytes and packets
  Controller can poll the counters
Multiple rules
  E.g., Web server traffic except for source 1.2.3.4
Solution: predicates
  E.g., (srcip != 1.2.3.4) && (srcport == 80)
  Run-time system translates into switch patterns
1. srcip = 1.2.3.4, srcport = 80
2. srcport = 80

## Slide 14: Dynamic Unfolding of Rules
Limited number of rules
  Switches have limited space for rules
  Cannot install all possible patterns
Must add new rules as traffic arrives
  E.g., histogram of traffic by IP address
  … packet arrives from source 5.6.7.8
Solution: dynamic unfolding
  Programmer specifies GroupBy(srcip)
  Run-time system dynamically adds rules
1. srcip = 1.2.3.4
1. srcip = 1.2.3.4
2. srcip = 5.6.7.8

## Slide 15: Suppressing Unwanted Events
Common programming idiom
  First packet goes to the controller
  Controller application installs rules
packets

## Slide 16: Suppressing Unwanted Events
More packets arrive before rules installed?
  Multiple packets reach the controller
packets

## Slide 17: Suppressing Unwanted Events
Solution: suppress extra events
  Programmer specifies “Limit(1)”
  Run-time system hides the extra events
packets
not seen by
application

## Slide 18: SQL-Like Query Language
Get what you ask for
  Nothing more, nothing less
SQL-like query language
  Familiar abstraction
  Returns a stream
  Intuitive cost model
Minimize controller overhead
  Filter using high-level patterns
  Limit the # of values returned
  Aggregate by #/size of packets
Select(bytes) *
Where(in:2 & srcport:80) *
GroupBy([dstmac]) *
Every(60)
Select(packets) *
GroupBy([srcmac]) *
SplitWhen([inport]) *
Limit(1)
Learning Host Location
Traffic Monitoring

## Slide 19: Writing State
Consistent Updates

## Slide 20: Avoiding Transient Disruption
Invariants
No forwarding loops
No black holes
Access control
Traffic waypointing

## Slide 21: Installing a Path for a New Flow
Rules along a path installed out of order?
  Packets reach a switch before the rules do
Must think about all possible packet and event orderings.
packets

## Slide 22: Update Consistency Semantics
Per-packet consistency
  Every packet is processed by
  … policy P1 or policy P2
  E.g., access control, no loops or blackholes
Per-flow consistency
  Sets of related packets are processed by
  … policy P1 or policy P2,
  E.g., server load balancer, in-order delivery, …
P1
P2

## Slide 23: Policy Update Abstraction
Simple abstraction
  Update entire configuration at once
Cheap verification
  If P1 and P2 satisfy an invariant
  Then the invariant always holds
Run-time system handles the rest
  Constructing schedule of low-level updates
  Using only OpenFlow commands!
P1
P2

## Slide 24: Two-Phase Update Algorithm
Version numbers
  Stamp packet with a version number (e.g., VLAN tag)
Unobservable updates
  Add rules for P2 in the interior
  … matching on version # P2
One-touch updates
  Add rules to stamp packets with version # P2 at the edge
Remove old rules
  Wait for some time, then remove all version # P1 rules

## Slide 25: Update Optimizations
Avoid two-phase update
  Naïve version touches every switch
  Doubles rule space requirements
Limit scope
  Portion of the traffic
  Portion of the topology
Simple policy changes
  Strictly adds paths
  Strictly removes paths

## Slide 26: Consistent Update Abstractions
Many different invariants
  Beyond packet properties
  E.g., avoiding congestion during an update
Many different algorithms
  General solutions
  Specialized to the invariants
  Specialized to a setting (e.g., optical nets)

## Slide 27: “Control Loop” Abstractions
SQL-like queries
OpenFlow
Switches
Consistent
Updates
Policy Composition