## Slide 1: Naming in Networking
Jennifer Rexford
COS 316 Guest Lecture

## Slide 2: Names
Type of Name | Example
Uniform Resource Locator | http://www.cs.princeton.edu/~jrex/foo.html
E-mail | jrex@cs.princeton.edu
Hostname | www.cs.princeton.edu
Internet Protocol | 128.112.7.156
Media Access Control | 00:15:C5:49:04:A9
Today’s lecture focuses on the last three!

## Slide 3: Internet Protocol Layers
Best-effort local packet delivery
Best-effort global packet delivery
Reliable streams
Applications
Messages
Link
Network
Transport
Application
Hostname
IP address
MAC address

## Slide 4: Internet Protocol Stack
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
Optical
interface
Optical
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Ethernet frame
Ethernet frame

## Slide 5: What’s in a Name?
Human readable?
  If end users interact with the names
Fixed length?
  If names must be processed at high speed
Large name space?
  If many nodes need unique names
Hierarchical names?
  If the system is very large and/or federated
Self-certifying?
  If preventing “spoofing” is important

## Slide 6: Different Layers, Different Names
Host name (e.g., www.cs.princeton.edu)
  Mnemonic, variable-length, appreciated by humans
  Hierarchical, based on organizations
IP address (e.g., 128.112.7.156)
  Numerical 32-bit address appreciated by routers
  Hierarchical, based on organizations and topology
MAC address (e.g., 00:15:C5:49:04:A9)
  Numerical 48-bit address appreciated by adapters
  Non-hierarchical, unrelated to network topology

## Slide 7: Hierarchical Allocation Processes
Host name: www.cs.princeton.edu
  Domain: registrar for each top-level domain (e.g., .edu)
  Host name: local administrator assigns to each host
IP addresses: 128.112.7.156
  Prefixes: ICANN, regional Internet registries, and ISPs
  Hosts: static configuration, or dynamic using DHCP
MAC addresses: 00:15:C5:49:04:A9
  Blocks: assigned to equipment vendors by the IEEE
  Adapters: assigned by the vendor from its block

## Slide 8: Host Names vs. IP Addresses
Names are easier (for us!) to remember
  www.cnn.com vs. 64.236.16.20
IP addresses can change underneath
  E.g., renumbering when changing providers
Name could map to multiple IP addresses
  www.cnn.com to multiple replicas of the Web site
Map to different addresses in different places
  E.g., to reduce latency, or return different content
Multiple names for the same address
  E.g., aliases like ee.mit.edu and cs.mit.edu

## Slide 9: IP vs. MAC Addresses
LANs designed for arbitrary network protocols
  Not just for IP (e.g., IPX, Appletalk, X.25, …)
  Different LANs may have different address schemes
A host may move to a new location
  So, cannot simply assign a static IP address
  Instead, must reconfigure the adapter
Must identify the adapter during bootstrap
  Need to talk to the adapter to assign it an IP address

## Slide 10: Hostname, IP, and MAC
 | Hostname | IP Address | MAC Address
Example | www.cs.princeton.edu | 128.112.7.156 | 00:15:C5:49:04:A9
Size | Hierarchical, human readable, variable length | Hierarchical, machine readable, 32 bits (in IPv4) | Flat, machine readable, 48 bits
Read by | Humans, hosts | Internet routers | LAN switches
Allocation, top-level | Domain name assigned by registrar (e.g., for .edu) | Variable-length prefixes, assigned by ICANN, RIR, or ISP | Fixed-sized blocks, assigned by IEEE to vendors (e.g., Dell)
Allocation, low-level | Host name assigned by local administrator | Interface, by DHCP or local administrator | Interface, by equipment vendor
Notes: whois –h whois.arin.net 128.112.155.165
http://standards.ieee.org/regauth/oui/oui.txt
Why both MAC and IP:
Need identifier to use in bootstrap process
IP address is topology-dependent, so cannot keep when host moves
- LAN was meant to handle many different network protocols (not just IP)

## Slide 11: Directory: Translate Name to Address
link
session
path
name
address

## Slide 12: Directory
A key-value store
  Key: name, value: address(es)
  Answer queries: given name, return address(es)
Caching the response
  Reuse the response, for a period of time
  Better performance and lower overhead
Allow entries to change
  Updating the address(es) associated with a name
  Invalidating or expiring cached responses

## Slide 13: Directory Design: Three Extremes
Flood the query (e.g., ARP)
  The named node responds with its own address
  But, high overhead in large networks

## Slide 14: Address Resolution Protocol (ARP)
Every host in a LAN maintains an ARP table
  (IP address, MAC address) pair
Consult the table when sending a packet
  Map destination IP address to dest MAC address
  Transmit the IP packet within an Ethernet frame
1.2.3.4
1.2.3.19
00:15:C5:49:04:A9
78:9A:B5:23:5D:98
Local Area
Network

## Slide 15: Address Resolution Protocol (ARP)
But, what if the key is not in the table?
  Sender broadcast: “Who has IP address 1.2.3.19?”
  Receiver answer: “MAC address 78:9A:B5:23:5D:98”
  Sender caches the result in its local ARP cache
1.2.3.4
1.2.3.19
00:15:C5:49:04:A9
78:9A:B5:23:5D:98
Local Area
Network

## Slide 16: Address Resolution Protocol (ARP)
Managing the ARP cache
  Storing all key-value pairs introduces overhead
  Entries become stale (e.g., IP assigned to new host)
  Remove an entry if not used for some period of time
1.2.3.4
1.2.3.19
00:15:C5:49:04:A9
78:9A:B5:23:5D:98
Local Area
Network

## Slide 17: Directory Design: Three Extremes
Flood the query (e.g., ARP)
  The named node responds with its address
  But, high overhead in large networks
Push data to all nodes (e.g., /etc/hosts)
  All nodes store a full copy of the directory
  But, high overhead for many names and updates
Central directory server
  All data and queries handled by one node
  But, poor performance, scalability, and reliability

## Slide 18: Distributed Directory Design
Hierarchical directory (e.g., DNS)
  Follow the hierarchy of the name space
  Distribute the directory, distribute the queries
  Enable decentralized updates to the directory
Distributed Hash Table (e.g., P2P applications)
  Directory as a hash table with flat names
  Each directory node handles range of hash outputs
  Use hash to direct query to the directory node

## Slide 19: Domain Name System (DNS)
Properties of DNS
  Hierarchical name space divided into zones
  Distributed over a collection of DNS servers
Hierarchy of DNS servers
  Root servers
  Top-level domain (TLD) servers
  Authoritative DNS servers
Performing the translations
  Local DNS servers and client resolvers

## Slide 20: Distributed Hierarchical Database
com
edu
org
ac
uk
zw
arpa
unnamed root
bar
west
east
foo
my
ac
cam
usr
in-
addr
12
34
56
generic domains
country domains
my.east.bar.edu
usr.cam.ac.uk
12.34.56.0/24

## Slide 21: DNS Root Servers
13 root servers (see http://www.root-servers.org/)
Labeled A through M
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software C. Palo Alto, CA (and 17 other locations)
I Autonomica, Stockholm (plus 3 other locations)
K RIPE London (also Amsterdam, Frankfurt)
m WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign, ( 11 locations)

## Slide 22: TLD and Authoritative DNS Servers
Global Top-level domain (gTLD) servers
  Generic domains (e.g., .com, .org, .edu)
  Country domains (e.g., .uk, .fr, .ca, .jp)
  Managed professionally (e.g., Verisign for .com .net)
Authoritative DNS servers
  Provide public records for hosts at an organization
  For the organization’s servers (e.g., Web and mail)
  Can be maintained locally or by a service provider
22

## Slide 23: Using DNS
Local DNS server (“default name server”)
  Usually near the end hosts who use it
  Local hosts configured with local server (e.g., /etc/resolv.conf) or learn the server via DHCP
Client application
  Extract server name (e.g., from the URL)
  Do gethostbyname() or getaddrinfo() to get address
Server application
  Extract client IP address from socket
  Optional gethostbyaddr() to translate into name

## Slide 24: DNS Queries
Host at cis.poly.edu wants IP address for gaia.cs.umass.edu
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Recursive query: #1
Iterative queries: #2, 4, 6

## Slide 25: Recursive vs. Iterative Queries
Recursive query
  Ask server to get answer for you
  E.g., request 1 and response 8
Iterative query
  Ask server who to ask next
  E.g., all other request-response pairs
requesting host
cis.poly.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server

## Slide 26: DNS Caching
DNS query latency
  E.g., 1 sec latency before starting a download
Caching to reduce overhead and delay
  Small # of top-level servers, that change rarely
  Popular sites visited often
Where to cache?
  Local DNS server
  Browser
requesting host
cis.poly.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server

## Slide 27: DNS Cache Consistency
Cache consistency
  Ensuring cached data is up to date
DNS design considerations
  Cached data is “read only”
  Explicit invalidation would be expensive
Avoiding stale information
  Responses include a “time to live” (TTL) field
  Delete the cached entry after TTL expires

## Slide 28: Setting the Time To Live (TTL)
TTL trade-offs
  Small TTL: fast response to change
  Large TTL: higher cache hit rate
Following the hierarchy
  Top of the hierarchy: days or weeks
  Bottom of the hierarchy: seconds to hours
Tension in practice
  Set low TTLs for load balancing and failover
  Browsers cache for 15-60 seconds

## Slide 29: Negative Caching
Broken domain names are slow to resolve
  Misspellings like www.cnn.comm and www.cnnn.com
  These can take a long time to fail the first time
Remember things that don’t work
  Good to remember that they don’t work
  … so the failure takes less time in the future
But don’t remember for too long
  Use a time-to-live to expire

## Slide 30: DNS Reliability
DNS servers are replicated
  Name service available if at least one replica is up
  Queries can be load balanced between replicas
Retransmission of lost queries
  No response to a query? Try again!
Try alternate servers on timeout
  Exponential back-off when retrying same server

## Slide 31: Conclusions
Network names
  To identify remote end-points
  Readability? Format? Length? Hierarchy?
  Hostnames, IP addresses, and MAC addresses
Network directories
  Key-value stores to map name to address
  Flooding (ARP), local copy, central server
  Hierarchical (DNS) or non-hierarchical (DHT)
More on protocol layers in a few weeks!