## Slide 1: COS 561: Advanced Computer Networks
Jennifer Rexford
(TAs: Mary Hogan and Srikar Kasi)
https://www.cs.princeton.edu/courses/archive/fall20/cos461/561.html

## Slide 2: Data Plane
Streaming algorithms that act on packets
  Matching on some bits, taking a simple action
  … at behest of control and management plane
Wide range of functionality
  Forwarding
  Access control
  Mapping header fields
  Traffic monitoring
  Buffering and marking
  Shaping and scheduling
  Deep packet inspection
Notes: Question to keep in mind: is there a common way to think about all of these data-plane operations

## Slide 3: Packet Forwarding
Control plane computes a forwarding table
  Maps destination address(es) to an output link
Handling an incoming packet
  Match: destination address
  Action: direct the packet to the chosen output link
Switching fabric
  Directs packet from input link to output link
Switching
Fabric
Processor

## Slide 4: Context for the Paper
Programmability
  Active networks (mid-to-late 1990s)
  Software-Defined Networking
High-performance data planes
  Operating system
  FPGAs and Network Processors
  ASICs
Prototyping new research ideas
  Reusable modules
  Simplifying integration into the kernel
  Building community
Programming languages

## Slide 5: OpenFlow
Prioritized list of rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 6: Protocol Independent Switch Architectures
Programmable data plane at “line rate”
  Programmable using languages like P4
Stages
Deparser
Parser
Memory
Persistent State
ALU
Match-
Action
Table

## Slide 7: Click Modular Router

## Slide 8: Click Motivation
Flexibility
  Add new features and enable experimentation
Openness
  Allow users/researchers to build and extend
  (In contrast to most commercial routers)
Modularity
  Simplify the composition of existing features
  Simplify the addition of new features
Speed/efficiency
  Operation (optionally) in the operating system
  Without the user needing to grapple with OS internals

## Slide 9: Router as a Graph of Elements
Large number of small elements
  Each performing a simple packet function
  E.g., IP look-up, TTL decrement, buffering
Connected together in a graph
  Elements inputs/outputs snapped together
  Beyond elements in series to a graph
  E.g., packet duplication or classification
Packet flow as main organizational primitive
  Consistent with data-plane operations on a router
  (Larger elements needed for, say, control planes)

## Slide 10: Click Elements: Push vs. Pull
Packet hand-off between elements
  Directly inspired by properties of routers
  Annotations on packets to carry temporary state
Push processing
  Initiated by the source end
  E.g., when an unsolicited packet arrives (e.g., from a device)
Pull processing
  Initiated by the destination end
  E.g., to control timing of packet processing (e.g., based on a timer or packet scheduler)

## Slide 11: Click Language
Declarations
  Create elements
Connections
  Connect elements
Compound elements
  Combine multiple smaller elements, and treat as single, new element to use as a primitive class
Language extensions through element classes
  Configuration strings for individual elements
  Rather than syntactic extensions to the language
src :: FromDevice(eth0);
ctr :: Counter;
sink :: Discard;
src -> ctr;
ctr -> sink;

## Slide 12: Handlers and Control Socket
Access points for user interaction
  Appear like files in a file system
  Can have both read and write handlers
Examples
  Installing/removing forwarding-table entries
  Reporting measurement statistics
  Changing a maximum queue length
Control socket
  Allows other programs to call read/write handlers
  Command sent as single line of text to the server