## Slide 1: Reasoning about Network Performance
COS 316: Principles of Computer System Design
Lecture 9
Wyatt Lloyd
Slides developed by Nicolaas Kaashoek

## Slide 2: Review: Performance
Why do we care about performance? Speed matters!
- Cost, competitive advantage, user experience
Goal: Deliver as close to hardware performance as possible
This lecture:
- How to send packets over the internet
- Workloads, deployments, and why they matter
Compare between TCP Reno* and BBR Congestion control
* Without slowstart

## Slide 3: Numbers that Matter
Two metrics we care about: latency and bandwidth
Focus on relative differences, not raw numbers!
Latency (RTT): Physical
Dorm to Cycles: ~1ms
Dorm to NYC: ~10ms
Dorm to VA: ~20ms
Dorm to CA: ~60ms
Dorm to EU: ~100ms
Dorm to JP: ~150ms
Dominated by speed of light
Bandwidth: Hardware
Bluetooth: 3 Mbps
Cellular (5G): ~5 Gbps
Wifi: ~10 Gbps
Ethernet: 100 Gbps
Infiniband: 400 Gbps
Dominated by technology

## Slide 4: Hardware that Matters
Computers/Servers
Senders/Receivers
Many on one network
Switches
Coordinate senders/receivers so they work simultaneously
Routers
Route packets from one network to another
Links
WiFi, Bluetooth, Fiber, Coaxial, etc.
Determines bandwidth

## Slide 5: Hardware that Matters
Computers/Servers
Senders/Receivers
Many on one network
Switches
Coordinate senders/receivers so they work simultaneously
Routers
Route packets from one network to another
Links
WiFi, Bluetooth, Fiber, Coaxial, etc.
Determines bandwidth
Notes: Switches work at L2. Routers work at L3. (Datacenter switches typically work at the L3 layer and do IP routing… this terminology is confusing!)

## Slide 6: Putting Hardware Together: Internet
How do you send a packet from your computer to someone?
“The Internet”

## Slide 7: The Internet on Earth

## Slide 8: Loss in Networks
Two sources: congestion and error
- Lots of control over congestion, none over error
Wireless errors:
Bit errors: mostly handle with forward error correction
Link layer collisions: mostly handle with link layer protocol
Interference: tell your neighbor to stop their microwave
Result: variable loss rates from near 0 to quite high
Wired networks:
Inside datacenter: almost 0
Across a city: almost 0 (but a bit higher)
Services degrade dramatically at 1% loss. 5% loss is very bad.

## Slide 9: Workloads Matter
Scenario 1: Single sender, single receiver
Relatively easy. No fairness, just need to get our rate right
Scenario 2: Many different senders
Complex! How do they interact? Fairness?
What metric are we optimizing for? Goodput? Latency?
Takeaway: Workloads matter!
Always think about who is using the system and in what situation

## Slide 10: Comparing CC Algorithms
What’s the metric that we care about?
End-to-end latency of a single task
What are things that contribute to that metric?
Bandwidth
Round-trip latency
Congestion

## Slide 11: Scenario 1 – Princeton Campus
Situation: Uploading your homework to TigerFile
How long to get to the TigerFile Server?
- 1 ms
What’s our bottleneck?
20 packets/ms
Packet = 1000 bytes
What’s our error rate?
- On campus? 0%.

## Slide 12: Scenario 1 – TCP Reno, Single Sender
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Window size | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
Repeating sawtooth pattern. Send 10, 11, 12, 13, … then cut in half at 21!
Every 12ms the pattern repeats. 10 + 11 + 12 + … + 20 + 20 = 185 packets
60ms to send 925 packets, 6 to send the remaining 75
Total time: 66ms
AI: Increase by 1 on successful window
MD: Decrease by half on failed window
Bottleneck Link Bandwidth: 20 packets/ms Bottle link has NO queue
Uploading single file, 1000 packets
RTT: 1ms
Network error rate: 0%
Initial congestion window size: 10 packets
Congestion control protocol: TCP
Notes: Here we have one sender and one receiver.
We’re trying to get 1000 packets through, and don’t start dropping anything until we get a window to size 21.
So, we send 10 + 11 + 12 + 13 + 14 + 15 + 16 + 17 + 18 + 19 + 20 + 21, one of which isn’t delivered, for a total of 185 packets in 12 ms. This pattern then repeats.
Floor(1000/185) = 5. 5 * 185 = 925 and 5 * 12 = 60, so in 60ms we send 925 packets, which leaves 75. 10 + 11 + 12 + 13 + 14 + 15 = 75, so it takes another 5ms to finish the transmission, for a total of 66ms.
There’s probably a fences and posts error here where each cycle actually drops 1 packet which has to be included in the next repetition of the pattern, but this calculation isn’t going to be off by more than a ms, and I think it nicely illustrates what happens in TCP without getting too complex.

## Slide 13: Scenario 1 – TCP Reno, Four Senders
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
Window Size | 10 | 5 | 6 | 3 | 4 | 5 | 6 | 3 | 4 | 5 | 6 | 3 | 4 | 5 | 6 | 3 | 4 | 5
AI: Increase by 1 on successful window
MD: Decrease by half on failed window
All senders start at the same time
Bottleneck Link Bandwidth: 20 packets/ms
Uploading single file, 1000 packets
RTT: 1ms
Network error rate: 0%
Initial congestion window size: 10 packets
Congestion control protocol: TCP
Repeating sawtooth pattern. Send 10, immediate loss! Then 5, 6, overflow again!
Every 4ms the pattern repeats. 3 + 4 + 5 + 5 + … = 17 packets
15 at the start in 3ms. 232ms to send remaining 985 packets
Total time: 235ms
Notes: Here we treat each sender as identical, and are assuming that packets arrive at the link at the same time. That is to say that if sender 1 sends 5 packets, and sender 2 sends 5 packets, and so on, then our link will receive them in the order: s1_p1, s2_p1, s3_p1, s4_p1, s1_p2, s2_p2, s3_p2, s4_p2, …
Here sX_pY means packet Y from sender X.
We make this assumption to make reasoning easier, as it ensures that all the senders behave in an identical manner. In a real network, it’s more likely you’d see more chaotic interleaving of the packets.
The math here is relatively straightforward: we send 10 packets. 5 of those get through. Then 5 more, which all get through, then 6, 5 of which get through. So, in 3ms, we get 15 packets of goodput through the link. That’s the 15 in 3ms.
This leaves us with 985 packets left. The repeating pattern of 3+4+5+5=17 packets will get 986 packets through in 232ms (ceiling(985/17) * 4).
So, our total is 235 ms.
Again, there might be a fences and posts error here with some packets rolling over into a new sending window, but for illustrative purposes this is good enough.

## Slide 14: BBR startup phase
BBR begins with a startup phase
  Ramp up: double sending rate until acked data does not increase past a threshold
  Drain: pace sending at a low rate until data in flight == estimated BDP
We will use a simple model:
  Ramp up: log2(⁡BDP x RTT)
  Drain: 2*BDP worth of extra data  2 RTTs to drain
  Total: log2(⁡BDP x RTT) + 2 RTTs
  Assume maximum throughput throughout

## Slide 15: Scenario 1 – BBR, Single Sender
BBR: First find RTT and Bandwidth estimates
Model: Takes x RTT to find, generates 2 x BDP extra
What’s our BDP? RTT x Bottleneck = 20
4.3ms to find estimates! Then we send at 20.
How long does this take in total?
6.3 ms to find BDP and drain 40 packets.
Assumed max tput for 4.3ms = 86 packets
(1000 – 86)/20 = 45.7 ms to send the rest
Total time: 52ms
Bottleneck Link Bandwidth: 20 packets/ms
Uploading single file, 1000 packets
RTT: 1ms
Network error rate: 0%
Initial congestion window size: 10 packets
Congestion control protocol: BBR
Notes: BBR is a slightly more complex case. The paper gives us two important pieces of information about how long it takes BBR to get a correct estimate of of the RTT and the bottleneck bandwidth.
First, it does a binary search to find the link bandwidth/rtt. This takes log_2 of the actual BDP (which is just RTT * bottleneck bandwidth), multiplied by the RTT to occur. In our situation, that’s log_2 20 * 1ms = 4.3ms.
Additionally, during this process, BBR will overflow the link to be sure it finds the max throughput. In a real deployment, this means that it’s going to enqueue some packets ahead of the bottleneck. To avoid maintaining that queue during normal operation, BBR needs to wait for it to drain. In our example here, where I’ve set the situation to have no queues, that means the sender will need to retransmit those packets that were dropped. Luckily, BBR tells us exactly how many of those packets exist: 2 * BDP, or 40 in our case.
With this, we know it’s going to take 4.3 ms to get our initial, correct sending rate. We’ll also generate 40 extra packets. Sending at 20 packets/ms (our bottleneck throughput) this takes another 2ms to finish, for 6.3ms total to find our estimates. In those 6.3ms, we’ll have sent 6.3 * 20 = 126 packets.
This leaves us with 1000 – 126 = 874 packets left, which we’ll send at exactly 20 packets/ms. This takes 874/20 = 43.7ms, for a total time of 50ms.

## Slide 16: Scenario 1 – BBR, Four Senders
Paper: Takes “a few” cycles to synchronize. Let’s say 3.
What’s our BDP now?
BBR is fair, everyone gets equal share of bottleneck link
BDP = 5
How long will it take us to send all the packets?
Bottleneck Link Bandwidth: 20 packets
Uploading single file, 1000 packets
RTT: 1ms
Network error rate: 0%
Probe time: x RTT + 2 RTT for draining
Initial congestion window size: 10 packets
Notes: See next slide.

## Slide 17: Scenario 1 – BBR, Four Senders
BDP = 5, Probe time = 2.3ms, Overflow packets = 10
3 cycles to sync, for a total of 6.9 ms. That generates 30 packets of overflow, while sending 6.9 * 5 = ~34 packets.
Drain overflow: 30 packets/5=6 RTTs = 6ms (wait this out)
Time to send remaining: (1000 – 34)/5 = 193.2ms.
Total time: 193.2 + 6.9 + 6 = ~206ms
Bottleneck Link Bandwidth: 20 packets/ms
Uploading single file, 1000 packets
RTT: 1ms
Network error rate: 0%
Initial congestion window size: 10 packets
Congestion control protocol: BBR
Notes: Our new BDP here is 5, because we’re only getting 5 packets/ms on the link (our fair share of the bandwidth when there’s four senders).
I’m assuming this is the number BBR uses to get its initial estimates, which should be correct if everyone is estimating at the same time.
There’s no way to easily predict how many estimation cycles it’ll take for all the senders to get the right estimates. 3 is a number I’ve picked that seems reasonable, but it’ll change depending on when each sender joins the network among other factors.
It now takes us log_2(5) = 2.3ms to find the estimates. 2.3 * 3 = 6.9ms for all the senders to get the right estimates. They’ll each have sent 6.9 * 5 = 34.5 packets, rounded down to 34. We round down here because it makes the situation worse for BBR, so is conservative.
During each of these estimation steps, BBR will generate a maximum of 2 x BDP overflow packets. Let’s assume worst case again and say that we’ve generated 3 x 2 x BDP = 30 overflow packets. Those drain in 30/5 = 6RTTs = 6ms.
So, after estimating, we need to transmit: 1000 - 30 - 34 = 936 packets, sending at a rate of 5 packets/ms.
936/5 = 187.2ms. Add our estimation time, and we get a total of 200.1ms. Round that to 200ms.

## Slide 18: Comparing BBR and TCP
Single sender TCP: 66ms
Four senders TCP: 235ms
Single sender BBR: 52ms
Four senders BBR: 206ms
Key point: Performance isn’t magic!
What happens as packets in transmission increases?
Bottleneck Link Bandwidth: 20 packets/ms
Uploading single file, 1000 packets
RTT: 1ms
Network error rate: 0%
Initial congestion window size: 10 packets

## Slide 19: Comparing TCP and BBR 2
Let’s add some more realistic numbers
Packet size: 1000 bytes.
Bottleneck = 100 MB/s, ~100 packets/ms
TCP Sawtooth: 50 + 51 + … + 100 + 100 = 3925 packets/52ms, or ~75 packets/ms
BBR: Sends at a flat 100 packets/ms
How long to send a MB file (1 thousand packets)?
How long to send a GB file (1 million packets)?
Bottleneck Link Bandwidth: 20 packets/ms
Uploading single file, 1000 packets
RTT: 1ms
Network error rate: 0%
Initial congestion window size: 10 packets

## Slide 20: Scenario 2 – Sending Across the WAN
New scenario: Studying abroad at Cambridge. Uploading homework to TigerFile.
How long to get from Cambridge to Princeton?
What’s our bottleneck link?
- Again, hard to say. Let’s use the same: 100 MB/s
What’s our loss rate?
- Assume 1% for demonstrative purposes

## Slide 21: Scenario 2 – TCP
What does TCP do when it sees a lost packet?
- Multiplicative decrease
Contrived loss scenario: every 100th packet is lost
What does the steady state look like?
Prev: 50, 51, …
Now:
Significant decrease in throughput
Bottleneck Link Bandwidth: 100 packets/100ms
RTT: 100ms
Network error rate: every 100th packet
Lossless steady state sending rate: 75 packets/100ms
50,
51,
25,
26,
27,
28,
14,
15,
16,
17,
18,

## Slide 22: Scenario 2 – BBR
How about BBR? What does 1% packet loss do?
BBR uses max—min to estimate network properties
1 missed packet in every 100 won’t change that!
BBR won’t lose any throughput under 1% loss
(goodput is 99 packets/100ms due to the error rate)
Bottleneck Link Bandwidth: 100 packets/100ms
RTT: 100ms
Network error rate: 1%
Lossless steady state sending rate: 100 packets/100ms

## Slide 23: Tradeoff: Fairness
We looked at TCP compared to BBR
Conclusion: BBR outperforms TCP in nearly every situation
But there’s a cost – fairness
BBR looks fantastic when everyone’s using BBR. What about when they’re not?

## Slide 24: Networks are Decentralized
Fairness is a real tradeoff – know nothing about network
Congestion control is decentralized
BBR works particularly well when everyone uses BBR
When can we guarantee this? In datacenters
It’s amazing this works at all!

## Slide 25: Tradeoffs – The Pantheon
See: pantheon.stanford.edu, a testing ground for many congestion control algorithms
Compares many modern congestion control algorithms
Comparison across many different situations/deployments

## Slide 26: Pantheon Results
Results taken from 2020 (no longer running)

## Slide 27: Conclusion
Internet infrastructure is complex, multilayered, and interconnected
Networks are complicated: performance reasoning is hard
Measure, measure, measure!
Networks have many emergent properties
Workloads/deployment scenarios matter.
Always consider the tradeoffs of one system over another.
- Not always directly performance related!