## Slide 1: Introduction Principles of System Design
COS 518: Advanced Computer Systems
Lecture 1
Mike Freedman

## Slide 2: Goals of this course
Introduction to
  Computer systems principles
  Computer systems research
    Historical and cutting-edge research
    How “systems people” think
Learn how to
  Read and evaluate papers
  Give talks and evaluate talks
  Perform basic system design and programming
  Build and evaluate systems

## Slide 3: What is a system?
System
  Inside v. outside: defines interface with environment
  A system achieves specific external behavior
  A system has many components
This class is about the design of computer systems
Much of class will operate at the design level
  Guarantees (semantics) exposed by components
  Relationships of components
  Internals of components that help structure
Notes: Rather than giving you a direct definition, I’ll tell you three properties

## Slide 4: Backrub (Google) 1997

## Slide 5: Google 2012

## Slide 6
100,000s of physical servers
10s MW energy consumption
Facebook Prineville:
$250M physical infro, $1B IT infra

## Slide 7: The central problem: Complexity
Complexity’s hard to define, but symptoms include:
Large number of components
Large number of connections
Irregular structure
No short description
Many people required to design or maintain

## Slide 8: Course Organization

## Slide 9: Learning the material
Instructors
  Professor Mike Freedman
  TA Andrew Or
  Office hours immediately after lecture or by appt
Main Q&A forum: http://www.piazza.com/
Optional textbooks
      Principles of Computer System Design. Saltzer & Kaashoek
      Distributed Systems: Principles and Paradigms. Tanenbaum & Van Steen
      Guide to Reliable Distributed Systems. Birman.

## Slide 10: Format of Course
Introducing a subject
  Lecture + occasional 1 background paper
  Try to present lecture class before reading
Current research results
  Signup to read 1 of ~3 papers per class
  Before class: Carefully read selected paper
  Beginning of class (before presentations): answer a few questions about readings (“quizlet”)
  During class: 1 person presents, others add to discussion

## Slide 11: Course Programming Assignment
New this year: “breadth” graduate courses require HW assignments
Most: Implement RAFT consensus algorithm
  Same assignment as #3 & #4 in COS418
Some of you have already taken 418
  Convert RAFT implementation to communicate with other students’ implementations
  Must successfully interoperate to implement RAFT between independent implementations

## Slide 12: Course Project: Schedule
Groups of 2 per project
Project schedule
  Team selection (2/9, Friday)
  Project proposal (2/23)
  Project selection (3/2): Finalize project
  Project presentation (before 5/15, Dean’s Date)
  Final write-up (5/15, Dean’s Date)

## Slide 13: Course Project: Options
Choice #1: Reproducibility
  Select paper from class (or paper on related topic)
  Re-implement and carefully re-evaluate results
  See detailed proposal instructions on webpage
Choice #2: Novelty (less common)
  Must be in area closely related to 518 topics
  We will take a narrow view on what’s permissible
Both approaches need working code, evaluation

## Slide 14: Course Project: Process
Proposal selection process
  See website for detailed instructions
  Requires research and evaluation plan
  Submit plan via Piazza, get feedback
  For “novelty” track, important to talk with us early
Final report
  Public blog-like post on design, eval, results
  Source code published

## Slide 15: Grading
10% paper presentation(s)
10% participation (in-class, Piazza)
10% in-class Q&A quizlets
20% programming assignments
50% project
  10% proposal
  40% final project

## Slide 16: Organization of semester
Introduction / Background
Storage Systems
Big Data Systems
Applications

## Slide 17: Storage Systems
Consistency
Consensus
Transactions
Key-Value Stores
Column Stores
Flash Disks
Caching

## Slide 18: Big Data Systems
Batch
Streaming
Graph
Machine Learning
Geo-distributed
Scheduling

## Slide 19: Applications
Publish/Subscribe
Distributed Hash Tables (DHTs)
Content Delivery Networks
Blockchain
Security
Privacy

## Slide 20: Principles of System Design

## Slide 21: Systems challenges common to many fields
Emergent properties (“surprises”)
  Properties not evident in individual components become clear when combined into a system
  Millennium bridge, London example

## Slide 22
Notes: Beautiful bridge, supposed to look like a “blade of light”
Opened in 2000 in London
Royal Institute of British Architects – very distinguished and prestigious architectural body had a competition for its design

## Slide 23: Millennium bridge
Small lateral movements of the bridge causes synchronized stepping, which leads to swaying
Swaying leads to more forceful synchronized stepping, leading to more swaying
  Positive feedback loop!
Nicknamed Wobbly Bridge after charity walk on Save the Children
Closed for two years soon after opening for modifications to be made (damping)

## Slide 24: Systems challenges common to many fields
Emergent properties (“surprises”)
Propagation of effects
  Small/local disruption  large/systemic effects
  Automobile design example (S & K)
Notes: (SEGUE: Auto design example on next slide)

## Slide 25: Propagation of effects: Auto design
Want a better ride so increase tire size
Need larger trunk for larger spare tire space
Need to move the back seat forward to accommodate larger trunk
Need to make front seats thinner to accommodate reduced legroom in the back seats
Worse ride than before
Notes: The point is that there is no small change!

## Slide 26: Systems challenges common to many fields
Emergent properties (“surprises”)
Propagation of effects
Incommensurate scaling
  Design for a smaller model may not scale

## Slide 27: Galileo in 1638
“To illustrate briefly, I have sketched a bone whose natural length has been increased three times and whose thickness has been multiplied until, for a correspondingly large animal, it would perform the same function which the small bone performs for its small animal…
Thus a small dog could probably carry on his back two or three dogs of his own size; but I believe that a horse could not carry even one of his own size.”
—Dialog Concerning Two New Sciences, 2nd Day
Notes: His overall point: things that work when small often don’t work when scaled up

## Slide 28: Incommensurate scaling
Scaling a mouse into an elephant?
  Volume grows in proportion to O(x3) where x is the linear measure
  Bone strength grows in proportion to cross sectional area, O(x2)
  [Haldane, “On being the right size”, 1928]
Real elephant requires different skeletal arrangement than the mouse

## Slide 29: Incommensurate scaling: Scaling routing in the Internet
Just 39 hosts as the ARPA net back in 1973

## Slide 30: Incommensurate scaling: Scaling routing in the Internet
Total size of routing tables (for shortest paths): O(n2)
Today’s Internet: Techniques to cope with scale
  Hierarchical routing on network numbers
    32 bit address =16 bit network # and 16 bit host #
  Limit # of hosts/network: Network address translation

## Slide 31: Incommensurate Scaling: Ethernet
All computers share single cable
Goal is reliable delivery
Listen-while-send to avoid collisions
Notes: Ethernet is the most common LAN today.
For example those data jacks on the wall are Ethernet. My office phone.
Originally designed in early 1970s, has evolved since then.
You’ll study it later in the term, but here’s a preview of one of its subtle properties.
Mention 1km early, don’t mention speed of light until late.
The point: expect surprises!

## Slide 32: Will listen-while-send detect collisions?
1 km at 60% speed of light is 5 μs
  A can send 15 bits before first bit arrives at B
Thus A must keep sending for 2×5 μs
  To detect collision if B sends when first bit arrives
Thus, min packet size is 2×5 μs×3 Mbit/s = 30 bits

## Slide 33: From experimental Ethernet to standard
Experimental Ethernet design: 3 Mbit/s
  Default header is 5 bytes = 40 bits
  No problem with detecting collisions
First Ethernet standard: 10 Mbit/s
  Must send for 2 × 20 μs = 400 bits
    But header is just 112 bits
  Need for a minimum packet size!
Solution: Pad packets to at least 50 bytes

## Slide 34: Systems challenges common to many fields
Emergent properties (“surprises”)
Propagation of effects
Incommensurate scaling
Trade-offs
  Many design constraints present as trade-offs
  Improving one aspect of a system diminishes performance elsewhere

## Slide 35: Binary classification trade-off
Have a proxy signal that imperfectly captures real signal of interest
Example: Household smoke detector
Notes: Can trade-off the two different misclassification rates

## Slide 36: Sources of complexity
Cascading and interacting requirements
  Example: Telephone system
    Features: Call Forwarding, reverse billing (900 numbers), Call Number Delivery Blocking, Automatic Call Back, Itemized Billing
  A calls B, B forwards to 900 number, who pays?
A
B
CNDB
ACB + IB
A calls B, B is busy
Once B done, B calls A
A’s # appears on B’s bill
Notes: first diagram: simple forwarding/forwarding interaction

## Slide 37: Interacting Features
Each feature has a spec
An interaction is bad if feature X breaks feature Y
These bad interactions may be fixable…
  But many interactions to consider: huge complexity
  Perhaps more than n2 interactions, e.g. triples
  Cost of thinking about / fixing interaction gradually grows to dominate software costs
Complexity is super-linear

## Slide 38: Sources of complexity
Cascading and interacting requirements
Maintaining high utilization of a scarce resource
  Ex: Single-track railroad line through long canyon
    Use pullout and signal to allow bidirectional op
    But now need careful scheduling
    Emergent property: Train length < pullout length
Notes: first diagram: simple forwarding/forwarding interaction

## Slide 39: Coping with complexity
Modularity
  Divide system into modules, consider each separately
  Well-defined interfaces give flexibility and isolation
Example: bug count in a large, N-line codebase
  Bug count ∝ N
  Debug time ∝ N × bug count ∝ N2
Now divide the N-line codebase into K modules
  Debug time ∝ (N / K)2 × K = N2/K
Notes: How can we tackle complexity? First tool is modularity

## Slide 40: Coping with complexity
Modularity
Abstraction
  Ability of any module to treat others like “black box”
    Just based on interface
    Without regard to internal implementation
  Symptoms
    Fewer interactions between modules
    Less propagation of effects between modules

## Slide 41: Coping with complexity
Modularity
Abstraction
  The Robustness Principle: Be tolerant of inputs and strict on outputs

## Slide 42: Robustness principle in action: The digital abstraction
Notes: Example from digital circuits
Combine logic gates together to form a big combinatorial circuit like you see above
Challenge – noise degrades the signals from each logic gate

## Slide 43: Coping with complexity
Modularity
Abstraction
Hierarchy
  Start with small group of modules, assemble
    Assemble those assemblies, etc.
  Reduces connections, constraints, interactions

## Slide 44: Coping with complexity
Modularity
Abstraction
Hierarchy
Layering
  A form of modularity
  Gradually build up a system, layer by layer
  Example: Internet protocol stack

## Slide 45: Layering on the Internet: The problem
Re-implement every app for every new tx media?
Change apps on any change to tx media (+ vice versa)?
No! But how does the Internet design avoid this?
Applications
Transmission
media
Skype
HTTP
SSH
FTP
Coaxial cable
Fiber optic
Wi-Fi

## Slide 46: Layering on the Internet: Intermediate layers provide a solution
Intermediate layers provide abstractions for app, media
New apps or media need only implement against intermediate layers’ interface
Intermediate layers
Applications
Transmission
media
Skype
HTTP
SSH
FTP
Coaxial cable
Fiber optic
Wi-Fi
Notes: Intermediate layers in this case is TCP and UDP running over IP, the Internet protocol

## Slide 47: Computer systems: The same, but different
Often unconstrained by physical laws
  Computer systems are mostly digital
  Contrast: Analog systems have physical limitations (degrading copies of analog music media)
  Back to the digital static discipline
    Static discipline restores signal levels
    Can scale microprocessors to billions of gates, encounter new, interesting emergent properties
Notes: …like overheating!

## Slide 48: Computer systems: The same, but different
Often unconstrained by physical laws
Unprecedented d(technology)/dt
  Many examples:
    Magnetic disk storage price per gigabyte
    RAM storage price per gigabyte
    Optical fiber transmission speed
  Result: Incommensurate scaling, with system redesign consequences

## Slide 49: Incommensurate scaling on the Internet
Normalized growth since 1981
Number of Internet hosts
Bits/second/$ (approximate)
Speed of light,
Shannon capacity,
Backhoe rental price
Notes: Internet scaling is an example of this. Note the log scale on the y – axis!
Network getting bigger, protocols have to cope.
Incommensurate: unequal orders of magnitude
Amount of internet traffic.

## Slide 50: Summary and lessons
Expect surprises in system design
There is no small change in a system
10-100× increase?  perhaps re-design
Complexity is super-linear in system size
Performance cost is super-linear in system size
Reliability cost is super-linear in system size
Technology’s high rate of change induces incommensurate scaling

## Slide 51: For Wed, everybody reads 1) Lampson’s Hints 2) Saltzer E2E