## Slide 1: Hubs, Switches, and Routers, Oh My!
Mike Freedman
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr20/cos461/

## Slide 2: Today: Hubs, Switches, and Routers, Oh My!
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Application
Transport
Network
Link

## Slide 3
Layer 7
Layer 4
Layer 3
Layer 2
Developed in
late 1970s / early 1980s

## Slide 4: Terminology
Hubs and Repeaters
  Connect machines on same “layer 2” LAN
  Broadcast: All frames are sent out all physical ports
Switches and Bridges
  Connect machines on same “layer 2” LAN
  Only send frames to selected physical port based on destination MAC address
Routers
  Connect between LANs at “layer 3”, e.g., wide area
  Only send packet to selected physical port based on destination IP address

## Slide 5: “Layer 2” Hubs and Switches

## Slide 6: Physical Layer: Repeaters
Distance limitation in local-area networks
  Electrical signal becomes weaker as it travels
  Imposes a limit on the length of a LAN
Repeaters join LANs together
  Analog electronic device
  Continuously monitors electrical signals
  Transmits an amplified copy
6

## Slide 7: Physical Layer: Hubs
Joins multiple input lines electrically
  Designed to hold multiple line cards
  Do not necessarily amplify the signal
Very similar to repeaters
  Also operates at the physical layer
hub
hub
hub
hub
7

## Slide 8: Limitations of Repeaters and Hubs
One large shared link
  Each bit is sent everywhere
  So, aggregate throughput is limited
Cannot support multiple LAN technologies
  Does not buffer or interpret frames
  Can’t interconnect between different rates/formats
Limitations on maximum nodes and distances
  Shared medium imposes length limits
  E.g., cannot go beyond 2500 meters on Ethernet
8

## Slide 9: Link Layer: Bridges
Connects two or more LANs at the link layer
  Extracts destination address from the frame
  Looks up the destination in a table
  Forwards the frame to the appropriate segment
Each segment can carry its own traffic
host
host
host
host
host
host
host
host
host
host
host
host
Bridge
9

## Slide 10: Link Layer: Switches
Typically connects individual computers
  A switch is essentially the same as a bridge
  … though typically used to connect hosts
Supports concurrent communication
  Host A can talk to C, while B talks to D
switch
A
B
C
D
10

## Slide 11: Bridges/Switches: Traffic Isolation
Switch filters packets
  Frame only forwarded to the necessary segments
  Segments can support separate transmissions
hub
hub
hub
switch/bridge
segment
segment
segment
11

## Slide 12: Self Learning: Building the Table
When a frame arrives
  Inspect the source MAC address
  Associate the address with the incoming interface
  Store the mapping in the switch table
  Use a timer to eventually forget the mapping
A
B
C
D
Switch learns how to reach A
12

## Slide 13: Self Learning: Handling Misses
When frame arrives with unfamiliar destination
  Forward the frame out all of the interfaces
  … except for the one where the frame arrived
  Hopefully, this case won’t happen very often!
When in doubt, shout!
13
A
B
C
D

## Slide 14: Switches vs. Hubs
Compared to hubs, Ethernet switches support
  (Y) Larger geographic span
  (M) Similar span
  (C) Smaller span
Compared to hubs, switches provides
  (Y) Higher load on links
  (M) Less privacy
  (C) Heterogenous communication technologies

## Slide 15: Looking closer…

## Slide 16: Basic Router Architecture
Each switch/router has a forwarding table
  Maps destination address to outgoing interface
Basic operation
  Receive packet
  Look at header to determine destination address
  Look in forwarding table to determine output interface
  Modify packet header (e.g., decr TTL, update chksum)
  Send packet to output interface

## Slide 17
Basic operation
  Receive packet
  Look at header to determine destination address
  Look in forwarding table to determine output interface
  Modify packet header (e.g., decr TTL, update chksum)
  Send packet to output interface
Lookup
Address
Data
Hdr
Basic Router Architecture
Address
Table
Update
Header
Queue
Addr
Next Hop
Line Card (I/O)

## Slide 18: Router
Switching
Fabric
Processor
Line Card
Line Card
Line Card
Line Card
Line Card
Line Card
data plane
control plane

## Slide 19: Router
Switching
Fabric
Processor
Line Card
Line Card
Line Card
data plane
Placement, behavior of lookup tables
Design of switching fabric

## Slide 20: Lookup algorithm depends on protocol
Protocol | Mechanism | Techniques
Ethernet (48 bits) MPLS ATM | Exact Match | Direct lookup Associative lookup Hashing Binary tree
IPv4 (32 bits) IPv6 (128 bits) | Longest-Prefix Match | Radix trie Compressed trie TCAM

## Slide 21: Longest Prefix Match
Each packet has destination IP address
Router looks up table entry that matches address
Prefix | Output
68.208.0.0/12 | 1
68.211.0.0/17 | 1
68.211.128.0/19 | 2
68.211.160.0/19 | 2
68.211.192.0/18 | 1
68.211.6.120

## Slide 22: Longest Prefix Match
Each packet has destination IP address
Router looks up table entry that matches address
Benefit of CIDR allocation and LPR
  Efficiency: Prefixes can be allocated at much finger granularity
  Hierarchical aggregation: Upstream ISP can aggregate 2 contiguous prefixes from downstream ISPs to shorter prefix

## Slide 23: How? Address lookup using trie
Prefixes “spelled out” by following path from root
To find the best prefix spell out address in trie
 | Prefixes
A | 111*
B | 10*
C | 1010*
D | 10101
1
1
1
0
1
0
1
A
B
C
D

## Slide 24: How? Address lookup using trie
Prefixes “spelled out” by following path from root
To find the best prefix spell out address in trie
1
1
1
0
1
0
1
A
B
C
D
1 per / lvl = max 32 lookups!
Too slow:
  E.g., “Optical Carrier 48” line (2.5 Gbps) requires 160ns lookup … or 4 memory accesses

## Slide 25: K-ary trie (k=2)
11
11
10
10
 | Prefixes
A | 111*
B | 10*
C | 1010*
D | 10101
10
B
A
A
11
10
C
D
D

## Slide 26: Alternatives to trie for LPM
Content-Address Memory (CAM)
  Input: tag (address)
  Output: value (port
  Exact match, but O(1) in hardware
Ternary CAM
  0, 1, *
  “value” memory cell and “mask” (care / don’t care) cell
LPM via TCAM
  In parallel, search all prefixes for all matches
  Then choose longest match
    Trick: choose first match, but already sorted by prefix length

## Slide 27: Alternatives to trie for LPM

## Slide 28: Decision: Forwarding table per line card
Switching
Fabric
Processor
Line Card
Line Card
Line Card
data plane
Each line card has own forwarding table copy
Prevents central table bottleneck (vs. early routers had table across shared bus)

## Slide 29: Decision: Crossbar switch
????
Processor
Line Card
Line Card
Line Card
Line Card
Line Card
Line Card
data plane
control plane

## Slide 30: Decision: Crossbar switch
Shared bus
  Only one input can speak to one output at a time
Crossbar switch / switched backplane
  Input / output pairs that don’t compete can send in same timeslot

## Slide 31: Crossbar switching
Every input port has connection to every output port
In each timeslot, each input connected to zero or more outputs
1
2
3
4
5
6

## Slide 32: Crossbar switching
Every input port has connection to every output port
In each timeslot, each input connected to zero or more outputs
1
2
3
4
5
6
Good parallelism
Needs scheduling

## Slide 33: Everything gets complicated…
1
2
3
4
5
6
Problem: Head-of-line blocking
  The packet in front of queue blocks packets behind it from being processed
  Say first packet at input 1 wants to go to output 5; second packet at 1 that wants 4 is still blocked

## Slide 34: Everything gets complicated…
1
2
3
4
5
6
Solution: Virtual output queues
  One queue at input per output port
  So avoids head-of-line blocking during crossbar scheduling

## Slide 35: Data, Control, & Management Planes
 | Data | Control | Management
Time-scale | Packet (ns) | Event (10 ms to sec) | Human (min to hours)
Tasks | Forwarding, buffering, filtering, scheduling | Routing, signaling | Analysis, configuration
Location | Line-card hardware | Router software | Humans or scripts
35
Switching
Fabric
Processor

## Slide 36: Cisco 8000 Series Routers
36
Up to 648 400 GbE
260 Tbps backplane

## Slide 37: Conclusions
Physical devices sharing L2 & L3 networks have many common features
  Forward table lookups
  Queueing and backplane switching
  Fast vs. slow paths
    Switches and routers separate routing decisions (control plane) from forwarding actions (data plane)
High speed necessitates innovation
  Specialized hardware
  Software algorithms