## Slide 1: Network Measurement
Mike Freedman
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr20/cos461/

## Slide 2: Why Measure the Network?
Scientific discovery
  Characterizing traffic, topology, performance
  Understanding protocol performance and dynamics
Network operations
  Billing customers
  Detecting, diagnosing, and fixing problems
  Planning outlay of new equipment

## Slide 3: Types of Measurement
active
measurements
packet and flow
measurements,
link statistics
topology,
configuration,
routing
end-to-end
performance
state
traffic
average download
time of a web page
link bit
error rate
link utilization
end-to-end delay
and loss
active topology
traffic matrix
demand matrix
active routes
TCP bulk
throughput

## Slide 4: Traffic Measurement

## Slide 5: Packet Monitoring
Definition
  Passively collecting IP packets on one or more links
  Recording IP, TCP/UDP, or application-layer traces
Scope
  Fine-grain information about user behavior
  Passively monitoring the network infrastructure
  Characterizing traffic and diagnosing problems

## Slide 6: Monitoring a LAN Link
Host A
Host B
Monitor
Shared media (Ethernet, wireless)
Host A
Host B
Host C
Monitor
S
w
i
t
c
h
Multicast switch
Host A
Host B
Bridge/
Monitor
Monitor integrated with a bridge

## Slide 7: Monitoring a WAN Link
Router A
Router B
Monitor
Splitting a point-to-point link
Router A
Line card that does packet sampling

## Slide 8: Selecting the Traffic
Filter to focus on a subset of the packets
  IP addresses/prefixes (e.g., to/from specific sites)
  Protocol (e.g., TCP, UDP, or ICMP)
  Port numbers (e.g., HTTP, DNS, BGP, Napster)
Collect first n bytes of packet
  Medium access control header (if present)
  IP header (typically 20 bytes)
  IP+UDP header (typically 28 bytes)
  IP+TCP header (typically 40 bytes)
  Application-layer message (entire packet)

## Slide 9: What to measure to..
Understand router workload model
  Distribution of packet sizes
Quantify web transfer sizes
  Number of packets/bytes per connection
Which servers are popular & who heavy clients are
  Collect source/destination IP address (on port 80)
  Collection application URLs (harder!)
If a denial-of-service attack is underway
  SYN flooding (spoofable)
  Unusual # requests to particular (expensive) page

## Slide 10: Analysis of IP Header Traces
Source/destination addresses
  Identity of popular Web servers & heavy customers
Distribution of packet delay through the router
  Identification of typical delays and anomalies
Distribution of packet sizes
  Workload models for routers
Burstiness of the traffic on the link over time
  Provisioning rules for allocating link capacity
Throughput between pairs of src/dest addresses
  Detection and diagnosis of performance problems

## Slide 11: TCP Header Analysis
Source and destination port numbers
  Popular applications; parallel connections
Sequence/ACK numbers and packet timestamps
  Out-of-order/lost packets; throughput and delay
Number of packets/bytes per connection
  Web transfer sizes; frequency of bulk transfers
SYN flags from client machines
  Unsuccessful requests; denial-of-service attacks
FIN/RST flags from client machines
  Frequency of Web transfers aborted by clients

## Slide 12: Packet Contents
Application-layer header
  HTTP and RTSP request and response headers
  FTP, NNTP, and SMTP commands and replies
  DNS queries and responses; OSPF/BGP messages
Application-layer body
  HTTP resources (or checksums of the contents)
  User keystrokes in Telnet/Rlogin sessions

## Slide 13: Application-Layer Analysis
URLs from HTTP request messages
  Popular resources/sites; benefits of caching
Meta-data in HTTP request/response messages
  Content type, cacheability, change frequency, etc.
  Browsers, protocol versions, protocol features, etc.
Contents of DNS messages
  Common queries, error frequency, query latency
Contents of Telnet/Rlogin sessions
  Intrusion detection (break-ins, stepping stones)

## Slide 14: Flow Measurement (e.g., NetFlow)

## Slide 15: IP Flows
flow 1
flow 2
flow 3
flow 4
Set of packets that “belong together”
  Source/destination IP addresses and port numbers
  Same protocol, ToS bits, …
  Same input/output interfaces at a router (if known)
Packets that are “close” together in time
  Maximum spacing between packets (e.g. 30 sec)
  E.g.: flows 2 and 4 are different flows due to time

## Slide 16: Flow Abstraction
Not exactly the same as a “session”
  Sequence of related packets may be multiple flows
  Related packets may not follow the same links
  “Session” is hard to measure from inside network
Motivation for this abstraction
  As close to a “session” as possible from outside
  Router optimization for forwarding/access-control
  … might as well throw in a few counters

## Slide 17: Traffic Statistics (e.g., Netflow)
Packet header info
  Source and destination addresses and port #s
  Other IP & TCP/UDP header fields (protocol, ToS)
Aggregate traffic information
  Start and finish time (time of first & last packet)
  Total # of bytes and number of packets in the flow
  TCP flags (e.g., logical OR over sequence of packets)
start
finish
4 packets
1436 bytes
SYN, ACK, & FIN
SYN
ACK
ACK
FIN

## Slide 18: Recording Routing Information
Input and output interfaces
  Input interface is where packets entered the router
  Output interface is “next hop” in forwarding table
Source and destination IP prefix (mask length)
  Longest prefix match on src and dest IP addresses
Switching
Fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
BGP table
forwarding table

## Slide 19: Measuring Traffic as it Flows By
input
output
source AS
source
prefix
source
dest AS
dest
prefix
dest
intermediate AS
Source and destination: IP header
Source and dest prefix: forwarding table or BGP table
Source and destination AS: BGP table

## Slide 20: Packet vs. Flow Measurement
Basic statistics (available from both techniques)
  Traffic mix by IP addresses, port numbers, protocol
  Average packet size
Traffic over time
  Both: traffic volumes on medium-to-large time scale
  Packet: burstiness of traffic on a small time scale
Statistics per TCP connection
  Both: volume of traffic transferred over the link
  Packet: frequency of lost or out-of-order packets

## Slide 21: Collecting Flow Measurements
Router A
Route CPU that generates flow records
…may degrade forwarding performance
Router A
Line card that generates flow records
…more efficient to support
measurement in each line card
Router A
Router B
Monitor
Packet monitor that generates flow records
…third party
CPU

## Slide 22: Mechanics: Flow Cache
Maintain a cache of active flows
  Storage of byte/packet counts, timestamps, etc.
Compute a key per incoming packet
  Concatenation of source, destination, port #s, etc.
Index into the flow cache based on the key
  Creation or updating of an entry in the flow cache
#bytes, #packets, start, finish
#bytes, #packets, start, finish
packet
key
header
key
key

## Slide 23: Mechanics: Evicting Cache Entries
Flow timeout
  Remove flows not receiving a packet recently
  Periodic sequencing to time out flows
  New packet triggers the creation of a new flow
Cache replacement
  Remove flow(s) when the flow cache is full
  Evict existing flow(s) upon creating a cache entry
  Apply eviction policy (LRU, random flow, etc.)
Long-lived flows
  Remove flow(s) persisting a long time (e.g., 30 min)

## Slide 24: Measurement Overhead
Per-packet overhead
  Computing the key and indexing flow cache
  More work when the average packet size is small
  May not be able to keep up with the link speed
Per-flow overhead
  Creation and eviction of entry in the flow cache
  Volume of measurement data (# of flow records)
  Larger # of flows when # packets per flow is small
  May overwhelm system collecting/analyzing data

## Slide 25: Sampling: Packet Sampling
Packet sampling before flow creation
  1-out-of-m sampling of individual packets
  Creation of flow records over the sampled packets
Reducing overhead
  Avoid per-packet overhead on 1 – (1/m) packets
  Avoid creating records for many small flows
time
not sampled
two flows
timeout

## Slide 26: BGP Monitoring

## Slide 27: Motivation for BGP Monitoring
Visibility into external destinations
  What neighboring ASes are telling you
  How you are reaching external destinations
Detecting anomalies
  Increases in number of destination prefixes
  Lost reachability or instability of some destinations
Input to traffic-engineering tools
  Knowing the current routes in the network
Workload for testing routers
  Realistic message traces to play back to routers

## Slide 28: BGP Monitoring: A Wish List
Ideally: know what the router knows
  All externally-learned routes
  Before applying policy and selecting best route
How to achieve this
  Special monitoring session on routers that tells everything they have learned
  Packet monitoring on all links with BGP sessions
If you can’t do that, you could always do…
  Periodic dumps of routing tables
  BGP session to learn best route from router

## Slide 29: Using Routers to Monitor BGP
Talk to operational
routers using SNMP or
telnet at command line
(-) BGP table dumps
are expensive
(+) Table dumps show all alternate routes
(-) Update dynamics lost
(-) Restricted to interfaces provided by vendors
Establish a “passive” BGP
session from a workstation
running BGP software
(+) BGP table dumps do not burden operational routers
(-) Receives only best route from BGP neighbor
(+) Update dynamics captured
(+) Not restricted to interfaces provided by vendors
eBGP or iBGP

## Slide 30: Collect BGP Data From Many Routers
Atlanta
St. Louis
San
Francisco
Denver
Cambridge
Washington, D.C.
Orlando
Chicago
Seattle
Los Angeles
Detroit
Houston
New York
Phoenix
San Diego
Austin
Philadelphia
Dallas
2
Kansas City
BGP is not a flooding protocol
Route
Monitor
Notes: 1
1
1
1
1
1

## Slide 31: BGP Table (“show ip bgp” at RouteViews)
Network Next Hop Metric LocPrf Weight Path
* 3.0.0.0 205.215.45.50 0 4006 701 80 i
* 167.142.3.6 0 5056 701 80 i
* 157.22.9.7 0 715 1 701 80 i
* 195.219.96.239 0 8297 6453 701 80 i
* 195.211.29.254 0 5409 6667 6427 3356 701 80 i
*> 12.127.0.249 0 7018 701 80 i
* 213.200.87.254 929 0 3257 701 80 i
* 9.184.112.0/20 205.215.45.50 0 4006 6461 3786 i
* 195.66.225.254 0 5459 6461 3786 i
*> 203.62.248.4 0 1221 3786 i
* 167.142.3.6 0 5056 6461 6461 3786 i
* 195.219.96.239 0 8297 6461 3786 i
* 195.211.29.254 0 5409 6461 3786 i
AS 80 is General Electric, AS 701 is UUNET, AS 7018 is AT&T
AS 3786 is DACOM (Korea), AS 1221 is Telstra

## Slide 32: BGP Events
Event 1
Event 2
Event 3
Event 4
Group of BGP updates that “belong together”
  Same IP prefix, originating AS, or AS_PATH
Updates that are “close” together in time
  Maximum spacing between packets (e.g. 30 sec)
  E.g.: events 2 and 4 are separated in time

## Slide 33: Conclusions
Measurement is crucial to network operations
  Measure, model, control
  Detect, diagnose, fix
Network measurement is challenging
  Large volume of measurement data
  Multi-dimensional data
Great way to understand the Internet
  Popular applications, traffic characteristics
  Internet topology, routing dynamics